The ERASECHK program will measure the effectiveness of bulk
  erasure of a floppy disk. If you have sensitive data, it would be
  wise to test a floppy after using an eraser to make sure no data
  remains on the disk.

    The program is written in Turbo Pascal (version 3.0) and runs
  under IBM PC-DOS, but it should also work under MS-DOS on IBM-
  PC clones and will probably run under Turbo 2.0. Currently the B:
  drive is hardcoded into the program as the drive the erasechk will
  be performed on.  

    ERASECHK attempts to read each sector on a disk and summarizes
  the results. A normal 360k-byte disk has 720 sectors (40 tracks x  2 
  heads x 9 sectors/track), each of which will be readable (return   
  code 0). A blank disk will have 720 "address mark not found" errors
  (return code 2). Partially erased disks will have mixed results:
  some sectors will be missing, others will have CRC (cyclic redundancy
  check) errors (return code 16), and some will be unaffected.