+----------------------------------------------------+
           !   (C)Copyright Lawrence Lee, Bartlesville, OK      !
           !   I6CGRAFS, Ver 1.00, 1983, 1984, 1985.            !
           !                                                    !
           !   A 16 Color Graphics driver for the IBM PC with   !
           !   - color/graphics adapter & RGB color monitor     !
           !   - at least 64K of read/write memory (may be)     !
           !   - any version of DOS (I think)                   !
           +----------------------------------------------------+

    This program is distributed at no charge.  You are encouraged to
    distribute copies of this program and ALL of its associated files or
    programs to others.  Any of the associated program may not be sold
    or included as part of the distribution of any other product to be
    sold.

    Now that we get the standard prologue off the way ...

    How about 16 color graphics on  IBM PC  equipped with standard color
    graphics adapter and RGB color monitor.  I have written an assembler
    program which provides such support at BIOS level using interrupts.
    All the available functions are available through  INT 10h  which is
    the Video I/O call.

    Programs written in assembler, C, Pascal etc which have access to software
    interrupt may be used to access I6CGRAFS.  I have choosen Turbo Pascal to
    demonstrate how this can be done.  The 16 color graphics functions is
    readily available to Turbo Pascal programs because its screen processings
    are all done through Video I/O interrupt calls.

    The demo files are :-

    I6CGRAFS.DOC     - This document.

    I6CGdemo.BAT     - The batch file used to execute the demo programs in
                       sequence.

    I6CGrafs.COM     - The BIOS level 16 color graphics program.  This
                       program must be executed prior to any other COM files.

    I6CGtext.COM/PAS - Demo program to show text support.

    I6CGart.COM/PAS  - Demo program to show graphics support.  This program
                       is a slight modification of the demo program ART.PAS
                       provided with the Turbo Pascal Compiler (Ver 2.0).
                       Modifications made are documented in the source code.

    I6CGhtpt.COM/PAS - An application program which takes advantage of the 16
                       color dot addressable graphics.  This program displays
                       the transient temperature profile of a flat plate with
                       given temperature boundaries.  This is normally refered
                       to as the heat plate problem.  Refer to any book on Heat
                       Transfer for detail.  This program may be stopped by
                       pressing any key.  (There will be a several seconds
                       delay.)

    I6CGcirc.COM/PAS - Demo program to show color circles along with text.

    I6CGpic.COM/PAS  - Demo program to show multi-color pictorial computer
                       graphics.

    I6CGpicL.DAT     - Data file for I6CGpic.COM.

    I6CGpicR.DAT     - Data file for I6CGpic.COM.


    To execute the demo programs, key in

       I6CGDEMO

    followed by the [Return] key under DOS prompt.

    Please note the following features in all the demo programs.

    A) The 16 color graphics mode is invoked by the procedure
       LoRes(Mode:integer).  This procedure in turn performs the necessary
       video interrupt function call(s).

    B) By default, the cursor is visible ( as shown in I6CGtext ).  The cursor
       may be turned off for cleaner graphics screen ( as shown in I6CGart ).
       I have lumped the cursor on/off function in the LoRes procedure for
       simplicity.  The proper way would be to call LoRes(Mode:integer) to
       activate the 16 color graphics mode ( with cursor visible by default )
       and then call Cursor(Visible:boolean) to turn cursor off.

    C) The use of the standard procedure TextMode or CrtExit is necessary to
       exit the LoRes mode as both DOS and Turbo Pascal are not aware of the
       new screen size in rows and columns.





    The 16 color graphics functions may be availabled to BASIC, FORTRAN etc
    through interface programs written as external assembler routines.  The
    following documents the technical/programming information to access the
    various functions of I6CGRAFS.


    M e m o r y

    Most of the BIO data area is used as documented in the IBM Technical
    Reference.  The followings are exception/addition/extention of the
    use of the BIO data area.

    Hex Address     Usage while in I6CGRAFS mode
    -----------     ----------------------------------------------------------
     0000:007C      (4 bytes) a segment:offset pointer to a 1Kbyte area for
                              graphics character generator for ASCII 128 to
                              255.  Immediately preceding this area is a
                              1Kbyte area for ASCII 0 to 127.
     0040:005E      (1 byte ) line at home position
     0040:005F      (1 byte ) number of rows on screen


    F u n c t i o n   C a l l s

    All function calls are via  INT 10h  which is the ROM BIO Video I/O call.
    Function number is passed to the interrupt service routine through
    register AH.  All registers except AX and as noted are preserved for all
    calls.  Register AX is usually destroyed.


*   (AH)=0         SET_MODE - set graphics mode
    (AL)=10h        80h by  48v dots BW    (10 columns by  6 rows)
         11h        80h by  48v dots Color
         12h       160h by 100v dots BW    (20 columns by 12 rows)
         13h       160h by 100v dots Color

*   (AH)=1         SET_CTYPE - set cursor type
    (CH)=bits 0-4  start scan line for cursor
         bit  5    0 for cursor visible
                   1 for cursor invisible
         bit  6    must always be zero
    (CL)=bits 0-4  end scan line for cursor

*   (AH)=2         SET_CPOS - set cursor location
    (DH)=          character row number
         0 -  5     80 x  48 dots mode
         0 - 11    160 x 100 dots mode
    (DL)=          character column number
         0 -  3     80 x  48 dots mode
         0 - 19    160 x 100 dots mode
    (BH)=          page number
         0 -  3     80 x  48 dots mode
         0         160 x 100 dots mode
    Note:          (DH,DL)=(0,0) is th top left.

*   (AH)=3         READ_CURSOR - read cursor type and location
    (BH)=          page number
         0 -  3     80 x  48 dots mode
         0         160 x 100 dots mode
    On Exit
    DH,DL          row,column of the current cursor location (0,0) is top left
    CX             current cursor mode [Ref. (AH)=1, SET_CTYPE]

*   (AH)=4         READ_LPEN - read light pen
                   + not supported +

*   (AH)=5         ACT_DISP_PAGE - select active display page
    (AL)=0 -  3    new page value (for 80 x 48 dots mode only)

*   (AH)=6         SCROLL_UP - scroll active display page up
    (AL)           number of rows to be scrolled up [Ref.(AH)=0]
                   AL=0 means clear screen
    (CH,CL)        row, column of upper left  corner of scroll
    (DH,DL)        row, column of lower right corner of scroll
    (BL)           color attribute to be used on blank line
                   hi nibble - background (0-15)
                   lo nibble - foreground (0-15)
                   (Only the background color is used, the forground color
                   is ignored.)

*   (AH)=7         SCROLL_DOWN - scroll active display page down
    (AL)           number of rows to be scrolled down [Ref.(AH)=0]
                   AL=0 means clear screen
    (CH,CL)        row, column of upper left  corner of scroll
    (DH,DL)        row, column of lower right corner of scroll
    (BL)           color attribute to be used on blank line
                   hi nibble - background (0-15)
                   lo nibble - foreground (0-15)
                   (Only the background color is used, the forground color
                   is ignored.)

*   (AH)=8         READ_AC_CURRENT - read attribute/character at current
                   cursor location
    (BH)=          page number
         0 -  3     80 x  48 dots mode
         0         160 x 100 dots mode
    On Exit
    AL             character read
                   Caustion !!!!!
                   This program cannot tell the difference between
                   ASCII 032 with ASCII 219,
                   ASCII 220 with ASCII 223, and
                   ASCII 221 with ASCII 222.
                   In these cases, the leading ASCII listed will always be
                   returned.
    AH             color attribute
                   hi nibble - background (0-15)
                   lo nibble - foreground (0-15)

*   (AH)=9         WRITE_AC_CURRENT - write attribute/character at current
                   cursor location
    (BH)=          page number
         0 -  3     80 x  48 dots mode
         0         160 x 100 dots mode
    (CX)           count of characters to write
    (AL)           character to write
    (BL)           color attribute
                   hi nibble - background (0-15)
                   lo nibble - foreground (0-15)

*   (AH)=10        WRITE_C_CURRENT - write character at current cursor
                   location
    (BH)=          page number
         0 -  3     80 x  48 dots mode
         0         160 x 100 dots mode
    (CX)           count of characters to write
    (AL)           character to write

*   (AH)=11        SET_COLOR - set set border color
    (BH)           don't care, will be zero'ed on exit to indicate setting
                   border color
    (BL)=0 - 15    border color

*   (AH)=12        WRITE_DOT - write a graphics dot
    (DX)           y-coordinate relative to current active display page
                   (topmost on screen is 0)
        =-192 to +192         80h x  48v dots mode
            0 to   99        160h x 100v dots mode
    (CX)           x-coordinate (leftmost on screen is 0)
        =   0 to   79         80h x  48v dots mode
            0 to  159        160h x 100v dots mode
    (AL)=0 -  15   color value (if bit 7 is set to 1, then the color is
                   exclusive or'ed with the current contents of the dot.

*   (AH)=13        READ_DOT - read a graphics dot
    (DX)           y-coordinate relative to current active display page
                   (topmost on screen is 0)
        =-192 to +192         80h x  48v dots mode
            0 to   99        160h x 100v dots mode
    (CX)           x-coordinate (leftmost on screen is 0)
        =   0 to   79         80h x  48v dots mode
            0 to  159        160h x 100v dots mode
    On Exit
    AL             color of the dot read (0-15)
                   AL=FFh if (CX,DX) is out of range.

*   (AH)=14        WRITE_TTY - write teletype
    (AL)           character to write
    (BH)=          page number
         0 -  3     80 x  48 dots mode
         0         160 x 100 dots mode

*   (AH)=15        VIDEO_STATE - get current video state
    On Exit
    AL             mode current set [Ref. (AH)=0, SET_MODE]
    AH             number of character column on screen
    BH             current active display page number


+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+- END -+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+