April 26, 1988

                                INLINE ASSEMBLER
                                  Version 2.19


        OVERVIEW

        INLINE.EXE is an assembler designed to produce Inline 8086/8088 
        and 8087 code for Turbo Pascal (tm) versions 3 and 4 programs.  
        Like other assemblers, INLINE accepts as input an assembly 
        language source file and produces an object file.  However, in 
        this case, the 'object' file is an ASCII file consisting of 
        Inline statements which may be inserted into the Turbo Pascal 
        program.

        Figure 1 illustrates a Pascal function with Inline code generated 
        by INLINE using the source file of Figure 2.


        LOADING AND RUNNING INLINE

        First create an EXE file, INLINE.EXE, by compiling INLINE.PAS 
        using version 4 of the Turbo Pascal compiler.  

        INLINE is called at the DOS prompt with two filename parameters 
        specifying the names of the source and object files.  If no 
        extensions are given, .ASM and .OBJ are used by default.  For 
        instance,

          INLINE ABC DEF

        will cause INLINE to look for a source file, ABC.ASM, and create 
        an object file, DEF.OBJ.  Files with no extension may be input or 
        created by using a simple '.' for the extension.

        If the object filename is missing from the command line, an OBJ 
        file will be created using the same name as the source file.  If 
        neither filename is specified, then names will be requested once 
        execution starts.

        Once execution begins, INLINE will run to completion with the 
        only console output being error messages.


        SYNTAX

        The appendix lists the mnemonics accepted by INLINE.  Syntax and 
        mnemonics correspond to that used by most assemblers but note 
        should be made of the following:




                                   1











          1. Turbo Pascal symbols may be used within instruction entries 
             by preceding the symbol with a '>' (16 bit symbol) or a '<' 
             (8 bit symbol).  The characters '+' and '-' are considered 
             part of the symbol.  This allows computations using symbols 
             to be passed on to the compiler where the computation can be 
             made.  For instance, in

                 MOV AX,[>SYMBOL+4]       ;'>SYMBOL+4' is passed on
                 MOV AX,[BP+>SYMBOL+4]    ;again '>SYMBOL+4' is passed on
                 MOV AX,>SYMBOL+4[BP]     ;also acceptable

             Note that

                 MOV AX,[>SYMBOL+4+BP]

             is not correct since the wrong instruction will be generated 
             and '>SYMBOL+4+BP' will be passed on.

          2. Labels (for use with jump instructions) may be defined 
             simply by appending a ':' to the first item on a line.  
             Avoid using CS:, DS:, ES:, and SS: as labels, as these 
             specify segment overrides.

          3. Numerical entries are assumed to be decimal unless preceded 
             by a '$' indicating a hexadecimal entry.  Characters within 
             single quotes may be used for numerical entries as:

                 CMP AL,'a'

          4. Square brackets are used to indicate 'contents of'.  If no 
             square brackets are used, an immediate operand is assumed.

                 MOV AX,[>DATA]  ;Load AX with the contents of DATA.
                 MOV AX,>DATA    ;Load AX with DATA.

          5. Instruction prefixes and segment override prefixes may 
             precede the instruction on the same line or may be included 
             on a previous line.  A colon is optional after the segment 
             prefix.

                 ES: MOV AX,[1234]    ;ok
                 REPNE MOVSB          ;ok
                 MOV AX,ES:[1234]     ;incorrect syntax for INLINE

          6. Comments may be included in the source.  They are delimited 
             by a ';'.

          7. Instructions which don't clearly specify the data size 
             require that BYTE PTR, WORD PTR, DWORD PTR, QWORD PTR, or 
             TBYTE PTR be used.  These may be abbreviated by using the 
             first two letters.



                                   2











                 INC BYTE PTR [>BDATA]
                 DEC WO >WARRAY[DI]
                 FLD QWORD [>DBL_REAL]

          8. JMP instructions may use SHORT, NEAR, or FAR (they should 
             not be abbreviated).  In the absence of one of these words, 
             a SHORT jump will be encoded if the label is already defined 
             and is within range.  If the label is not defined, a NEAR 
             JMP will be encoded unless SHORT is used.

             A FAR CALL or JMP may be made to a direct address by stating 
             both the segment and offset separated by a colon.

                 CALL FAR $1234:$5678

             For Turbo Version 3 only, direct CALL's or JMP's may be made 
             to other Turbo procedures and functions using symbolic 
             names.  The '*' location counter reference is required (not 
             available in version 4) to allow Turbo to determine the 
             correct displacement, as:

                 CALL >PROCNAME-*-2

             Null JMP's which may be required for delay between port 
             calls on the 80286, may be made as;

                 JMP >0        ;or
                 JMP SHORT <0

        Normally INLINE generates only one Inline statement per source 
        file.  However, the 'NEW' pseudo-instruction may be used to 
        terminate one Inline statement and begin another.  Using the NEW 
        instruction, it is possible to create a number of Inline 
        statements from one source file.


        FLOATING POINT INSTRUCTIONS

        An automatic WAIT (FWAIT) opcode is generated for each floating 
        point instruction except for the 'no wait' instructions (those 
        with 'N' for the second letter.  However, the WAIT instruction 
        may be required before a floating point instruction having a 
        segment override to insure the WAIT is properly positioned.

               WAIT
               ES:FMUL DWORD [BX]








                                   3











        CAVEATS

        INLINE has no way of knowing the value of any symbols used so the 
        user should be especially careful when using the '<' byte size 
        specifier.  A case in point is when referring to stack variables, 
        as:

             MOV AX,<ABC[BP]    or
             MOV AX,>ABC[BP]

        The use of '<' here will result in saving one byte but will only 
        work correctly if ABC is in the range -128 to 127.  Stack offsets 
        often exceed this in Turbo 4, so it is much safer to use  '>'.

        Note that just because a constant is byte size does not make it 
        safe to use '<'.  If ABC were defined as =255, then CMP BX,<ABC 
        would not assemble correctly as a constant in the range -128 to 
        127 would be expected.  Here again, it's safer to use '>'.

        Many instructions may be correctly assembled in more than one 
        way.  This has caused some confusion in the past when INLINE 
        produce a byte sequence different from that expected.  When in 
        doubt, check the byte sequence out using DEBUG or run it through 
        UNINLINE for verification.


        RESTRICTIONS

        The object file is limited to 32k.  This includes comments and 
        spaces.

        Symbols (including any addons from + and -) are limited to 32 
        characters.

        Labels may be used in jump statements only and not as data 
        references.  While there is a DB pseudo-opcode, it is not very 
        useful with this restriction.

        The number of statement labels that may be defined is limited 
        only by the heap space available.














                                   4











        VERSIONS

        2.00 Added 8087 instructions.
        2.01 Fixed bug which wiped out INT $A vector.
        2.02 Fixed bug which prevented labels from starting with BY, WO, 
             DW, QW, and TB.
        2.1  Add NEW pseudo-instruction.  Fixed bug which occurred with 
             filenames having no extension.  Other bugs fixed, notably 
             those effecting IN and OUT.
        2.11 Calculate restricted range for short jumps correctly.
             Fix bug so CALL/JMP <register> may be used.
        2.12 Allow CALL and JMP direct instructions.
        2.13 Allow JMP >0 and JMP SHORT <0 for null JMP's.
        2.14 Change output format to better sync with TMAP's line 
             numbers.
        2.15 Fix 'shl cl,1' which assembled as shl cl,cl
        2.16 Change byte size check in MemReg so the likes of
                     MOV [DI+$FE],AX will assemble right.
             Allow ',' in DB pseudo op instruction.
        2.17 Convert source to Turbo 4.
        2.18 Implement the sign extension bit for some instructions
        2.19 Fix problem in 2.18 with sign extension bit on AX,AL 
             instructions.


        (C) Copyright 1985,86,87 by L. David Baldwin.

        INLINE may be copied and distributed freely providing that no fee 
        is charged and it is not part of a package for which a charge is 
        made.

        Please report all bugs, suggestions, and problems to Dave 
        Baldwin, CompuServe ID #76327,53.

             22 Fox Den Rd., (Summer)     144 13th St. East,  (Winter)
             Hollis, NH 03049             Tierra Verde, FL 33715
             (603) 465-7857               (813) 867-3030


             Turbo Pascal is a trademark of Borland International Inc.














                                   5











        FUNCTION Scan(Limit :Integer; Ch :Char; Var T ): Integer;
         {Scan Limit characters for Ch. Return the number of characters
          skipped to find a match.  If not found, return result=Limit.
          Limit may be negative for a backwards scan.}
        Var
          Rslt : Integer;
        begin
        Inline(
          $FC/             {    cld              ;assume forward}
          $8A/$86/>CH/     {    mov al,>Ch[bp]   ;char to search for}
          $8B/$8E/>LIMIT/  {    mov cx,>Limit[bp];bytes to search}
          $09/$C9/         {    or cx,cx         ;check sign}
          $9C/             {    pushf            ;save flags}
          $79/$03/         {      jns x1}
          $F7/$D9/         {    neg cx           ;make positive}
          $FD/             {    std              ;but search in reverse}
          $89/$CA/         {x1: mov dx,cx        ;save full count}
          $C4/$BE/>T/      {    les di,>T[bp]    ;ptr to start}
          $F2/$AE/         {    repne scasb      ;search}
          $75/$01/         {      jne x2}
          $41/             {    inc cx           ;found a match}
          $29/$CA/         {x2: sub dx,cx        ;find count to match}
          $9D/             {    popf}
          $79/$02/         {      jns x3}
          $F7/$DA/         {    neg dx           ;make negative if reverse}
          $89/$96/>RSLT);  {x3: mov >Rslt[bp],dx ;put in function result}
        Scan := Rslt;
        end;

                           Figure 1: Pascal Function using Inline Code

            cld              ;assume forward
            mov al,>Ch[bp]   ;char to search for
            mov cx,>Limit[bp];bytes to search
            or cx,cx         ;check sign
            pushf            ;save flags
              jns x1
            neg cx           ;make positive
            std              ;but search in reverse
        x1: mov dx,cx        ;save full count
            les di,>T[bp]    ;ptr to start
            repne scasb      ;search
              jne x2
            inc cx           ;found a match
        x2: sub dx,cx        ;find count to match
            popf
              jns x3
            neg dx           ;make negative if reverse
        x3: mov >Rslt[bp],dx ;put in function result

                          Figure 2:  INLINE Input File



                                   6











        APPENDIX

          8086/8088 Opcode Mnemonics Recognized by INLINE

                AAA       HLT       JNE       LOOPNZ    ROR    
                AAD       IDIV      JNG       LOOPZ     SAHF   
                AAM       IMUL      JNGE      MOV       SAL    
                AAS       IN        JNL       MOVSB     SAR    
                ADC       INC       JNLE      MOVSW     SBB    
                ADD       INT       JNO       MUL       SCASB  
                AND       INTO      JNP       NEG       SCASW  
                CALL      IRET      JNS       NOP       SHL    
                CBW       JA        JNZ       NOT       SHR    
                CLC       JAE       JO        OR        SS     
                CLD       JB        JP        OUT       STC    
                CLI       JBE       JPE       POP       STD    
                CMC       JC        JPO       POPF      STI    
                CMP       JCXZ      JS        PUSH      STOSB  
                CMPSB     JE        JZ        PUSHF     STOSW  
                CMPSW     JG        LAHF      RCL       SUB    
                CS        JGE       LDS       RCR       TEST   
                CWD       JL        LEA       REP       WAIT   
                DAA       JLE       LES       REPE      XCHG   
                DAS       JMP       LOCK      REPNE     XLAT   
                DB        JNA       LODSB     REPNZ     XOR    
                DEC       JNAE      LODSW     REPZ   
                DIV       JNB       LOOP      RET    
                DS        JNBE      LOOPE     RETF   
                ES        JNC       LOOPNE    ROL    


          8087 Opcode Mnemonics Recognized by INLINE

                F2XM1     FDIVRP    FLD       FNOP      FSTP   
                FABS      FENI      FLD1      FNSAVE    FSTSW  
                FADD      FFREE     FLDCW     FNSTCW    FSUB   
                FADDP     FIADD     FLDENV    FNSTENV   FSUBP  
                FBLD      FICOM     FLDL2E    FNSTSW    FSUBR  
                FBSTP     FICOMP    FLDL2T    FPATAN    FSUBRP 
                FCHS      FIDIV     FLDLG2    FPREM     FTST   
                FCLEX     FIDIVR    FLDLN2    FPTAN     FXAM   
                FCOM      FILD      FLDPI     FRNDINT   FXCH   
                FCOMP     FIMUL     FLDZ      FRSTOR    FXTRACT
                FCOMPP    FINCSTP   FMUL      FSAVE     FYL2X  
                FDECSTP   FINIT     FMULP     FSCALE    FYL2XP1
                FDISI     FIST      FNCLEX    FSQRT     FWAIT  
                FDIV      FISTP     FNDISI    FST    
                FDIVP     FISUB     FNENI     FSTCW  
                FDIVR     FISUBR    FNINIT    FSTENV 





                                   7