November 15, 1985

                        INLINE ASSEMBLER


OVERVIEW

INLINE.COM is an assembler designed to produce Inline 8086/8088 
code for Turbo Pascal (tm) version 3 programs.  Like other 
assemblers, INLINE accepts as input an assembly language source 
file and produces an object file.  However, in this case, the 
'object' file is an ASCII file consisting of Inline statements 
which may be inserted into the Turbo Pascal program.

Figure 1 illustrates a Pascal function with Inline code generated 
by INLINE using the source file of Figure 2.


LOADING AND RUNNING INLINE

INLINE is called at the DOS prompt with two filename parameters 
specifying the names of the source and object files.  If no 
extensions are given, .ASM and .OBJ are used by default.  For 
instance,

  INLINE ABC DEF

will cause INLINE to look for a source file, ABC.ASM, and create 
an object file, DEF.OBJ.  Files with no extension may be input or 
created by using a simple '.' for the extension.

If one or more filenames are missing from the command line, they 
will be requested once execution starts.

Once execution begins, INLINE will run to completion with the 
only console output being error messages.


SYNTAX

The appendix lists the mnemonics accepted by INLINE.  Syntax and 
mnemonics correspond to that used by most assemblers but note 
should be made of the following:

  1. Turbo Pascal symbols may be used within instruction entries 
     by preceding the symbol with a '>' (16 bit symbol) or a '<' 
     (8 bit symbol).  The characters '+' and '-' are considered 
     part of the symbol.  This allows computations using symbols 
     to be passed on to the compiler where the computation can be 
     made.  For instance in




                           1











         MOV AX,[>SYMBOL+4]       ;'>SYMBOL+4' is passed on
         MOV AX,[BP+>SYMBOL+4]    ;again '>SYMBOL+4' is passed on
         MOV AX,>SYMBOL+4[BP]     ;also acceptable

     Note that

         MOV AX,[>SYMBOL+4+BP]

     is not correct since the wrong instruction will be generated 
     and '>SYMBOL+4+BP' will be passed on.

  2. Labels (for use with jump instructions) may be defined 
     simply by appending a ':' to the first item on a line.

  3. Numerical entries are assumed to be decimal unless preceded 
     by a '$' indicating a hexadecimal entry.  Characters within 
     single quotes may be used for numerical entries as:

         CMP AL,'a'

  4. Square brackets are used to indicate 'contents of'.  If no 
     square brackets are used, an immediate operand is assumed.

         MOV AX,[>DATA]  ;Load AX with the contents of DATA.
         MOV AX,>DATA    ;Load AX with DATA.

  5. Instruction prefixes and segment override prefixes may 
     precede the instruction on the same line or may be included 
     on a previous line.

  6. Comments may be include in the source.  They are delimited 
     by a ';'.

  7. Instructions which don't clearly specify the data size 
     require that BYTE PTR or WORD PTR be used.  These may be 
     abbreviated to BY or WO.

         INC BYTE PTR [>BDATA]
         DEC WO >WARRAY[DI]

  8. JMP instructions may use SHORT, NEAR, or FAR (they should 
     not be abbreviated).  In the absence of one of these words, a 
     SHORT jump will be encoded if the label is already defined 
     and is within range.  If the label is not defined, a NEAR 
     JMP will be encoded unless SHORT is used.

     A FAR CALL or JMP may be made to a direct address by stating 
     both the segment and offset separated by a colon.

         CALL FAR $1234:$5678




                           2











RESTRICTIONS

The object file is limited to 32k.  This includes comments and 
spaces.

Symbols (including any addons from + and -) are limited to 32 
characters.

Labels may be used in jump statements only and not as data 
references.  While there is a DB pseudo-opcode, it is not very 
useful with this restriction.

The number of statement labels that may be defined is limited 
only by the heap space available.


Please report all bugs, suggestions, and problems to Dave 
Baldwin, CompuServe ID #76327,53.




































                           3












FUNCTION SCAN(LIMIT :INTEGER; CH :CHAR; VAR T ): INTEGER;
{SCAN LIMIT CHARACTERS FOR CH. RETURN THE NUMBER OF CHARACTERS
 SKIPPED TO FIND A MATCH.  IF NOT FOUND, RETURN RESULT=LIMIT.
 LIMIT MAY BE NEGATIVE FOR A BACKWARDS SCAN.}
BEGIN    {SCAN MUST BE FAST--USE ASSEMBLY LANGUAGE}
Inline(
  $FC             {    CLD              ;ASSUME FORWARD}                      
  /$8A/$46/<CH    {    MOV AL,<CH[BP]   ;CHAR TO SEARCH FOR}                  
  /$8B/$4E/<LIMIT {    MOV CX,<LIMIT[BP];BYTES TO SEARCH}                     
  /$09/$C9        {    OR CX,CX         ;CHECK SIGN}                          
  /$9C            {    PUSHF            ;SAVE FLAGS}                          
  /$79/$03        {     JNS X1}                                               
  /$F7/$D9        {    NEG CX           ;MAKE POSITIVE}                       
  /$FD            {    STD              ;BUT SEARCH IN REVERSE}               
  /$89/$CA        {X1: MOV DX,CX        ;SAVE FULL COUNT}                     
  /$C4/$7E/<T     {    LES DI,<T[BP]    ;PTR TO START}                        
  /$F2/$AE        {    REPNE: SCASB     ;SEARCH}                              
  /$75/$01        {     JNE X2}                                               
  /$41            {    INC CX           ;FOUND A MATCH}                       
  /$29/$CA        {X2: SUB DX,CX        ;FIND COUNT TO MATCH}                 
  /$9D            {    POPF}                                                  
  /$79/$02        {     JNS X3}                                               
  /$F7/$DA        {    NEG DX           ;MAKE NEGATIVE IF REVERSE}            
  /$89/$56/$0C    {X3: MOV [BP+$C],DX   ;PUT IN FUNCTION RESULT}              
);
END;

           Figure 1: Pascal Function using Inline Code


    CLD              ;ASSUME FORWARD
    MOV AL,<CH[BP]   ;CHAR TO SEARCH FOR
    MOV CX,<LIMIT[BP];BYTES TO SEARCH
    OR CX,CX         ;CHECK SIGN
    PUSHF            ;SAVE FLAGS
     JNS X1
    NEG CX           ;MAKE POSITIVE
    STD              ;BUT SEARCH IN REVERSE
X1: MOV DX,CX        ;SAVE FULL COUNT
    LES DI,<T[BP]    ;PTR TO START
    REPNE: SCASB     ;SEARCH
     JNE X2
    INC CX           ;FOUND A MATCH
X2: SUB DX,CX        ;FIND COUNT TO MATCH
    POPF
     JNS X3
    NEG DX           ;MAKE NEGATIVE IF REVERSE
X3: MOV [BP+$C],DX   ;PUT IN FUNCTION RESULT

                  Figure 2:  INLINE Input File



                           4













APPENDIX

  8086/8088 Opcode Mnemonics Recognized by INLINE

        AAA       HLT       JNE       LOOPNZ    ROR    
        AAD       IDIV      JNG       LOOPZ     SAHF   
        AAM       IMUL      JNGE      MOV       SAL    
        AAS       IN        JNL       MOVSB     SAR    
        ADC       INC       JNLE      MOVSW     SBB    
        ADD       INT       JNO       MUL       SCASB  
        AND       INTO      JNP       NEG       SCASW  
        CALL      IRET      JNS       NOP       SHL    
        CBW       JA        JNZ       NOT       SHR    
        CLC       JAE       JO        OR        SS     
        CLD       JB        JP        OUT       STC    
        CLI       JBE       JPE       POP       STD    
        CMC       JC        JPO       POPF      STI    
        CMP       JCXZ      JS        PUSH      STOSB  
        CMPSB     JE        JZ        PUSHF     STOSW  
        CMPSW     JG        LAHF      RCL       SUB    
        CS        JGE       LDS       RCR       TEST   
        CWD       JL        LEA       REP       WAIT   
        DAA       JLE       LES       REPE      XCHG   
        DAS       JMP       LOCK      REPNE     XLAT   
        DB        JNA       LODSB     REPNZ     XOR    
        DEC       JNAE      LODSW     REPZ   
        DIV       JNB       LOOP      RET    
        DS        JNBE      LOOPE     RETF   
        ES        JNC       LOOPNE    ROL    





     Turbo Pascal is a trademark of Borland International Inc.

















                           5