January 20, 1985

                        INLINE ASSEMBLER
                           Version 2.0


OVERVIEW

INLINE.COM is an assembler designed to produce Inline 8086/8088
and 8087 code for Turbo Pascal (tm) version 3 programs.  Like
other assemblers, INLINE accepts as input an assembly language
source file and produces an object file.  However, in this case,
the 'object' file is an ASCII file consisting of Inline
statements which may be inserted into the Turbo Pascal program.

Figure 1 illustrates a Pascal function with Inline code generated
by INLINE using the source file of Figure 2.


LOADING AND RUNNING INLINE

INLINE is called at the DOS prompt with two filename parameters
specifying the names of the source and object files.  If no
extensions are given, .ASM and .OBJ are used by default.  For
instance,

  INLINE ABC DEF

will cause INLINE to look for a source file, ABC.ASM, and create
an object file, DEF.OBJ.  Files with no extension may be input or
created by using a simple '.' for the extension.

If one or more filenames are missing from the command line, they
will be requested once execution starts.

Once execution begins, INLINE will run to completion with the
only console output being error messages.


SYNTAX

The appendix lists the mnemonics accepted by INLINE.  Syntax and
mnemonics correspond to that used by most assemblers but note
should be made of the following:

  1. Turbo Pascal symbols may be used within instruction entries
     by preceding the symbol with a '>' (16 bit symbol) or a '<'
     (8 bit symbol).  The characters '+' and '-' are considered
     part of the symbol.  This allows computations using symbols
     to be passed on to the compiler where the computation can be
     made.  For instance in



                           1











         MOV AX,[>SYMBOL+4]       ;'>SYMBOL+4' is passed on
         MOV AX,[BP+>SYMBOL+4]    ;again '>SYMBOL+4' is passed on
         MOV AX,>SYMBOL+4[BP]     ;also acceptable

     Note that

         MOV AX,[>SYMBOL+4+BP]

     is not correct since the wrong instruction will be generated
     and '>SYMBOL+4+BP' will be passed on.

  2. Labels (for use with jump instructions) may be defined
     simply by appending a ':' to the first item on a line.

  3. Numerical entries are assumed to be decimal unless preceded
     by a '$' indicating a hexadecimal entry.  Characters within
     single quotes may be used for numerical entries as:

         CMP AL,'a'

  4. Square brackets are used to indicate 'contents of'.  If no
     square brackets are used, an immediate operand is assumed.

         MOV AX,[>DATA]  ;Load AX with the contents of DATA.
         MOV AX,>DATA    ;Load AX with DATA.

  5. Instruction prefixes and segment override prefixes may
     precede the instruction on the same line or may be included
     on a previous line.  A colon is optional after the segment
     prefix.

         ES: MOV AX,[1234]    :ok
         REPNE MOVSB          :ok
         MOV AX,ES:[1234]     :incorrect syntax for INLINE

  6. Comments may be included in the source.  They are delimited
     by a ';'.

  7. Instructions which don't clearly specify the data size
     require that BYTE PTR, WORD PTR, DWORD PTR, QWORD PTR, or
     TBYTE PTR be used.  These may be abbreviated by using the
     first two letters.

         INC BYTE PTR [>BDATA]
         DEC WO >WARRAY[DI]
         FLD QWORD [>DBL_REAL]

  8. JMP instructions may use SHORT, NEAR, or FAR (they should
     not be abbreviated).  In the absence of one of these words, a
     SHORT jump will be encoded if the label is already defined
     and is within range.  If the label is not defined, a NEAR
     JMP will be encoded unless SHORT is used.


                           2












     A FAR CALL or JMP may be made to a direct address by stating
     both the segment and offset separated by a colon.

         CALL FAR $1234:$5678


RESTRICTIONS

The object file is limited to 32k.  This includes comments and
spaces.

Symbols (including any addons from + and -) are limited to 32
characters.

Labels may be used in jump statements only and not as data
references.  While there is a DB pseudo-opcode, it is not very
useful with this restriction.

The number of statement labels that may be defined is limited
only by the heap space available.


Please report all bugs, suggestions, and problems to Dave
Baldwin, CompuServe ID #76327,53.




     Turbo Pascal is a trademark of Borland International Inc.
























                           3












FUNCTION SCAN(LIMIT :INTEGER; CH :CHAR; VAR T ): INTEGER;
{SCAN LIMIT CHARACTERS FOR CH. RETURN THE NUMBER OF CHARACTERS
 SKIPPED TO FIND A MATCH.  IF NOT FOUND, RETURN RESULT=LIMIT.
 LIMIT MAY BE NEGATIVE FOR A BACKWARDS SCAN.}
BEGIN    {SCAN MUST BE FAST--USE ASSEMBLY LANGUAGE}
Inline(
  $FC             {    CLD              ;ASSUME FORWARD}
  /$8A/$46/<CH    {    MOV AL,<CH[BP]   ;CHAR TO SEARCH FOR}
  /$8B/$4E/<LIMIT {    MOV CX,<LIMIT[BP];BYTES TO SEARCH}
  /$09/$C9        {    OR CX,CX         ;CHECK SIGN}
  /$9C            {    PUSHF            ;SAVE FLAGS}
  /$79/$03        {     JNS X1}
  /$F7/$D9        {    NEG CX           ;MAKE POSITIVE}
  /$FD            {    STD              ;BUT SEARCH IN REVERSE}
  /$89/$CA        {X1: MOV DX,CX        ;SAVE FULL COUNT}
  /$C4/$7E/<T     {    LES DI,<T[BP]    ;PTR TO START}
  /$F2/$AE        {    REPNE: SCASB     ;SEARCH}
  /$75/$01        {     JNE X2}
  /$41            {    INC CX           ;FOUND A MATCH}
  /$29/$CA        {X2: SUB DX,CX        ;FIND COUNT TO MATCH}
  /$9D            {    POPF}
  /$79/$02        {     JNS X3}
  /$F7/$DA        {    NEG DX           ;MAKE NEGATIVE IF REVERSE}
  /$89/$56/$0C    {X3: MOV [BP+$C],DX   ;PUT IN FUNCTION RESULT}
);
END;

           Figure 1: Pascal Function using Inline Code


    CLD              ;ASSUME FORWARD
    MOV AL,<CH[BP]   ;CHAR TO SEARCH FOR
    MOV CX,<LIMIT[BP];BYTES TO SEARCH
    OR CX,CX         ;CHECK SIGN
    PUSHF            ;SAVE FLAGS
     JNS X1
    NEG CX           ;MAKE POSITIVE
    STD              ;BUT SEARCH IN REVERSE
X1: MOV DX,CX        ;SAVE FULL COUNT
    LES DI,<T[BP]    ;PTR TO START
    REPNE: SCASB     ;SEARCH
     JNE X2
    INC CX           ;FOUND A MATCH
X2: SUB DX,CX        ;FIND COUNT TO MATCH
    POPF
     JNS X3
    NEG DX           ;MAKE NEGATIVE IF REVERSE
X3: MOV [BP+$C],DX   ;PUT IN FUNCTION RESULT

                  Figure 2:  INLINE Input File



                           4













APPENDIX

  8086/8088 Opcode Mnemonics Recognized by INLINE

        AAA       HLT       JNE       LOOPNZ    ROR
        AAD       IDIV      JNG       LOOPZ     SAHF
        AAM       IMUL      JNGE      MOV       SAL
        AAS       IN        JNL       MOVSB     SAR
        ADC       INC       JNLE      MOVSW     SBB
        ADD       INT       JNO       MUL       SCASB
        AND       INTO      JNP       NEG       SCASW
        CALL      IRET      JNS       NOP       SHL
        CBW       JA        JNZ       NOT       SHR
        CLC       JAE       JO        OR        SS
        CLD       JB        JP        OUT       STC
        CLI       JBE       JPE       POP       STD
        CMC       JC        JPO       POPF      STI
        CMP       JCXZ      JS        PUSH      STOSB
        CMPSB     JE        JZ        PUSHF     STOSW
        CMPSW     JG        LAHF      RCL       SUB
        CS        JGE       LDS       RCR       TEST
        CWD       JL        LEA       REP       WAIT
        DAA       JLE       LES       REPE      XCHG
        DAS       JMP       LOCK      REPNE     XLAT
        DB        JNA       LODSB     REPNZ     XOR
        DEC       JNAE      LODSW     REPZ
        DIV       JNB       LOOP      RET
        DS        JNBE      LOOPE     RETF
        ES        JNC       LOOPNE    ROL


  8087 Opcode Mnemonics Recognized by INLINE

        F2XM1     FDIVRP    FLD       FNOP      FSTP
        FABS      FENI      FLD1      FNSAVE    FSTSW
        FADD      FFREE     FLDCW     FNSTCW    FSUB
        FADDP     FIADD     FLDENV    FNSTENV   FSUBP
        FBLD      FICOM     FLDL2E    FNSTSW    FSUBR
        FBSTP     FICOMP    FLDL2T    FPATAN    FSUBRP
        FCHS      FIDIV     FLDLG2    FPREM     FTST
        FCLEX     FIDIVR    FLDLN2    FPTAN     FXAM
        FCOM      FILD      FLDPI     FRNDINT   FXCH
        FCOMP     FIMUL     FLDZ      FRSTOR    FXTRACT
        FCOMPP    FINCSTP   FMUL      FSAVE     FYL2X
        FDECSTP   FINIT     FMULP     FSCALE    FYL2XP1
        FDISI     FIST      FNCLEX    FSQRT     FWAIT
        FDIV      FISTP     FNDISI    FST
        FDIVP     FISUB     FNENI     FSTCW
        FDIVR     FISUBR    FNINIT    FSTENV



                           5