RUN96.ARC

   FORMAT96.COM
   FORMAT96.PAS  ....formats 720k diskettes in ds dd 96 tpi drive
                     on PC compatible.

   new96.dvd     ....device driver to read and write these 720k disks
                     on PC compatible

   new96.asm     ....source for above driver, derived from Zenith
                     MS-DOS 2.11 bios, Copyright 1983-4, Zenith
                     Data Systems


If you have some 96 tpi drives left over from your CP/M days, here's
a way to put them to good use on your Z-150. They will provide 720k
each of storage under DOS 2.11 or higher.

1) Your cable with 34 pin plug will plug onto the extra plug
   inside on the Z-150 disk controller. If you have a Z-158,
   you'll have figure out how to daisy-chain it to existing
   drive cables, since there is only one plug. If you have the
   37 pin DB connection on the back of the disk controller, you
   don't have a Zenith, but once you figure out the hardware,
   the software will work fine.

2) For the Z-150 configure the drives as DS0 and DS1, NOT
   DS2 and DS3.

3) Edit the config.sys file on boot disk to include
   DEVICE=NEW96.DVD

4) Copy the device driver NEW96.DVD onto the main directory of the
   boot disk.

5) Boot the system and format some disks using FORMAT96.COM.

6) Please note that the Z-150 believes the drive numbers set on the
   system board. I declare only two disk drives, and that's all that
   DOS knows about directly. The external drives are handled via
   the device driver above. The Z-158 is a little different. It does
   a hardware check instead of checking switches, so it will try to
   use the external drives as C: and D: respectively. Without other
   drives about, the driver would use the external drives as E: and
   F:. One solution is to use one of the preboot programs that lie
   about the hardware extant. Otherwise, be careful not to use the
   drives C: and D:

7) If you use DOS 3.2 or higher, you don't need these files, since the
   ability to use 96 tpi coincides with the 3.5" support.

8) See the assembly listing for information on customizing.

Clarence Wilkerson  January 27, 1987
Released for non-commercial usage only.