[1;4mTURBOCOMM[m

                         A Terminal Emulation Program
                  
                    by Stew Stryker, RONNIE Support Group

------------------------------------------------------------------------------
                               [4mDISCLAIMER[m

      The author and Digital Equipment Corp absolve  themselves  of  any
      possible  warranties  as  to the capabilities of this program, the
      contents of this document, and specifically disclaim  any  implied
      warranties  of  effectiveness.    They shall not be liable for any
      lost profits, or for any claim or demand against them.

      The program is donated to the public domain, and  as  such  should
      not  be  distributed  for profit.  The program is provided "as is"
      and no technical support  by  Digital  or  the  author  should  be
      assumed. 
------------------------------------------------------------------------------



      [4mINTRODUCTION[m

      This terminal emulation program was  written  entirely  in  MS-DOS
      Turbo Pascal (tm Borland International) for the DEC Rainbow.  It's
      main purpose is to act as an example program showing  how  to  use
      the  MS-DOS  communication  library.    Its secndary purpose is to
      provide support for ReGIS emulation in the Digital A-to-Z environ-
      ment.  It requires MS-DOS 2.05 or greater to run.



      [4mFEATURES[m

      Along with providing basic terminal emulation  capabilities,  this
      package supports:

        * User selection of baud rate on program startup
        * Directing characters received from the host to the local printer
        * Sending text files to the host computer
        * Receiving text files from the host computer
        * User selection of either VT2xx or VT102 emulation
        * Digital's A-to-Z video graphics requirements
        * ReGIS terminal emulation software
        * Terminal Identification inquiries
        * Full function key support
    	* Enter and save your own function key definitions
        * Commands to change Numeric Keypad mode
        * Terminal resets escape sequence trapping
        * Printer controller commands
        * Responding correctly to Printer Status Inquiries
        * The Break key
                                     


      [4mDIRECTIONS[m

      [1mSTARTING THE PROGRAM:[m
      
                type:         [4mTC[m {T} {VT102} {baud rate}<CR>

      
      The braces {} in the command line indicate that those portions are
      optional.

      The 'T' indicates that you wish to go immediately into [4mT[merminal
      emulation mode, by-passing the initial help display.

      The default terminal emulation mode is a VT2xx.   You  may  select
      VT102 emulation by typing 'VT102' in the command line.

      The 'baud rate' selects the baud rate you want the program to  run
      at  (which,  of course, must be compatible with your modem or data
      line).  The baud rate may be one of the following:

                  110 150 300 600 1200 2400 4800 9600

      If no baud  rate  is  selected,  the  program  uses  your  default
      communications settings (established in the Rainbow Setup mode).

      The program first displays help information  on  how  to  use  the
      function  keys.    At  this  point, you either press <DO> to enter
      terminal emulation mode, <HELP> for more information, or <EXIT> to
      return to the operating system.

      For example, to start the program running at 1200 baud instead  of
      your  default  baud  rate,  and skipping over the initial display,
      type:

                                    [4mTC T 1200[m<CR>



      [1mTO USE THE FUNCTION KEYS[m
      [1mONCE YOU ARE IN TERMINAL EMULATION:[m

      All the function keys, except <PRINT SCREEN>,  <BREAK>  and  <F4>,
      will  transmit  their  standard  escape  sequences  to  your  host
      computer.

        <BREAK> will send a break signal for .25 seconds.
        
        <F4> puts you in command mode for a single command.
        
        <PRINT> does nothing.
                                                          


      [1mCOMMAND MODE:[m
      
      From terminal emulation mode, press the [1m<F4>[m key, followed
      by the letter highlighted for the function you want:

        [1;4mC[0mlose      - If you are receiving a text file from the
                     host computer, this will stop receiving the
                     text, and close the file.  When you've success-
                     fully closed the file, your screen will flash.
                           
        [1;4mD[0misconnect - Drops the DTR signal to your modem, which
                     will hang up your phone.

        [1;4mP[0mrinter    - Toggles sending the displayed text to your
                     printer on and off.

        [1;4mQ[0muit       - Disconnect and exit.

        [1;4mR[0meceive    - Allows you to capture all characters from
                     your host onto a file on your Rainbow.

        [1;4mS[0mend       - Lets you send a text file from your Rainbow
                     to your host computer.

        e[1;4mX[0mit       - Ends running TurboComm.  This does not drop 
                     your DTR signal, so that your modem may still be con-
                     nected to your host computer.

      If you type any other character, besides  those  listed  above,  a
      line of help text will be displayed.

      You can  also  define  most of the function keys on your keyboard, 
      including: 
      
      	    INTERRUPT	    	FIND    	    	F17
      	    RESUME  	    	INSERT  	    	F18
      	    CANCEL  	    	REMOVE  	    	F19
      	    MAIN SCREEN	    	SELECT  	    	F20
      	    EXIT    	    	PREV SCREEN 	    	HELP
      	    ADDTNL OPTIONS  	NEXT SCREEN 	    	DO
      
      These  keys  are  defined  from  the command mode, by pressing the 
      function  key  you  wish  to  redefine.    You  then  type in your 
      definition, and  press  <F4>  to end the definition.  A definition 
      may contain any sequence of less than 80 keyboard characters.  

      When you exit TurboComm, you will be asked if you wish to save the 
      definitions.  If so,  you  will  be  prompted for a filename, with 
      TC.KEY as the default.  If you have defined a default function key 
      directory (see below), the file will be created in that directory, 
      otherwise, it will be created in the current directory.

      The next time you start up TurboComm,  the function key definition 
      file will be loaded automatically.
      

      [4mDEFINING A DEFAULT FUNCTION KEY DIRECTORY[m
      
      With the  latest  version  of  TurboComm, you can define a default 
      directory for your  function key definitions.  TurboComm will read 
      the MS-DOS Environmental Variable  'TC_DIR'  for  the  name of the 
      directory you keep your key  definition  files.  This will be used 
      for both the default function key  file,  as well as any you might 
      use  on  the TC command line.  That  is,  if  you  define  TC_DIR, [1mall[m 
      your function key definition files must reside there.
      
      For example, type:   [4mSET TC_DIR=E:\COMMAND[m

      would cause TC to look for TC.KEY in E:\COMMAND subdirectory.


      [4mTO COMPILE TURBOCOMM SOURCE CODE[m
      
      (You can run TC.COM directly, without recompiling the source code.
      If  you  want  to  modify  the program yourself, you'll need these
      instructions.)

      First, you must break the library file, TC.LBR, into its  separate
      files  with  the  LU.EXE utility (not included).  To break out all
      the components, type:  
                            LU A TC.LBR<cr>


      Next, you will probably want to edit the  main  file  (TC.PAS)  to
      match  the  version of MS-DOS Turbo Pascal you're using.  This was
      originally developed under Turbo Pascal version 2.0.  At the  last
      minute,  my  update  to  3.0  arrived  and  I modified some of the
      procedures to take advantage of some new capabilities.   Therefore
      some of the code requires Turbo Pascal 3.0 or greater.

      I did the only decent thing, and left the version 2.0 code in  the
      program,  but  commented  it  out.  If you're compiling with Turbo
      3.0, you can compile this "as is" (Though you may want  to  remove
      the  version  2.0  code  altogether.) If you are still using Turbo
      2.0, search through the source code in TC.PAS for  all  occurances
      of 'Turbo Pascal 3.0', and remove those routines.  Then search for
      the sections marked with '< 3.0' and remove the comment marks ( {}
      ), to activate those functions.

      After you've created the version of TC.PAS you  need,  you  simply
      compile it as you would any other Turbo Pascal program.