Commonly used Basic Peeks, Pokes and Subroutines

    Due to the lack of a comprehensive, published directory of commonly used
    pokes, peeks and subroutines this list has been compiled by the SMUG
    PROSIG as well as a many other hardworking PD sources. Thanks and a tip
    of the hat to all contributors! Additions to the list are encouraged and
    should be address to:

                 Don Watkins, CIS IBMSIG 76003,252

    There are, of course no warrenties or guarentees that any of stuff works
    and furthermore, if it blows up your machine it ain't my fault.
    ------------------------------------------------------------------------

    By specifying a DEF SEG=&H40 in any BASIC program, it is possible to
    reference the following vectors (fields) in the ROM BIOS area by using a
    PEEK function and the following offsets from the current segment as
    defined by the DEF SEG statement.


     &H0       -  RS232 Addresses on your IBM PC.
                  This will allow you to tell how many (up to
                  four) async cards are attached, if any.
     &H8       -  Printer Addresses on your IBM PC.
                  This will tell you what printer addresses,
                  and how many (up to four) exist. Each is
                  addressed by a two byte Hex value.
     &H10      -  Equipment Flag.
                  This field describes the setting of the
                  options switches. It describes what optional
                  devices are attached to the system. The
                  following lists the bit-significance of this
                  field:
                  Bit 0 - indicates that there are diskette
                          drives on the system.
                  Bit 1 - not used.
                  Bit 2,3 - Planar Ram Size (00=16K 10=32K 01=48K
                            11=64K)
                  Bit 4,5 - Initial Video Mode (00=Unused
                                                10=40x25 Color
                                                01=80x25 Color
                                                11=80x25 Mono)
                  Bit 6,7 - Number of Diskette Drives (00=1 10=2
                            01=3 11=4) only if bit 0 = 1.
                  Bit 8   - Unused
                  Bit 9,10,11 - Number of RS232 Cards attached
                  Bit 12  - Game I/O Attached
                  Bit 13  - Not used
                  Bit 14,15   - Number of printers attached
     &H13      -  Memory Size in K bytes.
     &H15      -  I/O RAM Size in K bytes.
     &H17      -  Keyboard Flag -- the following lists the masks
                  set to describe current keyboard status:
                  Byte 1;
                  &H80 - Insert state active
                  &H40 - Caps Lock State Has been toggled
                  &H20 - Num Lock State has been toggled
                  &H10 - Scroll Lock State has been toggled
                  &H08 - Alternate Shift key depressed
                  &H04 - Control Shift key depressed
                  &H02 - Left Shift key depressed
                  &H01 - Right Shift key depressed
                  Byte 2;
                  &H80 - Insert Key is depressed
                  &H40 - Caps Lock Key is depressed
                  &H20 - Num Lock Key is depressed
                  &H10 - Scroll Lock key is depressed
                  &H08 - Suspend key has been toggled
     &H49      -  Current CRT mode
                  &H00 - 40x25 BW
                  &H01 - 40x25 Color
                  &H02 - 80x25 BW
                  &H03 - 80x25 Color
                  &H04 - 320x200 Color
                  &H05 - 320x200 BW
                  &H06 - 640x200 BW
                  &H07 - 80x25 B&W Card -- specialized use, used
                         internal to the video routines.
     &H4A      -  Number of CRT columns
     &H50      -  Cursor Position (one of eight)
     &H60      -  Current cursor mode
     &H6C      -  Low word of Timer count
     &H6E      -  High word of Timer count
     &H71      -  &H07 - Break key depressed
     &HFA6E    -  Beginning of character regen memory
     &HFF53    -  PRTSC routine address

    ------------------------------------------------------------------
    Real stuff--

    TOGGLE NUM LOCK
     DEG SEG = &H40 : POKE &H17, PEEK(&H17) OR 32   'To turn on
     DEG SEG = &H40 : POKE &H17, PEEK(&H17) AND 223 'To turn off

    TOGGLE CAPS LOCK
     DEG SEG = &H40 : POKE &H17, PEEK(&H17) OR 64   'To turn on
     DEG SEG = &H40 : POKE &H17, PEEK(&H17) AND 171 'To turn off

    SET SCROLL WINDOW
     10 DEF SEG : POKE 91,20 : POKE 92,25            'Sets up window on line
     20 LOCATE X,20                                  'Force cursor to window

    SET WINDOW WIDTH
     DEF SEG : POKE 41,30                           'Sets window width to 30

    RESTORE FUNCTION KEYS TO DEFAULT
     10 DEF SEG = &HFACE
     20 K = 1
     30 I = 13
     40 T$ = STRING$(13,32): J = 1
     50 T1 = PEEK(I):IF T1 < 0 THEN MID$(T$,J,1) = CHR$(T1):J = J + 1:
        I = I + 1 : GOTO 50
     60 KEY K,LEFT$(T$,J-1):IF K <10 THEN K = K + 1: I = I + 1: GOTO 40 :
        ELSE KEY ON

     DETERMINE MONITOR TYPE
      10 DEF SEG = 0
      20 MONITOR.TYPE = PEEK(&H410) AND &H40
      30 IF MONITOR.TYPE = 1 PRINT "40 X 25 COLOR"
      40 IF MONITOR.TYPE = 32 PRINT "80 X 25 COLOR"
      50 IF MONITOR.TYPE = 48 PRINT "MONOCHROME"

     DETERMINE AMOUNT OF MEMORY INSTALLED (Only works for greater than 48k)
      DEF SEG = 0: MEMORY% = PEEK(&H413)+(256*PEEK(&H414))

     or, put another way:

                 Memory info:         DEF SEG=0

          ((PEEK(1040) and 12) + 4 ) * 4     -  Memory on Mother-board
          PEEK(1045) + 256 * PEEK(1046)      -  Expansion memory (add on)
          PEEK(1043) + 256 * PEEK(1044)      -  Total memory

     READ DRIVE SWITCHES
      DEF SEG = 0: NUMBER.OF.DRIVES% = PEEK(&H410) AND &HC0


      CURRENT DISK INFO:  DEF SEG=64
             DEF SEG=64
             PEEK(69)   -  Track
             PEEK(70)   -  Head
             PEEK(71)   -  Sector
         256^PEEK(72)   -  Bytes per sector

     DETERMINE IF GAME ADAPTER EXISTS
      10 DEF SEG = 0: GAME.ADAPTER% = PEEK(&H411) AND &H10
      20 IF GAME.ADAPTER% = 0 THEN GAME.ADAPTER$ = "No" ELSE GAME.ADAPTER$
         = "Yes --Installed"

     KEYBOARD STUFF
         To disable entire keyboard:  Def Seg=64: Out 97,204
         To re-enable keyboard:       Def Seg=64: Out 97,76

         Printer Status--- at least on Epson ---
            Def Seg=64
            A=peek(8)+256*peek(9)
            B=(inp(a+1) and 248) xor 72
            if (B and 128)<>128 then printer off line else on line

         Initialize Printer:           Def Seg: Out A+2,8
                                       Out A+2,12
         Note:  the A to initialize is from Printer status routine

         A short program to disable and re-enable ctrl break follows.

         100 DIM OLD%(4)
         110 DEF SEG=0
         120 ' save the old control break address
         130 FOR I=&H6C TO &H6F
         140   OLD%(I-&H6C)=PEEK(I)
         150 NEXT
         160 ' establish new control break address  (point to IRET)
         170 POKE &H6C,&H53
         180 POKE &H6D,&HFF
         190 POKE &H6E,&H0
         200 POKE &H6F,&HF0
         210 DEF SEG
         220 ' reset old control break address
         230 DEF SEG=0
         240 FOR I=&H6C TO &H6F
         250   POKE I,OLD%(I-&H6C)
         260 NEXT


                  Save and Restore a Screen Image

     1 DEF SEG = &HB800                      'Save screen image...change for
     2 INPUT FILENAME$                       'monochrome.
     3 BSAVE FILENAME$,0,&H4000
     1000 INPUT "Filename";FILENAME$         'Restore image
     1010 CLS
     1020 DEF SEG = &HB800                   'Change to &HB000 to mono
     1030 BLOAD FILENAME$

                         Nice to know
                        BASIC Unprotect
    Enter BASICA
    Type BSAVE "UN.P",1124,1
    Load "MYPROG
    BLOAD "UN.P",1124
    The program can now be listed, edited and SAVEd as a normal file.

    The list is growing but could be longer!  Any and all additions of
    commonly used subroutines and peek/poke locations will be gladly added.
    Address all additions to:  Don Watkins CIS 76003,252 (IBMSIG).  With a
    bit of your assistance this document can become an effective tool for the
    BASIC programmer....  so chip in.


    bit of your assistance this doc