The CompuServe Quick B Protocol
                 November 20, 1987  3:11 PM

 A. Introduction

    The CompuServe B protocol was developed in 1981 to provide
    support for a special purpose Vidtex terminal manufactured
    by the Tandy Corporation.  It was the outgrowth of a
    proposed Bi-Sync oriented protocol, but with a different
    packet structure and provision for more than even and odd
    packets.  The file transfer capability was added in 1982 to
    replace the CompuServe A protocol with a more robust
    protocol which was in keeping with the over-all B Protocol
    design.

    Some of the underlying assumptions made in designing the B
    Protocol were due to the capabilities of personal computers
    which were available at the time.  Such machines were
    generally limited in the amount of available memory, 64
    kilobytes being a large capacity.  Other factors, such as
    the lack of a true UART for data communications, resulted in
    the over all Bi-Sync nature of the protocol where only a
    single protocol packet at a time was sent.

    The explosive growth of the Personal Computer industry has
    given us a plethora of machines, most of which have far
    exceeded the early limitations of memory and communication
    ability.  This growth has been accompanied by a multitude of
    file transfer protocols, such as XMODEM, KERMIT, and ZMODEM.
    CompuServe, realizing the need for enhancement, has
    developed the Quick B Protocol to meet the increasing
    demands being made upon its communication network and hosts,
    and to provide added utility for its large family of users.

    As the name implies, Quick B is an extension of the B
    Protocol.  In particular:

         o  Ability to have the host send multiple packets
            without waiting for individual acknowledgements.
         o  Separation of the error detecting and retransmission
            layer from the file transfer layer.
         o  Larger data packets (up to 1k at present).
         o  Optional use of the XMODEM CRC-16 check method.
         o  Extensions to the standard control character
            quoting.
         o  Provision of a mechanism to exchange transport and
            application parameters.

    All of these features of the Quick B Protocol are optional.
    The default operational mode of Quick B is directly
    compatible with the former B Protocol, meaning that existing
    terminal emulation software which supports the B Protocol is
    not made obsolete.

 B. Quick B Packets.

    1. Notation.

       Throughout the reamainder of this document the following
       notational conventions will be used:]

            o  Protocol elements are enclosed within angle
               brackets.  For example:
                      <DLE>
               specifies the ASCII code for Data Link Escape.

            o  The C-language notation for hexadecimal values will
               be used.  Thus, the <DLE> character would also be
               shown as 0x10.

    2. Quoting of characters.

       Both B and Quick B support quoting of certain characters.
       The default set of quoted characters is:

            o  <NUL>  0x00
            o  <ETX>  0x03
            o  <ENQ>  0x05
            o  <DLE>  0x10
            o  <DC1>  0x11  (XON>
            o  <DC3>  0x13  (XOFF>
            o  <NAK>  0x15

       The quoting mechanism uses the <DLE> character to prefix the
       quoted character.  The quoted character with 0x40 added
       follows the <DLE>.  For example, <ETX> is quoted as:

            <DLE> <C>
            0x10 0x43

       The Quick B Protocol adds three additional levels of
       quoting.
       These are:

           1:  Not NUL
                 This is the default set, except that <NUL> is not
                 quoted.

            2:  Extended.
                 This is the Not NUL set, plus the same characters
                 with bit 7 set to 1, plus 0x7f and 0xff.  Thus,
                 the Extended Quoting set is:

                      0x03  0x05  0x10  0x11  0x13  0x15
                      0x83  0x85  0x90  0x91  0x93  0x95
                      0x7f  0xff


            3:  Full.
                 This level quotes all control characters, plus the
                 bit-7 set, plus 0x7f and 0xff.


       Quoting of the bit-7 characters is the same as normal
       quoting, except that the value 0x60 is added instead of
       0x40.  Thus 0x95 quotes as <DLE> <0x65>.

       The characters 0x1f, 0x7f and 0xff are special cases.  They
       quote as:

            o  0x7f = <DLE> </>  0x10 0x2f
            o  0xff = <DLE> <.>  0x10 0x2e
            o  0x1f = <DLE> <->  0x10 0x2d

    3. Check Value.

       Each Quick B packet contains a check value to allow
       detection of transmission errors.  Two Check Value otpions
       are allowed:

       a) Standard B Protocol Checksum.

          The standard checksum is calculated as follows:

               o  The checksum is initialized to zero.
               o  For each byte that is to be checksummed:
                    -  The old checksum is rotated left 1, with the
                       old bit 7 becoming bit 0 in the rotated value.
                    -  The new byte is added to the rotated checksum.
                    -  If addition of the new byte causes a carry,
                       then one is added to the new value.

          The following C-language code fragment illustrates the
          checksum calculation:

          int
            checksum;

          do_checksum (ch)
          unsigned int ch;
          {
              checksum = checksum << 1;

              if checksum > 0xff
                  checksum = (checksum  & 0xff) + 1;

              checksum += ch & 0xff;

              if checksum > 0xff
                  checksum = (checksum & 0xff) + 1;
          };

       b) XMODEM-Style CRC-16.

          Quick B implementations may optionally specify that the
          defacto standard XMODEM CRC-16 be used as a check value.
          The only departure is that the CRC-16 value is initialized
          to -1 instead of zero as for XMODEM.  The following
          C-language code illustrates how the XMODEM CRC-16 is
          calculated:

          /*
           * Calculates XMODEM-style CRC (uses the CCITT V.41
           * polynomial but
           * completely backwards from the normal bit ordering).
           */
          static unsigned crc_xmodem_tab[] = {
          0x0000,0x1021,0x2042,0x3063,0x4084,0x50A5,0x60C6,0x70E7,
          0x8108,0x9129,0xA14A,0xB16B,0xC18C,0xD1AD,0xE1CE,0xF1EF,
          0x1231,0x0210,0x3273,0x2252,0x52B5,0x4294,0x72F7,0x62D6,
          0x9339,0x8318,0xB37B,0xA35A,0xD3BD,0xC39C,0xF3FF,0xE3DE,
          0x2462,0x3443,0x0420,0x1401,0x64E6,0x74C7,0x44A4,0x5485,
          0xA56A,0xB54B,0x8528,0x9509,0xE5EE,0xF5CF,0xC5AC,0xD58D,
          0x3653,0x2672,0x1611,0x0630,0x76D7,0x66F6,0x5695,0x46B4,
          0xB75B,0xA77A,0x9719,0x8738,0xF7DF,0xE7FE,0xD79D,0xC7BC,
          0x48C4,0x58E5,0x6886,0x78A7,0x0840,0x1861,0x2802,0x3823,
          0xC9CC,0xD9ED,0xE98E,0xF9AF,0x8948,0x9969,0xA90A,0xB92B,
          0x5AF5,0x4AD4,0x7AB7,0x6A96,0x1A71,0x0A50,0x3A33,0x2A12,
          0xDBFD,0xCBDC,0xFBBF,0xEB9E,0x9B79,0x8B58,0xBB3B,0xAB1A,
          0x6CA6,0x7C87,0x4CE4,0x5CC5,0x2C22,0x3C03,0x0C60,0x1C41,
          0xEDAE,0xFD8F,0xCDEC,0xDDCD,0xAD2A,0xBD0B,0x8D68,0x9D49,
          0x7E97,0x6EB6,0x5ED5,0x4EF4,0x3E13,0x2E32,0x1E51,0x0E70,
          0xFF9F,0xEFBE,0xDFDD,0xCFFC,0xBF1B,0xAF3A,0x9F59,0x8F78,
          0x9188,0x81A9,0xB1CA,0xA1EB,0xD10C,0xC12D,0xF14E,0xE16F,
          0x1080,0x00A1,0x30C2,0x20E3,0x5004,0x4025,0x7046,0x6067,
          0x83B9,0x9398,0xA3FB,0xB3DA,0xC33D,0xD31C,0xE37F,0xF35E,
          0x02B1,0x1290,0x22F3,0x32D2,0x4235,0x5214,0x6277,0x7256,
          0xB5EA,0xA5CB,0x95A8,0x8589,0xF56E,0xE54F,0xD52C,0xC50D,
          0x34E2,0x24C3,0x14A0,0x0481,0x7466,0x6447,0x5424,0x4405,
          0xA7DB,0xB7FA,0x8799,0x97B8,0xE75F,0xF77E,0xC71D,0xD73C,
          0x26D3,0x36F2,0x0691,0x16B0,0x6657,0x7676,0x4615,0x5634,
          0xD94C,0xC96D,0xF90E,0xE92F,0x99C8,0x89E9,0xB98A,0xA9AB,
          0x5844,0x4865,0x7806,0x6827,0x18C0,0x08E1,0x3882,0x28A3,
          0xCB7D,0xDB5C,0xEB3F,0xFB1E,0x8BF9,0x9BD8,0xABBB,0xBB9A,
          0x4A75,0x5A54,0x6A37,0x7A16,0x0AF1,0x1AD0,0x2AB3,0x3A92,
          0xFD2E,0xED0F,0xDD6C,0xCD4D,0xBDAA,0xAD8B,0x9DE8,0x8DC9,
          0x7C26,0x6C07,0x5C64,0x4C45,0x3CA2,0x2C83,0x1CE0,0x0CC1,
          0xEF1F,0xFF3E,0xCF5D,0xDF7C,0xAF9B,0xBFBA,0x8FD9,0x9FF8,
          0x6E17,0x7E36,0x4E55,0x5E74,0x2E93,0x3EB2,0x0ED1,0x1EF0};

          unsigned CRC;
          UpdCrc (Byte)
          unsigned int ByteC;
          {  CRC =
               crc_xmodem_tab [(CRC >> 8 ^ Byte) & 0xff] ^ (crc << 8);
          };


    4. Quick B Packet Structure.

       Quick B Protocol (and B Protocol) packets consist of five
       parts as follows:

            o  Lead-in       <DLE> <B>
            o  Sequence      <0x30 thru 0x39>
            o  Type          <Single byte>
            o  Body          <zero to 1024 data bytes>
            o  Trailer       <ETX> <Check Value>

       The Sequence is incremented by one for each successfully
       received or transmitted packet.  It wraps from 0x39 back to
       0x30.  (Note that 0x30 is the ASCII character 0 and 0x39 is
       9.)

       The Sequence, Type, all Body data, and <ETX> are included in
       the Check Value.  Note that <Body> and <Check Value> are
       Quoted, and that the Check Value is computed on the actual
       data bytes rather than their quoted replacements; the
       quoting <DLE> is not included.  Hence, if the character 0x13
       is to be sent, it is sent as <DLE> <S> but the value 0x13 is
       included in the Check Value.

       If Standard Checksum is used, <Check Value> consists of a
       quoted byte.

       If the XMODEM CRC-16 Check Value is used, then it consists
       of two quoted bytes with the most significant byte appearing
       first.  By performing the CRC calculation on the XMODEM
       CRC-16 value,  the result should be 0x0000.

       A complete Quick B Protocol packet is as follows:

       <DLE> <B>  <7>  <T>  <D>  <A>  <S>  <.>  <C> <ETX> <0x2A>
       0x10 0x42 0x37 0x54 0x44 0x41 0x53 0x2E 0x43 0x03  0x2A

       If the packet was sent using the XMODEM CRC-16 option, the
       Check Value would be <0x57> <0xFF>.  In addition, if the
       Extended Quoting option was in effect, the Check Value would
       be sent as <0x57> <DLE> <.>  (the <DLE> <.> being the
       representation of 0xFF).

    5. Quick B Packet Types.

       The following Packet Types are the minimum required to
       support the Quick B Protocol:

       a) <+>  0x28

          This is the Quick B Transport Parameters Packet.  It
          describes sender's Transport capabilities.  The Body of the
          <+> packet is a series of five bytes as follows:

               <ws> <wr> <bs> <cm> <dq>

          where:

               <ws> = Window Send.  00 implies that a single packet at
                    a time is sent, 01 two packets.  Larger values are
                    not supported at this time.

               <wr> = Window Receive.  00 implies that he sender
                    cannot receive other than a single packet at a
                    time (that is, requests the other end to use
                    <ws> = 00).

               <bs> = Block Size.  This specifies the maximum size of
                    the <Body> divided by 128.  Thus 4 represents 512
                    bytes and 8 is 1024 bytes.

               <cm> = Check Method.  00 is standard checksum, 01 is
                    XMODEM CRC-16 initialized to -1.

               <dq> = Data Quoting.  This specifies the level of data
                    quoting desired:

                         00 = Default
                         01 = Default without <NUL>
                         02 = Extended
                         03 = Full

          The current Transport Parameters Packet sent by the
          CompuServe host is:

                <0x01> <0x01> <0x08> <0x01> <0x03>

          which indicates that the host can:

               o  Send two packets before waiting for an ACK
               o  Receive two packets before the remote
                  has to wait for an ACK
               o  Handle 1024 character data blocks
               o  Use XMODEM CRC-16
               o  Support all four levels of Data Quoting.


       b) <?>  0x3f

          This is the Application Capabilities Packet.  Its body
          consits of a series of flag bytes indicating whether or not
          the particular application packet is supported.  At the
          present time only the <T> application packet is supported.

          The <Body> of the <?> packet returned by the remote should
          therefore be empty until the Application Parameters have
          been determined.

       c) <F>  0x46

          This is the general Failure Packet.  A Failure Packet may be
          sent at any time; the value of the <Sequence> field is
          ignored.  The <Body> of the Failure Packet indicates the
          nature of the failure:

               <A>  0x41
                    Abort.  Usually sent if the user requests that the
                    terminal program cease tranferring data.

               <C>  0x43
                    Capacity failure.  Out of memory or disk.

               <E>  0x45
                    Processing error.  Any error other than described
                    by another Failure Packet.

               <N>  0x4E
                    Unimplemented.  The other end has received an
                    packet which it does not support.

       d) <T>  0x54

          This is the standard File Transfer packet.  Its <Body>
          consists of three fields as follows:

               <Direction> <Data type> <File name>

          1) Function.
                  <D> = Download (ie, sent from the host to the remote).
                  <U> = Upload (send from the remote to the host).
                  <C> = Close.  End of Upload or Download.

          2) Data type.
                  <A> = ASCII data.
                  <B> = Binary data.

             Note that this is necessary in order that the host be able
             to properly store and retrieve the data.

          3) File Name.

             This field is variable length and specifies the name of the
             tile to be transfered.

             A sample <T> packet is:

             <D> <A> <R> <A> <B> <B> <I> <T> <.> <D> <A> <T>

             which specifies that the ASCII file RABBIT.DAT is about to
             be downloaded to the remote.

             Note that there are no guidelines as to what the remote is
             to do with the <T> packet.  In particular, the implementor
             is free to locally verfify the request, permit the file name
             to be changed, etc.

             If the remote does not wish to comply with the request made
             in the <T> packet, a Failure Packet should be returned to
             the host.

       e) <N>  0x4E>

          This is a data packet.  The data being transferred is broken
          up into a series of <N> packets.  The final <N> packet may
          be shorter than the negotiated Block Size.

    6. Quick B Control Sequences.

       The Quick B Protocol defines several control sequences other
       than the basic packet.  These are used to request and
       provide various kinds status information between the host
       and remote computers.

       a) <ENQ>  0x05

          The <ENQ> Control Sequence is sent in one of two
          circumstances:

               o  The remote is in terminal mode and the host wants to
                  synchronize its <Sequence> number, and to tell the
                  remote to set up for normal B Protocol.  When the
                  <ENQ> is received, the remote is expected to:
                    -  Prepare for 512 byte data blocks
                    -  Prepare for normal B Protocol Checksum
                    -  Initialize its sequence number to <0> 0x30
                    -  Return the string:

                         <DLE> <+> <DLE> <0x30>

                       to the host.  If Quick B is not supported, the
                    <DLE>      <+> is omitted.

                    -  Return to terminal mode.  Note:  The terminal
                       program  definately should NOT enter B Protocol
                       mode when the <ENQ> is received.

               o  Either the host or the remote has lost track of what
                  <Sequence> is expected.  Typically this is sent
                  while a Packet is being sent and the sender has
                  received a Negative Acknowledge,  and serves to
                  resynchronize the sender's packets.  In this case
                  the expected reply to the <ENQ> is:

                         <DLE> <Last Validly Received Sequence>

       b) Positive Acknowledge.

          When either the host or remote receives a correctly
          sequenced and checksummend packet, it should send a Positive
          Acknowledge Control Sequence.  This consists of:

               <DLE> <Sequence>

          where <Sequence> is the <Sequence> of the newly recieved
          packet.

       c) Negative Acknowledge.

          When the host or remote receives a packet with an unexpected
          <Sequence> or improper checksum, it sends a Negative
          Acknowledge to the other ent.  This consists of the single
          byte:

               <NAK>  0x15

          Upon receiving a Negative Acknowledge, the last packet may
          be resent, or if packet send-ahead is being used, an <ENQ>
          may be sent to determine if a Positive Acknowledge was lost.
          In the latter case, wait for a Positive Acknowledge to be
          returned after sending the <ENQ>.

       d) Panic Abort.

          The Quick B Protocol recognizes a series of four <DLE>
          characters as a panic abort.  The need for such a facility
          can arise if the remote computer becomes locked up during a
          transfer, and it is necessary to reboot.  Since <DLE> is
          really control-P, sending it is a very simple procedure.

          In addition, the host recognizes the seqeunce:

               <DLE> <+>

          while waiting for a Positive Acknowledge as being incorrect,
          and will abort the transfer.  This can happen as above, but
          before the operator can press control-P the host sends an
          <ENQ> during a down-load to find out what is happening.  The
          remote, now in terminal emulation mode, responds with:

               <DLE> <+> <DLE> <0>

          and the host will abort cleanly.  For this reason it is
          essential that any Quick B implementation observe the rules
          for <ENQ>:  If in terminal mode, send the <DLE> <+>;
          otherwise
          do not.

 C. Negotiation of Transport Parameters.

    Normally the host begins a Quick B protocol session by
    sending an <ENQ> while the remote is in terminal mode.  The
    remote should clear its Quick B status (that is, revert to
    normal checksum, normal quoting, and 512 byte data block),
    return the sequence:
                  <DLE> <+> <DLE> <0>
    then return to terminal mode.

    The host, detecting the <+>, sends a Transport Parameters
    packet as shown earlier.  Note that this will be sent under
    normal B Protocol.  When the remote properly receives this
    packet, it should send back to the host a Transport
    Parameters packet indicating its own choices for the various
    parameters, again using normal B Protocol.  Each end then
    establishes its operating configuration based on the minimal
    matching parameters.  In particular, the host and remote
    each choose the minimum of:

       Own         Other's
    Parameter   Parameter

      <ws>        <wr>
      <wr>        <ws>
      <bs>        <bs>
      <cm>        <cm>
      <dq>        <dq>

    For example, if the host sends the sequenece:
             <0x01> <0x01> <0x08> <0x01> <0x03>
    and the remote returns:
             <0x00> <0x01> <0x04> <0x00> <0x01>
    then the following parameters are used:
        Parameter      Host      Remote

          <ws>         0x01      0x00      Host sends 1 packet
                                           ahead
          <wr>         0x00      0x01      Remote sends 1 packet
                                           and waits for Postive
                                           Acknowledge
          <bs>         0x04      0x04      Both use 512 byte
                                           data body
          <cm>         0x00      0x00      Standard Checksum
          <dq>         0x01      0x01      Default Quoting
                                           without <NUL>.

    The next <DLE><B> packet will be under Quick B Protocol.

 D. Terminal Program States.

    This section describes the expected state transitions for a
    terminal program which supports the Quick B Protocol.

    Current State      Event     Action         Next State
    ------------------------------------------------------------
    Terminal      <ENQ> Rcvd.    Return:        Terminal
                             <DLE><+><DLE><0>
                             Set up for normal
                             B Protocol

                  <DLE> Rcvd.    None.          DLE_Seen

                  <Other>        Process as an
                                 ASCII char.    Terminal

    ------------------------------------------------------------
    DLE_Seen      <B> Rcvd.      None.          Get_First_Packet

                  <other> Rcvd.  None.          Terminal

    ------------------------------------------------------------
    Get_First_Packet        Receive the Packet
                  Valid packet :

                  <+>      Process Transport     Terminal
                            Parameters; set
                            up for Quick B if
                            successful exchange

                  <?>      Process Application   Terminal
                            Parameters

                  <T>      Process Transfer      Terminal
                            Request

                  <other>  Return Failure        Terminal
                            Packet N

    ------------------------------------------------------------

 E. Timing Considerations

    Under most circumstances the remote should utilize a
    per-character time-out of about 30 seconds.  Using anything
    less can result in a loss of good control over the exchange
    of packet and control sequences.  If conditions over a
    switched network degrade sufficiently, a small time out can
    lead to excessive retransmissions of data.

    In addition to having a long time out, the receiver should
    issue a single NAK for any situation (time out, bad check
    value or sequence number, etc.) until it has received an
    <ENQ> from the sender.  Doing this reduces the "crossed in
    the mail" syndrome, where the receiver sends a NAK, which
    due to network traffic is delayed until the host resends the
    packet, the receiver times out and sends another NAK, then
    receives the packet, which is good and so ACKs it, but there
    is already a NAK on its way, which the host receives and
    resends, the remote gets the good packet for the second time
    and sends an ACK, etc.  By sending a single NAK and ignoring
    errors until an <ENQ> or a good packet is received, the
    chances of repeated bogus retransmissions will be reduced
    considerably.



 F. Receiving a Packet

    Quick B Packets may be received with a six-state automaton.
    The states are:

        o  R_Get_DLE   Wait for the initial <DLE> (0x10).
        o  R_Get_B     Receive the <B> (0x42).
        o  R_Get_Seq   Receive the the <sequence> digit.
        o  R_Get_Data  Receive and save the data.  Note that
                       the initial charcter in the data buffer
                       will be the Packet Type.
        o  R_Get_Cks   Receive checksum and verify packet.
        o  R_Time_Out  More than thirty seconds elapsed while
                       waiting for a modem character.
        o  R_Send_ACK  Send an ACK sequence (<DLE><sequence>).

    The inital state is normally R_Get_DLE.  If the initial
    <DLE><B> has already been processed, such as from the
    DLE_Seen state of the Terminal Emulator or from Send Packet,
    then the initial state is R_Get_Seq.

    The state machine is as follows:

    State         Received  Action                   Next State
    ===========================================================
    R_Get_DLE     <DLE>     ...                      R_Get_B
                  <ENQ>     ...                      R_Send_ACK
                  <Other>   ...                      R_Get_DLE
                  Time Out  ...                      R_Time_Out

    R_Get_B       <B>       ...                      R_Get_Seq
                  <ENQ>     ...                      R_Send_ACK
                  Time Out  ...                      R_Time_Out
                  <Other>   ...                      R_Get_DLE

    R_Get_Seq     <ENQ>     ...                      R_Send_ACK
                  Time Out  ...                      R_Time_Out
                  <0>..<9>  Initialize Check Value
                            Add <Seq> to Check Value
                            Initialize to receive    R_Get_Data
                  <Other>   ...                      R_Get_DLE

    R_Get_Data    <ETX>     Add <ETX> to Check Value R_Get_Cks
                  Time Out  ...                      R_Time_Out
                  <Other>   Add <Other> to Check Value
                            Put <Other> in receive
                              buffer                 R_Get_Data

    R_Get_Cks     Time Out  ...                      R_Time_Out
                  <Cks>     Validate Check Value and
                            <Sequence>
                                 Invalid             R_Time_Out
                                 Valid
                                      Save <Seq> as
                                      <Last Seq>     [ Success ]

    R_Time_Out    ...       Count error
                            If too many errors then  [ Failure ]
                            If NAK not sent
                              then Send <NAK>        R_Get_DLE

    R_Send_ACK    ...       Send <DLE><Last Seq>     R_Get_DLE

 G. Sending a Packet

    Quick B Packets may be sent by means of a six state
    automaton.  The states are:

        o  S_Send_Packet    Send the entire packet
        o  S_Get_DLE        Get the receiver's <DLE>.
        o  S_Get_Num        Get the receiver's <Seq> (ACK).
        o  S_Get_Packet     Do a Receive Packet process.
        o  S_Time_Out       Time out waiting for response.
        o  S_Send_NAK       Send a <NAK> to the receiver.

    The initial state is S_Send_Packet.

    State         Received  Action               Next State
    ============================================================
    S_Send_Packet ...       Send <DLE><B>
                            Initialize Check Value
                            Send <Next Seq> & update
                              Check Value
                            Send <Type> & update
                              Check Value
                            Send all data & update
                              Check Value
                            Send <ETX> & update
                              Check Value
                            Send <Check Value>   S_Get_DLE

    S_Get_DLE     <DLE>     ...                  S_Get_Num
                  <ETX>     ...                  S_Send_NAK
                  <NAK>     Count error
                            If too many errors
                              then    ...        [ Failure ]
                              else    ...        S_Send_Packet
                  <Other>             ...        S_Get_DLE
                  Time Out  ...                  S_Time_Out

    S_Get_Num     <0>..<9>  If received <Seq>
                              matches <Next Seq>
                              then
                                 Update Next Seq [ Success ]
                              else               S_Time_Out
                  <B>       ...                  S_Get_Packet
                  <NAK>     Count error
                            If too many errors
                              then    ...        [ Failure ]
                              else    ...        S_Send_Packet
                  Time Out  ...                  S_Time_Out
                  <Other>   ...                  S_Time_Out

    S_Get_Packet  ...       Invoke Read Packet
                            If success and not <F>
                                 Packet
                               then    ...       [ Success ]
                               else    ...       S_Time_Out

    S_Time_Out    ...       Count error
                            If too many errors
                              then    ...       [ Failure ]
                              else Send <ENQ>   S_Get_DLE

    S_Send_NAK    ...       Count error
                            If too many errors
                              then      ...     [ Failure ]
                              else Send <NAK>   S_Get_DLE



 H. Packet Send Ahead

    One of the most useful features of the Quick B Protocol,
    from the user's point of view, is its ability to send more
    than one packet ahead of receiving the acknowledgment of the
    oldest one.  This improves thru-put by overlapping the I/O
    performed on both the host and remote computers, including
    the time required for the remote computer's acknowledgement
    to arrive at the host and wake up the host application
    program.  This section outlines the Send Ahead Process,
    first proposed by Charles McGuinness of CompuServe
    Incorporated.

    The Packet Send Ahead is accomplished by keeping a set of
    buffers in memory, one for each permitted outstanding
    packet.  Each buffer contains the corresponding packet's
    <Sequence>, count, and the data itself.  In addition a
    counter of outstanding packets (ie, not yet ACKed) is
    maintained and incremented whenever a packet is sent for the
    first time.

    Two indicies into the set of buffers are used to keep track
    of the Send Ahead status.  One keeps track of which buffer
    holds the oldest packet and the other which buffer may be
    filled with new data.

    When a packet is about to be sent, the outstanding count is
    checked to see if the maximum number of outstanding packets
    has been reached.  If so, a routine (GetACK) is invoked
    which waits for the ACK to arrive for the oldest outstanding
    packet.  Several possibilities exist:
        o The oldest packet is ACKed.  In this case, move the
          Oldest Outstanding index to point to the next oldest
          packet and decrement the outstanding packet count.
        o Some other packet in the buffer pool has been ACKed.
          This implies an ACK has been missed.  Move the Oldest
          Outstanding index to point to the buffer following the
          received ACK, and decrement the Outstanding Count
          accoringly.
        o A NAK is received.  Retransmit all packets which are
          outstanding.

    If the Outstanding count is still at the maximum, stay in
    GetACK.

    Finally, a procedure is necessary which calls GetACK until
    either a failure occurs or the Outstanding count is zero.

    The Send Ahead Process proceeds as follows:
                                                Receiver's
    Packet   Sequence  Buffer    Outstanding    Response
      1        '1'       0           1            ...
      2        '2'       1           2            ...
      3  GetACK                                 ACK '1'
               '3'       0           2            ...
      4  GetACK                                 ACK '2'
               '4'       1           2            ...
      5  GetACK                                 ACK '3'
               '5'       0           2            ...   (Last)
         GetACK                                 ACK '4'
                                     1            ...
         GetACK                                 ACK '5'
                                     0            ...  (Success)


    Sample Download using Quick B Protocol:
        Time
    [ 11:06:10 ]  B_SYNC: Sending ENQ
    [ 11:06:10 ]  B_SYNC: Get DLE
    [ 11:06:10 ]  B_SYNC: <DLE><+> received
    [ 11:06:10 ]  B_SYNC: Get DLE
    [ 11:06:10 ]  B_SYNC: Digit 0 received
    [ 11:06:10 ]  B_T_Par: Sending 5 parameters:   1  1  8  1  3
    [ 11:06:10 ]  B_SEND: Sending 6 bytes to buffer 0:
    [ 11:06:10 ]  B_DMP_BLK: Sending block 1 from buffer 0
    [ 11:06:10 ]  B_GET_ACK: 1 outstanding blocks
    [ 11:06:10 ]  B_GET_ACK: Get_DLE
    [ 11:06:11 ]  B_GET_ACK: Get_NUM
    [ 11:06:11 ]  B_GET_ACK: <DLE><B> received
    [ 11:06:11 ]  B_GET_ACK: '+' packet received
    [ 11:06:11 ]  B_GET_ACK: Sending ACK for 2 : 5 bytes
    [ 11:06:11 ]  B_T_Par: Received 4 parameters:  0  1  4  0  0
    [ 11:06:11 ]  B_T_Par: Quick B Protocol established:

    WS = 1, WR = 0, BS = 4, CM = 0, DQ = 0, Buffer size = 512

    [ 11:06:11 ]  B_SEND: Sending 10 bytes to buffer 0:
    [ 11:06:11 ]  B_DMP_BLK: Sending block 3 from buffer 0
    [ 11:06:11 ]  B_GET_ACK: 1 outstanding blocks
    [ 11:06:11 ]  B_GET_ACK: Get_DLE
    [ 11:06:11 ]  B_GET_ACK: Get_NUM
    [ 11:06:11 ]  B_GET_ACK: Digit 3 received
    [ 11:06:11 ]  B_GET_ACK: Releasing block 3, buffer 0
    [ 11:06:11 ]  B_SEND: Sending 512 bytes to buffer 1:
    [ 11:06:11 ]  B_DMP_BLK: Sending block 4 from buffer 1
    [ 11:06:12 ]  B_SEND: Sending 512 bytes to buffer 0:
    [ 11:06:12 ]  B_DMP_BLK: Sending block 5 from buffer 0
    [ 11:06:12 ]  B_SEND: Sending 512 bytes to buffer 1:
    [ 11:06:12 ]  B_GET_ACK: 2 outstanding blocks
    [ 11:06:12 ]  B_GET_ACK: Get_DLE
    [ 11:06:15 ]  B_GET_ACK: Get_NUM
    [ 11:06:15 ]  B_GET_ACK: Digit 4 received
    [ 11:06:15 ]  B_GET_ACK: Releasing block 4, buffer 1
    [ 11:06:15 ]  B_DMP_BLK: Sending block 6 from buffer 1
    [ 11:06:15 ]  B_SEND: Sending 512 bytes to buffer 0:
    [ 11:06:15 ]  B_GET_ACK: 2 outstanding blocks
    [ 11:06:15 ]  B_GET_ACK: Get_DLE
    [ 11:06:18 ]  B_GET_ACK: Get_NUM
    [ 11:06:18 ]  B_GET_ACK: Digit 5 received
    [ 11:06:18 ]  B_GET_ACK: Releasing block 5, buffer 0
    [ 11:06:18 ]  B_DMP_BLK: Sending block 7 from buffer 0
    [ 11:06:18 ]  B_SEND: Sending 512 bytes to buffer 1:
    [ 11:06:18 ]  B_GET_ACK: 2 outstanding blocks
    [ 11:06:18 ]  B_GET_ACK: Get_DLE
    [ 11:06:21 ]  B_GET_ACK: Get_NUM
    [ 11:06:21 ]  B_GET_ACK: Digit 6 received
    [ 11:06:21 ]  B_GET_ACK: Releasing block 6, buffer 1
    [ 11:06:21 ]  B_DMP_BLK: Sending block 8 from buffer 1
           ........... etc ...........
    [ 11:06:55 ]  B_GET_ACK: Releasing block 8, buffer 1
    [ 11:06:55 ]  B_DMP_BLK: Sending block 0 from buffer 1
    [ 11:06:55 ]  B_FLUSH: 2 outstanding blocks
    [ 11:06:55 ]  B_GET_ACK: 2 outstanding blocks
    [ 11:06:55 ]  B_GET_ACK: Get_DLE
    [ 11:06:56 ]  B_GET_ACK: Get_NUM
    [ 11:06:56 ]  B_GET_ACK: Digit 9 received
    [ 11:06:56 ]  B_GET_ACK: Releasing block 9, buffer 0
    [ 11:06:56 ]  B_GET_ACK: 1 outstanding blocks
    [ 11:06:56 ]  B_GET_ACK: Get_DLE
    [ 11:06:57 ]  B_GET_ACK: Get_NUM
    [ 11:06:57 ]  B_GET_ACK: Digit 0 received
    [ 11:06:57 ]  B_GET_ACK: Releasing block 0, buffer 1
    [ 11:06:57 ]  B_DONE

    Elapsed time:              46 seconds
     at 1800 baud
    Data Bytes Sent:         7723  = 168 bytes per second =  93%
    Data Bytes Received:        0  = 0 bytes per second =   0%
    Packet Bytes Sent:       7858  = 171 bytes per second =  95%
    Packet Bytes Received:     50  = 1 bytes per second =   1%