:ts=8



	NameName

	setdate - AT&T PC 6300 clock program

	SyntaxSyntax

	setdate [-r] [-s]

	DescriptionDescription

	setdate_______ is a program for manipulating the real time clock in the
	AT&T PC 6300.  setdate_______ will use the real time clock to set DOS date
	and time or setdate_______ can use DOS date and time to set the real time
	clock.  setdate_______ is loosely based on the Xenix date program.

	If no argument is given, the current DOS date and time are printed.

	The -r option reads the real time clock and sets DOS to the date and
	time found there.

	The -s option uses the current DOS date and time to set the real
	time clock.  You must use the DOS date____ and time____ commands to set the
	correct DOS date and time before using the -s option.  setdate_______
	waits until the next minute before setting the real time clock.

	LimitationsLimitations

	The year is not stored as the actual year in the real time clock.  A
	value in the range 0-7 is maintained and a leap year is added to that.
	1984 is used as the leap year in this version.  If anyone is still
	using this program in 1991, it will have to be recompiled with a new
	base leap year.  Incidentally, AT&T's MS-DOS 2.11 suffers the same
	limitation.

	The real time clock does not automatically increment the year on
	Jan 1.  You will have to set the correct date using the DOS date____
	command and then set the internal clock using the -s option.

	The seconds and tenths of seconds are read-only ports, hence the wait
	for the next minute.

	See AlsoSee Also

	AT&T PC 6300 System Programmer's Guide

	BugsBugs

	The MS-DOS 2.11 AT&T supplies with the PC 6300 does not set the day
	of week port in the real time clock.  This may cause setdate_______ to
	display the day of the week incorrectly the first time it is run.
	setdate_______ correctly sets the day of the week when the -s option is
	used.