BOOT.COM
                                 Karl Brendel
                                 316-241-2340
                                 8 April 1985

                            For the IBM PC-AT only!

     This routine allows a warm boot to be called from a batch file or the 
keyboard.  It bypasses the RAM check which is made at the beginning of a cold
boot and when apparently similar routines such as IPL.COM are run.  

     This routine violates the IBM philosophy of accessing the BIOS.  Rather 
than doing that through INT calls, this sets a value into a specific memory 
address, then jumps to a specific ROM address.  The result of this means of 
accessing the BIOS is that it may not work with ROMs other than those 
identical to mine.  To determine if yours is identical to mine, use DEBUG to 
dump addresses f000:0000 thru 000d.  You should see 66118811002289.  
     
     If that is not what you find, then the situation may get a little messy.  
Remove any memory-resident applications such as SideKick, Newkey, etc., from
RAM (the best was is to rename your autoexec file and do a Ctrl-Alt-Del)  Still
using DEBUG, do this:
           a cs:100<    (< means enter)
           int 16<
           <
           t=100 2<
Look at the display of the last trace output line, which should appear 
something like
          F000:XXXX       STI
Add to XXXX, 201 hex, giving (say) XYYY.  Do
          d f000:XYYY L b
The bytes shown (not their character representations, shown at the right of 
the DEBUG dump display) should be
          F6 06 17 00 04 74 31 3C 53 75 2D
If they are, then you may use this routine with no patches.
     
     If you have made it this far and do not feel that you have a compatible 
BIOS ROM, then you have a couple of alternatives:  You may take this stuff and 
trash it.  You may use this and a copy of the AT DOS 3.0 BIOS and revise the 
routine to support your ROM.  You may use a public domain routine such as IPL 
which will allow you the same operation, but will not bypass the RAM check.  
Whatever you do, I wish you luck and hope that this has at least stimulated 
some thought.
             
     Boot functions by jumping into the middle of the BIOS Keyboard IO 
routines.  It first stores a value into the keyboard flags register to 
simulate the presence of the Ctrl-Shift combination.  It then places the code 
for the Del key into the AL register and makes a direct jump to the portion of 
the BIOS where a check is made for Ctrl-Alt-Del.
     
     Note that the actual code is only 17 bytes long, although the file you 
downloaded is somewhat longer.  That has to do with the structure of LBR files 
and transmission protocols.  You may use DEBUG to eliminate the excess after 
the 17th byte.
              
     The assembler code:

B84000        MOV     AX,0040              SET UP DS
8ED8          MOV     DS,AX
C606170004    MOV     BYTE PTR [0017],04   PUT FLAG FOR CTRL-SHFT
                                           IN KB_FLAG
B053          MOV     AL,53                PUT DEL KEY CODE IN AL
EAC93100F0    JMP     F000:31C9            JUMP TO WHERE TEST IS MADE