Program:  SETKEY.COM  09/02/85  for the IBM AT only!!
Written by Kevin M. Crenshaw - May 85 PC Tech Journal
Modifications and documentation by Terry Barr. (CIS- 70406,377)

The default setting for the AT is equivalent to >SETKEY M2
    
The possible settings are A-Z, [, \, ], ^, _, ` and then 1-4.
If you just type SETKEY you will get a default of A1.

****************** SET TYPEMATIC RATE/DELAY (HEX F3) **********************

    The program issues the command 0F3h to the keyboard input port 60h.
    It then sends the parameter to change the typematic rate and delay to
    input port 60h.  The typematic rate and delay parameters are 
    determined by the value of the byte following the command.
    
    Bit 7, is always 0.
    Bits 6 and 5 serve as the delay parameter.
    Bits 4, 3, 2, 1, and 0 serve as the rate parameter.
    
    The delay is equal to 1 plus the binary value of bits 6 and 5 
    multiplied by 250 milliseconds.  This gives you delay factors
    of 250, 500, 750 ms. or 1.00 second.  The AT has a default of
    500 milliseconds.  

    The typematic period is equal to the following equation:
                       
    Period = (8+A) * (2^B ) * 0.00417 seconds, where A=binary value 
    of bits 2,1, and 0 and B=binary value of bits 4 and 3.
    
    The typematic rate is 1/period.  Where period is determined by
    the above equation.  The AT has a default typematic rate of 10.0.
    
    The following table shows the results:
    
    Letter	Bit	Rate		Letter	Bit	Rate
    =================================================================
    	A	00000	30.0		    Q	10000	7.5
    	B	00001	26.7		    R	10001	6.7
       	C	00010	24.0		    S	10010	6.0
    	D	00011	21.8		    T	10011	5.5
    	E	00100	20.0		    U   10100	5.0
    	F	00101	18.5		    V	10101	4.6
    	G	00110	17.1		    W	10110	4.3
    	H	00111	16.0		    X	10111	4.0
    	I	01000	15.0		    Y	11000	3.7
    	J	01001	13.3		    Z	11001	3.3
    	K	01010	12.0		    [	11010	3.0
    	L	01011	10.9		    \	11011	2.7
    	M	01100	10.0		    ]	11100	2.5
    	N	01101	 9.2		    ^	11101	2.3
    	O	01110	 8.6   		    _	11110	2.1
    	P	01111	 8.0		    `	11111	2.0
    =================================================================   		    _	11110	2.1
    	P	01