r
                             MEMBRAIN DOCUMENTATION 
 
 
 
    - Description 
 
         MEMBRAIN.EXE Version 1.21 creates a file named 'MEMBRAIN.SYS ', 
    a DOS device driver for an emulated disk drive configured to your 
    specifications. MEMBRAIN is installed through the DOS device driver 
    interface using a 'DEVICE= ' statement in 'CONFIG.SYS '. DOS will 
    assign to the drive the next available drive letter. For example, if 
    your system has disk drives A: and B:, MEMBRAIN will be drive C:. On 
    a PC-XT with drives A: and C:, MEMBRAIN will be drive D:. 
 
 
    - System Requirements 
 
         An IBM PC or XT with at least 128K of memory and DOS 2.X 
 
 
    - Installation 
 
    1) Enter on the DOS or QSYS command line: 
 
    MEMBRAIN  disk size,sector size,cluster size,directory entries,path 
 
         disk size - The requested size of the emulated drive in Kbytes. 
              An error is returned if the resulting configuration would 
              leave less than 64K of free memory. If this parameter is 
              omitted, the default disk size is 160K. 
 
         sector size - The size of each logical sector in bytes. Sector 
              size should be a multiple of 128 and will be rounded up to 
              the next 128 byte multiple. For example, if the parameter 
              is entered as 150, then the actual sector size will be 256 
              bytes. The default is 512 bytes per sector. 
 
         cluster size - The number of sectors per cluster. An error will 
              be returned if the number of bytes per cluster exceeds 2048. 
              Refer to 'Configuration Tips ' for more information. The 
              default is 1 sector per cluster. 
 
         directory entries - The maximum number of filenames that the disk 
              directory can hold. This parameter will be adjusted upward as 
              necessary to a multiple of sector size. The default is 64. 
 
         path - The drive and directory path in which MEMBRAIN.SYS is to be 
              created. This parameter is entered in the form 'd:\path '. If 
              drive is omitted, then the default drive will be used. If the 
              path is omitted, then the current directory will be used. 
 
    NOTES: 
         - MEMBRAIN.EXE passes a return code upon termination that can be 
           tested in a batch file with the 'IF ERRORLEVEL ' batch file 
           command. A non-zero return code indicates that an error occured. 
 
 
 
 
 
                                                                PAGE 1 
 
 
 
 
 
                             MEMBRAIN DOCUMENTATION 
 
 
 
    2) To create a CONFIG.SYS file: 
 
         Enter on the DOS command line: 
 
          COPY CON: CONFIG.SYS        'Copies keyboard input to CONFIG.SYS 
          DEVICE=MEMBRAIN.SYS         ' this goes into the file 
          Press F6 and then <ENTER>   ' this writes the file to disk 
 
    NOTES: 
         - CONFIG.SYS must be on the drive used to boot DOS. 
         - If you already use CONFIG.SYS, then edit it to include the 
           statement 'DEVICE=MEMBRAIN.SYS '. 
         - Multiple 'DEVICE= ' statements can be used in CONFIG.SYS to load 
           more than 1 MEMBRAIN device driver. This is less efficient than 
           using a single, larger device driver, and is not supported by 
           the QSYS INSTALLATION AID. 
 
    3) Re-boot DOS either by powering the system off and then back on, or 
       with the key sequence 'Ctrl-Alt-Del '. The MEMBRAIN.SYS device 
       driver is automatically loaded and initialized by DOS. 
 
 
    - Configuration Tips 
 
         MEMBRAIN.EXE displays a summary of disk space utilization as it 
    creates MEMBRAIN.SYS. The following example illustrates how to use 
    the data provided. 
 
    MEMBRAIN 20,128,1,8,C:\            'Command used to invoke MEMBRAIN.EXE 
 
    <<<< M e m  B r a i n >>>>         'Title 
       (C) 1984 Dennis Lee 
       20K MemBrain Created            'disk size       \   These are the 
                                                         \  values created, 
      128  bytes per sector            'sector size       \ and may differ 
        1  sectors per cluster         'cluster size      / from requested 
        8  directory entries           'directory entries/  values. 
 
        1  reserved sector             'boot record          \ 
        2  FAT sectors                 'file allocation table > overhead 
        2  directory sectors           'directory            / 
      155  data sectors                'usable file space 
    -------------------------- 
      160  total sectors               '160 sectors X 128 bytes/sect = 20K 
 
    This summary can be used to analyze the overhead of the configuration. 
    Since a change in the configuration has no effect until the next time 
    DOS boots, MEMBRAIN.EXE may be executed several times to analyze the 
    effects of different parameters. The following notes are general tips. 
 
 
 
 
 
 
 
                                                                PAGE 2 
 
 
 
 
 
                             MEMBRAIN DOCUMENTATION 
 
 
 
    1) Sector and Cluster Sizes 
 
         Each cluster requires 1.5 bytes of space for the file allocation 
    table, and the total is rounded up to next multiple of the sector size. 
    The general rule for adjusting sector size and cluster size is to use 
    small sector and cluster sizes for smaller drives, or when small files 
    will be stored, since less space will be wasted when part of a cluster 
    is left unused between files. Larger sector and/or cluster sizes may 
    provide more usable disk space per Kbyte of disk size, and a slight 
    performance gain with larger drives, or when a few large files are to 
    to be stored, since less space will be used for FAT sectors, wasted 
    space between files is less of a consideration, and DOS will spend less 
    time finding a given amount of data. 
 
    2) Directory Entries 
 
         Each directory entry requires 32 bytes of space, and the total is 
    rounded up to the next multiple of sector size. For example, with 128 
    byte sectors, you get 4 directory entries per sector. Any request for 
    directory entries would be rounded up to a multiple of 4. The only key 
    to allocating directory entries is to allocate slightly more than you 
    think you'll need, because it's frustrating to have free disk space and 
    no available directory entries, but not too many, since extra entries 
    are wasted space. MEMBRAIN uses one directory entry for a volume label. 
 
 
    - Operational Charactaristics 
 
         MEMBRAIN looks to DOS like a non-IBM fixed disk. This device type 
    is used because it provides an operational interface to DOS consistent 
    with it's performance charactaristics. The following list outlines it's 
    important operational charactaristics. 
 
         1) Since MEMBRAIN is a non-IBM device, the 'FORMAT ' command will 
            not work with it. It doesn't need to be formatted! 
         2) Since MEMBRAIN can be any non-standard size, and is considered 
            fixed media, 'DISKCOPY ' will not work with it. 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                                                PAGE 3







Press ENTER to continue: 
 
 
 
 
 
                                                                PAGE 3