I've noticed lately that many terminals and computers have the
ability to blank their screens after a period of inactivity
in order to keep the phosphor from being eaten away.  I thought
this was a silly frill until I blanked my monochrome display
in reverse video and looked closely.  And I've had it less
than a year!

The MONBLNK1.COM program disables the video on a monochrome display
The COLBLNK1.COM program disables the video on the Color Display

after five minutes of inactivity.  Everything disappears except the
flashing cursor.  The display is re-enabled when either a video I/O
or keyboard interrupt occur.  Note that some programs (for example
Wordstar 3.0, or Monoclok.com), access the video ram directly and
thus circumvent the video I/O interrupt.  If you are using such a
program and don't touch the keyboard for five minutes, the screen
will blank even if there is video I/O going on.  If this happens,
just press any key, even a shift key, and the display will return.

Run the program once in DOS and it will stay resident until power
down or re-boot.

To adjust the time delay, get into debug with the program and patch
the bytes at 0129H and 014AH with a new value.  The delay will be
about 14 seconds times the number at these locations.

Rich Winkel
*******************************************************************
Rich has uploaded New versions for the color and the mono which do
work . as of 07/17/83
CAPITAL PC Softsig. 301-949-8848 IBMPC
s uploaded New versions for