Recovery From Trashed Hard Disk

                                MSDOS ONLY


               WARNING THIS TECHNIQUE DESTROYS ALL INFO ON
               YOUR HARD DISK !!!!!!!!


               If you trash your hard disk system and are
               able to run format on the drive, but still
               get multiple error messages or format will
               not run at all the following technique is
               worth a try prior to taking your machine to
               your friendly dealer. If you have had an actual
               physical crash this will not help. However, if
               the problem is caused by something written on
               your drive that format will not remove, this
               should do the trick.


               The following code is entered with DEBUG. It
               involves sending the full device control block
               directly to the disk controller chip (here, to the
               PC XT-compatible BIOS on the host adapter card).
               While not yet tested, this process should work
               on the XT controller as well.  The command set is
               identical, and can be found in the IBM PC
               Technical Reference Manual under Fixed Disk
               Adapter. This technique has also been used
               successfully on an ATT 6300 PC.

               The comments in the below example are set off with
               semicolons, and are not entered into DEBUG.

===================================================================


;low level formatting of 20 MB drives with Centan controller
;place MSDOS disk with debug in dive A:

A>debug C:
-o 321 0             ;write port controller reset
-o 322 0             ;write port controller select

-o 320 0c            ;init drive characteristics command------
-o 320 0             ;..
-o 320 0             ;..
-o 320 0             ;..
-o 320 0             ;..
-o 320 0             ;..

                     ;-------8-byte parameter block-------------
-o 320 02            ;max number of cylinders - high byte
-o 320 64            ;max number of cylinders - low byte (264H = 612D)
-o 320 04            ;maximum number of heads (= 4)
-o 320 02            ;reduced write cylinder - high byte
-o 320 64            ;reduced write cylinder - low byte (264H = 612D)
-o 320 01            ;write precomp cylinder - high byte
-o 320 00            ;write precomp cylinder - low byte (100H = 256D)
-o 320 0b            ;ECC burst length (0BH = 11)

-i 320               ;read controller hardware status
00                   ;result here should be "00". If not, abort
                     ;  and restart the sequence.

                     ;-----optional---------------------------
-o 322 0             ;write port controller select
-o 320 0             ;check for Drive Ready command----------
-o 320 0             ;"0" for drive 0, "20" for drive 1
-o 320 0             ;..whole command is optional, but may be
-o 320 0             ;..required with some disks.
-o 320 0             ;..
-o 320 0             ;..

-i 320               ;read controller hardware status
00                   ;again, result here should be "00" for
                     ;..logical drive 0, "20" for logical drive 1.  If not,
                     ;..abort and restart.
                     ;-------end optional command----------------

-o 322 0             ;write port controller select
-o 320 4             ;format drive command-----------
-o 320 0             ;drive 0, starting head 0 (00d hhhhh), "20" drive 1
-o 320 0             ;starting cyl high (cc 000000) = 0
-o 320 0             ;starting cyl low (cccccccc) = 0
-o 320 4             ;interleave factor (000 iiiii)
-o 320 0             ;retries, step option (r 0000 ssss) = 0

-                    ;disk drive will start formatting--watch for
                     ;..drive busy light to go out.
-quit

     Now either warm boot with <Ctrl><Alt><Del> or cold boot with
a power cycle.  Some drives or controllers may require the cold
boot to reset the disk parameters.

     Then from DOS (in the floppy drive), use FDISK to redefine
the partition and FORMAT to format for the DOS version you are
using.

(* This last step is very important !!!!!!!!!!!!!!!!!!!!!!   *)