**********************************************************************

  The TSR package is a group of programs useful in managing
  DOS memory, and in particular managing memory-resident
  utilities. TSR stands for "Terminate and Stay Resident".

**********************************************************************

MARK.COM and RELEASE.COM are used to remove memory-resident
programs from memory, without the usual problems of creating
holes or leaving interrupts dangling. The two programs are used
simply as follows:

1) Run the program MARK.COM before installing any memory-
   resident program that you may wish to deinstall later.
   This marks the current position in memory and stores the
   DOS interrupt vector table (all interrupts from 0 to FFH).

2) Install whatever TSRs that you want to use, in the normal
   way that you install them.

3) When you want to deinstall all TSRs above the last MARK,
   run the program RELEASE.COM. This will release all of the
   memory above (and including) the last MARK, and restore
   all interrupt vectors taken over by the memory resident
   programs.

MARK and RELEASE can be "stacked" as many times as desired.
RELEASE releases the memory above the last MARK call.
MARK uses about 1600 bytes of memory each time it is called.
This 1600 byte region is also released when a RELEASE is done.
MARK memory usage is dominated by the copies of the DOS
interrupt vector table (interrupts 0..FFH) and the copy
of the EMS page map (blocks 0..31 only) which MARK keeps
when it goes resident.

MARK and RELEASE can optionally be called with a single command
line parameter:

  MARK MarkName
  RELEASE MarkName

In this way a particular mark is given a name. Calling RELEASE
with the same name will release all memory above and including
the mark of that name, also releasing any intermediate marks in
the process. If no mark of the proper name is found, RELEASE will
halt with a warning. A RELEASE call with no MarkName specified
will release the last MARK, whether or not that MARK was named.

The MarkName can be any text string up to 126 characters in length.
It may not contain embedded blanks or tabs. Case (upper or lower)
is not important when matching MarkNames.

As of version 1.4, MARK and RELEASE also control Expanded memory
(Lotus/Intel/Microsoft EMS). They have been tested with READY!
and with the TurboPower Software expanded memory disk cache, as
well as with the device drivers used by the STB Expanded Memory
Card.

WARNING: if a resident application allocates expanded memory
at some time >after< going resident and after the last MARK made,
that expanded memory will be released by a call to RELEASE.
The current expanded memory manager (EMM) does not give us enough
information to avoid this possibility. Fortunately, there are
no known memory resident programs which perform this dynamic
allocation of expanded memory. We hope that the EMM will be
upgraded before such applications are designed.

As of version 1.6, RELEASE takes special precautions to allow
it to release extra invocations of the DOS command processor.
In the simplest form, an extra command processor is obtained
by typing COMMAND at the DOS level. Many multitasking or
switching utilities also utilize this feature of DOS, and these
utilities can now be managed via MARK and RELEASE.

**********************************************************************

MAPMEM.COM is used to display the current DOS memory map. It shows
the resident programs, how much memory they use, and what interrupt
vectors each currently owns. MAPMEM also shows information about
expanded memory when such a card is installed. Calling MAPMEM with
a "V" command line parameter (i.e., MAPMEM V) will show additional
information about each program . The "Files" column shows the number
of file handles that each resident program has kept open.

RAMFREE.COM supplies a quick way to determine the amount of free RAM
(without going through CHKDSK).

EATMEM.COM is useful for development work where you want to test
software in an environment with a desired amount of available memory.
Note that the memory used by EATMEM can be freed up by using MARK
and RELEASE. EATMEM is called with a single command line parameter,
specifying (in decimal) the number of KILOBYTES to eat up.

**********************************************************************

All of these programs should work on any system running PCDOS or
MSDOS 2.0 or later. They were developed on a Compaq Deskpro
286 running Compaq DOS 3.0. Source code is available in the file
TSRSRC.ARC (the programs are written in assembly language (CHASM)
and Pascal (Turbo)).

Written by Kim Kokkonen, TurboPower Software.
Version 1.6 - 3/20/86.
Telephone: 408-378-3672 (M-F 9AM-5PM only)
Compuserve: 72457,2131

The programs have been released to the public domain for personal,
non-commercial use only. You may use them yourself, give them to
your friends or co-workers, or distribute them for a cost-based
fee as part of a user's group or bulletin board service. If you
wish to distribute these programs as part of a commercial package,
please contact us for a license agreement.