************************************************************************

				XLT86

	Translates Intel 8080 assembly language source code
	   to Intel 8086 assembly language source code.

			11/11/84 Frank J. Zerilli


************************************************************************

     XLT86 processes lines with DR's exclamation point statement
separator correctly.  It strips trailing blanks or tabs from lines.  It
replaces initial asterisks in lines with semicolons.  It provides
several options to format the output file for best appearance.  This
program gives the choice of converting the case of instructions to upper
or lower case or of trying to preserve the case of instructions.  An
activity dot is printed on the console for every 100 lines of input
processed.

     The program removes any colons terminating symbols on the same line
with the pseudo-operators EQU, DB, DW, or RS and insures that all other
labels are terminated with a colon.




 
 Command line:

     XLT86 [d:]srcfile[.typ] [d:destfile.typ]

     All parameters in brackets are optional, and, if omitted, the
default values are:

  Source file-type      -- ASM
  Destination file-type -- A86
  Destination file-name -- same as the source file-name
  Drive                 -- current drive



Examples:

XLT86 PRGM1                   --     translates PRGM1.ASM to PRGM1.A86
XLT86 PRGM1 PRGM2             --     translates PRGM1.ASM to PRGM2.A86
XLT86 PRGM1.TXT PRGM2.MAC     --     translates PRGM1.TXT to PRGM2.MAC




FLAG LOCATIONS:

 103H -- Change to non-zero value to suppress translation of several
	 non-standard opcodes:

	  REQ, RNE, RLT, RGE, CEQ, CNE, CLT, CGE
	  JEQ, JNE, JLT, JGE,
	  ENT, NAM, RAM, ROG, IFC, ICL, LST, MAC


 104H -- If non-zero (default) XLT86 converts lines with multiple
	 statements separated by DR's EP separator into separate lines.
	 Change to zero for output on a single line with the translated
	 statements separated by exclamation point (!).


 107H -- If zero (default) XLT86 translates

		PUSH PSW			POP PSW

	 to

		LAHF				POP AX
		PUSH AX				SAHF

	 Otherwise, the translation is

		LAHF				POP AX
		XCHG AH,AL			XCHG AH,AL
		PUSH AX				SAHF
		XCHG AH,AL

 108H -- If zero (default) XLT86 translates

		INX rp				DCX rp

	 to

		INC rp'				DEC rp'

	 Otherwise, the translation is

		PUSHF				PUSHF
		INC rp'				DEC rp'
		POPF				POPF

 109H -- If zero (default) XLT86 translates

		DAD rp

	 to						-------------
							| rp  | rp' |
		ADD BX,rp'				|-----|-----|
							| B   | CX  |
	 Otherwise, the translation is			| D   | DX  |
							| H   | BX  |
		PUSHF					| SP  | SP  |
		ADD BX,rp'				-------------
		POPF



     The distributed version of XLT86 uses 4K of buffer space, 2K for
the input buffer and 2K for the output buffer.  This can be changed by
changing the equate MEMSIZ (currently set to 4) to the total buffer
space desired (in Kb) and reassembling the program.  However, increasing
the buffer space beyond 4K will not significantly increase the speed of
translation.  For example, a 36K file was translated in 44 seconds
(input and output files on the same double density 8" floppy) with
MEMSIZ = 4 and in 42 seconds with MEMSIZ = 32.  Disk activity may be
less with larger buffers, however.

     This program is based on similar programs for 8080-Z80 conversion
(XLATE2, XLT80, XLTZ80). It is a simple-minded program.  While a simple
minded program is ok for translation between 8080 and Z80 mnemonics, it
is not as good for 8080 to 8086 conversion so that you will have to do a
fair amount of editing of the converted file to get it to work properly.
Following is a list of items to check for (it's by no means complete) in
your post-conversion editing.

     Some of the following items are specific to CPM-86 and Digital
Research's ASM86 although many will also apply to Intel's ASM86
assembler.


1) BDOS FUNCTION CALLS

   Replace call to location 0005 (CALL BDOS) with INT 224:
   for example, replace

BDOS	EQU	5

   with

BDOS:	INT	224
	RET

   Alternatively, replace all CALL BDOS or CALL 5 with INT 224.


2) RETURN TO CCP

   Replace jumps to location 0000 (abort) with call to BDOS function 0:
   for example, replace

ABORT	EQU	0

   with

ABORT:	MOV	CL,0
	MOV	DL,0
	CALL	BDOS

   An alternative is to restore the CCP stack pointer (you have to have
   saved it, of course) and do a RETF.

*** Important Note: if the program uses a local stack instead of the CCP
   stack then be sure to set SS (stack segment) register to the same value
   as the CS (code segment) register.


   For example:

START:	MOV	AX,SS
	MOV	CCPSS,AX	; save CCP SS register
	MOV	CCPSP,SP	; save CCP stack pointer

	MOV	SP,OFFSET STACK	; set local stack
	MOV	AX,CS
	MOV	SS,AX		; set SS register to CS register
	.
	.
	.

ABORT:	MOV	AX,CCPSS
	MOV	SS,AX		; restore CCP SS register
	MOV	SP,CCPSP	; restore CCP stack pointer
	RETF			; return to CCP

CCPSS	RW	1
CCPSP	RW	1
	RW	STACKLENGTH
STACK	EQU	$


3) ALLOWED CHARACTERS IN SYMBOLS

   Change any '$' in symbols to '@' or '_'.


4) PAGE 0 EQUATES

   Replace equates which define page 0 addresses with data defining
   pseudo-ops:  for example, replace

DFCB1	EQU	005CH

   with

	ORG	005CH
DFCB1	RS	16

   Alternatively, add '.' to references to page 0 equates.  For example,
   change any reference like

	MOV	AL,DFCB1

   to

	MOV	AL,.DFCB1

   Reason:  MOV	AL,DFCB1 is probably the translation of LDA DFCB1 (it
   could also have come from MVI A,DFCB1 but this would only be due to
   the weirdness of the programmer).  The period operator converts a
   symbol of type number (DFCB1 got the type of number from the EQU to
   005CH) into a variable.



5) LABELS WHICH SHOULD HAVE THE WORD TYPE ATTRIBUTE

   Change statements like

WORDLABEL RS	2

   to

WORDLABEL RW	1

   At the same time, change statements like

	MOV	AL,WORDLABEL+1

   to

	MOV	AL,BYTE PTR WORDLABEL+1

   Reason:  the assembler is very fussy about typing of operands


6) LABELS WHICH ARE ADDRESSES OF EXECUTABLE INSTRUCTIONS

   Change statements like

	MOV	AL,CODELABEL

   to

	MOV	AL,BYTE PTR CODELABEL

   (where CODELABEL is the symbol for a code segment address)


7) CONVERTING ADDRESSES TO NUMBERS

   Change statements like

	CMP	AL,(BUFFER_ADDRESS + BUFFER_LENGTH)/256

   to

	CMP	AL,(OFFSET BUFFER_ADDRESS + BUFFER_LENGTH)/256


8) CONVERTING ADDRESSES TO NUMBERS (continued)

   Change statements like

	MOV	CL,TABLE_END - TABLE_START

   to

	MOV	CL,OFFSET TABLE_END - OFFSET TABLE_START



9) OPCODES WHICH AFFECT FLAGS

   Watch out for this:  unlike the 8080, incrementing and decrementing
   16 bit registers in the 8086 will affect the flags.  So if you have
   some 8080 code like

RETZER:	MVI	B,1
	LXI	H,0
	DCR	B
	INX	H
	RET

  which would return with the zero flag set, it will be translated to

RETZER:	MOV	CH,1
	MOV	BX,0
	DEC	CH
	INC	BX
	RET

  which will return with the zero flag reset !   Therefore, the code
  must be changed to

RETZER:	MOV	CH,1
	MOV	BX,0
	INC	BX
	DEC	CH
	RET

   which will return the flag as originally intended.

   XLT86 has a option (set location offset 108H non-zero) to translate
   INX rp or DCX rp (rp stands for register pair B, D, H, or SP) to the
   sequence

	PUSHF
	INC or	DEC rp'
	POPF

   There is a similar problem with DAD rp which affects only the carry
   flag in the 8080.  Its translation is ADD BX,rp' which affects sign,
   zero, half carry, parity, and overflow as well as the carry flag.
   Setting location offset 109H in XLT86 to non-zero will PUSHF and POPF
   as for INX and DCX but in this case there is still a problem if the
   result of the operation on the carry flag must be preserved.


10) PUSH or POP PSW

   In the 8080, the A registers is the high byte of the word pushed onto
   the stack.  The translation is PUSH AX in which the register
   corresponding to A is AL which is the low byte of the word pushed
   onto the stack.  This is would not be a problem unless the program
   tries to pick the register directly from the stack.  Setting the
   location offset 107H in XLT86 to non-zero will cause the translated
   program to include an XCHG AH,AL before and after pushing to (and
   after popping from) the stack.