;----------------------------------------------;
;   ATT 6300  Resident Time Display, Automatic ;
;          Screen Dimmer with Panic key        ;
;                                              ;
;                                              ;
;                by                            ;
;         Arnold Burkhoff                      ;
;         18 Tina Lane                         ;
;         Warren, NJ 07060                     ;
;                                              ;
;    For FREE distribution only                ;
;                                              ;
;                                              ;
; A RAM resident utility which, when active,   ;
; constantly displays the time in the          ;
; upper right corner.  Once the utility is     ;
; installed, the time is activated or          ;
; deactivated with Alt-32 (hold down the Alt   ;
; key and type 32 on the numeric keypad, then  ;
; release the Alt key).  The program is        ;
; initially activated when first installed.    ;
;                                              ;
; Additionally the module will monitor the     ;
; hardware for keyboard and video interrupts,  ;
; and when no interrupts occur for 3 minutes   ;
; the screen will be dimmed.  The screen may   ;
; be manually dimmed, PANIC mode, by entering  ;
; ALT-33 (hold down the Alt key and type 33 on ;
; the numeric keypad, release the Alt key).    ;
; The video monitor will be reactivated by     ;
; pressing any key or when a module executes a ;
; video request.                               ;
; Once assembled, to install, just type:       ;
;                                              ;
; ATTTIME   for hh:mm display                  ;
;                                              ;
; ATTTIME S for hh:mm:ss display (this blinks) ;
;                                              ;
; The time is updated once per second (after   ;
; 18 or 19 clock ticks) and displays the       ;
; time in the ATT hardware clock.  The time    ;
; display overwrites whatever is on the screen ;
; at that location.                            ;
;                                              ;
; Note when setting the time on the ATT6300    ;
; be sure to enter only hours and minutes,     ;
; then wait for the minute to arrive and hit   ;
; the enter key.  This is necessary because    ;
; the clock cannot set seconds or hundredths   ;
; although it will read them out.              ;
;                                              ;
; This program may not be compatible with      ;
; other RAM resident type programs. It is      ;
; absolutely not compatible with non ATT6300   ;
; hardware.                                    ;
;                                              ;
; Thanks to Eric Tauck for the Wolfware        ;
; Assembler.  Available on Compuserve          ;
; (GO IBMSW, Library 4, WASM.ARC). It is fast! ;
;                                              ;
;                                              ;
; Disclaimer:                                  ;
; I do not warrant that the documentation      ;
; is accurate, or that the module operates     ;
; as designed.  I will not be liable for       ;
; any damages of any kind sustained through    ;
; use of this program.  By using this program  ;
; you agree to these terms.                    ;
;                                              ;
;                                              ;
;                                              ;
;----------------------------------------------;