COLOR640.COM -- 1986, B. DuBose, Quendimar Industries

COLOR640 is a memory resident routine that uses the Color Select Register on
the 6845 CRT Controller of the IBM (presumably compatables, too) CGA to change
the current color in high-resolution (640 X 320) graphics mode.  It will also
work in other graphics modes, but the result is different.

Normally, upon entering the high-resolution graphics mode, the screen colors
are set to intense white on black.  While you are still limited to only two
colors (one of them black), they do not necessarily need to be WHITE on black.

Sending the appropriate code to the Color Select Register (at address hex 3D9
on the CGA) can change the colors sent to the monitor.  The CSR decodes as
follows for high resolution graphics:

         -----------------------------------------------------------
        |    32   |    16   |    8    |    4    |    2    |    1    |
         -----------------------------------------------------------
          NOT USED  NOT USED  bright    RED on    GREEN on  BLUE on
                              colors

This "attribute byte" of sorts also has other functions in other graphics and
text modes, refer to the IBM Options and Adapters Tech. Ref. for further info.

When COLOR640 installs, it redirects interrupts 9h and 16h (keyboard int's),
and looks for the combination of ALT-GreyPlus or ALT-GreyMinus to be pressed. 
If Alt-GreyPlus is pressed, value of the byte sent to the CSR is incremented by
two, and this new value is sent out, changing the color.  Alt-GreyMinus does
the same thing, except that the initial value for Alt-GreyMinus' byte is 1,
whereas Alt-GreyPlus' is zero.  The fact that the code increments it by two is
a bug that I can't seem to get rid of, so to access all combinations of colors,
I needed to use two systems, one that handles the odd numbers, and one that
handles the even numbers.  Alt-GreyPlus takes care of the even colors, and
Alt-GreyMinus the odd numbers.  Try experimenting; that's the easiest way to
figure out what's going on.

Even though COLOR640 was designed for high-resolution color graphics, using it
in 80 X 25 text mode will work -- it changes the border color.  Which, is a
nice way to put the screen back to normal after the Norton Utilities NU.COM
program has run, since it ALWAYS leaves me with an irritating blue border!

COLOR640 takes up about 700 bytes of memory, and does not appear to interfere
with programs such as SideKick or PCTools.

Suggestions, comments, and especially a fix for the two-step bug can be sent to
Bob DuBose, c/o the Lattice Bulletin Board, or c/o Fido 100/10 (McDonnell
Douglas RCC).