VIDEO GRAPHICS ADAPTER - PALETTE TOOL V2.01

       (C) Copyright 1987 by clySmic software.  All rights reserved.

     

     This *improved* version of VPT allows VGA (PS/2 Model 50, 60 or
     80) or Display Adapter/2 owners to:

     o    view the quarter-million color palette they've been hearing
          about,

     o    set any attribute (0 - 15) to any color,

     o    have the colors "stick" with most programs,

     o    load and save their favorite settings,

     o    and to use the program in batch mode.

     
     Use - Interactive Mode
     -----------------------

     Command: VPT

     VPT operates in text mode and allows setting of any or all of the
     sixteen attributes available in text mode.  There are three
     sliders (one each for Red, Green, and Blue), each of which can
     assume any of 64 values (0 through 63).  These are moved with the
     left and right arrow keys.  Control left and control right arrow
     moves five positions.  To move between R, G, or B, the up and
     down arrow keys are used.  To move between attributes the Page Up
     and Page Down keys are used.  R resets the colors to the ones
     that were in effect when the program was started, and D selects
     the default, boot-up colors.  S saves the current settings in a
     file, and L loads the saved file.  The End key exits the program.

     
     Use - Batch Mode
     ----------------

     Command: VPT <option>

     Where <option> is one of the following (capitalization does not
     matter):

     /L   This loads the saved palette, if there is one.  If there
          isn't, you will get an error message.

     /D   This loads the default palette.  These are the colors
          assigned by IBM and are the ones you would see if you didn't
          use VPT.

     /X   This resets the "palette load on mode change" option to true
          (see "Technical" below, for an explanation)

     /?   Presents a small help list recapping your options.

     Any other options will generate an error message.

     The main reason for batch mode is to include VPT in your
     AUTOEXEC.BAT file.  First you would run VPT interactively, find
     the colors you like, save them, then include a line like the
     following:

     VPT /L

     in your AUTOEXEC file.  This will load your saved colors when you
     start up your computer.  VPT.COM should be placed in a directory
     on your path.  If you don't wish to see the informational
     messages produced by VPT in batch mode, you can redirect the
     output to the null device (a.k.a. the bit bucket) as follows:

     VPT /L >NUL:

     Note that error messages *cannot* be redirected and will still be
     seen.

     
     Technical Information
     ---------------------

     * General

     VPT works by making BIOS calls that manipulate the DAC (digital
     to analog converter) color registers; each register (there are
     256, to allow for the 300x200x256 mode) contains 18 bits, 6 each
     for Red, Green, and Blue.  Each RGB value can go from 0 to 63,
     all the combinations makes for 262,144 possible colors.  You can
     show up to sixteen of these at a time in the text modes, each of
     the sixteen "attributes" can be any color (or all the same color)
     out of the quarter-million.

     * Mode Sets

     Normally BIOS resets the EGA and DAC color registers whenever a
     mode set is done.  VPT makes its colors stick across a mode
     change by using the "Default Palette Loading During Mode Set"
     BIOS call to disable this action.  If, for some reason, you
     desire to return this to its default, boot-up condition, use VPT
     /X.  Then a subsequent mode change, like MODE CO80, will cause
     the default conditions to prevail.

     * Registers, Registers Everywhere

     The DAC color registers are mapped through the EGA palette
     registers, so, for instance, the attribute "Brown" (6) maps to
     the color $14 on an EGA (out of its 64 possible colors); on the
     VGA, DAC color register $14 contains $2A,$15,$00 for the R, G,
     and B values (these are all default values).

     In order to not to be foiled by EGA-aware programs, VPT resets
     the EGA palette registers to their default values each time it is
     run.  If a program remaps the EGA registers, and then counts on a
     mode set to return them to normal when it exits, the registers
     will *stay* remapped because of the disabling of the "palette
     load on mode set".  Simply type VPT /L and it will remap the EGA
     registers to their default values.

     Note that EGA-aware programs will still use their own colors
     while the program is running; VPT can't prevent that.

     * References

     VPT was written based on technical information from IBM's Display
     Adapter/2 Technical Reference.  There is very little discussion
     of some aspects of the VGA, but all the BIOS calls are there
     (even if they're not explained well).  If anyone has any other
     sources of tech info (especially about the MCGA) please let me
     know.

     
     Caveats
     -------

     I don't believe VPT will run on the MCGA in the Models 25 and 30.
     I only have a Model 50 to test it on, but since part of the
     program relies on mapping through the EGA palette registers
     (which I assume the MCGA doesn't have), I don't see how it could
     work.  I also don't know if the VGA detection routine in VPT
     would think the MCGA is a valid VGA or not.  EGA-aware and VGA-
     aware programs still will run with their own colors, all (okay,
     almost all, who knows what's out there?) other programs will use
     the colors VPT sets.

     VPT should run on the *real* VGA clones when they become
     available; however, the pseudo-VGAs (really EGAs with 640x480
     mode) won't run it - they still have only 64 colors total (and
     will cause grief for their buyers, I suspect).

     * The Palette File

     The saved palette file is called VPT.PAL.  For DOS 3.x users, it
     is stored in the same directory that VPT is run from.  For
     instance, say VPT is stored in the C:\BIN directory, that
     directory is on your path, and you are in C:\ZUUL.  The palette
     file will be stored in C:\BIN.  For DOS 2.x users, the file will
     be stored in the root directory.  DOS 1.x users are quite out of
     luck, why do you have advanced video but DOS 1.x anyway?


     Enhancements
     ------------

     VPT currently sets the border to black.  If there is sufficient
     interest, control over the border color could be added.  Also,
     multiple, named palette files, loadable from the command line,
     are a possibility.  All suggestions are welcome.


     All that Legal Brouhaha
     -----------------------

     The program is copyrighted by clySmic software, but may be copied
     and posted on BBS systems, as long as it is not altered and both
     files (VPT.COM and VPT.DOC) are kept together.



                                                        -- Ralph Smith
                                                         CIS 76156,164