I had the opportunity to try the HP LaserJet Printer that the HP salesman left
with me for a few days on the IBM-PC.  I was impressed with the quality of the
output. I connected an RS232 cable to the COM1 port and used the following 
software. "PRINT filename" will queue a file to the laser printer. To print in 
"landscape" orientation, "COPY LAND PRN" before giving the print command (uses 
the ROMAN 8 font cartridge). 
                                       
                        Ted Shapin, Oct. 18. 1984.

In AUTOEXEC.BAT, add:

mode com1:9600,n,8,1,p   [sets the baud rate and 8-bits]
xonxoff                  [this is a program that does x-on/x-off handshaking]
copy port prn            [this initializes the printer for portrait mode]
- - - - - - - - - -
This is the PORT file:   [replace "#" by an escape character in the next lines]
#&l0O#&l61F              [set portrait orientation, 61 lines/page]
#&a5L#&l6D               [set left margin at 5, 6 lines/inch]

This is the LAND file:
#&l1O#(s17H#&l8D#&a20L   [set landscape mode, font pitch to 17, 8 lines/inch
                                left margin in column 20]

- - - - - - - - - - -    [assemble the following file and convert to .COM]
        page    60,132
        title   xonxoff - asynch xon/xoff support

;
;       XONXOFF - asychronous flow control using XON XOFF 
;                 (DC1 and DC3 control characters)
;
;       this routine replaces the MODE command redirection of
;       LPT1 to COM1, in addition it handles the XON XOFF flow
;       control
;
;       note: this is a preliminary version, it will be modified
;             to handle COM1 and COM2 and a Cntrl-break out of XOFF
;             state

;
;       Author: Jim Sturtevant
;               Coherent Software
;               June 23, 1983
;               (415) 593-7567
;
;       (c) Copyright, 1983, Coherent Software
;
;
;       constant definition
;
xon             = 17                    ;DC1, control-Q
xoff            = 19                    ;DC3, control-S
com_init_port   = 0                     ;from tech ref page a-20
com_send        = 1                     ;doc for interupt 14h
com_read        = 2
com_status      = 3
com_line        = 0                     ;0 = COM1:, 1 = COM2:

com1_lsr        = 3fdh
com1_rbr        = 3f8h


;
;       define necessary segments
;
stack   segment para stack 'stack'
        db      28h dup ('stack')
stack   ends

data    segment para public 'data'
msg     db      'XON/XOFF Enabled$'
data    ends

        page
;
;       initial code segement
;
;               .changes INT 17h to point to this programs
;                intr procedure
;               .displays message
;               .exits and stays resident
;
code    segment para public 'code'
intload proc    far
        assume  cs:code,ds:data,ss:stack,es:nothing
        push    ds
        mov     ax,data                 ;point to our data segment
        mov     ds,ax
        mov     ax,0                    ;es to point to interupt vec
        mov     es,ax
        mov     word ptr es:5ch,offset intr ;change interup rtn ptr
        mov     ax,cs
        mov     word ptr es:5eh,ax

        mov     dx,offset msg
        mov     ah,9
        int     21h                     ;display message (DOS)

        pop     ds                      ;set up for exit stay res call
        sub     ax,ax
        pushf
        push    ds
        push    ax
        mov     dx,300h                 ;length of segment to retain
        mov     ax,word ptr es:9eh
        push    ax
        mov     ax,word ptr es:9ch
        push    ax
        ret
intload endp

        page
;
;       INTR - line printer interupt routine replacement
;
;               .this routine checks the COM line for incomming
;                characters before each character output
;               .scan for XOFF if received wait for matching XON
;               .otherwise output character
;
intr    proc    far
        sti
        push    ds
        push    dx
        push    cx
        push    bx
        push    ax
        or      ah,ah                   ;func = 0 (write character)?
        jnz     irtne                   ;no, exit
        call    chkcom                  ;check for XOFF
        mov     ah,com_send             ;write character function
        mov     dx,com_line             ;com line number
        int     14h                     ;rs232 call
        jmp     irtne

irtne:  pop     ax
        mov     ah,90h                  ;return no error status
        pop     bx                      ;See INT 17h for doc on AH
        pop     cx
        pop     dx
        pop     ds
        iret
intr    endp

;
;       this routine checks to see if there is data avaialable
;       from the COM line, if so the data is read in and checked
;       for XOFF. If XOFF another loop is begun to wait for match
;       ing XON.
;
chkcom  proc    near
        push    ax

chkagain:
        mov     ah,com_status           ;return COM status in AX
        mov     dx,com_line             ;set port #
        int     14h

        and     ah,1                    ;data ready?
        jz      chkexit                 ;no, return

;       mov     ah,com_read             ;receive data
;       int     14h
        mov     dx,com1_rbr
        in      al,dx

        cmp     al,xoff                 ;pause output?
        jne     chkagain                ;nope, keep looking

;
;       we have received an XOFF, loop until XON received
;
xonloop: mov    ah,com_status           ;return COM status
        mov     dx,com_line
        int     14h

        and     ah,1                    ;data available?
        jz      xonloop                 ;no, keep checking

;       mov     ah,com_read             ;yes, read it
;       int     14h
        mov     dx,com1_rbr
        in      al,dx

        cmp     al,xon                  ;did we get an unpause?
        jne     xonloop                 ;nope, keep looking
        jmp     chkagain                ;ok, make check COM line

chkexit: pop    ax
        ret
chkcom  endp


code    ends
        end     intload