LQ (tm)

                               by Mark Harris


                    Granny's Old-Fashioned Software (tm)
                               Rt 4, Box 216
                              Boone, NC 28607
                               (704) 264-6906

                                 July, 1986
                                Version 2.0

                       (C) 1985, 1986 by Mark Harris
                            All Rights Reserved

          The unmodified LQ distribution diskette, containing a
          copy of this manual, may be freely copied and shared,
          but printed copies of this document may not be copied.












                             Table of Contents

          1. Introduction                                       1
          2. LQ installation                                    2
          3. Using LQ in the resident mode                      7
          4. Using LQ in the file mode                         11
          5. Control sequences                                 14
          6. The LQ parameter line                             18
          7. Creating or modifying a configuration file        21
          8. Tips for better printouts                         28
          9. Character sets available in LQ                    30
          10. Editing character sets: the EDCHAR program       33
          11. The graphics mode                                38
          Appendix A. About 'Shareware'                        40
          Appendix B. ASCII codes                              41

          Introduction                                          1



                                     LQ
                  Letter quality for dot matrix printers.

                       (C) 1985, 1986 by Mark Harris
                            All rights reserved.

          1. Introduction.

              LQ is a program for the IBM PC and compatible
          computers which will allow you to produce high-quality
          text on inexpensive dot matrix printers.  Most such
          printers are supported, but you may have to install or
          create a configuration file (see Section 5) if yours
          deviates significantly from an Epson.

              LQ offers these features:

            1. LQ can be 'locked' into memory to function
               inconspicuously with your favorite word processor
               or other program, or it can be used only as needed
               to process disk files.

            2. Most control sequences for turning on special
               modes (boldface, underline, superscript, etc.)
               will produce the corresponding results with LQ, so
               you may not have to modify your word processor to
               accommodate LQ.

            3. LQ includes a print spooler which can be set to
               any length from 1 - 200K characters.  The spooler
               has been customized to work with LQ's long
               graphics sequences very efficiently (using about
               1/40 the space required by a conventional
               spooler); you can continue using your computer for
               other tasks while documents print in the back-
               ground.  If you use single sheet feed, LQ will
               interrupt your work to prompt you to change paper
               then return to you to the point at which you were
               interrupted.

            4. The spooler and several of LQ's options can be
               controlled using a 'pop-up window' which is
               available at any time.  This is particularly
               convenient for toggling letter-quality mode on and
               off and for flushing the buffer to abort a
               printout.


          2                                       LQ installation

            5. Special modes such as proportional spacing, extra-
               large and graphics printing are available. Using
               the graphics mode you can create letterheads and
               other pictures in the middle of your printouts.
               (In Version 2 of LQ creating these pictures is a
               tedious process; Version 3 is expected to include
               a picture editor to make this easier.)

            6. Four fonts are available at any time, and others
               can be swapped into memory when desired.  You can
               switch between these fonts using codes in your
               text or by using the LQ Control Window.

            7. You can modify an existing character set or edit
               your own from scratch using the EDCHAR program
               included in the package.

              You will probably want to take a look at LQ's
          output before reading about all the details.  Following
          is a procedure to get some quick results if you have an
          Epson-compatible printer; if yours is different, skip
          this test and read on.

            1. Boot DOS.
            2. Insert the LQ disk and type LQDEMO.
            3. Turn on your printer and press a key when prompted.
               For best results, leave friction on if you have
               friction feed.
              If you want to experiment a little with LQ now, try
          the following:  type 'LQ' at the DOS prompt to load the
          program into memory, then run any other program (such
          as a word processor) which generates printed output.
          At any time you can bring up the LQ menu by pressing
          both shift keys simultaneously.  If your output is
          garbled, don't panic yet - read on!

          Note:  The file READ.ME describes revisions to LQ and
          other important information.  To view this file on the
          screen enter TYPE READ.ME; to obtain a printed copy
          enter COPY READ.ME PRN.

          2. LQ installation.

              There is a good chance that LQ is already config-
          ured properly for your use; if you have an Epson-
          compatible printer we recommend that you skip this
          section on first reading of the manual and come back to
          it later.

              There are two levels of installation which may need
          to be performed in order to use LQ.  You should

          LQ installation                                       3

          configure your word processor or other application for
          an Epson MX 80 (or IBM Graphics Printer) if it uses
          control codes to exploit a printer (to print italics,
          emphasized print, etc.), and you should run LQINST if
          you have a printer which is not Epson-compatible (or if
          you want to change the size of the buffer, assign a
          different key combination to bring up the LQ Control
          Window or change the default character sets used by
          LQ).

              LQ will make your printer appear to a word
          processor as an Epson MX 80 (or IBM Graphics Printer)
          when printing in the letter-quality mode.  Most word
          processors will let you choose a printer when a
          documented is printed, so you can maintain one printer
          description file for draft mode (based on what your
          printer really is) and another one for LQ mode.  For
          example, PC-Write gives the prompt

              Print control file name (Esc:exit Enter:none):

          and MultiMate lets you select a PAT (Printer Action
          Table) file when documents are printed.

          LQINST.

              LQINST alters the LQ.COM program, so it is wise to
          make a copy of the LQ disk before starting the
          installation procedure.  Insert a working copy of the
          disk in your computer's default drive and enter
          'LQINST'.  You will be prompted to enter the disk
          containing the file LQ.COM; since this file is on the
          distribution disk, no disk exchange is necessary.
          Throughout this installation procedure you can ignore
          messages to insert disks if you are working with a copy
          of the distribution disk; later on if you use separate
          disks for different character sets or other LQ data you
          should swap disks as prompted. The screen should now
          show:

          4                                       LQ installation

          _______________________________________________________

              LQ installation menu:

              1. Change default character sets.

              2. Change printer parameters.

              3. Change keys for LQ window.

              4. Change buffer size.

              5. Quit.

                    Which? (1 - 5)
          _______________________________________________________

          Each option will be described below, but if this is
          your first use of LQ you will probably be content to
          use only option 2 (and that only if your printer is not
          Epson-compatible).

          Option 1:  Change default character sets.

              The LQ.COM program includes four character sets
          within its code; initially these are the sets COURIER,
          COURITAL, HELV and PALATINO.  (See Section 9 for a
          listing of these and other available sets.)  If your
          use of other sets is infrequent it is best to load them
          explicitly using the LQ parameter line (see Section 6)
          but if you would like different sets to be used by
          default then this installation option is in order.
          Installation of a new set is a two-step process: first
          you indicate which set you want to install, then you
          assign it the number (1 - 4) used to turn on the set.

              After this option is selected you are shown a list
          of character sets and prompted to enter the number of
          the set to install:
          _______________________________________________________

             1  COURIER     7  HELVITAL     13  SANS2ITA
             2  COURIER2    8  MAIN         14  SANSITAL
             3  COURITAL    9  MAINITAL     15  SANSSER
             4  GREEK      10  PALATINO     16  SANSSER2
             5  HELV       11  ROMAN        17  SPIRAL
             6  HELV2      12  ROMANITA

                Enter number of set to install:
                 (press <Enter> to quit)
          _______________________________________________________

          LQ installation                                       5


          After you enter the number of the set to install you
          are prompted

              Enter installed character set number (1-4):

          This second number is used in control sequences, in the
          LQ parameter line, or in the LQ Control Window to
          switch to the corresponding set.  Any of the four sets
          can be used at any time, but the first two sets have
          special roles of which you should be aware.  The first
          set is used by default, so it should be the one you use
          most often.  The second set can be turned on by the
          control sequence you normally use to switch to italics,
          so it is best (but by no means required) to make it the
          italicized version of the first set.  For example, you
          could make the first set SANSSER and the second
          SANSITAL.

              After you enter the 'installed character set
          number' the cycle is repeated:  you are again prompted
          to choose a set to install.  You can continue until all
          four sets are changed, or you can retain previous sets
          for those you don't change.  When you are finished,
          press <Enter> without typing a number.

              The changes you make in this and other LQINST
          options are not made permanent until you exit the
          program, so don't worry about doing anything lethal.
          Even if you do save a revised version of LQ.COM, you
          can always run LQINST again to restore it to the way it
          was.

          Option 2:  Change printer parameters.

              The second option lets you change the default Epson
          printer parameters to those for another printer.
          Printer parameters are contained in files with the
          suffix 'PAR' which you may edit or create yourself.
          (See Section 7.)  If you are a registered LQ user and
          experience problems installing a non-Epson printer, we
          will create a parameter file for you on request.  See
          Section 7 for a description of the printer requirements
          for using LQ.

          Note:  After you have performed this installation
          process, your LQ/printer combination will act like an
          Epson MX or IBM Graphics Printer regardless of what
          kind of printer you actually have.  When using LQ you
          should make certain that your word processor or other

          6                                       LQ installation

          application 'thinks' you have one of these models.
          Again, see Section 7.

              When you select this option you are prompted to
          insert the LQ disk, then you are shown a list of all
          parameter files on the disk.  Currently these are

               1  EPSON
               2  IMAGE
               3  PROPRINT
               4  CITOH
               5  STAR

          A given file may work for more than one type of
          printer; for example the Epson parameters are
          appropriate for the IBM Graphics printer.  Enter the
          number of your choice.

              Some experimentation may be required to find or
          create the right file.  Rest assured that you won't do
          any harm by installing the wrong parameters; your
          printer may appear to run amuck, but the only cost is
          the paper.

          Option 3:  Change keys for LQ window.

              There are four shift keys on the PC keyboard:
          Ctrl, Alt, Left Shift, Right Shift.  Many background
          utilities use combinations of these keys to spring into
          action; for example, 'Sidekick' normally requires that
          the Ctrl and Alt keys be depressed simultaneously.  The
          LQ Control Window is normally brought up by pressing
          the left and right shift keys together, but you can
          change this to any pair of shift keys.  Use LQINST to
          make this change permanent or use the K option to
          pass the key combination (temporarily) on the LQ
          parameter line (see Section 6).

              When the third option is selected the following
          screen is displayed:

          LQ installation                                       7

          _______________________________________________________

              Key installation.

              The pop-up window used to control LQ operation
              is normally brought up by pressing the right and
              left shift keys simultaneously.

              You can change this combination to any two of the
              following:

              Ctrl

              Lft Shift         Rt Shift

              Alt


              Press the two keys you would like to use:
          _______________________________________________________

          As soon as you press the desired key combination, you
          are returned to the main menu of LQINST.

          Option 4:  Change buffer size.

              Printing in LQ mode is slow enough that you will not
          enjoy sitting idly by waiting for a printout to finish.
          LQ includes a 'print spooler' for printing in the
          background while you use your computer for other tasks.
          The default size of the buffer used by this spooler is
          16K, which will accommodate about six pages of text.
          You can change the buffer size to any value from 1K to
          200K;  when you select option 4 you are prompted to
          enter this value.  For example, if you want a 20K
          buffer just enter the number 20.

          Option 5:  Quit.

              The last option is used to exit from LQINST.  If
          you have made changes you are prompted

                  Save modifications? (Y,N)

          If you press 'N' then LQ.COM is unchanged, otherwise
          all changes you have made in this LQINST session are
          made permanent.  (You can always run LQINST again to
          make further changes.)



          8                         Using LQ in the resident mode

          3. Using LQ in the resident mode.

              The preferred way to use LQ is in the 'resident'
          mode in which LQ stays in memory while other programs
          are run; this mode offers print spooling and the
          Control Window for changing LQ's parameters.  The
          disadvantage of the resident mode is the memory
          consumption:  with the default 16K buffer the program
          uses about 100K of RAM.  If you don't have enough
          memory to run other programs with LQ installed you
          should use the file mode described in the next section.
          While the latter mode is less convenient you can still
          obtain exactly the same printouts.

              If you want to use LQ as a resident program for
          only part of your session on the computer you can enter
              LQ R
          to remove LQ from memory.  This works only if no other
          resident programs have been loaded above LQ, so if you
          plan on using this technique load LQ last (after
          installing other programs such as Sidekick).

              To load LQ in the resident mode simply type 'LQ' at
          the DOS prompt.  A variety of options can be set by
          adding parameters to this entry; for example
              LQ C1'SANSSER'
          loads LQ and replaces the first character set with
          SANSSER.SET.  A full description of command line
          parameters is given in Section 6.

              Once LQ is loaded you can generally use your accus-
          tomed software with no changes other than improved
          printouts.  (You may have to change your word proc-
          essor's printer description table to accommodate an
          Epson MX 80 or IBM Graphics Printer; see Section 2.)

              Some interaction with LQ can increase its effec-
          tiveness.  This section describes how to use the
          Control Window and print spooler to really master your
          printer.

          The spooler.

              A print spooler is a program which directs pending
          printouts to an area of memory (buffer) and sends
          characters from this intermediate storage to the
          printer only when the computer is relatively idle.  The
          process takes place in the background so that you can
          use your word processing program or other application

          Using LQ in the resident mode                         9

          without interruption.  A number of fine print spooling
          programs are available, some of them public domain.

              LQ obtains its high quality print by printing in
          the 'graphics mode', and this presents special dif-
          ficulties for a conventional spooler.  Without LQ a
          character is sent to the printer as a single byte or
          unit of information, but LQ requires about 40 bytes to
          'draw' a single character.  A single page of text can
          balloon to over 100K bytes, more than enough to fill
          the typical buffer.  Once the buffer is full a spooler
          no longer yields any advantage - other activities must
          stop until the backlog subsides.

              LQ includes an integrated spooler with a default
          buffer of 16K.  Characters are spooled in the standard
          compact form and expanded to graphics in small
          increments.  The default buffer size will accommodate
          about six pages of text and you can increase the size
          to as much as 200K (see Section 2).  The spooler also
          works in draft mode (LQ loaded but turned off), so it
          may be attractive to keep LQ in memory even if your
          demands for letter-quality print are infrequent.

              If you find that a pending printout contains an
          error (such as spelling or formatting) you will
          probably want to abort the printing and correct your
          document.  To do this you must 'flush the buffer':  you
          must tell LQ to stop printing and to ignore the
          presence of any remaining characters in its queue.
          This entails a single keypress in the LQ Control Window
          described below.

          The LQ Control Window.

              There are three ways to select options in LQ:

          in the LQ command line (as when you enter
              LQ C1'SANSSER'
          at the DOS prompt to load the character set SANSSER),

          using control sequences embedded in your text (such as
            <Esc> <Esc> '2'  to switch to character set 2),

          using the LQ Control Window.

          When LQ is in the resident mode you can bring up the
          Control Window by simultaneously pressing the right and
          left shift keys (or another pair of shift keys
          installed with LQINST - see Section 2).  You'll
          see the following menu:

          10                        Using LQ in the resident mode


              Buffer   0% full.  Flush?  Yes
              Current character set:     1
              Wait at form feeds?        No
              Proportional print?        No
              Lines per page:            66
              LQ mode enabled:           Yes

          The cursor is initially positioned at the 'Yes' on the
          first line.  The keys you may use are:

          down arrow: move down a line,
          up arrow: move up a line,
          space bar: change this option,
          'A': advance the printer a little,
          <Esc>: exit this menu.

          The options you can change are:

          Flush the buffer:  If you press the space bar on this
            line, any pending printout is aborted.  Use this
            option to remove an errant document from the buffer.

          Change character set:  The character set number is
            rotated in the set 1,2,3,4.  If character set
            number two is currently in use and the space bar is
            pressed, then set number three will be used at the
            next opportunity.

          Wait at form feeds:  The space bar toggles the status
            of LQ's response to a form feed character (ASCII code
            12).  When this is set to 'Yes', LQ will interrupt a
            program in progress after a form feed is received and
            prompt you to change paper.  In response to the
            prompt, <Enter> will continue printing and <Esc> will
            abort printing.  In either case you are returned to
            the program you were using without interference.

          Proportional print:  You can set proportional print on
            or off.  Using proportional print the sequence 'iiii'
            will occupy less space than 'MMMM'.  This makes text
            more attractive but disrupts the spacing of tables
            and text separated by white space.  Try this option
            to see if it is appropriate for your document style.

          Lines per page:  The default line spacing, and the one
            normally expected by other programs, is 66 lines per
            page.  If you want to change this, press the space
            bar and then enter the new value (from 1 to 95).
            Because of physical limitations of your printer, not
            all these values are possible; for example, if you

          Using LQ in the resident mode                        11

            enter the number 58 you may see this rounded to 59
            (the nearest acceptable value).

          LQ enabled:  The LQ mode can be toggled on and off.  In
            the 'off' setting your printer will operate as if LQ
            were not installed, except that print spooling will
            still be functional.

          Advance:  Pressing 'A' any time the Control Window is
            open will result in a small (1/216") advance of the
            paper when the window is closed.  With many printers
            the first line of a printout may appear smudged;
            advancing the paper with this option will fix the
            problem.  This is done automatically in the LQ file
            mode (see Section 4) or when LQ is loaded in the
            resident mode (if the printer is on).  You can also
            perform this action by embedding the <Esc> <Esc> B
            control sequence in your text (see Section 5).

          When you are finished using the Control Window, press
          <Esc> to return to your previous application.

          12                            Using LQ in the file mode

          4. Using LQ in the file mode.

              When LQ is invoked with the 'F' option a file is
          printed in letter quality but LQ does not remain
          resident.  An example of this use is
              LQ F'MYFILE'
          which prints the file MYFILE.  The primary reason for
          using the file mode is to accommodate systems with
          insufficient memory for using LQ in the resident mode.
          (Another use is for using LQ in batch files for
          printing letterheads and other designs; see Section
          11.)  Since LQ is not resident in the file mode no
          spooling is performed and you must wait for a printout
          to finish before using your computer for other tasks.
          Also, the Control Window is not available in the file
          mode.

              You can use a variety of options in the LQ command
          line; for example
              LQ F'MYFILE' W
          prints MYFILE and waits at form feeds for paper to be
          changed.  See Section 6 for a complete description of
          avaiable options.

              When using the F(ile) option, you can stop
          printing at any time by pressing a key; you will be
          asked if you want to abort the printout or continue.

              The way you create files to be printed by LQ varies
          from one application to another.  Most word processors
          store documents in special formats which make sense
          only to the program itself; let's call these 'source'
          documents.  You want to print not these but rather the
          'output' documents that correspond to the characters
          which would normally go to the printer.  For example
          when one asks WordStar to print a file the program
          prompts
              Output to disk file?
          and gives the user a chance to channel output to a file
          which would otherwise go to the printer.  Such an
          output file is also called an ASCII file since it
          contains only standard ASCII character codes.  (See
          Appendix B.)

              PC-Write is another popular word processor which
          produces ASCII files easily.  The command
              PR MYFILE
          formats and prints the source document MYFILE, and the
          command
              PR MYFILE YOURFILE

          Using LQ in the file mode                            13

          sends the output to the second file YOURFILE instead of
          a printer.  PC-Write is an outstanding Shareware
          product; the distribution disk can be obtained for $10
          from Quicksoft, 219 First N. #224, Seattle, WA 98109,
          206/282-0452.

              The vast majority of word processing, database and
          spreadsheet programs on the market can produce ASCII
          files; consult your program's manual for details.

              If you have a previously-created text file
          'printout' you want to print in a letter quality mode
          you can take two different approaches.
                 LQ F'filename' [parameter list]
          will function as described above, or you can enter
                 COPY filename PRN
          if LQ is resident in memory.  In either case, you may
          want to add additional control codes within the text
          before printing; Section 5 contains a list of control
          codes and their functions.  For example, suppose you
          have used your word processor to create an output file
          with the lines
              This is a test.
              This is only a test.
          The control sequence used to initiate a line of large
          character is '<Esc> <Esc> L'; let's look a couple of
          ways to insert these codes before the first line.  If
          you have Sidekick on your system, you can enter a
          control code such as <Esc> by first pressing <Ctrl P>,
          so you would position the cursor at the start of the
          first line and type
              <Ctrl P> <Esc> <Ctrl P> <Esc> L
          A more universal (but less convenient) method is to use
          EDLINE.COM, the line editor which is included with your
          DOS system disk.  You can edit a given line in the same
          way you edit a line at the DOS prompt; here is a
          summary of line editing functions from the DOS User's
          Guide:


          14                            Using LQ in the file mode

            DOS           Description
            Editing Key
            Ins           Allows you to insert characters within
                          a line.
            Del           Deletes one character in the input
                          buffer.  The character in the buffer is
                          not displayed and the cursor does not
                          move.
            Esc           Cancels the line currently being
                          displayed.  The buffer remains
                          unchanged.
            F1 or ->      Displays one character from the buffer
                          each time it is pressed.
            F2            Displays all characters up to a
                          specified character.
            F3            Displays all characters in the buffer.
            F4            Displays all characters after and
                          including the specified character.  F4
                          is the opposite of F2.
            F5            Accepts the line you edited as the
                          current buffer line.

              Assuming you had saved the previous file under the
          name MYFILE, you would begin your EDLIN session by
          entering
              EDLIN MYFILE.
          Find the number of the line you want to edit by using
          the List or Search commands (see the DOS manual for
          details), then enter this number to edit the line.  In
          this case we know in advance that we want to edit the
          first line, so we would enter the number '1'.  The
          screen should show
              1:*This is a test.
              1:*
          Control characters can be entered by using the <Ctrl V>
          prefix; for example, <Ctrl T> can be entered by typing
          <Ctrl V> T, and <Esc> can be entered by typing
          <Ctrl V> [.  Press Ins to enter the insert mode, then
          type <Ctrl V> [ <Ctrl V> [ L.  Press F3 to display the
          rest of the buffer ('This is a test.') and press
          return.  To save the modified file, enter 'E'.

              Many word processors (including PC-Write) allow
          the direct entry of control codes, so you may not need
          to go through such an extra step to use LQ's special
          features.  Consult your word processor's manual for
          details.



          Control sequences                                    15

          5. Control sequences.

              A 'control sequence' in a document is a sequence
          of codes or characters which has a special meaning to
          your printer (or the program controling it), and which
          changes the way in which subsequent characters are
          printed.  You have probably used such codes for some
          time, perhaps without realizing it.  When you tell your
          word processor to print a book's title in boldface or
          to print a subscript, you are telling your software to
          insert the appropriate control characters for perform-
          ing these functions.

              Regardless of what kind of printer you are using,
          LQ will make your printer appear to a word processor or
          other application as an Epson MX 80 (or IBM Graphics
          Printer).  Assuming that you have installed your
          application program for this printer you can get
          extensive use out of LQ without any direct involvement
          with control sequences.

              If your program does not support all the features
          of an Epson MX 80 (italics, underlining, emphasized
          print, superscript/subscript, etc.) or if you want to
          use some of the special features of LQ (large char-
          acters, proportional print, graphics), you will need to
          insert control codes on your own.  You can always use
          EDLIN.COM (a line editor included with your DOS system
          disk) to do this; you probably have an easier way at
          your disposal.  Read Section 4 for details on inserting
          control codes.

              If the LQ feature you want to use will not change
          during a printout, you can request it in the LQ command
          line rather than using control sequences.  For example,
          'LQ C3' turns on character set number three (out of the
          four in memory) as an alternative to '<Esc> <Esc> 3'
          within your document.  The LQ command line options are
          described in the following section.

              You can also use the Control Window to use some LQ
          features; see Section 3.

              In addition to inserting control codes or using the
          Control Window to switch character sets, one other
          technique is available.  Most word processors have a
          way of turning on italics; since the italic set is
          expected to be the second of LQ's four sets, you can
          change to any second set by turning on italics.  If you
          want to use this method, have LQ load the desired

          16                                    Control sequences

          alternate character set with a command such as
              LQ C2'SANSSER'
          (which loads SANSSER.SET as character set number 2,
          replacing italics).

          Control functions available in LQ.

              Following is a list of LQ functions which may be
          used or changed within a document using control
          sequences.  Those functions which can be renamed (with
          different control sequences which will have the same
          effect) are indicated with an asterisk; the renaming is
          done in a 'configuration file' (see Section 7.)  Each
          control sequence is shown in two forms: the sequence of
          keys to press, then the corresponding sequence of
          (decimal) ASCII codes.  For example,
            <Esc> 'E' = 27,69
          indicates that the sequence consists of the escape key
          code followed by the code for the capital E character.
          Sequences beginning with <Esc> <Esc> are unique to LQ;
          all others correspond to standard Epson control codes.
          The standard codes are usually inserted automatically
          by a word processor when the associated mode is
          requested, but the additional LQ modes must be added
          explicitly.

          * Turn on boldface:
            <Esc> 'E' = 27,69  or  <Esc> 'G' = 27,71

          * Turn off boldface:
            <Esc> 'F' = 27,70  or  <Esc> 'H' = 27,72

          * Turn on italics (character set #2):
            <Esc> '4' = 27,52

          * Turn off italics (turn on set #1):
            <Esc> '5' = 27,53

          * Turn on double-wide print:
            <Ctrl N> = 14

          * Turn off double-wide print:
            <Ctrl T> = 20

          * Turn on underline:
            <Esc> '-' #  = 27,45,#    where # corresponds to any
             code except 0 or '0'.  For example, use
             <Esc> '-' '1' = 27,45,49.


          Control sequences                                    17

          * Turn off underline:
            <Esc> '-' #  = 27,45,#    where # corresponds to
             either '0' or 0.  For example, use <Esc> '-' '0' =
             27,45,48.

          * Superscript:
            <Esc> 'S' # = 27,83,#   where # corresponds to '0' or
            0.  For example, <Esc> 'S' '0' = 27,45,48.

          * Subscript:
            <Esc> 'S' # = 27,83,#   where # corresponds to any
             code except 0 or '0'.  For example, use <Esc> 'S'
             '1' = 27,45,49.

          * Superscript/subscript off:
            <Esc> 'T' = 27,84

            Switch to character set n (1 <= n <= 4):
            <Esc> <Esc> 'n'.  For example, <Esc> <Esc> '3' =
             27,27,51  turns on character set number 3.

            Advance paper a little to put tension on paper
             (recommended for preceding first line of printout;
             this function is performed automatically when the
             F(ile) option is used.):
            <Esc> <Esc> 'B' = 27,27,66

            Turn on graphics mode:
            <Esc> <Esc> 'C' = 27,27,67
             The graphics mode suppresses the normal space
             between characters and between lines so that you can
             produce letterheads and other pictures.  See Section
             11 for details.

            Turn off graphics mode:
            <Esc> <Esc> 'D' = 27,27,68

            Turn on triple-high (large) characters in the current
            set:
            <Esc> <Esc> 'L' = 27,27,76
             The large mode stays on for the entire line
             regardless of where in the line it was turned on,
             and the mode is turned off automatically at the end
             of the line.

            Turn on proportional spacing:
            <Esc> <Esc> 'P' = 27,27,80

            Turn off proportional spacing:
            <Esc> <Esc> 'Q' = 27,27,81


          18                                        LQ parameters

            Set line space to n units (where one unit is either
             1/144" or 1/216" depending on the smallest line
             advance your printer supports):
            <Esc> <Esc> 'S' # = 27,27,83,#
             where # is the number (from 1 to 255) of increments
             desired.  For example, the smallest Epson line
             advance is 1/216", so <Esc> <Esc> 'S' '$' =
             27,27,83,36 sets the line space to 36/216" = 1/6".
             It is generally easier to use the L(ines per page)
             parameter when activitating LQ or the lines per page
             option in the Control Window to determine the number
             of lines on an 11" page.

            Wait for key to be pressed at page breaks:
            <Esc> <Esc> 'W' = 27,27,87

            Don't wait at page breaks (the default):
            <Esc> <Esc> 'X' = 27,27,88

          Other control codes.

              Three additional control codes are recognized by
          LQ: 10 (line feed), 12 (form feed) and 13 (carriage
          return).  All other control codes (ASCII codes less
          than 32) besides those listed above (or the substitutes
          given in a parameter file) are ignored.  It is unlikely
          that your word processor or other application program
          will insert such codes without your having explicitly
          requested them, so you should not have any unpleasant
          surprises in store.  However, just in case you see an
          occasional mystery character in your printouts, here is
          what could happen: if your word processor puts the
          sequence <Esc> 'A' in your text, expecting some
          response from your printer, the <Esc> would be stripped
          by LQ but the 'A' would be printed.  If the <Esc> 'A'
          corresponds to a needed printer function, you may need
          to specify it in a configuration file;  if the sequence
          is superfluous when used with LQ then you should
          install it as one of the sequences to ignore.  In
          either case, see Section 7 for more information.


          6. The LQ parameter line.

              An easy way to set one-shot options LQ is in
          the command line typed when LQ is installed.  For
          example if you want proportional spacing for all your
          printing,
              LQ MP
          will install LQ with the proportional mode turned on.
          The 'LQ' file must be loaded each time an LQ command is

          LQ parameters                                        19

          given, so if LQ is not on the default drive, give the
          full path name for LQ, e.g. B:LQ MP (if LQ is on the
          disk in drive B).  You select as many options as you
          like in a single line by separating parameters with
          spaces.  For example,
              LQ MPE F'MYFILE' W
          turns on proportional spacing, emphasized printing
          for the file MYFILE, pausing at form feeds.  This
          section lists all command line options.  Parameters are
          shown in upper case, but you can mix upper and lower
          case freely.

          B
            Set the buffer size (1 - 200) in K bytes.  For
            example LQ B64 dedicates 64K of RAM to the print
            spooler.  (The default is 16K.)  The command
            LQ BF flushes the buffer.  (It is easier to flush the
            buffer using the Control Window.)

            The buffer can be installed only when LQ is first
            loaded.  To change the buffer size, first remove LQ
            (see the R option below) then load again.

          C
            Specifies a  character set in memory, or loads a new
            set.  Four sets are embedded in LQ, and the first of
            these is normally used as the default.  LQ C4
            switches printing to the fourth set; when used in
            this way, 'C' can be followed by one of the digits
            1,2,3, 4.  The standard sets installed in LQ are:
              1 - COURIER.SET
              2 - COURITAL.SET
              3 - HELV.SET
              4 - PALATINO.SET
            These defaults can be changed with the LQINST
            program described in Section 2.  You can see a list
            of all character sets on the LQ disk by typing DIR
            *.SET at the DOS prompt '>'.  A printout of current
            sets is given in Section 9.

            If the 'C' option is followed by a file name in
            quotes, the character set having this name is loaded
            to the indicated set number.  For example,
                      LQ C2'PRETTY'
            would load the character set PRETTY.SET as set number
            two (without switching to it).  The 'SET' suffix is
            the default; you should stick with this naming
            convention to maintain compatibility with the
            character editor EDCHAR.  You can simultaneously load
            a set and switch to it by using 'C' in both contexts;
            e.g.,     LQ C2'PRETTY' C2.

          20                                        LQ parameters

            You can load all four sets in one line:
                      LQ C1'FIRST' C2'SECOND' ...
            You can also use path names in the file
            specification:
                      LQ C1'/MYDIR/FIRST'

          F
            If you have a file named MYFILE, the command
                      LQ F'MYFILE'
            will print MYFILE without locking LQ into memory.
            This is an important option if your computer doesn't
            have enough memory to keep LQ resident, or if most of
            your printing is in draft mode.  The file to be
            printed should be a standard text file, possibly
            containing some of the control sequences described in
            Section 3.  The file mode is described in Section 4.

          K
            This lets you override the default key combination
            used to bring up the Control Window and assign a new
            pair of keys.  Use the following values:

               3 - Right Shift + Left Shift,
               5 - Right Shift + Ctrl,
               9 - Right Shift + Alt,
               6 - Left Shift + Ctrl,
              10 - Left Shift + Alt,
              12 - Ctrl + Alt,
               N - Disable window.

            For example, LQ K12 specifies the <Ctrl> <Alt>
            combination, and LQ KN disables the window.

          L
            Sets the number of lines printed on a standard 11"
            page.  The default is 66; LQ L70 changes this to 70.
            The number entered must be from 1 to 95.  Spacing
            between lines is micro-adjusted using the smallest
            line advance supported by your printer (1/216" or
            1/144").

          M
            Sets one or more of the following modes:
             P: proportional spacing,
             W: double-wide printing,
             E: emphasized printing.
            For example, LQ MPEW could be used to set all three
            modes.  Modes omitted default to the opposite state.


          LQ parameters                                        21

          Q
            Suppresses the display of LQ's 'welcome' screen and
            begins execution immediately.  This is useful in
            batch files; for example, the commands
              LQ F'MYFILE' C1'SANSSER' Q
              LQ F'YOURFILE' C1'HELV' Q
            could be executed without the need for an operator to
            press a key to continue.

          R
            The command
              LQ R
            removes LQ from RAM and returns the memory previously
            used to your system.  This option can be used only if
            LQ was the last 'memory-resident' utility loaded.

          S
            Sets the space per line in units of the smallest
            possible line advance.  For example, on an Epson
            (which advances in multiples of 1/216"), the command
            LQ S30 would set the distance between the tops of
            successive lines to 30/216".  The 'L' parameter
            generally offers an easier way of accomplishing the
            same objective.

          W
            Wait at page breaks.  Use this for printing with
            single-sheet paper.  Each time the form feed
            character  (ASCII code 12) is encountered in a
            printout you will be prompted to
              Press <Enter> for next page:
            (In the file mode you can also press <Esc> to abort
            the printout.)

          #
            Specify printer number (0,1 or 2) to be used by LQ.
            If you have just one printer don't use this
            parameter; the proper value (0) is set by default.

          22                                  Configuration files

          7. Creating or modifying a configuration file.

              If your printer is compatible with an Epson or
          another printer for which a configuration file (with
          suffix PAR) exists on the LQ disk, just follow the
          directions in Section 2 for letting LQ know what you
          have.  If neither the built-in configuration nor any of
          the PAR alternatives work, you will have to write your
          own configuration file.  If you have problems, send us
          a copy of the control code section of your printer
          manual and we will try to write the file for you.  For
          LQ to work properly, your printer must support

            1. a graphics mode in which 8 pins of the print head
               can be individually controlled, and

            2. a minimum line advance of either 1/216" or 1/144".

          In addition, the graphics mode must be intialized with
          a control sequence telling the printer how much
          subsequent data will be in graphics mode.  A prominent
          counterexample is the Okidata 92, which

            1. controls only 7 pins in graphics mode, and

            2. uses one control sequence to turn graphics on and
               another to turn it off.

          Later model Okidata printers and those equipped with
          the 'Plug and Play' ROM do support LQ.

              A configuration file is a text file named with a
          suffix of PAR which contains lines typically starting
          with a symbol indicating a definition category,
          followed by a letter specifying the function to be set,
          then the '=' character, then a word or sequence of
          characters and numbers giving the definition itself.
          For example,
              %A=27,'E'
          indicates that emphasized print will be turned on with
          the <ESC> 'E' sequence (that normally used by the
          Epson).  A control sequence is a list of codes and/or
          characters separated by commas; characters are put
          within quotes (one pair of single quotes per character)
          and codes are given as decimal numbers.  The definition
              %A=27,69
          is equivalent to that above since 69 is the ASCII code
          for 'E'.  (See Appendix B for a listing of ASCII
          codes.)  The leading symbol indicates one of the
          following categories:

          Configuration files                                  23

              % - a control sequence for a mode definition,
              & - a control sequence to ignore,
              $ - one of the words TRUE, FALSE,
              # - a decimal number.
          A line starting with any other symbol is treated as a
          comment.

              While a complete listing of LQ parameters is given
          below, there are only a few that you will need to
          change to create a customized PAR file for a new
          printer.  These are:
            %N, %O, %P, %Q, %R
            $A, $B, $C
            #A, #B
          To install LQ with your new printer XYZ we recommend
          the following procedure:

            COPY EPSON.PAR XYZ.PAR

            Edit the XYZ.PAR file (using EDLIN or another editor
            which can handle standard ASCII files): modify the 10
            parameters listed above to describe your printer's
            functions.

            Run LQINST as described in Section 2.

          Remember that LQ will make your printer appear to a
          word processor as an Epson MX 80 (or IBM Graphics
          Printer), so perform the necessary installation on your
          word processor as well.

              Two values have special significance in a control
          sequence.  The number 0 will match 0 or '0' (the
          character whose ASCII code is 48), and the number 255
          will match anything else.  For an illustration, see the
          description of the &A parameter in the EPSON.PAR
          listing below.

              Here is the information LQ needs (any one of these
          omitted defaults to the Epson value):

                 % parameters.

            %A - control sequence for turning on emphasized
                 print,

            %B - sequence for turning off emphasized print,

            %C - sequence for turning on double-strike print,

            %D - sequence for turning off double-strike print,

          24                                  Configuration files


            %E - sequence for turning on italics,

            %F - sequence for turning off italics,

            %G - sequence for turning on double-wide print,

            %H - sequence for turning off double-wide,

            %I - sequence for turning on underline mode,

            %J - sequence for turning off underline mode,

            %K - sequence for turning on superscript,

            %L - sequence for turning on subscript,

            %M - sequence for turning off superscript/subscript,

            %N - prefix for turning on high-resolution graphics.
                 For example, the Epson MX 80 manual describes
                 its high-resolution mode as follows:
                 <ESC> L  Sets dot graphics mode to 960 dots per
                          8" line.
                          Format: <ESC> 'L' N1 N2, N1 and N2
                          determine line length.  Line length =
                          N1 + 256*N2
                          1 <= N1 <= 255, 1 <= N2 <= 255
                 Thus you would enter the prefix in your
                 configuration file as %N=27,'L' or %N=27,76.
                 (You would also set the number of graphics bytes
                 to 2 with #A=2, and non-ASCII (binary) number
                 format with $B=FALSE.  See below.)
                 If you have several graphics densities to choose
                 from, pick the one closest to 960 dots per 8"
                 line (120 dots per inch).

            %O - In a similar fashion, %O gives the prefix used
                 to set line feeds in units of the smallest
                 possible increment.  Again, here is the
                 appropriate material from the Epson manual:
                 <ESC> 3  Sets line spacing to N/216".  Format:
                          <ESC> '3' N, 1 <= N <= 255
                 You would enter %O=27,'3' (and set the number of
                 line feed bytes with #B=1).

            %P - The control sequence used to put your printer in
                 'unidirection' mode.  Most dot matrix printers
                 print in both directions to speed up output, but
                 the resulting characters are apt to vary in
                 alignment.

          Configuration files                                  25


            %Q - The sequence of characters you would like sent
                 to your printer when LQ is disabled from the
                 Control Window.  This should include an
                 appropriate line feed setting and a return to
                 bidirectional printing.  You can also reset your
                 printer by turning its power off and on.

            %R - The sequence of characters you would like sent
                 at the start of each line printed by LQ.  Epson-
                 compatible printers don't need this parameter,
                 but it can be very useful for other printer
                 types.  For example, the C. Itoh doesn't have a
                 separate 'high-resolution' graphics mode;
                 graphics printing functions in the last
                 character pitch (pica, elite, compressed,...)
                 set.  The most appropriate pitch is compressed;
                 %R=27,'Q' sets this at the start of each line.

                 & parameters.

            &A - A sequence of characters to ignore (filter) from
                 a printout.  Word processors often send
                 initialization sequences which might appear as
                 'garbage' when printed by LQ.  The '&'
                 parameters have been set to take care of any
                 problems that could arise with the Epson MX /
                 IBM Graphics Printer.

            &B, ... ,&L -
                 Additional sequences to ignore.

                 $ parameters.

            $A - You control 8 pins on the print head in graphics
                 mode.  The pins correspond to the numbers
                 1,2,4,8,16,32,64,128; for example, to fire the
                 two pins corresponding to the numbers 2 and 16,
                 the code 18 is sent to the printer.  If the
                 highest pin corresponds to 1 and the lowest to
                 128, set $A=TRUE; if the order is reversed, set
                 A$=FALSE.

            $B - There are two ways various printers accept
                 numeric values: ASCII and binary.  To indicate
                 to an Epson printer that 300 graphics positions
                 are about to be printed, the prefix
                  <ESC>,'L',44,1
                 is sent.  The numbers 44 and 1 are combined as
                 44 + 256*1 to obtain the number 300; this is the
                 binary format.  On many other brands of printers

          26                                  Configuration files

                 the number 300 would be sent as '3','0','0' or
                 '0','3','0','0' in ASCII format.  Set $B=TRUE
                 for ASCII or $B=FALSE for binary.

            $C - Set $C=TRUE if the minimum line space your
                 printer will accept is 1/216"; if this value is
                 1/144", set $C=FALSE.

                 # parameters.

            #A - The number of bytes after the graphics prefix
                 (specified with %N) used to set the number of
                 bytes expected by the printer.  For example, to
                 print 300 bytes in high-resolution graphics you
                 first send the Epson the sequence
                 <ESC>,'L',44,1; since the prefix takes up two of
                 these four bytes, the remaining two determine
                 the setting #A=2.  The same task on a C. Itoh
                 requires sending <ESC>,'S','0','3','0','0', so
                 you would set #A=4.

            #B - The number of bytes after the line feed prefix
                 (specified with %O) to determine the space
                 advanced by a line feed.  (See #A.)

              Any setting omitted in a configuration file
          defaults to the corresponding Epson value; see the
          EPSON.PAR listing below.

          Creating the configuration file.

              Now that you know what to put in your config-
          uration file, how do you actually create one?  Any
          screen or line editor will do; you will probably want
          to use your accustomed word processor.  If you have no
          other alternative, you can always use the EDLINE line
          editor which comes with DOS.  Just make sure that you
          create a standard ASCII file, not a file in a special
          non-ASCII format used internally by your program.  To
          see if you can make such a file, try writing a 2-line
          test file and store it under the name TESTFILE.  Then
          (at the DOS prompt '>') enter TYPE TESTFILE; if the
          lines look right on your screen, you are probably in
          luck.  Check your word processor index under ASCII for
          details.

              If you have an unusual printer and succeed in
          creating a new configuration file for it, please send
          us a listing of your file.  In return, if your

          Configuration files                                  27

          configuration is significantly different from those we
          already have on record we will send you a free LQ
          update.

          The EPSON.PAR configuration file.

              If you are using an Epson printer or close
          compatible you should never need a configuration file;
          all needed parameters are already set by default.
          However, if you are creating a new configuration file
          for a different printer it is instructive to look at
          the EPSON.PAR file which lists the Epson parameters;
          the form of the file may be helpful, and you should
          know what the defaults are in case you omit a parameter
          line.  Here are the Epson values:

            {emphasized on:}
            %A=27,'E'
            {emphasized off:}
            %B=27,'F'
            {double-strike on:}
            %C=27,'G'
            {double-strike off:}
            %D=27,'H'
            {italics on:}
            %E=27,'4'
            {italics off:}
            %F=27,'5'
            {double wide on:}
            %G=14
            {double wide off:}
            %H=20
            {underline on:}
            %I=27,'-',255
              {the 255 code will match any 1-byte value except
               for 0 and '0'=48.  Likewise, 0 matches 0 or
               '0'=48.  This means you can turn off underlining
               in a document with the sequence <ESC> '-' '0',
               which is much easier to insert than <ESC> '-' 0.}
            {underline off:}
            %J=27,'-',0
            {superscript on:}
            %K=27,'S',0
            {subscript on:}
            %L=27,'S',255
            {superscript/subscript off:}
            %M=27,'T'
            {hi-res graphics prefix:}
            %N=27,'L'
            {set line feed:}
            %O=27,'3'

          28                                        Printing tips

            {unidirection:}
            %P=27,'U',1
            {restore:}
            %Q=27,'U',0,27,'2'
            {start each line with:}
            %R=
            {no sequence needed for the Epson}

            {ignore:}
            &A=27,'3',255
            {<Esc> '3' N sets line space to N/216}
            {255 matches any value but 0 or 48}
            &B=27,'A',255
            &C=27,'C',0,255
            &D=27,'C',255
            &E=27,'N',255
            &F=27,'O'
            &G=27,'Q',255
            &H=27,'W'
            &I=27,'0'
            &J=27,'1'
            &K=27,'2'
            &L=27,'<'

            {true/false:}
            $A=FALSE
            {pin 128 on top}
            $B=FALSE
            {numbers in binary, not ASCII}
            $C=TRUE
            {min linefeed=1/216}

            {numbers:}
            #A=2
            {2 bytes allocated for number of graphics bytes}
            #B=1
            {1 byte for length of linefeed length}


          8. Tips for better printouts.

              LQ obtains its high quality print by making three
          passes over each line, placing dots at very precise
          positions.  Any 'play' in the paper can disrupt this
          precision and blur a line of print.  To keep the
          alignment precise, it we recommend that you use
          friction feed if possible, even if you are using pin-
          feed paper.  LQ works fine without friction feed, but
          you must make certain that the paper feeds evenly and
          that there is uniform tension on the paper.


          Character sets                                       29

              As previously mentioned, the first line of print
          is something of a special case.  When your printer is
          first turned on there is not apt to be sufficient
          tension on the paper to obtain the needed precision on
          the first line.  This problem is solved by advancing
          the paper a negligible distance; this is done
          automatically when you use the F option for printing
          files or when LQ is loaded in the resident mode (if the
          printer's power is on).  In other cases you can use the
          Control Window to advance the paper by pressing the 'A'
          key.  You can also begin a document with a blank line
          or with <Esc> <Esc> B (see Section 5).

              Proportional spacing can improve the appearance of
          a docoument, but this mode must be used with caution.
          Since extra 'white space' between characters is removed
          and since the amount of such space varies considerably
          (e.g. compare the characters 'i' and 'w'), tables of
          data can be distorted.  For example, if the two lines
              iiii            xxxx
              wwww            yyyy
          were printed with proportional spacing, the 'yyyy'
          would be further left than 'xxxx'.  One way to avoid
          this problem is to turn proportional spacing off (with
          <ESC> <ESC> 'Q') just before the table and back on
          (<ESC> <ESC> 'P') at the end of the table.

              Most LQ modes are enhancements of familiar print
          styles, so your word processor should not require
          special consideration.  However, triple-high characters
          will definitely come as a surprise to any program which
          thinks it is counting 1/6" lines; you will use up a
          sheet of paper three times faster than your word
          processor expects.  To fix this, you can change the
          number of lines per page in your word processor, or
          take charge yourself in other ways.  One compromise has
          been made to keep margins consistent:  if the string
             '       This is a test.'
          (7 spaces preceding 'This') is printed in 'large
          character' mode, the leading spaces are printed as
          normal characters.  This lets you set the margin to a
          fixed value in your word processor rather than worrying
          about whether the margin is in terms of large or
          regular spaces.



          30                                       Character sets

          9. Character sets available in LQ.

              The following list of LQ character sets will
          almost certainly be incomplete; new sets are being
          created on a regular basis.  To see a list of all
          character sets on the LQ disk, type DIR *.SET.  (These
          sets will all appear the same if you are printing these
          instructions yourself.  If you have an Epson-compatible
          printer you can see a printed copy of all character
          sets on the LQ distribution disk by typing PRINSETS.)

          COURIER
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          COURIER2
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          COURITAL
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          GREEK
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          HELV
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          HELV2
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          HELVITAL
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          MAIN
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          MAINITAL
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          PALATINO
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          Character sets                                       31


          ROMAN
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          ROMAN2
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          ROMANITA
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          SANS2ITA
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          SANSITAL
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          SANSSER
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~

          SANSSER2
               !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNO
              PQRSTUVWXYZ[\]^_`abcdefghijklmnopqrstuvwxyz{|}~


          LQ's default character sets.

              The default sets installed in LQ are

              1 - COURIER.SET
              2 - COURITAL.SET
              3 - HELV.SET
              4 - PALATINO.SET

          The second set is an italicized version of the first
          and will be used automatically when you tell your word
          processor to use italics.  The other such pairs of sets
          are
              HELV.SET            HELVITAL.SET
              MAIN.SET            MAINITAL.SET
              ROMAN.SET           ROMANITA.SET
              SANSSER.SET         SANSITAL.SET
              SANSSER2.SET        SANS2ITA.SET

          Other sets currently included do not have italicized
          companions.

          32                                       Character sets


              You can change the fonts which are loaded
          automatically as part of LQ with the LQINST program.
          You can also create or change fonts with the EDCHAR
          program.


          10. Editing character sets: the EDCHAR program.

              Sooner or later you will probably want to modify
          one of the character sets provided with LQ, or make a
          new set from scratch.  For example, you may need a
          couple of special technical symbols occasionally, or
          you may fall in love with an altogether new font.  The
          EDCHAR program included on the LQ disk offers a
          convenient way to edit characters in the format
          expected by LQ.  The basic sequence is to run the
          program, specify the character set you want to edit
          (which may be an existing set or a new one), edit one
          or more characters corresponding to the ASCII codes 32-
          127, then save the revised (or created) set.  EDCHAR
          also lets you move characters from one set to another
          easily.

              To get started simply insert the LQ disk and type
          EDCHAR.  If you want to edit an existing set, you will
          want to load it now; if you are creating a new set, you
          can skip this step.  Press 'L' to get the following
          L(oad) submenu:

            1. Load main character set.
            2. Load auxiliary character set.
            3. Return to Character Editor.

          If you choose one of the first two options you are
          shown a list of all character sets in the current
          directory, and you are given a chance to select a set
          or to change the directory from which you will select a
          set.  For example, if you enter '\MYDIR\', the path
          will be changed to the indicated directory and all
          character sets (files ending in '.SET') in this new
          directory will be listed.  Similarly, if the font you
          want is in the main directory of drive B you would
          simply enter 'B:'.  You can browse through all your
          directories in this fashion, and when you find the one
          containing the set you want just type the set's name.
          The set will be loaded into memory as the main or
          auxiliary set depending on your previous menu
          selection.  The main difference between these two
          categories is that the main set can be altered but the
          auxiliary set cannot.  The only reason to use an

          Editing character sets                               33

          auxiliary set at all is to transfer characters to the
          main set.

              Let's assume that you have loaded a main and/or
          auxiliary character set if necessary and that you are
          ready to edit a character.  Press 'G' to obtain the
          G(et) submenu:

            1. Get character from current set.
            2. Get character from auxiliary set.
            3. Edit new character.
            4. Return to Character Editor.

          If you choose one of options 1 - 3, you will be
          prompted to enter the ASCII code of the character or
          the character (preceded by a single quote) itself.  For
          example, you can specify the letter 'A' by entering the
          code 65 or by entering 'A.  If you selected option 1 or
          2, you will see the existing character from the
          appropriate set ready for editing; if you choose option
          3 you will see a clear edit window.  (See Figure 1 for a
          typical display.)  A character is edited as a 24 X 10
          matrix of dots, each of which is turned on or off.  You
          can use the arrow keys along with the Home, End, Pg Up
          and Pg Dn keys to position the cursor.  Pressing the
          space bar toggles the state of the dot under the
          cursor.  At any time you can also select any of the
          menu options listed on the right of the screen.


          34                               Editing character sets

            0   1   2   3   4   5   6   7   8   9      Edit character set:
          A°°°°ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ            A    HELV
          B    ÛÛÛÛ                    ÛÛÛÛ        B
          C    ÛÛÛÛ                        ÛÛÛÛ    C   Auxiliary set:
          D    ÛÛÛÛ                        ÛÛÛÛ    D
          E    ÛÛÛÛ                        ÛÛÛÛ    E
          F    ÛÛÛÛ                        ÛÛÛÛ    F   Edit character B
          G    ÛÛÛÛ                        ÛÛÛÛ    G        code =  66
          H    ÛÛÛÛ                    ÛÛÛÛ        H
          I    ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ            I
          J    ÛÛÛÛ                    ÛÛÛÛ        J   Options:
          K    ÛÛÛÛ                        ÛÛÛÛ    K
          L    ÛÛÛÛ                        ÛÛÛÛ    L   B)ackup character
          M    ÛÛÛÛ                        ÛÛÛÛ    M   C)lear character
          N    ÛÛÛÛ                        ÛÛÛÛ    N   G)et character
          O    ÛÛÛÛ                        ÛÛÛÛ    O   L)oad character set
          P    ÛÛÛÛ                        ÛÛÛÛ    P   M)iddle (center char)
          Q    ÛÛÛÛ                        ÛÛÛÛ    Q   P)ut character
          R    ÛÛÛÛ                    ÛÛÛÛ        R   Q)uit
          S    ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ            S   R)estore character
          T                                        T   S)ave character set
          U                                        U   W)rite character
          V                                        V
          W                                        W
          X                                        X
                                  Figure 1

              When the character has been edited to your
          satisfaction, you can put it into the main character
          set with the P(ut) option.  You will be given a chance
          to change the code under which the character will be
          stored, but more than likely you will use the default:
          the code you used with the G(et) command.

              There are three levels of storage used in EDCHAR.
          The ultimate (and only safe) storage site is your
          disk, and only complete sets, not individual
          characters, are saved as files on disk.  There are also
          the main and/or auxiliary character sets in your
          computer's volatile memory; since the power may flicker
          at any time, you should backup a set you are editing on
          a regular basis.  Finally, there is the individual
          character being edited: modifying this character
          affects neither the set in memory nor the set on disk.
          Only when you P(ut) the character to a set is the set
          in memory changed, and only when you S(ave) the set in
          memory is the set on disk changed.

              When editing a character, you have at your disposal
          the following options:


          Editing character sets                               35

            B)ackup character - pressing 'B'makes a copy in
              memory of the character definition currently
              displayed.

            C)lear character - pressing 'C' blanks the character
              matrix, but doesn't affect the corresponding
              character in the set being edited.  (Remember, only
              the P(ut) command changes that.)

            G)et character - the first step in editing a
              character.  You are shown the following menu:
              1. Get character from current set.
              2. Get character from auxiliary set.
              3. Edit new character.
              4. Return to Character Editor.
              In order to get a character from a set (options 1
              and 2) you must first L)oad the set.

            M)iddle - lets you center a single character or an
              entire set.  You are shown the following menu:
              1. Center character.
              2. Center entire set.
              3. Return to Character Editor.
              Selecting the first option centers the character
              definition on the screen, while choosing the second
              centers all of the character definitions in the main
              character set.  If characters are not centered then
              spacing within words can appear irregular; it is
              always a good idea to center the entire set when you
              are finished editing it.

            P)ut character - replaces corresponding character in
              the main set with that shown on the screen.  If you
              don't press 'P' your editing will not change the
              character set.  You are asked whether the character
              on the screen should be saved under the code under
              which it was loaded or under a different code.  For
              example, you could load a 'P', modify it a little,
              then save it as the character 'R'.

            Q)uit prompts you to make certain you're serious,
              then returns to DOS.

            R)estore character is the reverse of backup - the
              last character definition backed up with the 'B'
              option replaces that being displayed.

            Backup and restore let you experiment with a
            character definition without altering a set on disk.


          36                               Editing character sets

            S)ave character set - pressing 'S' lets you save the
              set being edited under the name used for loading
              the set, or under any other name.  You are prompted
              to enter the name of the set or the path for
              saving.  You can overwrite the previous version
              simply by pressing return, or you can create a
              separate second version by changing the path or
              name.  You will want to use the S(ave) option often
              since it provides cheap insurance against power
              fluctuation and other perils to your data.

            W)rite character lets you see how your character
              looks on paper if you have an Epson-compatible
              printer attached.  You will be prompted to turn on
              your printer, then the character being displayed
              will be printed in LQ mode.  (LQ should not be
              installed in memory if you use this option.)  Note
              that while LQ works with printers which are not
              Epson-compatible (through the use of PAR
              configuration files), EDCHAR does not.  This simply
              means that if you want to see your new characters
              on paper, you may have to wait until you exit
              EDCHAR and run LQ.

          Tips on editing character sets.

              Make certain that you use the same 'base lines' for
          all the characters in a given set, so that the
          characters will line up properly when printed.  The
          following should be aligned:
            the base of characters without descenders,
            the top of lower case letters such as 'a' and 'c',
            the top of upper case letters.

              If you want to create a new font, you may want to
          work from an existing font.  For example, you might
          reuse the punctuation symbols but change the letters
          and numbers.  To do this, copy (at the DOS prompt) the
          set to be edited to a new name:
           A> COPY OLD.SET NEW.SET.
          Now you can run EDCHAR and edit the new set without
          risking your old set.  The same thing can be
          accomplished from within EDCHAR by loading a set,
          editing it, then saving it to a different name, but you
          must be sure to enter the new name or your old set will
          be lost.



          The graphics mode                                    37

          11. The graphics mode.

              It's not easy (in the current version of the
          package), but you can use LQ to produce pictures.  This
          is worth doing if you want to create a letterhead to be
          used frequently, but it involves too much effort for
          casual applications.

              The basic idea is that all LQ characters are
          arbitrary graphics shapes anyway, so a block of them
          can be combined to make a larger image.  The only
          problem is the space that is normally inserted between
          characters and between lines.  By preceding a sequence
          of characters with the control code '<Esc> <Esc> C', no
          space will be inserted; '<Esc> <Esc> D' returns LQ to
          the usual mode.  If the graphics mode is active at the
          end of a line then the next line will start exactly
          where the last line left off regardless of the current
          line space setting.

              Each LQ character is a 24 x 10 array of dot
          positions.  One way to create a picture is to draw or
          transcribe an image on (say) a 192 x 120 square section
          of a sheet of graph paper, then mark this into 8 rows
          of 12 character definition (each 24 x 10 squares).
          These 96 'characters' can then be entered as ASCII
          codes 32 - 127 in a new set using EDCHAR.










                                  Figure 2

              As an example consider the set SPIRAL.SET on the LQ
          disk.  The file SPIRAL.PIC is a simple list of
          characters which can be printed with LQ to produce a
          picture of a spiral (Figure 2).  To try this with your
          printer, type LQ C1'SPIRAL' F'SPIRAL.PIC'.  The file
          being printed consists of 8 lines described below:

          The first line is the control code '<Esc> <Esc> C'
          followed by the sequence ' !"#$%&'()*+'.  The control
          code turns on graphics and the remaining characters
          correspond to ASCII codes 32 - 43.  If all control

          38                                    The graphics mode

          sequences were removed from the file, a listing would
          appear thus:

                !"#$%&'()*+
               ,-./01234567
               89:;<=>?@ABC
               DEFGHIJKLMNO       graphics mode,
               PQRSTUVWXYZ[
               \]^_`abcdefg
               hijklmnopqrs
               tuvwxyz{|}

          The actual file includes three additional control
          sequences besides that mentioned above.  The words
          'graphics mode,' are preceded by the sequence
              <Esc> <Esc> D <Esc> <Esc> 4
          to turn off graphics and switch to the fourth character
          set, and followed by the sequence
              <Esc> <Esc> C <Esc> <Esc> 1
          to switch back to graphics and the first (SPIRAL) set.
          Finally, the last line is terminated by
              <Esc> <Esc> D <Esc> <Esc> 4
          to return to printing text.

              Note that the worst part of the listing concerns
          switching back and forth between graphics and text.  If
          you want the picture without any text then only the
          initial '<Esc> <Esc> C' is needed.

          About Shareware                                      39

          Appendix A. About 'Shareware'.

              'Shareware' is a relatively new means of software
          distribution with several advantages to you the
          consumer.  The complete package including this
          instruction manual is contained on a single diskette
          which may be freely copied and distributed.  Word of
          mouth provides a more accurate and less expensive way
          of making a product known than magazine advertisements,
          and the savings keep LQ's cost down.

              Shareware does not mean 'public domain'.
          Distribution is permitted only if the package stays
          intact; all files should be passed on in unmodified
          form.

              You can obtain the current LQ disk from Granny's
          Old-Fashioned Software for $10 or a registered package
          for $35.  Registration provides the following benefits:

            1. A current version of LQ including all available
               character sets,
            2. a mail-in card for a future version of LQ,
            3. a $10 commission each time someone registers from
               one of your copies,
            4. telephone support for your technical questions.

          To register, phone (with MC or VISA) (704) 264-6906 or
          mail payment to:

                    Granny's Old-Fashioned Software
                    Rt 4, Box 216
                    Boone, NC 28607

          North Carolina residents please add 4.5%.

          Please include the registration number from the upper
          right of LQ's initial display so that we can reimburse
          the person from whom your copy originated.

          40                                          ASCII codes

          Appendix B. ASCII codes.



                0                               32        SP
                1        ^A                     33         !
                2        ^B                     34         "
                3        ^C                     35         #
                4        ^D                     36         $
                5        ^E                     37         %
                6        ^F                     38         &
                7        ^G                     39         '
                8        ^H                     40         (
                9        ^I                     41         )
               10        ^J                     42         *
               11        ^K                     43         +
               12        ^L                     44         ,
               13        ^M                     45         -
               14        ^N                     46         .
               15        ^O                     47         /
               16        ^P                     48         0
               17        ^Q                     49         1
               18        ^R                     50         2
               19        ^S                     51         3
               20        ^T                     52         4
               21        ^U                     53         5
               22        ^V                     54         6
               23        ^W                     55         7
               24        ^X                     56         8
               25        ^Y                     57         9
               26        ^Z                     58         :
               27       Esc                     59         ;
               28                               60         <
               29                               61         =
               30                               62         >
               31                               63         ?

          ASCII codes                                          41






               64         @                     96         `
               65         A                     97         a
               66         B                     98         b
               67         C                     99         c
               68         D                    100         d
               69         E                    101         e
               70         F                    102         f
               71         G                    103         g
               72         H                    104         h
               73         I                    105         i
               74         J                    106         j
               75         K                    107         k
               76         L                    108         l
               77         M                    109         m
               78         N                    110         n
               79         O                    111         o
               80         P                    112         p
               81         Q                    113         q
               82         R                    114         r
               83         S                    115         s
               84         T                    116         t
               85         U                    117         u
               86         V                    118         v
               87         W                    119         w
               88         X                    120         x
               89         Y                    121         y
               90         Z                    122         z
               91         [                    123         {
               92         \                    124         |
               93         ]                    125         }
               94         ^                    126         ~
               95         _                    127       Del





rrent LQ disk from Granny's
          Old-Fashioned Software for $10 or a registered package
          fo