I have seen numerous suggestions how to set Prowiter/NEC 8023 printer
switches and they have one thing common: Something is missing and you
are not able to use all printer capabilities.

From experience I can tell that it is waste of time to call Leading
Edge or eg. try to correct the writer of the Creative Computing IBM
Images column.

To settle this for once and for all please make record of the following
switch settings:

SW 1 -->        1,2,3,4,5,8-Open  6,7-Closed

SW 2 -->        2,3,4,5,8-Open  1,6,7-Closed

This settup works also with 123 PrintGraph program. If you want the best
quality of graphics print you need to close SW2-8 to disable bidirectional
printing.

When using Wordstar you will be able to print ASCII, CRAPHIC, GREEK and
Japanese KATAKANA character sets. The only unfortunate side effect is
that backslash (\) from ASCII prints like Yen sign but you still can print
backslash from the graphics set. I have downloaded also WS printer patches
for both version 3.2 and 3.3 . These files are named: WS320NEC.DOC  and
WS330NEC.DOC .

Kauko Laurinolli
404-981-9550