.fo LQ-Print Version 0.1        -#-            (C)Copyright 1984
                        LQ-Print

LQ-Print  was  written to provide letter quality printing  on  an 
Epson MX printer (with Graftrax) or IBM Graphics printer.  A main 
part  of  the  effort was to make WordStar files look  good  with 
these  printers.   Another  function of the program is  to  allow 
access  to  the  printers  internal  functions,   therefore  this 
document  refers to the printers mode and Letter Quality mode  as 
if  two  totally  separate  programs  exist.   Any  questions  or 
comments should be given to:  Steve Lass (408)732-8987.

The Menu

Typing in the letters  LQ  will display the following menu:

     CHANGE PRINTER MODE:

          R - Reset printer
          C - Condensed (not for Letter Quality)
          E - Emphasized (not for Letter Quality)
          D - Double strike
          M - Microjustification (Letter Quality only)
          N - eNlarged print
          S - proportional Spacing
          8 - 1/8 inch line spacing

     P - Print file (Letter Quality)

     X - eXit to system

Descriptions of Menu Commands

R - Reset printer

     The  reset command puts the printer into its power up  state 
     (determined  by dip switches internal to the  printer).   It 
     will  also reset all letter quality modes  including:   1/8" 
     line  spacing,   proportional  spacing,  microjustification, 
     enlarged, and doublestrike.

C - Condensed (not for Letter Quality)

     This puts the printer into condensed mode (17 characters per 
     inch).  This will not effect the Letter Quality mode.

E - Emphasized (not for Letter Quality)

     This  command puts the printer into emphasized mode and will 
     not effect the Letter Quality mode.
D - Double strike

     The  double strike command will put the printer into  double 
     strike  mode and also set the Letter Quality mode to  double 
     strike.    
.pa
.fo                            -#-
M - Microjustification (Letter Quality only)

     Microjustification works with WordStar files to evenly space 
     the words and characters accros a line.  WordStar puts soft-
     spaces (hex A0) into the line to justify the right  margins.  
     LQ-Print replaces the soft-spaces with incremental spaces so 
     the  output  looks much  more  evenly  distributed.   Micro-
     justification  will  be turned off for any line with a  hard 
     carriage return (one not entered by WordStar).

N - eNlarged print

     This  command puts the printer into enlarged (double  width) 
     mode.   It will also make the Letter Quality files print  in 
     enlarged mode until turned off by ^T in the file.

S - proportional Spacing

     This  puts the printer into proportional spacing mode  (each 
     character  takes up a different amount of space depending on 
     its size).   It will also make Letter Quality files print in 
     proportional  spacing  mode  intil turned  off  by  a  Reset 
     command (or exit from the program).

8 - 1/8 inch line spacing

     Line  spacing is normally 1/6" and can be changed to 1/8" in 
     the printer and also in Letter Quality mode.

P - Print file (Letter Quality)

     This  command  takes an ascii DOS file and prints it  (using 
     high  resolution graphics) in Letter Quality.   Any  of  the 
     above  commands  (not  those specifically  marked  "not  for 
     Letter  Quality") entered before the "P" command will be  in 
     effect.  Note: on entry all modes are cleared.

Control Characters

Print  control characters can be entered into the ascii file  and 
have the following meanings:

     Boldface  is  achieved  by using a ^B.   This  is  a  toggle 
     command so the first ^B turns on boldface, the next ^B turns 
     it off.

     Doublestrike  is  achieved by using a ^D.   This is  also  a 
     toggle command.

     Underline is achieved by using a ^S.   This is also a toggle 
     command.   Underline  is setup to not underline  the  spaces 
     between words.
.pa
     Enlarged  mode is initiated by a ^N and terminated by a  ^T.  
     These  are the same control codes that put the Epson printer 
     into enlarged mode.  For some reason WordStar will not allow 
     the  ^N  to remain in the file through the "print  to  file" 
     command  so  you  must enter a ^A before the ^N  when  using 
     WordStar  (^N  normally changes  the  character  pitch,  but 
     doesn't work with the Epson printer anyway).  (^T is normal-
     ly  used  for superscripts which are not supported  in  this 
     program,  however  if  the  file is going to be  printed  by 
     WordStar,  another  ^T should be entered to toggle  off  the 
     superscript mode.)
     WARNING:   Enlarged  mode takes twice the  width  of  normal 
     characters.   If an entire line is written in enlarged mode, 
     or you forget to turn it off, the type may run off the page.

     Strikeout can be achieved by entering a soft carriage return
    ---------
     (no line feed) which is a ^M.  Whatever is typed on the next 
     line is combined with the line above before printing.  There 
     will  be  no microjustification on the line  with  the  soft 
     carriage return.


Getting a WordStar file ready for LQ-Print

     From  WordStar  you must print the file into  another  file.  
     After  editing  type  a ^KD to finish the  editing  session.  
     Then from the main menu type a  P  for print.  Then the file 
     name  must be entered followed by a carriage  return.   Then 
     you are asked "DISK FILE OUTPUT?" and must answer Y for yes.  
     Then  you are asked what to call the output file (I  usually 
     use the extension DOC for the WordStar file and TXT for  the 
     output  file).    All  other  print  control  questions  are 
     answered  the  same as if you were sending the file  to  the 
     printer (press <Esc> for default settings).
.pa
Invoking LQ-Print

Type:

     LQ   
          This  brings up the menu,   all commands can be entered 
          through  the  menu.   If  the  command  is  understood, 
          another "Make Selection" line will be displayed, if not 
          the menu will be redisplayed.

     LQ/R
          This will reset the printer, then exit the program.

     LQ/C
          This puts the printer into condensed mode.

     LQ/E
          This puts the printer into emphasized mode.

     LQ/D
          This puts the printer into doublestrike mode.

     LQ/N
          This puts the printer into enlarged mode.

     LQ/S
          This puts the printer into proportional spacing mode.

     LQ file.ext
          This  prints  the  file in  letter  quality  mode.   An 
          optional drive may be specified as follows:
          LQ b:file.ext

     LQ/M file.ext
          This  prints the file in microjustified letter  quality 
          mode.

     LQ/M/S file.ext
          This  prints  the  file in  proportional  justification 
          letter quality mode.


Note:  All legal commands may be entered on one line:

       LQ/R/C/E/D/N/S

Note:   Certain  print modes cannot be mixed in the Epson,  check 
        your manual for details.

Note:  Upper or lower case characters may be used.

.pa
Initialization

     My experience has shown that "sometimes" when the printer is 
     not  powered  up  when the IBM PC is turned on  the  printer 
     cannot  be turned on later wihtout re-booting the  PC.   LQ-
     Print allows the printer to be initialized wihtout rebooting 
     the  PC.   If  the  printer is not ready  when  LQ-Print  is 
     invoked the following message will be displayed:

          PRINTER NOT READY, Retry or Initialize (R or I)?

     At this point you must check to see if the printer is turned 
     off or just "off line".  If it is off, turn the power on and 
     check  to see if the "on line" LED comes on.   If  not,  the 
     printer needs to be initialized (type I).   The next message 
     displayed will be:

          Monochrome/printer board or Printer adapter (M or P)?

     If your not sure try one.

     If your printer was just off line when the PRINTER NOT READY 
     message was displayed you have two options.  The first is to 
     turn the printer on line by pressing the "on line" button on 
     the  printer  then type R for Retry and you should  see  the 
     menu.   The  second method to get the printer on line is  to 
     type I for Initialize.  This will initialize the printer and 
     put it "on line" automatically.

     If  you have a non standard board and LQ-Print's  initiliza-
     tion doesn't work, you must re=boot.

     Note:   The  initialization program will not be used if  the 
     printer is ready when LQ-Print was invoked.

     Note:   LQ-Print can be executed from WordStar to initialize 
     the printer or setup any of the printers internal functions.
e:   LQ-Print can be executed from WordStar to initialize 
     the printer or setu