==================================================
       FXPR4.DOC  08/22/83   T. E. McCormick
==================================================


   FXPR4 is a printer setup utility program for the
Epson FX-80 (160 cps) printer.	It is useful for
changing the character fonts, boldness, pitch,
vertical lines per inch, etc. quickly with a single
command line such as  FXPR4 RESET P12 LEFTM 5 SKIP.

   Gary Novosielski wrote PRINTER.C (c) 1982 for the
MX-80.	This program was derived from that one,  and
Gary's approach was simple extended to other features,
and some minor changes were made to convert it from
CP/M BDS C to IBM PC DOS 2.0 Lattice C.  Both authors
have copyrighted their versions, and sale or commercial
use is forbidden without the authors' consent in writing.

   The program is offered by the authors without charge
to individuals for their personal use only.

   If you have an MX with graftrax plus, you may
be able to use this utility for most functions.

   The purpose of this program is quickly set several
options with a single command from the system prompt.







	     PURPOSE OF THE PROGRAM:

	From a single command, several printer
option commands may be sent to the FX-80.

	The Epson printers have an extremely wide
range of software selectable print font sizes and
styles (called modes).	Line width, characters per
inch, lines per vertical inch, print intensity,
tab stops, style (pica, elite, italics, etc.),
left/right margin settings, and "global" commands
to perform several commonly used settings such as
for letter writing in pica, elite or proportional
can readily be set with a quick keyboard entry.

	It is clearly not convenient to go into
BASIC or any other indirect means of sending those
commands out the printer port.	This program gets
the job done with a single command.

   The Epxon FX-80 includes the "graftrak" option as
standard, and implements some new features in
addition to the 160 charater per second speed. Pin
addressing commands, and many advanced features are
not included in this program but you may be add them
since the source file is available.

   FXPR4 will compile under  Lattice C ver 1.03 and
IBM PC DOS version 2.0.

   Simply entering  FXPR4  will cause a menu
of options to be displayed.  These can be used as
parameters following  FXPR4  the next time it is
entered.



   That menu appears as:

FXPR4 for Epson FX  (c) Tom McCormick  05/01/83
      from PRINTER.C (c) 1982 G.P. Novosielski
FXPR4 <opt> [<opt>.....]   where <opt> may be:
					      
RESET	   QUIET       PITCH 10    PITCH 17	DOC
LPI3	   LPI4        LPI5	   LPI6 	DOC1
LPI8	   LPI10       LPI12	   PLINCH 1-22	DOC1S
WIDTH 80 [....or any value between 2 and 137 ]	DOC8
SKIP	   NOSKIP      EJECT	   TABS n n n	DOC8S
PROPOR	   DRAFT       TEXT		      
PICA	   ELITE       ITALIC	   LEFTM  n   
TINY	   TINYER      ROMAN	   RIGHTM n   
LTRITA	   LTRITB      LTRELI		      
EMPHAS	   CONDEN      ENLARG	   DOUBLE     
XEMPHA	   XCONDE      XENLAR	   XDOUBL     
Various pitches (CPI) and bold or very bold...
 P5	P6	      P10     P12     P17     
 P5B	P6B    P9B    P10B    P12B    P17B    
 P5VB	P6VB   P9VB   P10VB		      
					      
\n  Example: FXPR4 RESET LPI6 PITCH 10 ELITE  


There are more than 50 keyword options, and God knows how many combinations.
They have NOT all been tested !!  Be aware that the FX-80 treats various
combinations as toggles, or serially.  Some features have priorities
with regard to others, and some negate others.	The 150+ page manual has
several tables that will help, but you will have to experiment a little too.

It is a good idea to use RESET as your first keyword to "baseline" the
subsequent commands.  If you don't, you may simply be adding new parameters
to the previous mix of them.

The "RESET" command mentioned above will reset ALL modes to the power-on
configuration you have chosen via the DIP switches at installation.



	       FXPR4  PROGRAM OPTIONS:	ENTER ONE OR MORE

	CONDEN	Condensed print mode
	CONDEN ENLARG Condensed/enlarged mode at 6 characters per inch.
	DOC	Global: RESET LPI6 ELITE LEFTM 8 RIGHTM 95 DOUBLE
	DOC1	Global: RESET LPI6 ELITE LEFTM 8 RIGHTM 95 (single intensity)
	DOC1S	Global: RESET LPI6 ELITE LEFTM 8 RIGHTM 95 skips over perf
	DOC8	Global: RESET  LPI8 ELITE LEFTM 8 RIGHTM 95 eight lines per in
	DOC8S	Global: RESET  LPI8 ELITE LEFTM 8 RIGHTM 95 skips over perf
	DOUBLE	Double-strike mode: strikes each char twice to darken.
	DRAFT	Cancels any double-strike mode, or super/sub scripting.
	EJECT	Sends printer to top of next page.
	ELITE	Elite type style
	EMPHAS	Emphasized printing
	ENLARG	Large lettering
	ITALIC	Print in Italic style.
	LEFTM	LEFTM n   sets left  margin to n column position
	LPI	LPI n  (where n = 3 to 216) will cause the vertical
		spacing to be n/216 inches per line......
		    7 LPI = 31	  9 LPI = 24   11 LPI = 20.
	LPI3	Three  lines per inch vertical spacing
	LPI4	Four   lines per inch vertical spacing
	LPI5	Five   lines per inch vertical spacing
	LPI6	Six    lines per inch vertical spacing
	LPI8	Eight  lines per inch vertical spacing
	LPI10	Ten    lines per inch vertical spacing
	LPI12	Twelve lines per inch vertical spacing
	LTRELI	Global command for RESET ELITE	P12  WIDTH 132	Normal
	LTRITA	Global command for RESET ITALIC P12  WIDTH 132	Normal
	LTRITB	Global command for RESET ITALIC P12B WIDTH 132	Bold
	NOSKIP	The perforation will not be skipped over with blank lines.
	P5	Pitch 5  characters to an inch horizontally
	P5B	Pitch 5  and bold
	P5VB	Pitch 5  and very bold
	P6	Pitch 6  characters to an inch horizontally
	P6B	Pitch 6  and bold
	P6VB	Pitch 6  and very bold
	P9B	Pitch 9  and bold  (Note: there is no P9)
	P9VB	Pitch 9  and very bold
	P10	Pitch 10 and normal intensity
	P10B	Pitch 10 and bold
	P10VB	Pitch 10 and very bold
	P12	Pitch 12 and normal intensity
	P12B	Pitch 12 and bold
	P17	Pitch 17 and normal intensity
	P17B	Pitch 17 and bold
	PICA	Pica type style
	PITCH	Characters per inch:  PITCH 10	or  PITCH 17 are valid.
	PLINCH	Set page length in inches ( 1 - 22 ); PLINCH 11
	PROPOR	Proportional spacing of letters (horizontally).
	QUIET	Slow to 80 char per second (half speed) to quiet operation.
	RESET	Cause printer to return to power-on option settings.
	RIGHTM	RIGHTM n  sets right margin to n column position
	ROMAN	Print in Roman	style.
	SKIP	Skip over perforation specifying 6 lines.
	TABS	Sets horizontal tab positions:	TAB n n n
	TEXT	From original program.
	TINY	Subscript sized, 10 lines per inch,  93 lines per 11" page,
		skips over perf leaving one inch bottom margin.
		LEFTM / RIGHTM may be used after TINY.
	TINYER	Subscript sized, 12 lines per inch, 108 lines per 11" page,
		skips over perf leaving one inch bottom margin.
		LEFTM / RIGHTM may be used after TINYER.
	WIDTH	WIDTH 80  or  [..any value between 2 and 137 ].
	XCONDE	Cancels condensed mode.
	XDOUBL	Cancels double-strike mode.
	XEMPHA	Cancels emphasized mode.
	XENLAR	Cancels enlarged mode.



	The following print lines are useful in various combinations
	to test FXPR4x after your modifications.....................



LINETEST
	 1	   2	     3	       4	 5	   6	     7
12345678901234567890123456789012345678901234567890123456789012345678901234567890

+++++++++1+++++++++2+++++++++3+++++++++4+++++++++5+++++++++6+++++++++7++++++++++++++++++++++++96+++++++++++++++++++++120+++++++++132  137


ABCDE abcde @#$%&?




ABC abc @#$






XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX
This is lllllower case. 1111111111
THIS IS UUUUUPPER CASE. 2222222222
IIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIII
iiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiii
wwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwwww
WWWWWWWWWWWWWWWWWWWWWWWWWWWWWWWWWW

All lines have same # characters..



=-=-=-=-=-=-=-=-=-= end of FXPR4.DOC =-=-=-=-=-=-=-=-=-=-=

WWWWWWWWWWWWWWWWWWW

All lines have same # characters..



=-=-=-=-=-=-=-=-=-= end of FXPR4.DOC =