The IBM Personal Computer file print command, PRT, is used to print a PC-DOS
file on a device attached to the serial port.  It is most useful for printing
a file when other than a straight line-by-line listing, such as that obtained
by using ctl-PrtSc in conjunction with the TYPE command, is desired or when
special printer features are to be used.

The format of the PRT command is:

+-------+---------------------------------------------------------------------+
|       |                                                                     |
|  PRT  |  [filespec [/][option] [/][...][;]                                  |
|       |                                                                     |
|       |  options:                                                           |
|       |  INIT    RESET    ENLarged    CONDensed    ENHanced    EMPHasized   |
|       |  NOINIT  NORESET  NOENLarged  NOCONDensed  NOENHanced  NOEMPHasized |
|       |                                                                     |
|       |  HEX    Header    CC    LPI 6  PAGESIze n  FROM n  FOR n            |
|       |  NOHEX  UHeader   NOCC      8                                       |
|       |         NOHeader                                                    |
|       |                                                                     |
+-------+---------------------------------------------------------------------+

where:

filespec     specifies the PC-DOS file name and file extension ("filetype") of
             the disk file to be printed.  "filespec" may optionally be pre-
             fixed with a drive specification (e.g., "B:") to override the
             current default drive.  If "filespec" is specified as "?", a
             brief summary of the PRT command options are displayed on the
             monitor.

             If "filespec" is omitted, you will be prompted ("IN_FILE: ") to
             enter it from the terminal.

             If no options are specified following "filespec", you will be
             prompted ("OPTIONS: ") to enter them from the terminal.  If you
             are satisfied with the default values for all the options, and
             don't want to enter a null line in response to the "OPTIONS: "
             prompt, you can specify the character ";" following "filespec"
             to suppress the prompt and cause the defaults to be used.

options:

INIT         specifies that various codes, as specified by the [NO]ENLARGED,
             [NO]CONDENSED, [NO]ENHANCED, [NO]EMPHASIZED, and LPI n options
             (or their associated defaults), are to be sent to the printer
             prior to printing the file.  This is the default.

NOINIT       specifies that NO printer codes are to be sent prior to printing
             the file--in other words, the printer attributes in effect prior
             to issuing the PRT command are used for printing the file.  Spec-
             ifying the NOINIT option causes the specification of any of the
             following options (or their negations) to be ignored:  ENLARGED,
             CONDENSED, ENHANCED, EMPHASIZED, and LPI.

RESET        specify whether (RESET) or not (NORESET) the default printer
NORESET      attributes are to be restored after the file has been printed.
             RESET is the default.  If RESET is specified or allowed to
             default, the printer attributes are reset to: NOENLARGED,
             NOCONDENSED, NOEMPHASIZED, NOENHANCED, LPI 8, and no "skip over
             perferations".

ENLARGED     specify whether (ENLARGED) or not (NOENLARGED) the file is to be
NOENLARGED   printed using the "enlarged" character set generated by the
             printer.  NOENLARGED is the default.  Note that ENLARGED can be
             combined with CONDENSED to produce "enlarged condensed"
             characters which are different in size from normal, enlarged,
             and condensed characters.

CONDENSED    specify whether (CONDENSED) or not (NOCONDENSED) the file is to
NOCONDENSED  be printed using the "condensed" character set generated by the
             printer.  NOCONDENSED is the default.  Note that CONDENSED can
             be combined with ENLARGED to produce "enlarged condensed"
             characters which are different in size from normal, enlarged,
             and condensed characters.

ENHANCED     specify whether (ENHANCED) or not (NOENHANCED) the characters
NOENHANCED   are to be double printed (by printing the character, advancing
             the paper by 1/216 inch, and then printing the same character
             again).  NOENHANCED is the default.

EMPHASIZED   specify whether (EMPHASIZED) or not (NOEMPHASIZED) the characters
NOEMPHASIZED are to be given a strong impression on the printer.  NOEMPHASIZED
             is the default.

HEX          specify whether (HEX) or not (NOHEX) lines are to be printed
NOHEX        along with the hexadecimal representation of each byte.  If HEX
             is specified, each line from the input file is preceded by a
             line on the printer containing the input file line number and
             length.  The the line itself is printed (with all characters
             between X'00' and X'1F', and X'FF' changed to a blank).  This
             line is followed by a line containing the high-order hex digit
             of the byte directly above it.  Then another line is printed
             showing the low-order hex digit in a similar fashion.  NOHEX is
             the default.

HEADER       specifies that before the first line from the file is printed,
             and after every PAGESIZE - (LPI/2) lines after that, a formfeed
             is to be sent to the printer to position it at the top of form.
             A "page header" is then printed which gives the input filespec,
             the date it was last updated, the date and time the PRT command
             was issued, and the page number.  This header is followed by
             LPI/2 - 1 blank lines (2 if LPI 6, 3 if LPI 8) prior to printing
             the first/next line from the input file.  HEADER is the default
             unless CC (see below) is in effect.

UHEADER      works in a similar fashion to HEADER, except you are prompted
             to enter a heading from the terminal to be used in place of the
             one generated by the PRT command.  If the first character of
             the header is ",", then it can be followed by up to 50 characters
             that are used to replace "date last updated" and "current date and
             time" fields mentioned above.  If the entered header does not
             begin with a comma, it can contain up to 70 characters which
             replace all fields in the page heading except the page number.

NOHEADER     causes LPI/2 blank lines to be printed at the top of each page
             (i.e., a 1/2 inch blank margin is left at the top of the page).

CC           specifies that the carriage control characters imbeded within
             the file (i.e., formfeeds and linefeeds) are to be used to
             format the listing rather than the PRT command keeping track
             of lines and performing page ejects and printing page headings.
             If CC is in effect, any HEADER/UHEADER/NOHEADER specification
             is ignored.  CC is the default if "filespec" contains a file
             extension ("filetype") of "LST".  Any other extension causes
             NOCC to be the default.

NOCC         causes PRT to keep track of the lines read from the input file
             and to skip over page perforations as described for the "xHEADER"
             options above.  Linefeeds encountered in the input file are
             honored and used to increment the line count.  Formfeeds are
             treated as linefeeds.  NOCC is the default unless "filespec"
             contains a file extension ("filetype") of "LST".

LPI 6        specify the number of lines to be printed per vertical inch of
    8        paper.  The only valid values are "6" and "8", with "6" being
             the default.

PAGESIZE n   specifies the maximum number of lines that are to be printed on
             a page prior to automatically sending a formfeed character to
             the printer and printing the appropriate page heading.  The
             actual number of lines from the input file that are printed on
             a page is PAGESIZE - (LPI/2) less the number of linefeed and
             formfeed characters encountered.  PAGESIZE 63 is the default
             (unless CC is in effect, in which case PAGESIZE is ignored).
             "n" must be 5 or larger.

FROM n       specifies the line number of the input file from which printing
             is to commense.  This can be used to print the first n-1 lines
             (ignoring linefeeds and formfeeds) in the file.  "FROM 1" is
             the default.

FOR n        specifies the maximum number of lines (ignoring linefeeds and
             formfeeds) that are to be read from the file.  This can be used,
             often in conjunction with the FROM option, to only print a
             selected number of lines from the file.  "FOR 32767" is the
             default.

notes:

Options can be prefixed with a "/" character to be compatible with the
options on some other PC-DOS commands, although the "/" specification is not
required.  If and when a ";" is encounted in the option specification,
it and any characters that follow are ignored.  While this technique can
be used to place comments on the end of the command line, its primary use
is to suppress the prompt for the entry of options when the default option
values are satisfactory.

The PRT command is written in IBM PASCAL.  The source code is available
and the "VALUE" section can be examined to modify the printer codes (see
the "INIT_xxxx_ON" and "INIT_xxxx_OFF" variables) if they differ slightly
for your printer.

The PRT command has been tested only with the Epson MX-100 printer.  It
should also work with the MX-80 printer since they are very similar (and
the PRT command doesn't use any of the MX-100's graphics features),
although this has never been verified (due to the lack of an MX-80
printer to play with!).