Installing the device driver for 720K drive in XT or AT:

Using a suitable editor make the following entry into your 
CONFIG.SYS file on the root directory of your hard drive.  
If you do not have a CONFIG.SYS file create one.

DEVICE=DVR35.COM /d

Replace "/d" with the drive parameter you chose from the 
chart below depending on how the 720K drive was installed:

  Firt floppy drive   ...  /0
  Second floppy drive ...  /1
  Third floppy drive  ...  /2
  Fourth floopy drive ...  /3  

Boot your system.  The following message will appear during 
the boot process.

DVR35 v1.xx       External Disk Driver
Copyright 1986    J&M Systems, Ltd.
Driver loaded successfully for drive x:.

Formatting 720K diskettes:

FORMAT35.COM command syntax

   [d:][path]FORMAT35 d:[/B][/V][/I=interleave factor]
   Parameters:  [d:][path]  preceding FORMAT35 to indicate 
                drive and path; default is the current drive 
                and directory.  Optional.  
                   
                [/B]  reserves sectors for system files to 
                be later installed by using the SYS command 
                in DOS.  Optional.  
 
                [/V]  will prompt user to enter a volume 
                label.  Optional.

                [/I=interleave factor {1..8}]  resets the 
                interleave factor the disk is initialized to 
                when formatted.  Valid factors 1 through 8.  
                Default is 1, which is the fastest in speed 
                of formatting.  Optional.  

  4-29-87 

If you are installing MACH 3.5 on a PC AT or compatible, be sure you
run your setup program and configure drive B: as a DOUBLE SIDED drive.


5-28-87
 
Note that if you are using version 2.x of DOS that the drive 
letter designator used by the 3.5" drive will be 1 greater than
your last drive.  For example, you have two 5.25" floppies
and one 3.5" floppy in addition to a single hard drive.  The 
following would be your configuration:

		A:  first 5.25" floppy		360K
		B:  second 5.25" floppy		360K
		C:  3.5" floppy, 360K format
		D:  hard drive
		E:  3.5" floppy, 720K format

Drives C: and E: are the same drive!  Two LOGICAL devices are
implemented on the same PHYSICAL device.  Use drive E: for 
general use and drive C: when a mirror image copy of a 5.25" 
disk is required.