Page 1 of 2                                              Dorn's Disk Driver



                         D O C U M E N T A T I O N

          Operating instructions for the Dorn's Disk version 2.00

Dorn's  Disk  Driver is a device driver for  use  with  DOS  2.00  and  up.  
Dorn's  Disk Driver is a disk emulator that uses memory unallocated by DOS.  
By  using  memory   for  temporary  file  storage,   a  great  increase  in 
throughput can be noticed (especially with disk bound processes).

Dorn's Disk uses memory above DOS.   Typically,  DOS uses memory below  the 
system   switch  setting,   and Dorn's Disk uses memory above the  setting.   
For  example:   If you have 512K of memory,  you can allocate 192K  to  DOS 
leaving  320K   for  the Dorn's Disk;   do this by  changing  the  internal 
switches  on   the  system board to represent 192K of  memory.    You  must 
allocate at least 64K of memory to DOS.

To  use Dorn's Disk with the XT,   a configuration utility  named   SizeDos 
must   be  used.    This  program patches Dorn's Disk which  instructs  DOS  
to  allocate  a specified amount of memory for the system,   regardless  of  
the system  switch settings.    Without using this program,    DOS will use  
all available memory--leaving no space for Dorn's Disk.   This program  has 
its  own  help messages,   so simply call it up by typing `SizeDos' and  it 
will supply more  information on this subject.    SizeDos only needs to  be 
used  once  to configure Dorn's Disk,   but may be used again to change the 
amount of  memory allocated to DOS.


                      Dorn's Disk Driver Installation

Two  items  must be done before Dorn's Disk can be used with  DOS.   First, 
the Dorn's Disk device driver file, named DornDisk.SYS, must be copied onto  
your bootable system disk.  Second, the line `DEVICE=DornDisk.SYS' must  be  
added  to the current CONFIG.SYS file.    IF CONFIG.SYS  does  not exist on 
your  DOS disk,   then you will need to make one using the IBM DOS  manual.  
See  section  9 in the DOS 2.00 manual (or the appropriate section in  your 
DOS Manual)  for more details on the  CONFIG.SYS file.


  Page 2 of 2                                              Dorn's Disk Driver

           FEATURES OF Dorn's Disk Driver  (Virtual Disk Driver)

1.   Dorn's  Disk  Driver  operates functionally like a  conventional  disk 
      drive:   files  can  be written and read from  it,  and  a  directory 
      listing can be obtained.

2.   The  number  of  directory entries is based on the amount  of   memory 
      available for Dorn's Disk Driver:

                      15 entries for  32K or less memory
                      31 entries for  33K to  64K of memory
                      47 entries for  65K to  96K of memory
                      63 entries for  97K to 160K of memory
                      79 entries for 161K to 224K of memory
                     111 entries for 225K to 339K of memory
                     128 entries for 340K or more of memory

3.  Dorn's  Disk Driver  can be of any size from 16K to 768K bytes long  in  
      1K  byte increments.

4.  The  user  can change the amount of memory allocated to DOS and  Dorn's 
      Disk Driver without reconfiguring the system disk. Dorn's Disk Driver 
      determines  how  much memory it is  allocated  by looking  above  DOS 
      (this  is normally based on the  system memory  settings   except  on 
      the XT),   and Dorn's Disk Driver uses the  memory  above  the memory  
      defined by the switches.   Dorn's Disk will also utilize  any  memory 
      found in the 192k buffer above the video area (C0000h-EFFFFh). 

5.  The  programs  stored on Dorn's Disk Driver normally are not  disturbed 
      during a re-boot.   Stored data may be lost,  however, if the SizeDos 
      program was used to configure Dorn's Disk. Files in Dorn's Disk on an 
      XT will always be lost during a re-boot.

6.  Since  Dorn's  Disk Driver is all contained in memory,   there  are  no 
      moving parts  and therefore operates at a significantly greater speed 
      than  conventional  disk devices,  and Dorn's Disk  Driver  needs  no 
      maintenance.

7.  The  disk  letter of Dorn's Disk Driver depends on the number of 5  1/4 
      inch  disks and  hard disks installed.   Dorn's Disk will be assigned 
      the next  available drive letter after all other drives.



There are a few limitations of Dorn's Disk Driver, they are as follows:


1.  The DOS utilities FORMAT,   DISKCOPY,   and DISKCOMP will not work with 
      Dorn's Disk drive.    These utilities require that the disk be  160K, 
      180K,  320K  or  360K  which severely limits the use of  Dorn's  Disk 
      Driver.

2.  The  files  stored  on  Dorn's Disk Driver will be  lost  if  power  is 
      interupted.

3.  Dorn's Disk Driver version 2.00 will only work with DOS 2.00 and up.


                                Have a good day!

					Dorn W. Stickle.........