--------------------------------------------------------------

                  F A S T D I S K

                        by

                 Michael A. Quinlan

--------------------------------------------------------------


*** DESCRIPTION ***

  FASTDISK is a PC DOS 2.00 device driver that implements an
in-storage virtual diskette.  It is similar to the driver
listed in Chapter 14 of the IBM PC DOS 2.00 reference manual.


*** FILES IN THE SYSTEM ***

  1. FASTDISK.DOC (this file) contains the documentation

  2. FASTDISK.SYS is the device driver

  3. FDCONFIG.EXE is the virtual diskette customization program


*** REQUIREMENTS ***

  An IBM PC with at least 64K of memory (256K to do anything
useful; more is even better) and PC DOS 2.00.  I assume that
the programs will work with PC DOS 2.10 but they have not
been tested there.


*** INSTALLATION ***

  Copy the FASTDISK.SYS file to your boot disk and add the
following entry to the CONFIG.SYS file:

    DEVICE=FASTDISK.SYS

When the system is booted, the FASTDISK driver will be
loaded and memory will be allocated for the virtual diskette.
A single disk drive name will be assigned to the virtual
diskette by PC DOS (if you have a two diskette system, the
virtual diskette will be assigned drive C:).

--------------------------------------------------------------

                  F A S T D I S K

                        by

                 Michael A. Quinlan

--------------------------------------------------------------


*** CUSTOMIZATION ***

  The FDCONFIG program is used to specify the size of the
virtual diskette.  It will ask for the following information:

  Name of file to update:
    (you will use FASTDISK.SYS unless you have renamed the
     driver program)

  Number of 512 byte sectors per allocation unit:
    (I recommend that you use 1 sector per allocation unit;
     the valid values are 1, 2, 4, and 8)

  Number of directory entries:
    (you specify the number of entries in the root directory;
     the value will be rounded up to a multiple of 16, the
     default is 112)

  Number of allocation units:
    (specify the size of the diskette; the default is 256
     allocation units giving 128K for storage of files)

Once all the information has been supplied, FDCONFIG will
update the driver file.  The new values will take effect the
next time the system is booted.

--------------------------------------------------------------

                  F A S T D I S K

                        by

                 Michael A. Quinlan

--------------------------------------------------------------


*** SPECIAL CONSIDERATIONS ***

  1. All the data in the virtual diskette will be lost
     whenever the system is booted.  I suggest keeping
     .COM, .EXE, .BAT, and temporary work files on the
     virtual diskette rather than data or program source
     files.

  2. Some other systems (such as non-IBM hard disks) use the
     CONFIG.SYS file to specify device drivers.  In more than
     one case I have had to change the order of the DEVICE
     commands so that FASTDISK.SYS was specified last.  It
     seems that some programs look at the number of
     diskette drives installed and assume that their drive
     names will begin with the next letter; inserting FASTDISK
     in front of these drivers messes them up.

     FASTDISK does not care where it is placed in CONFIG.SYS.
     The only effect is that the drive name assigned to the
     virtual diskette by PC DOS will depend on the order of
     the DEVICE entries.


*** SUPPORT ***

  I would appreciate your sending me any information regarding
bugs or problems with this software.  Please send comments to:

    Michael A. Quinlan
    645 East 200 South # 1
    Salt Lake City, Utah  84102

  Be certain to indicate that your comments are regarding the
FASTDISK system.

  I cannot guarantee that FASTDISK will work in your
hardware/software environment or that it will be appropriate
for your application.


*** PERMISSION TO COPY ***

  Permission is granted to copy this documentation and the
FASTDISK and FDCONFIG programs provided that the copies are
not made or distributed for direct commercial advantage.