1.    HDPREP.EXE

                  HARD DISK PREPARATION program 1.0
                  KFH ASSOCIATES,           1984
                  2771, Middleborough
                  SAN JOSE, CA 95132

                   FOR IBM PC,XT AND AT & COMPATIBLES
                         DOS 2.0/2.1/3.0
                   ALSO  XEBEC 1210A
                         DTC   5150BX
                         ADAPTEC 2002A
                         W DIGITAL 1002
                         ETC. PC CONTROLLER BOARDS

                  ** If you think the program is usefull to you,
                     $35.00 donation to    H. King   at above
                     address will register for updating notices

2.  The program READ in the hard disk drive parameters from the
    controller to determine the available number of heads and cylinders
    for each attached drive, if the controller follows the IBM BIO
    convention. Otherwise, the program defaults to 2 head and 306
    cylinders for each drive. You can use option 9 to change this
    settings.

3.  Hard disk preparation uses the controller default parameters.


Instructions:

The program is manual driven and self explanatory. The following is a
summary.

Options:

1. Select the drive to be operated on. Drive 0 is the first hard disk
   drive attached to the controller (usually the C:), Drive 1 is the
   second one (usually the D:).

2. Perform the controller FORMAT of the specified drive by option 1.
   See option 3. Run FDISK and Dos FORMAT after this step.

3. Perform the controller FORMAT of the specified drive by option 1
   and scan the disk for bad tracks and mark them bad. Run FDISK and
   DOS FORMAT after this step. This option 3 is preferred to option 2.
   After this step, you still can use the option 7 to mark additional
   bad tracks if you know it is bad and this step did not catch it.
   This step will list any bad track found and marked at the end of the
   process.

4. Move the head to track 0 for the specified drive.

5. Exit this program.

6. Set the interleave number for the controller FORMAT. The default is
   6 which is used by IBM PC/XT. Do not use other number unless you
   have enough knowedge on the controller.

7. If you know a specific track and head location is bad, you can use
   this option to mark the track bad. Use DOS FDISK AND FORMAR after
   this step.

8. If you want to remark a bad track to reuse the track, you can use this
   option. This option can not physically correct the defect track.

9. Use this option to define the number of heads and cylinders for each
   drive for this program to use. This parameter does not overwrite
   the controller defined parameter nor affect the controller FORMAT
   operation. An enhanced version allows the actual overwrite is not
   implemented here.

A. The same operation as the option 3, except during the verify process
   more data patterns are used. The process can take twice longer then
   the option 3. Usually, the option 3 is good enough.