DOS Low Level Format for Hard Drives

                           by Keith Turbyfill


        Most hard drives have bad sectors when they are new.  In 
        order to initialize the disk and lock out these bad 
        sectors, all hard drives are pre-formatted.  This 
        pre-format is commonly referred to as a "low-level format".
        Later, the hard disk is partitioned with FDISK and 
        formatted with the DOS FORMAT command.  This second format 
        is commonly referred to as a "soft format".

        The low-level format is usually done when a disk is 
        still at the manufacturer or distributor.  Usually, the
        disk is never formatted again... but in some cases, damage 
        to the disk, controller, or PC sometimes requires that 
        the hard drive be reformatted.  Most times, the soft 
        format can be executed to clear the disk and make it 
        reusable; however, sometimes the low-level format must be 
        executed to repair the disk.

        Of course, simply executing the low-level format will not 
        always fix the hard drives problems.  Other problems with 
        the machine or serious damage to the drive can require 
        repair or replacement of parts.  The low-level format is 
        one of several "last ditch" efforts to repair the disk 
        before costly maintenance or replacement.  NOTE:  The 
        use of the low-level format, FDISK, and FORMAT will all 
        destroy data on the disk.  

        IBM has its own Advanced Diagnostics which will allow 
        you to do (among many other things) a low-level format.
        Some versions of DOS have their own special utility 
        program to low-level format hard drives (One program  
        from Microsoft to low-level format is HSECT).  With 
        most MS-DOS and PC-DOS versions 3.0 and above, the low-level 
        format can also be done from command level using DEBUG.  The 
        following example outlines the procedure to [1] low-level 
        format, [2] partition (with FDISK), and [3] soft format 
        the hard drive.  This example assumes the machine has one 
        hard drive, designated as C: 

        







                             Low-Level Format




        1.  Open the case of the machine and examine the labels on 
            the top of the hard drive.  One of these labels 
            should have a "damage map" of bad sectors.  These 
            sectors will be designated by CYLINDER and HEAD.  For 
            example:



            CYL        HD          SECTORS

            389        2            2343
            402        2            1098



            Something similar to this example will be found on 
            the label.  Record ALL of the cylinders and heads.  
            You will need this information later to mark these 
            sectors as bad.  There may be several (or no) cylinders 
            and heads listed.  

        2.  Boot the machine with a DOS 3.0 or above diskette in 
            the A: drive.  After entering the correct date and 
            time, you should have the A> prompt.

        3.  Type and enter the word DEBUG.  (If you receive the 
            error "File not found", place the supplemental DOS
            in the A: drive and try again.)

        4.   When DEBUG is loaded, you will be given a short dash 
             (-) prompt:

             -

        5.   At this dash prompt, type and enter:

             G=C800:5

             The G stands for "Go", telling DOS to execute the 
             code (or program) in the hexadecimal memory location 
             which follows.  If the machine hangs, then the release
             of DOS you are using probably does not support this type 
             of low-level format or has a different starting memory
             location.
             
        6.  After you press return, you will receive a warning 
            that you are about to destroy all data on the disk.  
            You must enter   Y  to continue.







        7.  The routine will then examine the controller and 
            determine the manner in which the switch settings 
            (jumpers) are enabled.  The total number of cylinders 
            and heads of the hard drive  (actually the number the 
            controller is set to) will be displayed.  Usually, 
            this will be correct unless the controller or hard 
            drive has been changed -- or the installer really 
            screwed up.  In most cases, assume it is correct and 
            continue by answering  Y.

        8.  You will then be prompted to enter the interleave 
            factor.  The interleave is the amount of space or 
            time that the hard drive will "skip" as the head 
            spins.  High quality fast drives usually have an 
            interleave factor of 1 or 2.  Slower hard drives 
            normally have a factor between 3 and 5.  If you do 
            not know what the manufacturer's recommended 
            interleave is, use 3.

        9.  Next you will be prompted to enter the cylinder 
            number and head number of the bad sectors you 
            recorded from the hard drive label.  If there where 
            any, answer  Y  to continue and enter each cylinder 
            and head.  Continue until you enter all of the cylinder 
            and head numbers listed.

       10.  When you are finished listing the bad sectors, the 
            low-level format will proceed.  When completed, you 
            must partition the hard drive with FDISK and soft 
            format with FORMAT.

        







                      Partitioning the Drive with FDISK




        11.  Next, run FDISK.  FDISK will be contained on one of
             the two original DOS diskettes.  Choose option [1] 
             to create a DOS partition.  Answer  Y  to use the 
             entire disk for DOS.  After a short pause, the 
             program will instruct you to place the DOS program 
             disk in the A: drive.  When you press a key, the 
             system will reboot (restart).  NOTE: Different 
             partitions can be created -- if you have a need to 
             create several partitions (i.e. to run dual operating 
             systems or handle a drive larger than 30 Megabytes)
             refer to the hard drive documentation and the DOS 
             manual.

        12.  After you enter the correct time and date, you will 
             be given the A> prompt.  The final step is to soft 
             format the hard drive.

        







            Soft Formatting the Hard Drive with FORMAT.COM





        13.  Then, the most familiar type of format is done.
             From the A: prompt, type and enter:
          
             FORMAT C:/S/V

             The /S parameter causes the System to be transferred 
             to the disk.  This makes the disk bootable.

             The /V parameter causes DOS to prompt you to enter a
             Volume label for the disk.

        14.  Finally, don't forget to create a CONFIG.SYS and 
             AUTOEXEC.BAT.  A generic CONFIG.SYS would be:


             DEVICE=ANSI.SYS
             FILES=20
             BUFFERS=25

         
             ANSI.SYS is the driver for standard BIOS graphics, 
             and generally should be available for all machines.  
             The file ANSI.SYS must be copied to the root 
             directory.

             FILES and BUFFERS are set as the maximum space for 
             DOS to handle file I/O.  The values in this example 
             should handle most configurations and program 
             requirements.

             The AUTOEXEC.BAT is usually customized, but standard 
             items include:

             ECHO OFF
             CLS
             PROMPT $P$G
             VERIFY ON

             A command to extract the time and date from an 
             internal clock is almost always used.  Consult 
             individual manuals for the specific command.
             (Note:  AST boards commonly use ASTCLOCK to 
             retrieve the time.)


             







                              Quick Summary





        1.  Low-level format  DEBUG (- G=C800:5)
        2.  FDISK
        3.  FORMAT C:/S/V
        4.  Restore the CONFIG.SYS and AUTOEXEC.BAT