PW.SYS by Bob Montgomery 1/5/87

     This is a device driver to include in your CONFIG.SYS file to ask the 
     user for the password each time the machine is booted, or a calling 
     program (LOCK.COM) is run. It allows 3 tries, and then locks up the 
     machine if the incorrect password was given. It is a simplification 
     of PASSWRD5.SYS which was originally PWORD.SYS by an unknown author. 
     This was subsequently modified by John R. Petrocelli on 2/5/85 and 
     4/30/85, and by D. Drummond on 10/13/86 to produce the final 
     PASSWRD5.SYS, which included: limiting the number of tries, making 
     the password case insensitive, disabling Ctrl-Break, and making 
     provisions for another program (LOCK.COM) to invoke the password 
     request.
     
     The program was completely redone to make it shorter and have a more 
     logical flow, while retaining all the features of PASSWRD5.SYS. The 
     companion program LOCK.COM was also redone, and is now only 4 bytes 
     long. Being a device driver, PW.SYS is loaded and run before 
     AUTOEXEC.BAT is run, and cannot be bypassed by pressing Ctrl-Break or 
     Ctrl-C, which will break out of a batch file. It is resident in 
     memory at all times, so length is important; the resident portion is 
     only 590 bytes long, and most of this is the fancy ANSI text. To get 
     the color display, PW.SYS should occur after ANSI.SYS in your 
     CONFIG.SYS file; if you don't use ANSI.SYS, delete all the ANSI 
     escape sequences in the message area of the program.
     
     The source code for PW.SYS (in A86 assembler format-note the lack of 
     SEGMENT, ASSUME, ENDS, PROC, etc.) is included for those interested 
     in how it works, and is a good example of how to write a character 
     type device driver. It can be converted to MASM format by adding the 
     required ASSUMEs, SEGMENT, ENDS, END, etc. Basically, when DOS sees a 
     device in CONFIG.SYS, it loads it and then calls the Strategy routine 
     and passes the address of the Request Header (RH) for that device in 
     ES:BX. The Strategy routine must store the RH address in the program 
     data area, and then do a far return to DOS. Next, DOS calls the 
     Interrupt routine to allow the device to initialize itself; in this 
     case, the device installes the vector for Int 66h (an unused vector) 
     for the LOCK program, then disables Cntl-Break and asks for the 
     password. If the correct password is given within 3 tries, the 
     program enables Cntl-Break and then writes the address of the 
     first byte not required for the resident portion of the program 
     (generally the Strategy and installation code) in the RH Data area. 
     It then sets the done bit in the RH Status byte (thats why we had to 
     save the address of the Request Header), and returns (far) to DOS. 
     DOS then installs any other device drivers, and then runs 
     AUTOEXEC.BAT. This device was given a very weird name, unlikely to be 
     typed (even inadvertantly), which would trigger DOS to send info to 
     or try to get info from the device, and cause strange things to 
     happen.
     
     The LOCK.COM program is included to use with PW.SYS to ask for the 
     password without rebooting. Remember that the vector for Int 66h was 
     pointed to the proper place in PW.SYS to do a password check when 
     PW.SYS was installed. So, all LOCK.COM has to do is call Int 66h and 
     then terminate if the correct password was given. If the wrong 
     password was given 3 times, the machine locks up and can only be 
     restarted by cycling power (or pressing the RESET button if you have 
     one). The source for LOCK.COM is:
               Int  66h  ; Do a password check
               Int  20h  ; and terminate thru DOS
     If the correct password is not given, the program never returns from 
     Int 66h.
     
     The password can be changed by changing the entry labeled 'Password' 
     in the source and reassembling, or use DEBUG. The first byte is the 
     number of characters in the password, followed by the ASCII 
     representation of the password; up to 16 characters are allowed. In 
     the supplied source, the password is PASSWORD and there are 8 
     characters. If you want to distinguish between upper and lower case 
     characters in the password, delete the 'Convup' subroutine and the 
     two 'call Convup' instructions.
     
     If you have any comments or suggestions, I can be contacted at the 
     Black Hole BBS in Orlando, Fl. (305) 260-6397, 1200/2400 baud.
     Enjoy the program. Bob Montgomery, voice (305) 869-6481.