APPENDIX A
			     MEMBRAIN DOCUMENTATION


    - Description

	 MEMBRAIN.EXE creates a file named 'MEMBRAIN.SYS ', a DOS device
    driver for an emulated disk drive configured to your specifications.
    MEMBRAIN is installed through the DOS device driver interface using
    a 'DEVICE= ' statement in 'CONFIG.SYS '. DOS will assign to the drive
    the next available drive letter. For example, if your system has disk
    drives A: and B:, MEMBRAIN will be drive C:. On a PC-XT with drives A:
    and C:, MEMBRAIN will be drive D:.


    - System Requirements

	 An IBM PC or XT with at least 128K of memory and DOS 2.X


    - Installation

    1) Enter on the DOS or QSYS command line:

    MEMBRAIN  disk size,sector size,cluster size,directory entries,path

	 disk size - The requested size of the emulated drive in Kbytes.
	      An error is returned if the resulting configuration would
	      leave less than 64K of free memory. If this parameter is
	      omitted, the default disk size is 160K.

	 sector size - The size of each logical sector in bytes. Sector
	      size should be a multiple of 128 and will be rounded up to
	      the next 128 byte multiple. For example, if the parameter
	      is entered as 150, then the actual sector size will be 256
	      bytes. The default is 512 bytes per sector.

	 cluster size - The number of sectors per cluster. An error will
	      be returned if the number of bytes per cluster exceeds 2048.
	      Refer to 'Configuration Tips ' for more information. The
	      default is 1 sector per cluster.

	 directory entries - The maximum number of filenames that the disk
	      directory can hold. This parameter will be adjusted upward as
	      necessary to a multiple of sector size. The default is 64.

	 path - The drive and directory path in which MEMBRAIN.SYS is to be
	      created. This parameter is entered in the form 'd:\path '. If
	      drive is omitted, then the default drive will be used. If the
	      path is omitted, then the current directory will be used.

    NOTES:
	 - MEMBRAIN.EXE passes a return code upon termination that can be
	   tested in a batch file with the 'IF ERRORLEVEL ' batch file
	   command. A non-zero return code indicates that an error occurred.





								APP - A1





				   APPENDIX A
			     MEMBRAIN DOCUMENTATION


    2) To create a CONFIG.SYS file:

	 Enter on the DOS command line:

	  COPY CON: CONFIG.SYS	      'Copies keyboard input to CONFIG.SYS
	  DEVICE=MEMBRAIN.SYS	      ' this goes into the file
	  Press F6 and then <ENTER>   ' this writes the file to disk

    NOTES:
	 - CONFIG.SYS must be on the drive used to boot DOS.
	 - If you already use CONFIG.SYS, then edit it to include the
	   statement 'DEVICE=MEMBRAIN.SYS '.
	 - Multiple 'DEVICE= ' statements can be used in CONFIG.SYS to load
	   more than 1 MEMBRAIN device driver. This is less efficient than
	   using a single, larger device driver, and is not supported by
	   the QSYS INSTALLATION AID.

    3) Re-boot DOS either by powering the system off and then back on, or
       with the key sequence 'Ctrl-Alt-Del '. The MEMBRAIN.SYS device
       driver is automatically loaded and initialized by DOS.


    - Configuration Tips

	 MEMBRAIN.EXE displays a summary of disk space utilization as it
    creates MEMBRAIN.SYS. The following example illustrates how to use
    the data provided.

    MEMBRAIN 20,128,1,8,C:\	       'Command used to invoke MEMBRAIN.EXE

    <<<< M e m	B r a i n >>>>	       'Title
       (C) 1984 Dennis Lee
       20K MemBrain Created	       'disk size       \   These are the
							 \  values created,
      128  bytes per sector	       'sector size       \ and may differ
	1  sectors per cluster	       'cluster size      / from requested
	8  directory entries	       'directory entries/  values.

	1  reserved sector	       'boot record          \
	2  FAT sectors		       'file allocation table > overhead
	2  directory sectors	       'directory            /
      155  data sectors 	       'usable file space
    --------------------------
      160  total sectors	       '160 sectors X 128 bytes/sect = 20K

    This summary can be used to analyze the overhead of the configuration.
    Since a change in the configuration has no effect until the next time
    DOS boots, MEMBRAIN.EXE may be executed several times to analyze the
    effects of different parameters. The following notes are general tips.







								APP - A2





				   APPENDIX A
			     MEMBRAIN DOCUMENTATION


    1) Sector and Cluster Sizes

	 Each cluster requires 1.5 bytes of space for the file allocation
    table, and the total is rounded up to next multiple of the sector size.
    The general rule for adjusting sector size and cluster size is to use
    small sector and cluster sizes for smaller drives, or when small files
    will be stored, since less space will be wasted when part of a cluster
    is left unused between files. Larger sector and/or cluster sizes may
    provide more usable disk space per Kbyte of disk size, and a slight
    performance gain with larger drives, or when a few large files are to
    to be stored, since less space will be used for FAT sectors, wasted
    space between files is less of a consideration, and DOS will spend less
    time finding a given amount of data.

    2) Directory Entries

	 Each directory entry requires 32 bytes of space, and the total is
    rounded up to the next multiple of sector size. For example, with 128
    byte sectors, you get 4 directory entries per sector. Any request for
    directory entries would be rounded up to a multiple of 4. The only key
    to allocating directory entries is to allocate slightly more than you
    think you'll need, because it's frustrating to have free disk space and
    no available directory entries, but not too many, since extra entries
    are wasted space. MEMBRAIN uses one directory entry for a volume label.


    - Operational Characteristics

	 MEMBRAIN looks to DOS like a non-IBM fixed disk. This device type
    is used because it provides an operational interface to DOS consistent
    with it's performance characteristics. The following list outlines it's
    important operational characteristics.

	 1) Since MEMBRAIN is a non-IBM device, the 'FORMAT ' command will
	    not work with it. It doesn't need to be formatted!
	 2) Since MEMBRAIN can be any non-standard size, and is considered
	    fixed media, 'DISKCOPY ' will not work with it.



















								APP - A3