ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
        º                                                              º
        º            A GUIDE TO HARD DISK SECTOR INTERLEAVING          º
        º                              by                              º
        º                         Steven Gibson                        º
        º                                                              º
        º                  GIBSON RESEARCH CORPORATION                 º
        º                        22991 La Cadena                       º
        º                    Laguna Hills, CA 92653                    º
        º                                                              º
        º                     Phone: (714) 830-2200                    º
        º              Tech Support:       830-2500                    º
        º                       Fax:       830-0300                    º
        º               24-hour BBS:       830-3300                    º
        º                                                              º
        ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


        In these "sophisticated" days of computers, where AUTOEXEC.BAT 
        and CONFIG.SYS make casual conversation, it's rare to find a 
        topic as interesting and critical but still mis-understood, as 
        hard disk sector interleaving. 

        Our researches into this area have discovered that MOST IBM AND 
        COMPATIBLE personal computers are performance-crippled by mis-
        interleaved hard disk drives.  

        Unfortunately, many disk controller companies, in competing with 
        each other, have set their disk interleave defaults too tightly 
        for many computers.  Such "specsmanship" directly hurts the 
        innocent computer user (you) by dramatically limiting his hard 
        disk data transfer rate.  This GUIDE carefully explains the 
        situation and shows how to use the two included programs to 
        determine whether your own IBM PC or compatible's hard disk 
        drives have their sector interleave set correctly. 

        Responding to this problem, Gibson Research Corp., publisher of 
        the popular display screen enhancement utility FlickerFree, has 
        recently developed an inexpensive software SOLUTION which first 
        determines your system's optimum hard disk interleave factor 
        then RESETS IT while leaving all your hard disk data in place! 



                   UNDERSTANDING HARD DISK SECTOR INTERLEAVING

        It's a rare person who would not wish for additional performance 
        from his personal computer's hard disk drive.  While much 
        attention is given to the drive's Average Seek Time, which is a 
        measure of the time required to move the read/write head from 
        one track to another, there is another vital detail which 
        determines overall hard disk performance and which is subject to 
        the user's control. 

        We will see that the too often neglected SECTOR INTERLEAVING 
        factor of a hard disk has a dramatic impact on data transfer 
        rates. 

        As most people know,  the information stored on a floppy or hard 
        disk is arranged in a series of concentric circular paths called 
        tracks.  The disk drive's read/write head is specifically 
        positioned over any desired track with an operation called a 
        SEEK.  Thus an obvious limit on the speed with which a drive can 
        find or place information would be the so called track-to-track 
        and average seek times. 

        A single track of a standard IBM compatible PC contains 
        approximately nine thousand bytes of data.  But since we usually 
        deal with data in much smaller chunks, each track is divided 
        into smaller sections called sectors.  Think of a spinning pizza 
        which has been cut into seventeen identical, and numbered, 
        slices.  (Drives with RLL encoding pack 50% more data onto every 
        track resulting in more than thirteen thousand bytes per track 
        divided into 25 or 26 sectors.) 

        Now suppose that we need to read the information contained in 
        sector 1 of our current track.  We patiently wait for sector 1 
        to rotate under our read/write head, reading its data at that 
        time.  After absorbing this freshly read information, we realize 
        that we also need to read the next sector, number 2.  However, 
        by the time sector 1 has been moved into our computer and we've 
        decided to read sector 2, the beginning of sector 2 has already 
        started passing under the read/write head.  So we have no choice 
        but to wait for the disk to rotate all the way around once more 
        to deliver sector 2.  If we wished to read a nine thousand byte 
        file composed of all seventeen disk sectors on this track, 
        seventeen complete rotations of the disk, one for each sector, 
        would be required! 

        It wasn't long before a bright engineer realized that the entire 
        problem could be easily resolved by spreading the sequentially 
        numbered sectors out around the disk:  Instead of placing sector 
        2 immediately after sector 1, sector 2 could be placed a few 
        sectors later!  In this way, after reading sector 1, sector 2 
        would be just about ready for reading by the time we were ready 
        for it.   Such an elegant solution! 

        If, for example, sequentially (logically) numbered sectors were 
        staggered out every three physical sectors, then each rotation 
        of the disk could read every third sector.  Therefore only three 
        revolutions of the disk would be required to read an entire 
        track.  Quite an improvement over 17 revolutions!  This sector 
        staggering is known as SECTOR INTERLEAVING or SECTOR MAPPING.  
        The physical spacing between logically consecutive sectors is 
        known as the INTERLEAVE FACTOR.  This example used an interleave 
        factor of three, shown as "3:1" and pronounced: "3 to 1". 

        The new higher-density RLL controllers need to be correctly 
        interleaved too.  With 26 sectors per track a non-interleaved or 
        mis-interleaved disk would require 26 revolutions for an entire 
        track transfer! 

        Now here's the real rub:  In the current environment of mix and 
        match highly modular personal computing, responsibility for 
        determining and setting your hard disk drive's optimal sector 
        interleave factor has "fallen through the cracks" as it were.  

        You've never worried about it have you?  If you're inclined to 
        believe that someone else has, (like your local dealer perhaps) 
        you might be in for a real surprise.  Experiments with a wide 
        variety of computers, drives, controllers, clock speeds, and 
        interleave factors have shown that the hard disks of MOST 
        PERSONAL COMPUTER SYSTEMS ARE NOT PROPERLY INTERLEAVED TODAY!

        So many computers are so badly interleaved that it's quite 
        likely that you could increase your own hard disk's performance, 
        by FOUR TO SEVEN TIMES just by optimally setting your disk's 
        interleave factor!

        The interleave factor can be either too "loose" or too "tight".  
        The result of operating with an interleave factor which is too 
        loose is lower performance than a particular drive-controller-
        computer combination could achieve with tighter interleaving. 
        For example the original IBM PC/XT is interleaved at 6:1 but can 
        readily achieve 5:1 in a standard 4.77 Mhz machine and 4:1 in an 
        8 Mhz PC.  This means that disks on accelerated PC's can read 
        and write at 150% of their current rate! 

        The consequence of operating with an interleave factor which is 
        too tight is more disastrous, since missing that next sector 
        induces the significant delay of another entire disk revolution!

        You might be saying to yourself "so what's an extra disk 
        revolution between friends?", but consider this:  If your disk 
        is properly interleaved, say with a factor of 3, the entire nine 
        thousand byte track will be read or written in just 3 disk 
        revolutions.  However, if the particular controller in your 
        particular computer cannot achieve that interleave of 3, then 17 
        or 18 entire revolutions will be required to read the same 
        track.

          3 revolutions versus 18 is a performance difference of 600%! 

        Since many files and most programs are well over nine thousand 
        bytes long, and since DOS DOES REQUEST an entire track transfer 
        in such cases, these 17-revolution track reads add up quickly.  
        You would certainly feel the difference between waiting 3 
        seconds for a program to start up, versus 18 seconds! 

        The damning thing about proper hard disk sector interleave is 
        its total dependency upon EVERY factor of your system.  For 
        example, the AT&T 6300 requires 20 REVOLUTIONS for a full track 
        transfer when reading a disk which is interleaved at the most 
        common factor of 3:1!  Even it's faster brother, the 6300 Plus, 
        requires 14 revs!  We have found that the AT&T's hard disk data 
        transfer rate can be made FOUR TIMES FASTER when its interleave 
        is optimized for it!  If you're using a 6300 or 6300+, your disk 
        transfer rate is one quarter of what it could be! 

        Another example:  Western Digital's RLL hard disk controller 
        formats drives at a default interleave of 3.  Believe it or not, 
        this interleave is too tight for good old standard 4.77 Mhz XT!  
        Consequently 28 entire disk revolutions are required to read a 
        SINGLE track!  If the interleave is set to 4 then only 4 revs. 
        are required to read the same data, for a 700% throughput boost! 

        So by now you're dying to know what's happening with the hard 
        disk sector interleave of your own computers!  What interleave 
        factors are being used, are they correct, and what you can do 
        about it if not! 

        Included with this INTLEAVE.DOC file are two small programs:  
        SPINTEST.COM and SPINTIME.COM

        The main program, SPINTEST.COM determines how many disk 
        revolutions your IBM compatible personal computer requires to 
        read an entire 17 sector track from its hard disk.  (SPINTEST is 
        also fully compatible with the 25 or 26 sector tracks used with 
        the high-density RLL controllers.) 

        Running SPINTEST on the many computers at Gibson Research, and 
        in many local computer dealerships, we discovered something 
        quite surprising:  Most computers being sold today are horribly 
        interleaved.  We turned up many machines which required more 
        than 17 entire revolutions just to read or write one full track!  
        These same machines flew along at 4:1 but not at 3:1. 

        For example, Gibson Research has a vintage Leading Edge Model-D 
        with a standard Western Digital hard disk controller.  This 
        machine always seemed to run more quickly than a newer generic 
        PC clone equipped with a different Western Digital controller.  
        Both hard disks received their original low-level (interleaving) 
        format at the Western Digital default interleave of 3.  After 
        all, those dealers must have thought, Western Digital knows 
        what's best.   Right?   NOT NECESSARILY!  

        Since the controller AND computer together determine the optimal 
        interleave, it is IMPOSSIBLE for any controller manufacturer to 
        set a single optimal interleave for everyone.  In fact, even the 
        controller's revision level can be a determiner!  One of our two 
        WD controllers ALWAYS MISSES sectors when the disk is inter-
        leaved at 3, while the other controller makes 3:1 ... in the 
        same computer! 

        To test this, one of our hard disks was given a low-level format 
        at an interleave of four.  Afterward, the SPINTEST timing 
        diagnostic program and a stop watch confirmed our suspicions:  
        An MS-DOS file copy operation on the hard disk which had 
        required 139 seconds when the disk was interleaved at 3:1 now 
        took only 39 seconds at an interleave of 4:1! 

        Interestingly, that "slower" controller which can't make the 
        interleave of 3 on a standard 4.77 Mhz XT does just fine on a 
        faster 8 Mhz clone computer.  So as you can see, the COMPUTER 
        makes a difference too!  Any way you look at it, the issue of 
        sector interleaving involves the complex interactions among the 
        disk drive, the controller make and model (even the revision 
        level), the processor, and system clock rate. 



                 OVERVIEW OF THE INTERLEAVE DIAGNOSTIC PROGRAMS

        The issues of hard disk sector interleaving have gone unnoticed 
        for so long because there has never been a clear way to see 
        what's really going on deep inside a hard disk.  After seeing 
        the importance of this issue, we decided to change this.  The 
        two programs SPINTEST and SPINTIME determine, for any standard 
        MFM or RLL controller, exactly how many revolutions the disk 
        requires to transfer one entire track of data.  The programs 
        were hand written in 100% machine language (as is everything 
        Steve Gibson writes and Gibson Research publishes) to give them 
        the required measuring resolution speed.



                              THE SPINTEST PROGRAM

        SPINTEST determines exactly how many revolutions your hard disk 
        currently requires to perform a full track transfer. DOS 
        transfers a full track whenever programs or files larger than 9K 
        are read or written ... which is most of the time.  SPINTEST 
        does NOT directly read your drive's interleave, but the drives 
        interleaving performance can be easily inferred from SPINTEST's 
        full track transfer revolution count. 

        SPINTEST averages the time required for each of over two hundred 
        full track reads in order to accurately determine the revolution 
        count per read, then the number of revolutions required to read 
        just one track and the controller's full-track data transfer 
        rate are computed.  SPINTEST only reads data from your drive so 
        data is NEVER altered. 

        Over two hundred track reads were used because of the 
        inconsistent disk transfer behavior of AT&T's 6300 machines.  
        These exhibit a maddening inconsistency in their ability to 
        transfer disk data.  Sometimes they get the next sector, and 
        often not.  This means that a much looser than normal interleave 
        generates MUCH BETTER overall disk throughput for AT&Ts.  For 
        this reason, and to guarantee correct results on any machines 
        which may behave similarly, SPINTEST performs many track reads 
        and averages the results. 



                              THE SPINTIME PROGRAM

        Since SPINTEST measures track read time, it must assume a given 
        ratio between elapsed time and disk rotation rate.  Some weirdo 
        clone computers have a clock which runs faster than normal when 
        in their "turbo" (8 Mhz) mode, and some lap computers have tiny 
        hard disks spinning at weird speeds.  If these do not sound like 
        your situation SPINTEST will deliver correct readings and you'll 
        not need SPINTIME's confirming measurements. 

        But if EITHER of these cases might be you (if you have a weirdo 
        clone computer or hard disk sporting laptop) SPINTIME will tell 
        you for sure.  SPINTEST is only usable when SPINTIME gives 
        standard readings.  The single (not surprising) exception to 
        this is for the AT&T 6300 and 6300 Plus machines.  Due the 
        overall problems they experience with disk transfers, SPINTIME 
        may show a lower-than-3600 RPM reading.  For 6300's this is 
        normal. 

        SPINTIME is interesting regardless since it determines EXACTLY 
        how fast your hard disk is really spinning! 



                                    SPINTEST

        To run SPINTEST, simply type its name at the DOS prompt.  
        IMPORTANT!: Read the section IMPORTANT SPINTEST AND SPINTIME 
        NOTES below, before you begin! 

        Since SPINTEST takes the average of over 200 track reads, the 
        time required to run this test will vary between approximately 
        14 seconds for a fast 2:1 interleaved machine to 98 seconds for 
        an incorrectly interleaved 26-sector RLL encoded hard disk.  So 
        simply type: SPINTEST at the DOS prompt and wait a minute or 
        two. 


                                    SPINTIME

        SPINTIME has two purposes:  To determine the speed of your 
        system's clock (if you suspect that it might be weird) , and to 
        verify that your system's hard disk is spinning at close to the 
        standard 3600 RPM standard.  Your system's clock is checked by 
        measuring SPINTIME's exact execution time.  It should require 
        EXACTLY 60 SECONDS to run ... no matter what.  During that time, 
        it is busy watching your hard disk spin, counting every revolu-
        tion.  After EXACTLY 60 seconds, it displays your drive's exact 
        RPM (within its measuring resolution.)  IF SPINTIME's total 
        execution time is NOT EXACTLY 60 seconds, OR the displayed RPM 
        is not close to 3600, SPINTEST's reported revolution count won't 
        mean anything either. 

        SPINTIME's real value is to assure you that SPINTEST is 
        delivering worthwhile answers. 



                     IMPORTANT SPINTEST AND SPINTIME NOTES!             

        Both programs assume and require DOS 2.0 or higher.  They 
        operate on your system's FIRST hard disk only (drive C).  The 
        hard disk must be bootable, have its controller plugged into a 
        slot, not requiring special CONFIG.SYS device drivers for 
        operation. 

        SPINTEST and SPINTIME will never disturb your hard disk data, 
        but if your disk is some kind of odd-ball they may not function 
        correctly. 

        The tests will be more accurate if your normal collection of 
        memory resident programs (if any) are not in memory at the time.  
        Many resident programs "steal" so much time from the computer 
        that a delicate timing analysis could be upset.  It would be 
        wise to boot your machine from a plain DOS diskette when running 
        these tests for maximum reliability. 

        Also, turn off (or better yet remove) any disk caching software 
        you might be using.  Disk caching intercepts the disk reading 
        performed by the programs and renders their measurements invalid 
        (and rather humorous).  By the way, disk caching program per-
        formance is significantly improved through proper disk 
        interleaving. 



                                WHAT IT ALL MEANS

        So now you're wondering:  What do the numbers mean?  How do they 
        compare with industry norms and everyone else's?  Should I be 
        dancing on roof tops or wringing my dealer's neck? 

        A hard disk spins at 3600 revolutions per minute, or 60 
        revolutions per second.  A track has 17 sectors of 512 bytes per 
        sector.  This means that data passes under your drive's head at 
        a rate of 522,240 bytes per second.  (This number is 768,000 for 
        RLL con-trollers with 25-sector tracks.) Your system will 
        achieve some fraction of this maximum possible rate as 
        determined by the number of rotations required to read or write 
        each track.  522,240 (or 768,000) is divided by the number of 
        revs per track (as SPINTEST does) to calculate your drive's data 
        transfer rate.  

        Since your system's performance is meaningful only when compared 
        to other properly and improperly interleaved systems, the 
        following table will give you a feeling for where the industry 
        stands: 


           1:1 - There IS a controller which achieves 1:1, 
                 unfortunately it lacks Error Correcting Code 
                 (ECC) which is critical for reliable operation.

           2:1 - Compac machines achieve 2:1.  Adaptec's 2070A
                 RLL controller can do 2:1 with an 8 Mhz machine 
                 even though their low-level formatter stubbornly 
                 refuses to allow a setting of less than 3! 

           3:1 - Newer WD controllers and many other controllers 
                 will handle 3:1.  The Adaptec 2070A RLL con-
                 troller will do 3:1 in a 4.77 Mhz machine. 

           4:1 - Older WD controllers need 4:1, original IBM XT 
                 controllers can do 4:1 in an 8 Mhz machine.  
                 The AT&T 6300 Plus works best at 4:1 and WD's 
                 RLL controller can only do 4:1. 

           5:1 - IBM's original XT controller can do 5:1 in a 
                 4.77 Mhz XT but comes interleaved at 6:1.  The 
                 AT&T 6300 is best at 5:1 which increases over-
                 all throughput 400% over its default! 

           6:1 - Only the original IBM PC/XT seems to have been 
                 way out here.  These machines can be tightened 
                 up, and if it has an inexpensive accelerator it 
                 can probably run at 4:1 for 150% disk boost. 


        We have seen that WD controllers which miss at 3:1 will do 
        beautifully at 4:1.  Several InfoWorld readers have 
        independently confirmed that AT&T machines (with WD controllers) 
        perform best at the very loose interleave of 6:1.  Even the old 
        true blue IBM controller which runs at 6:1 can always do 5:1, 
        and even 4:1 in a faster than 4.77 Mhz machine. 



                               DETERMINING FACTORS

        So what system factors influence and determine the optimal 
        interleave setting for a given set of equipment?  After a sector 
        of data has been read it must be moved from the controller's on-
        board buffer into the computer.  This is done with a process 
        known as DMA (Direct Memory Access.)  The time required to 
        transfer the sector determines how soon the controller will be 
        ready to read the next sector. For this reason add-in 
        Accelerator "Turbo" Cards do not generally change a machine's 
        optimum interleave since the main system clock speed, which 
        continues to control DMA memory accesses, is not changed.  The 
        less expensive "Speed Booster" products which alter the basic 
        system clock timing DO have a tremendous impact on optimal 
        interleave by running the DMA faster and thus moving the data in 
        and out faster. 



                        GIBSON RESEARCH AND INTERLEAVING

        When we began these experiments we had NO IDEA that so many 
        personal computers were so poorly interleaved.  Without the aid 
        of SPINRITE, changing a hard disk's sector interleave "manually" 
        requires first backing-up all hard disk data onto some secure 
        medium.  Then a low-level re-formatting is performed.  This 
        messy task was never designed for the casual computer user since 
        it requires unpublished knowledge of the internal details of 
        your controller, using the DOS DEBUG command to poke hexadecimal 
        values into the 8088's machine registers and starting the low-
        level format.  After this, the FDISK and FORMAT commands are 
        used to create a partition table and lay down the high-level 
        formatting information.  After all this, the backed up data must 
        be copied back onto the drive. 

        Then, if the experimentally chosen interleave was not correct, 
        most of the process would have to be repeated with a different 
        trial interleave factor. 

        Responding to the clear need for a better solution to the task 
        of hard disk sector interleaving optimization, we developed the 
        now-famous SpinRite product to automated and streamline this 
        "re-interleaving" process.

        SpinRite quickly determines the optimal interleave setting for 
        any disk of any size in any system with any clock rate.  Once 
        determined, the existing interleave of the disk can be RESET 
        automatically, and in just a few minutes, leaving all your disk 
        data intact and in place!  It also performs several other useful 
        hard disk utility functions which have never before been 
        available. 



                         GET YOUR DISK SPINNING RIGHT!! 

        Even if SPINTEST turned in excellent results of 3 or 4 revs, you 
        should STILL check out Gibson Research's new product for the 
        other surprising (NEVER before offered) hard disk capabilities 
        it brings ... and if you received results like 10, 12, or even 
        17, 18, or 19 revolutions, there is NO DOUBT that your system 
        could be running FOUR TO FIVE TIMES FASTER ... in minutes!

        To receive all the details about SpinRite simply phone, or send 
        your name and address either through our 24-hour BBS, or through 
        the US Mail.  Ask for our completely descriptive SpinRite 
        literature.

                        ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                        º  GIBSON RESEARCH CORPORATION  º
                        º        22991 La Cadena        º
                        º    Laguna Hills, CA 92653     º
                        º        (714) 830-2200         º
                        ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                            Thanks for your interest!