TESTDISK DISK PERFORMANCE TESTER

                         COLUMBIA DATA PRODUCTS, INC.
                           851 W.S.R. 436 SUITE 1015
                         ALTAMONTE SPRINGS, FL  32714
                             (305 OR 407) 869-6700

       Welcome  to  the  world of  hard  disk  performance  measurement!
       Because  you  are reading this file,  it would be safe to  assume
       that you are interested in finding out how "fast" a certain  disk
       is.  Well,  if you know anything about disk performance, then you
       know  that  it  is an extremely difficult thing  to  measure  and
       quantify because "fast" is an extremely relative term.  This disk
       test  was designed to give you a general idea of how a given disk
       will perform OVERALL.  This sounds like a difficult task, because
       it IS a difficult task.

       Other  disk  performance  testers  report  average  access  times
       (expressed   in  milliseconds)  and  data  rates  (expressed   in
       Kilobytes  (1024  bytes) per Second (KBS)) and leave it at  that.
       This  tells very little about the overall performance of  a  disk
       system.   The REALLY important aspects of disk system performance
       are just not shown.

       Let's take a disk that has an access time of 20 milliseconds, for
       example.   Does  that  mean  that  just  because  it  has   a  20
       millisecond access time that it is fast?  Well,  yes and no.   It
       means that it can move the disk head from one spot on the disk to
       another   spot   on  the  disk  in  an  overall  average  of   20
       milliseconds.   As  far  as access times  go,  a  20  millisecond
       average access time disk drive is pretty quick.  But it tells you
       nothing  of  how it will perform on your computer.   So you  ask,
       "Well then, how do I tell if a disk drive is fast?"  Read on!!

       Disk performance really starts at your hard disk controller,  and
       not  at your disk.   Disk performance is a function of  how  fast
       data  can  be transferred from the hard disk into your  computer.
       This  means  it all really starts at your  hard  disk  controller
       card.  If you have a disk controller that can move data at 29,000
       characters per second (which is not uncommon),  then it stands to
       reason  that  to load your 174,000 character spreadsheet it  will
       take  you  six  seconds.   So,  you see,  whether you have  a  20
       millsecond hard disk or a 65 millisecond hard disk it still takes
       six seconds to recover your spreadsheet!!

       As  you  can probably tell,  disk performance that tells you  how
       long  you  are  going to wait for something  to  load  into  your
       computer  from your hard disk can best be expressed in characters
       per second.   Since one character is equal to one byte,  and most
       disk systems move data in thousands of bytes (or characters)  per
       second,  the  standard term for data rate is kilobytes per second
       (KBS).

       Some  disk performance testers actually DO report your data  rate
       from your hard disk.  They only report, however, the highest data
       rate  your disk drive can achieve on your computer.   Now if  you
       read  closely,  you will notice that I said the HIGHEST data rate
       your  disk drive can achieve on your computer.   Does  this  mean
       that  there is more than one data rate expressed in KBS that  can
       be acheived by your disk system?  The answer is YES!

       Whenever  the  disk  system is asked to move data from  the  hard
       drive  into  memory or vice versa,  it takes time  for  the  disk
       system to figure out what you are asking for,  where it is on the
       disk,  and  how it is to move the data.   This time lag is called
       command processing latency.   It is this initial time lag  before
       data  is actually moved to or from the disk that is the  evil  of
       disk performance.  Since this time lag is pretty much a constant,
       it is wise to get as much data off of the disk at one time rather
       then ask it for data off of the disk repeatedly in small  chunks.
       For  example,  if  you wanted to move  327,680 bytes off  of  the
       disk   and  the  initial  command  processing  latency   was   70
       milliseconds  (70/1000  of a second),  and the 327,680 bytes  was
       moved in  512 byte chunks,  you would be asking the disk to  move
       data 640 times and your command processing latency alone would be
       44.8 seconds (640 X .070 seconds)!!

       If,  however,  you  moved  the 327,680 bytes off the disk  65,536
       bytes  (64 KB) at a time,  you would be asking the disk  to  move
       data  only  5 times and your command processing latency would  be
       35/100's of a second (5 X .070 seconds).  That is 992 % faster!!!
       44.8  seconds compared to a fraction of a second and  that's  not
       even  counting the time to move the data!!  That is extremely eye
       opening isn't it?

       So,  you see,  it doesn't appear to be very wise to ask the  disk
       for data in small chunks, now does it?  But this is precisely the
       way most application programs (such as Lotus, Dbase, etc) DO move
       their  data.   512  bytes  at  a  time.   Now  these  other  disk
       performance  testers  I mentioned,  test the disk by moving  data
       65,536 bytes at a time.  So, you have absolutely no idea how fast
       Lotus, Dbase, or any of the other application programs, which use
       the  disk a lot, will be.  All you know,  is that IF YOUR PROGRAM
       MOVED  DATA 64K AT A TIME OFF THE DISK THIS IS HOW FAST IT  WOULD
       BE!!   In essence then, to measure disk performance in 64K chunks
       is  utterly  useless to you if you really want to know  how  fast
       your application program can load data.

       This disk performance tester doesn't just move data off the  disk
       in  64K  chunks.   It moves the data in 8 different size  chunks:
       1/2K,  1K,  2K,  4K,  8k, 16K, 32K and 64K.  This will give you a
       clear idea of how fast your disk system really is.   When you run
       this  on a disk system that is 650 KBS at 64K chunks you  may  be
       surprised  to  find  that it is only 120 KBS (or  less)  at  1/2K
       chunks.  You  may even find that you paid a premium for a  "fast"
       disk  system  and  you  never will see the  "speed"  because  the
       programs you run cannot utilize it.

       One  last word about average access times.   They are  important.
       We at Columbia Data Products do not dispute that.   They  account
       for  a sizeable portion of your command processing  latency.  You
       should  not,  however,  pay a premium for a "fast" access time if
       you  can't  take  advantage  of it.   This  test  will  help  you
       determine that. The last example I wish to give, will compare two
       hard  drives.   The first hard drive has a 1 millisecond  average
       access  time  and the other has a 100 millisecond average  access
       time.  The 1 millisecond access time hard drive can move data off
       of  itself and into the computer at 100 thousand bytes per second
       (100 KBS).   The 100 millisecond access time hard drive can  move
       data  off  of itself and into the computer at 900 thousand  bytes
       per second (900 KBS).

       To  move 900 thousand bytes,  the 1 millisecond access time  hard
       drive  takes 9 seconds while the 100 millisecond access time hard
       drive   takes  only 1 second.   Therefore,  the  100  millisecond
       access time hard drive is 9 times faster moving data even  though
       it  is 100 times slower moving its head!  It probably costs a lot
       less too.   I think you are beginning to see the  picture.

       RUNNING TESTDISK

       To start testdisk,  simply type TESTDISK  and press enter.  First
       you must choose whether or not you want to run testdisk in color.
       Next,  you will  be asked  whether or  not your printer can print
       the two characters that are  displayed  on the screen.  A printer
       that  can  print  the  IBM  character  set  will  have no trouble
       printing the displayed characters.  The printer will print out  a
       graph of the test  results, if you  desire, at the  completion of
       the test.

       You will then  be asked for  a DOS drive  letter (C:, D:  etc) to
       test.  Next you will be asked  how much data in K you  would like
       to read (we recommend at least 1000K for an accurate test).   The
       test then proceeds to perform  a verification pass to insure that
       the area being tested is error-free. If it is not,  an error will
       occur  and the test will stop. If it is error-free, the test will
       continue.

       TESTDISK starts by reading the amount of data requsted  in groups
       of 1/2K at a time, and then progressively  changes to 1K, 2K, 4K,
       8K, 16K, 32K and 64K. So, if you are reading 1000K by reading  in
       1/2K groups, you will access the disk drive 2000 times to get the
       data. For the 1K group, you will access the disk 1000 times,  and
       500 times for the 2K group, and 250 times for the 4K group,and so
       on. The sequential test reads the data sequentially, meaning that
       we start by reading data sector 1 on the hard  drive and then add
       1/2K  each time we  access the disk until we have read the amount
       requested. When we start the 1K sequential test, we start back at
       sector 1 and add 1K  each time until we  have read the  requested
       amount, and so on up to 64K.

       The non-sequential test reads the same data over and over  again,
       accessing  the same spot on the  disk every time  reading in 1/2K
       chunks, up to 64K chunks.

       Happy Testing!!!