----------------------------------------------------------------
       ZIP - Integrated File Handler Package - Version 0.7
----------------------------------------------------------------

     An All-purpose Directory Utility and Command Shell for
          the IBM Personal Computer & Close Compatibles

                       By Edward V.  Dong
                          July 08, 1985

  Copyright (c) 1985 by Edward V.  Dong.  All rights reserved.

----------------------------------------------------------------

1.0     INTRODUCTION

     The  ZIP  program  is  an  integrated  file handling utility
package, written mainly in DeSmet C version 2.3 for PC/MS-DOS 2.0
or  later, with some assembly language subroutines embedded.  The
following is a brief summary of functions currently supported:

    o   Sorted directory, showing hidden, read-only, system files.
    o   File attribute read/set, to hide/unhide files, etc.
    o   View text files, standard ASCII.
    o   View WordStar files in addition to standard ASCII.
    o   Edit text files, with limited screen editing capabilities.
    o   Hexadecimal/ASCII dump of files.
    o   Copy/print/delete multiple files.
    o   Rename files.
    o   Squeeze/unsqueeze files.
    o   Library functions: list libraries, extract members.
    o   Add members to existing libraries; create libraries.
    o   Ability to execute files (.BAT, .COM, .EXE).
    o   300/1200 BPS ASCII/Xmodem telecommunications.

     The following are additional features that may be  added  in
the future.

    o   Label disks.
    o   Auto-catalogue files to master directory, with comments.

     ZIP version 0.7C is currently distributed as "User Supported
Software",  under the "FreeWare" or "ShareWare" concepts.  With a
few restrictions, this allows the program, although  copyrighted,
to  be  freely copied and distributed.  Version numbers less than
1.0 are beta test versions, where user comments and  testing  are
solicited.   When  sufficient testing (and fixes and/or upgrades)
has been completed, the version will go to 1.0 or higher.   Whole
numbers  will  indicate  a significant upgrade or revision, while
fractional numbers will indicate minor upgrades or bug fixes.

     The  current version number is identified in the top line of
the ZIP display as a decimal number enclosed in  brackets,  e.g.,
[0.7].   When  followed  by  the  letter  "C", the version number
indicates a version done in the "C" language;  else  indicates  a
version done in Turbo Pascal.

     Version history is as follows:

   o Version 0.0 - original beta version.
   o Version 0.1 - Edit bugs fixed; disk label bug fixed.
   o Version 0.2 - add capability to execute files or manual
                   commands as if entered from DOS prompt line.
   o Version 0.3 - add print capability; show number of files
                   which are tagged; additional error checking;
                   verify option on copy.
   o Version 0.4 - added new Edit/View options; copy, squeeze,
                   unsqueeze now run much faster; added basic
                   telecommunications capability.
   o Version 0.5C- previous versions written in Turbo Pascal 2.0;
                   revisted/translated to "C", DeSmet ver. 2.3.
                   Edit not supported yet under C; view is more
                   basic.  Library functions expanded to include
                   library creation & add/update library members.
   o Version 0.6C- View now supports string search, paging, and
                   automatically strips high-order bit, thus
                   allowing WordStar file browsing.  Telecom
                   expanded to handle some non-Hayes modems.
                   ZIP LBR files now compatible with LUT, LUE,
                   LUU, and LAR, and with some versions of LU86.
                   ZIP will show LBR member file date & time, if
                   available.  Copying speed increased 16 times.
   o Version 0.7C- Screen editing now supported.

     When all bugs have been exterminated, the version level will
then become 1.0.  Help me to do that!

1.1     WARRANTY  &  GUARANTEE.

     There aren't any, implied or otherwise.

     The  author  is  not  responsible  for  possible  consequent
damages  arising  out  of  the use of ZIP under any circumstances
whatsoever.  Remittance or contribution shall not provide for any
warranties  or  guarantees  of  performance or against consequent
damages, implied or express or otherwise.

1.2     DISTRIBUTION & COPYING.

     ZIP  may be freely used, distributed, and copied, as long as
ZIP is only for personal (not commercial)  use;   and  that  this
product  must  be  copied  and distributed as a complete package.
This  includes  both  the  ZIP  program  (ZIPxxx.EXE)  and   this
documentation file (ZIPxxx.DOC), where xxx is the current version
number.  ZIP is copyrighted and may not be distributed if altered
or  modified  in  any  way.  Finally, no fee is to be charged for
copying  or  distributing  the  programs  without   the   written
permission  of the author;  and commercial users should remit the
$10 contribution (or actually  "fee"  in  this  case),  to  avoid
possible legal hassles.

     In  short,  ZIP  may be copied and distributed to anyone who
wishes it  as  long  as  it  is  a  complete  unmodified  package
including  the  program  and documentation and no fee is charged;
and freely used except in a commercial environment.  In  turn,  a
small  contribution  of  about  $10.00  is  suggested  but please
contribute  whatever  you  feel  the  program  is  worth.    Your
contributions  will help offset development costs and thus assure
future updates and products.

     However, for the contribution of $35, a DSDD  disk  will  be
sent,   containing   the   latest   version   of   the   program,
documentation, and complete source files.

     Even  if  you  don't  feel  that  the   program   merits   a
contribution, please continue to copy and share this program with
others.


                              Edward V. Dong
                              12205 Alexandria Place
                              Chino, California 91710


1.3     REQUIRED CONFIGURATION

     ZIP needs the following environment:

        1. IBM PC or close clone
        2. Color Graphic screen adapter
        3. MS/PC-DOS 2.0 or 2.1
        4. At least 128K (256K is recommended)

     For  best results, you should set CONFIG.SYS to "Files = 15"
and "Buffers = 16", or greater.   Consult  your  DOS  manual  for
details on the setup of CONFIG.SYS.  The "Buffers" statement will
speed up disk  accesses,  especially  when  dealing  with  floppy
drives.

     ZIP  won't  run  properly  on a PCJr, because display memory
organization is different on a PCJr.  (Recent note:  I have  been
informed  that  ZIP will display properly on a PCJr, but has some
problems handling disk directories.) Since I don't have access to
EGA or to an AT, there is no guarantee that ZIP will run on an AT
or an EGA device.  If there is a demand for the use of ZIP on the
PCJr, or EGA/AT, special versions will be written.

     ZIP should run under  MS-DOS  2.11  or  later.   For  speed,
however,  of  display  generation,  ZIP has been customized to an
IBM-PC, so it may not run on some PC clones which do not  support
the same display generation capabilities.

     ZIP  makes  use  of  color,  and  assumes  a  color/graphics
adapter.  ZIP does run on a color PC-3270 -- ZIP makes NO use  of
any  true  graphics, and only assumes a color alphanumeric setup,
with display memory  at  B8000H.   This  means  that  green/amber
screen  monitors and IBM-style monochrome monitors cannot be used
with ZIP.  Again, if there is a demand for ZIP on these  devices,
special versions will be written.

1.4     BUG REPORTS & OTHER COMMENTS.

     Address bug reports and  other  comments  (praise  won't  be
unwelcome,  of course;  naturally, the highest praise being ca$h)
to the above address.  E-Mail may be  addressed  at  the  present
time  to  me  ("Edward  Dong")  via:

     Rod Bowman's "PC-Spectrum" IBMPC-RBBS
     Chino, California
     714-980-8607,
     300/1200/2400 baud, 24 hrs/day.

     Matt Zilmer's FIDO
     Claremont, California
     714-626-1843
     300/1200/2400 baud, 24 hrs/day.

2.0     USING ZIP VERSION 0.7C

     All  you  have  to  do  is  type in:  ZIP.  A help screen is
provided as a quick summary of the available functions.  A  brief
discussion of these functions follows.

2.1     Directory

     ZIP  immediately  displays  the  sorted  directory  for  the
current drive, showing all files,  including  hidden,  read-only,
and  system,  as  well  as directory and volume-label files.  The
current attribute is shown next to the file name;   however,  for
space considerations, only one attribute is shown at a time.

     These  are:   h(idden),  r(ead-only), s(ystem), d(irectory),
and v(olume-label).

     By hitting ENTER when a high-lighted file is a  d(irectory),
ZIP  will  put  you  into  that  directory,  and then display the
contents of that directory.

     If you want to change drive, enter L for Login to new drive;
ZIP  will  prompt for the new drive/directory.  When entered, the
sorted directory for the new drive/directory, will be  displayed.

     NOTE:   If  you then chose to exit ZIP after Login, you will
     be in that drive and/or directory.

     PgDn  and  PgUp can be used to scroll through the directory,
if the total directory  cannot  be  fitted  to  the  current  CRT
window.

     NOTES:  A simple sorting function  was  previously  used  in
     ZIP, so it was rather slow for those systems with more  than
     50-60  files.   This  has been corrected in the "C" version,
     using Quick Sort.  The previous Pascal version used software
     floating point for calculation of  file  sizes  larger  then
     32767, which also made it  slower;   happily,  "C"  supports
     LONG integers, so this has gone away.

2.2     File Attributes

     As  you  may  or may not know, DOS generally marks each file
with one or more attributes.  These are:

        o A(rchive):    If set, means this file has not been
                        backed up.

        o D(irectory):  If set, means that this file constitutes
                        a subdirectory with or without files in
                        that subdirectory.

        o V(olume):     If set, means that the filename is the
                        label for the disk in the current drive.

        o S(ystem):     If set, means it is a system file,
                        like a device driver.

        o R(eadonly):   If set, means that the file cannot be
                        deleted or modified.

        o H(idden):     If set, means that the file cannot be
                        normally listed, deleted, copied, or
                        read.

     ZIP provides through the "F"(ile) command, the means to read
the  total  set of file attributes (some can be combined), and to
set these attributes.   The  "V"  attribute  is  not  modifiable,
however.

     When  ZIP  displays  the  sorted  directory for a drive, the
highest priority file attribute is  displayed  (as  a  lower-case
letter next to the file name).  The A(rchive) attribute, however,
is NOT displayed (except through the "F"(ile) command), as nearly
all files in a directory will likely have this on.

2.3     Editing

     By using the cursor keys and/or PgDn/PgUp keys, you point to
a high-lighted file shown on the directory display.  Then at  the
command  prompt  (last line on the screen), enter "E".  This will
put you into a screen editing mode for the high-lighted file.

     A brief command line description appears at  the  bottom  of
the  screen, indicating the type of editing you can perform.  You
can insert/delete lines;  insert/delete characters;   and  scroll
back  and forth through the file.  The complete scroll capability
is provided only if the entire file can fit  into  the  available
memory.   If you have not much memory, then only a portion of the
file can fit.

     While screen editing of files is supported by ZIP, you can't
use  ZIP  to  create a new file to be edited.  This will probably
change in the next version of ZIP.

     ZIP editing, like EDLIN or IBM's  Personal  or  Professional
Editors,  performs  editing  in memory.  If the size of a file is
larger than your available memory, the first segment of the  file
is  loaded  for  editing.   When  you  finish  this segment, this
segment is written to a temporary file called  ZIP.$$$,  and  the
next segment is loaded.

     Once  a  segment  has  been written to ZIP.$$$, and the next
segment is loaded for editing, you CAN'T go back  to  an  earlier
segment.

     ZIP,  when  you  have  SAVEd  your  file, erases/deletes the
original file, and then renames  ZIP.$$$  to  the  original  file
name.   ZIP DOES automatically make a backup copy of the original
file name, with the extension .BAK.  If another file of this name
exists (*.BAK), it will be deleted and replaced.

     Editing files are limited to 78-character lines.  If a  file
being edited is longer than 78 characters, the excess will NOT be
displayed.  The resultant SAVEd file, however, will have the full
string  --  you  just  cannot edit that portion of the line.  ZIP
isn't intended to replace your standard editor or word processor;
if it did, ZIP would have to be twice as large.

     Beginning with beta version 0.4, EDIT supports the following
commands:

        F1 - Display list of EDIT/VIEW commands.
        F2 - Find string, starting with current line to the
             end of the current segment loaded.
        F3 - Get/put -- writes current segment to disk, and
             fetches the next segment.
        F4 - Quit.  Same as END.
        F5 - Insert new line (initialized to a single blank).
        F6 - Delete current line.

        HOME - Go to top of current segment.
        END  - Save or quit current EDITed file & terminate.

     Additionally, the top line  of  the  display  shows  current
status  of  file, i.e., segment loaded, and number of total lines
in that segment.

     NOTE:  Tab characters (which are expanded  under  VIEW)  are
     not    expanded   under   EDIT.    They   will   appear   as
     strange-looking  little  circles.   The   reason   for   not
     performing the expansion is to show as much of the  line  as
     possible for EDITing.

2.4     Viewing

     By using the cursor keys and/or PgDn/PgUp keys, you point to
a  high-lighted file shown on the directory display.  Then at the
command prompt (last line on the screen), enter "V".   This  will
put you into a full-screen browse or viewing for the high-lighted
file.

     A brief command line description appears at  the  bottom  of
the  screen,  indicating the commands you can enter:  PgUp, PgDn,
HOME (to take you back to the top  of  the  file),  and  END  (to
quit).  Scrolling is limited to paging forward or backward.

     Pressing  F2  invokes  a  string  search function.  ZIP will
prompt for the string to find, and  will  attempt  to  find  this
string,  searching  the entire file if necessary.  When the first
occurrence is found, all occurrences of that string on the  given
display page will be highlighted.

     If  you  are  past that displayed page, and wish to find the
string again, press the letter A (upper or lower case).  ZIP will
search for the next occurrence of the string.

     Viewing  files are limited to 80-character lines.  If a file
being viewed is longer than 80 characters,  the  excess  will  be
lopped  off  and  not  displayed.   Expressed another way, a file
being viewed  of  length  greater  than  80  characters  will  be
truncated  to  the  first 80 characters.  VIEW will automatically
strip the high-order bit, so that WordStar files  can  be  viewed
without modification or conversion.

     Beginning  with  version  0.7C, VIEW will also automatically
expand tab  characters  found  into  the  appropriate  number  of
blanks.   ZIP  assumes  that  tab's  are  meant  to space every 8
characters, so if the file uses tab's to space a different number
of characters, the display will look a little strange.

2.5     Squeezing/Unsqueezing

     By using the cursor keys and/or PgDn/PgUp keys, you point to
desired files shown on the directory display.  Then you press the
space  bar  to  "mark"  or  "unmark"  the files.  Finally, at the
command prompt (last line on the screen), enter "S" for squeezing
the  file  or  "U" for unsqueezing ALL the marked files.  As each
file is SQueezed or UnSQueezed, the bottom line  of  the  display
will  show the operation(s) as each file is processed.  Beginning
with version 0.7C, ZIP no longer  opens  a  window  to  show  the
operation.

2.6     Library

2.6.1   Library List/Extract

     By using the cursor keys and/or PgDn/PgUp keys, you point to
a high-lighted file shown on the directory display.  Then at  the
command  prompt  (last line on the screen), enter "B" for liBrary
functions.  ZIP will  open  a  new  window,  display  the  sorted
directory  for  the  library  (LBR  file),  and  generate a brief
command line at the bottom of the screen.

     Available options are displayed if you press the "?" key.

     Beginning  with version 0.65C, you can direct the extraction
to another disk or directory, by pressing "C".  ZIP will ask  for
the  new  disk/directory.   To  direct to C:\NEWDIR, for example,
type
     C:\NEWDIR\
You MUST enter the second backslash.  To direct to another drive,
say, B:, type
     B:
The colon is required.

     You can either Extract one or many LBR members, or Quit.  To
extract  one  or  more  members, use the cursor/PgDn/PgUp keys to
point to each member, and then use the  spacebar  to  mark/unmark
the member for extraction.  When finished with the marking, enter
"E", and each file will be extracted in turn.  ESC is accepted as
Quit as well.

     If the LBR file has been created by ZIP 0.64 or later, or by
any of Vern Buerg's LUU routines, ZIP will also show the creation
date and time of the members of the LBR file.

     If  you  have  extracted  any  members, ZIP will re-read the
current drive and provide a new sorted directory listing display.

2.6.2   Library Create/Update

     You  can  create a library, and add members to this library,
or to an existing library.

     To create a  library  or  to  add  members  to  an  existing
library, you must first "mark" the files in the current directory
to be added to that library.

     To  create,  point (via cursor and/or PgDn/PgUp keys) to any
file in the directory which is NOT a library file.  Then  at  the
command  prompt  (last line on the screen), enter "A" for library
Add-member functions.  ZIP will ask  if  you  want  to  create  a
library (because the current file is NOT a library file);  and if
so, will ask what name you  want  to  give  it.   If  it  can  be
created, then ZIP will automatically add the files which you have
marked, to that library.  The library name can  include  optional
drive  and  directory,  to  build  an  LBR on another disk and/or
directory.  You must then enter the COMPLETE file  name  for  the
desired LBR.

     To  add  members  to  an existing library, simply point to a
file which IS a library file.  Then proceed as above.

     That's all there is to it.

2.7     Copying/Printing/Deleting

     By using the cursor keys and/or PgDn/PgUp keys, you point to
a  high-lighted  file  shown  on the directory display.  Then you
"mark" the file by using the spacebar.  You toggle the "mark" off
or  on, with the spacebar.  When finished with the marking, enter
"C" for Copy, or "D" for Delete, or (beginning with beta  version
0.3) "P" for Print.

     C(opy)  will  ask  for  the new drive/directory to which the
files are to be  copied  to;   with  appropriate  error  messages
sounded  with  a  beep.   Beginning with beta version 0.3, C(opy)
will prompt for a VERIFY.  The VERIFY uses DOS's verify  function
on disk writes.  The VERIFY is either enabled or disabled for the
multiple files "marked" with the spacebar.

     NOTE:  When copying to a new drive, you can specify only the
     drive  letter.   ZIP  will  copy  the  file(s)  to  the root
     directory on that drive.

     NOTE:  When copying  to  a  new  drive/directory  or  a  new
     directory  (the  drive  letter  will  default to the current
     Login  disk  drive),  you  MUST enter a second backslash (as
     explained under the Library functions).

     D(elete) will first prompt if you really want to perform the
deletion, and then ALL the marked files will be  deleted.   There
is NO undelete function in ZIP.

     P(rint)   will   print   all   marked   files  in  sequence,
automatically doing a page eject between file printouts.  You can
embed  your  printer's  command codes into the files if you wish,
but you have to do this with a non-ZIP editor or word  processor.
ZIP performs NO formatting.

2.8     Command/File Execution

     Beginning with beta version 0.2,  ZIP  supports  the  direct
execution  of  a  file (.BAT, .COM, or .EXE) by using the cursor,
PgDn, PgUp keys to high-light  a  file  present  in  the  current
displayed directory;  and then entering "X" at the prompt.

     You  can  also enter a command as if from the DOS prompt, by
entering "I" at the ZIP  command  line  prompt.   ZIP  will  then
prompt  for  the  DOS  or  other  command  you  wish to enter.  A
carriage return,  with  no  other  keys  struck,  will  take  you
immediately out of the DOS command mode, back to ZIP.

     ZIP  will  initiate  the  command  or  execute  the file, as
follows.  The CRT will be cleared, the command or file  executed,
and then a prompt message will appear to take you back to ZIP.

     WARNING:   ZIP  uses COMMAND.COM as both a basic file loader
     (when you are using the "X"  command)  and  DOS  interpreter
     (when you are using the "I" command).  ZIP will search the
     root directories in drives F through A (starting with F)  to
     find  COMMAND.COM.   If this file is NOT there, ZIP won't be
     able to perform a DOS command.

     An error message will be generated, if it's not possible  to
execute  the  command  or  file.   This will be because:  (1) you
don't have enough memory to run ZIP and to execute the file -- in
which  you  have to Q(uit) ZIP to run that file;  or (2) the file
selected or command  entered  are  not  valid,  legal  executable
file(s)/command(s).

     POSSIBLE GLITCHES:  DOS may freeze up if there is not enough
     memory  to  execute  the command, or if the command clobbers
     memory  that  does  not  belong  to  it.   In these cases, a
     re-boot is needed.

2.9     Telecommunications

     Beginning with beta version 0.4, ZIP supports basic 300/1200
BPS  ASCII/Xmodem  telecommunications.  To enter this mode, enter
"T" at the ZIP prompt.

     NOTE:   Beginning  with  ZIP  0.63C,  ZIP will automatically
     switch to an  alternate  modem  communications  routine  for
     certain non-Hayes modems.  A brief message will be displayed
     when this occurs.

     The screen will clear, and then present  a  command  summary
for  this  mode  in  the  upper  part of the screen.  You will be
prompted for communications  parameters  to  be  set;   ZIP  will
automatically  set defaults to COM1 (communications port 1), 1200
BPS, No parity, 8 data bits, 1 stop bit, and local  echo.   Local
echo  causes everything you type to be "echoed", i.e., displayed.
Turn the local echo off or on, via function key F9, if the remote
host  computer  to  whom  you're  communicating, uses full-duplex
(i.e., the host will echo your inputs for you).

     WARNING:  For this  C  version  of  ZIP,  telecommunications
     presently  is  limited  to  COM1.   Please do not try to use
     COM2.

     The command summary is fairly clear:

  o  COLLECT TEXT allows you to capture  ASCII  (text)  files  or
     other text output from the remote host computer, into a file
     of your choosing.

  o  SEND TEXT allows you to send text files to the remote  host.
     However,  ZIP  does NOT implement "Pacing" characters in the
     mode  of  PC-TALK or QMODEM;  and will send the file as fast
     as it can.

  o  SEND  XMODEM  and  RECEIVE  XMODEM  transfers  files via the
     Xmodem/Checksum  method,  which is standard for most RBBS's.
     A  window,  set  off  in  white  on blue, will be generated,
     showing the Xmodem transaction.

  o  RETURN TO ZIP suspends the telecommunications  session,  but
     does not hang up the telephone.  You should still be on-line
     after you do whatever it was you wanted to do  in  ZIP,  and
     return to telecommunications.

  o  QUIT disables the selected COM port, and returns you to ZIP.
     You won't be on-line.

     In   order   to   incorporate   ZIP-TERM   (ZIP's   terminal
telecommunications mode), ZIP does NOT provide the full  features
of  CrossTalk,  PC-TALK, or QMODEM, or any commercially available
telecommunications program.

     You MUST use your modem's command set (such as  ATDT  <phone
number> for a Hayes-compatible modem), if you have a smart modem.
However, if you have a smart modem, an acceptable substitute  for
these  functions  is  to SEND_TEXT for the commands particular to
your modem.  For Hayes and Hayes-compatible modems, remember that
the  text file sent must NOT have an embedded line feed character
in it (i.e., decimal 10, or hex 0A), as this will be  interpreted
by the modem as a keyboard abort of the command string.

     Auto-dialing,  redialing,  hanging  up, etc., are simply NOT
supported, as are not pacing, translation, color/music  graphics,
etc.

     Color/graphics  are  supported  if your system has installed
ANSI.SYS (or equivalent), and if the remote host  is  using  ANSI
ESCape  sequences.   Music,  however,  whether or not ANSI.SYS is
installed, is simply NOT supported.

2.10    Hexadecimal Dump

     Beginning with beta version 0.5C, ZIP provides a mainframe -
style hexadecimal/ASCII dump of the current file.   The  contents
of  the file will be displayed in hexadecimal, 16 bytes per line,
plus  printable  ASCII  equivalents.   If  the  byte  cannot   be
displayed  as a printable ASCII symbol, then it will be displayed
as ".".

3.0     CREDIT WHERE CREDIT IS DUE

     The  following  describes  where some of the features in ZIP
originated.   ZIP  would  not  be  possible  except  for  various
authors,  known and unknown, who contributed their source code to
the public domain.  As a result, this  section  is  dedicated  to
selfless  programmers  (CPM and MS/PC-DOS) noted here, and to all
those who contribute to the public domain.

Windowing
---------

     Some of the windowing and  fast  pop/push  screen  functions
were  derived  from a program called WINDOW.LBR, by R.  McVay.  I
modified it considerably to make it much faster,  by  customizing
it for the IBM PC color/graphics adapter.

Directory Listing
-----------------

     The  basic  directory  function  is  a  "C"  translation  of
DIRSRCH.PAS by Jim Holtman.  ZIP's version adds sorting and  fast
display  capabilities.   While  ZIP  is  running, assuming enough
memory is available, it maintains the complete directory  listing
in memory.

Squeeze/Unsqueeze
-----------------

     The  squeeze  and  unsqueeze  functions are based on Richard
Greenlaw's "C" versions.

Library (LBR) Functions
-----------------------

     The  library  functions  are  based  on  various   assembler
versions  written  originally  by  Vernon  Buerg,  but mostly  on
Tom Jennings' LU.C.

Command/File Execution
----------------------

     ZIP uses the DeSmet built-in EXEC function.   I've  added  a
shell  around this, to search for COMMAND.COM.  Unfortunately, at
the present time, DeSmet C does not allow  me  to  read  the  DOS
environment  directly (which indicate what COMMAND.COM DOS thinks
should be used).

Telecommunications
------------------

     ZIP-TERM, ZIP's telecommunications, is based on earlier work
done by a number of individuals, including Alan Bishop.  The bulk
of ZIP-TERM is based on Phillip R.  Burns'  PIBTERM  of  January,
1985.   Mr.   Burns  designed an Xmodem protocol in Turbo Pascal,
which was adapted and heavily  modified  (i.e.,  optimized);   he
also  provided  the  Xmodem/CRC  methodology  also.  PIBTERM also
provided a VT-52 emulation, which is rather neat.  The windowing,
command  set  used  in ZIP-TERM, and ZIP interfaces are solely E.
Dong's.

     The  basic  asynchronous  communciations  interrupt  handler
routines  are  based  on a set of Lattice C callable functions to
support interrupt driven character I/O on the IBM PC,  originally
written by Curt Klinsing, which I converted to DeSmet C v2.3. The
following notes are mine.

     All data  is  in  the  code  segment,  since  ASM88  (DeSmet
assembler)  doesn't  allow  multiple segments other than DSEG and
CSEG.  Attempts to put data into DSEG fail to work, because there
is no way of setting the DS register properly via ASM88.

                                                                          
Other ZIP Functions
-------------------

     All  other  functions are solely the creation of the author,
Edward V Dong.  These are:

        o Change Directory function.
        o Screen Edit function (C and Pascal versions only).
        o Hex dump function (C versions only).
        o Full-screen Browse/View function.
        o Fast disk access.
        o Copy/Delete/Print function.

plus,   of   course,  the  total  integration  package  that  ZIP
represents.