MDIR  -	 Memory	resident DIRectory

MDIR is	a small	(assembly language based) memory resident routine
that will display directory entries. MDIR gives	both an
"automatic" mode, where	the current directory is shown sorted
alphabetically,	and a "command line" mode, where MDIR will
"screen" files (like the DOS DIR command does),	and display the
file list with your choice of sort mechanism (by date/time, name,
extension, unsorted).

This routine takes about 14k of	memory when installed, and can
make use of a second screen (if	you have both monochrome and
color/graphics installed).

This routine will put the directory on the "alternate" screen if
two monitors are available.

Usage:
	  MDIR
	   <or>
	  MDIR 2

causes MDIR to install itself in memory.

The 2 indicates	that both a color and a	monochrome monitor are
available on the system.  (MDIR	does NOT check to see if the
second monitor is actually installed.)	If you tell the	routine
that both monitors are available, the directory	will be	printed
to the monitor that is NOT currently being used.

If only	ONE monitor is installed, or if	MDIR is	executed without
the '2'	on the command line, then the directory	will be	shown on
the monitor that is currently being used.  If this is the case,
MDIR will "save" the screen currently being used, and restore it
when done.

To use MDIR once it has	been installed,	it is activated	by
pressing either	the <Alt><8> or	the <Alt><9> key combinations
together (where	the number keys	are those above	the alpha keys on
the keyboard, NOT the ones from	the numeric keypad).

If you press the <Alt><8> keys,	the directory will be displayed
in alphabetical	order. If you press <Alt><9>, MDIR will	prompt
you for	a "command line" to be used.  The command line can
duplicate a command given to the DOS DIR command.  For example:

[assume	the <Alt><9> keys have been pressed together]

	MDIR prompt		your response		   results
ÉÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍ» ÉÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍ» ÉÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍ»
command	line (/H for help):  *.*		    all	files in the current
						    directory
			     \masm\files	    all	files in the sub-
						    directory named
						    \masm\files
			     *.pas		    any	file in	the current
						    directory with the
						    extension .PAS
			     \masm\files\*.arc	    any	file in	the sub-
						    directory named
						    \masm\files	with the
						    extension .ARC
			     b:*.*		    all	files in the
						    current directory
						    on drive B:

In addition, there are several options,	detailed below,	that are
triggered by the / switch.  /H given at	the command line will list
the options.

     [options] * /A - List hidden files.
	       * /W - wait when	screen full.
	       * /R - Include directory	entries.
	       * /M - Display Modified entries only.
		 /X - Sort by extension.
		 /S - Sort by size.
		 /D - Sort by date/time.
		 /N - Do not sort, original order.
		 /H - Help - only display options.
       Default = *.* sorted by name.ext	with screen erase.
       * - Option may be combined with other options.



CAVEATS:
   1.  Because MDIR reads information from the disk, avoid
       "triggering" this utility when an operating program
       is working with the disks -- results can	be
       unpredictable (and fatal).
   2.  The code	is set up to prevent MDIR from being triggered twice
       in a row	-- a key other than the	"trigger" keys must be pressed
       between uses.
   3.  MDIR currently saves space for 256 directory entries.  If you
       need more space,	please adjust the source code.
   4.  MDIR does its best to trap floppy disk errors --	such as	an open
       door on a floppy	disk drive.  MDIR does NOT check to see	if a
       hard drive is ready.
   5.  Some software saves information in the alternate	pages of
       the video memory	IF you are using a color/graphics adaptor
       (PC-Write, for example, stores its help screens in the memory
       of the other c/g	pages).	 MDIR only saves the current video
       page, so	you can	scramble help screens when MDIR	switches
       monitors.
   6.  MDIR doesn't check if a drive has been ASSIGNed.  If you
       request a directory for drive B:, MDIR will look	for physical
       drive B:.

I've used this routine with a variety of software, including:
       Lotus' 123
       PC-Write
       PC-TALK
       TURBO Pascal

Source code (with its origins mentioned) is included in	this archive.
Please do with it what you will	to tweek it to your system/preferences.

Please let me know about any bugs/comments that	you have via
Gene Plantz' IBBS, 312-882-4227.
						     Mike Pechnyo
						     ID1206

------------------------- Changes ---------------------------------------------

    Changed use	of Interrupt 67	to 62.	(Interrupt 67 is used by the Lotus/
      Intel/Microsoft Expanded Memory device driver.  Interrupt	61 is used
      by Chris Dunford's PCED command editor.  So, I picked 62.)
    Deleted Help screen	line that referenced /E	(erase)	option.
    Deleted Help screen	line that referenced /W	(wait) option -	this is
      already done by default.
    Changed Alt-9 function to put out Help screen before prompting for
      the command line.	 Deleted /H option.
    Changed "Press any key..." routine,	when page is full, to do a CR so
      that the next line will overwrite	it.

						    Earl Hall 5-27-86
						    Plantz ID1723