ZIP File ANSI Sequence Killer
                                Version 1.2

                               July 19, 1989
























(c) 1989 Metro Consulting Group, Inc.

Authored By:  Todd A. Scalzott

              Metro Consulting Group, Inc.
              10605 Lakeside Oak Court
              Burke, VA  22015
              (703) 250-9271



What is it?

   ANSIKill is designed to remove all embedded ANSI code sequences from the
   comment fields of ZIP files -- both the individual file comments and the 
   ZIP file comment itself.

   Why remove the ANSI sequences?  Phil Katz's PKZIP and PKUNZIP programs
   display the contents of all ZIP file comments whenever they are executed.
   That is, one does not have to perform a specific function to display the
   comments.  All PKZIP and PKUNZIP functions result in display of the comment
   fields.

   As a very simple (and not TRULY validated--there would be more involved in
   reality) case, let's assume that ANSI.SYS is installed on a machine and the
   contents of a recently obtained ZIP file is to be viewed.  PKZIP is
   executed on the ZIP file and a nice and informative comment is displayed.
   So far, so good.

   Until the next command is typed in.   DIR, for example.  Surprisingly, the
   DIR command was executed when ENTER was pressed, but after the directory
   list is presented, a command of DEL *.* seems to have been typed in and
   even ENTER appears to have been pressed!  Knowing that this is NOT what
   you want to do, you answer with a "N" at the "are you sure (y/n)?" prompt.
   Surpise again!  When the letter "N" was pressed, a "Y" appeared and was
   ENTERed.  NOW what?  What happened?

   What happened was that a devious (and perhaps cruel) individual embedded a
   set of ANSI sequences within the ZIP file's comment.  The ANSI sequence
   re-mapped the keyboard.  Although this was a very simple (and not fool-
   proof) example, there are MANY other possibilities, such as automatically
   reformatting a hard disk.

   If a bulletin board was used to download the ZIP file, even the SysOp's
   machine could be at risk.  Many bulletin board systems perform a test of
   all uploaded ZIP files, thus "infecting" their own machines.

   In addition, ANSIKill will let you have control over the internal DOS file
   attributes of each file within the ZIP.  Since PKZIP was designed to be a
   total archive and compression system, it will archive all files with their
   attributes intact.  I know that it is silly, but one could archive a few
   hidden files which would remain hidden after you unZIPed them.



What does it do?

   ANSIKill removes ONLY embedded ANSI code sequences (not just keyboard
   remapping) from within the comments -- NOT the entire comment.  The textual
   portion of the comment is left intact.  ANSIKill's intent is to leave
   harmless comments untouched in the hope that they are informative.
   Hopefully those comments which do contain harmful sequences will also
   contain useful information.  Therefore, sequences are replaced with blanks.

   The main thrust of ANSIKill is two-part:  1) as stated above, comments are
   left intact if at all possible; 2) since the sequences are replaced with
   blanks (when and if encountered), there is no need to create a new ZIP
   file from the original.  Extra available disk space is not needed while
   processing and the processing time itself is greatly reduced.

   ANSIKill may also be instructed to reset the internal attributes of each
   HIDDEN, SYSTEM, or READONLY file in the ZIP.  This insures that each file 
   unZIPed will be a normal (visible) DOS file.

   There are several controls in place which are intended mostly for use by
   bulletin board sysops, but can be equally useful to the inquisitive user.
   Options are available for extended ERRORLEVEL processing, ZIP impropriety
   logging, comment logging of improper ZIPs, and automatic overrides of 
   disk errors for unattended operation.



SHAREWARE

   ANSIKill is SHAREWARE.  Please support it.  The shareware policy employed
   for this product is very simple.  If you use this product, please
   register it.  If you use this product in a commercial environment, you
   MUST register it.

   To register:
                Send a $7 donation with your name, address, phone number, and
                ANSIKill version number to:

                Metro Consulting Group, Inc.
                10605 Lakeside Oak Court
                Burke, VA  22015

   Our phone number is (703) 250-9271.   We welcome all comments, suggestions,
   and offer technical support on all of our products.

   Please make checks payable to Metro Consulting Group, Inc.  
   
   All donations of $16 or more entitle you to the next released version of 
   ANSIKill -- it will arrive in your mail shortly after it is released.



Disclaimer

   It seems that these are necessary.

   Metro Consulting Group disclaims all warranties of any kind, implied or
   otherwise, pertaining to this software.  MCG will not be liable for damages
   of any kind incurred during the use of ANSIKill.  This includes instances
   in which MCG is aware of possible damages occuring.

   There are no warranties, neither expressed nor implied.



Technical Support

   If you have a problem or question, please call us.  If you find a bug or
   have a suggestion that you think would lead to a better product, please
   call us.

   Metro Consulting Group, Inc.
   (703) 250-9271



Who Are We?

   Metro Consulting Group, Inc. is a professional and technical services
   firm located in the Washington D.C. area, specializing in areas such as
   office automation, Local Area Networks, mainframe and minicomputer software
   development, and much more.  If you are in need of computer consulting
   services, at LOW RATES please call or write for more information.

   Metro Consulting Group, Inc.
   10605 Lakeside Oak Court
   Burke, VA  22015
   Phone:  (703) 250-9271



Using ANSIKill

   To use ANSIKill is simple.  The requires only one parameter which is a 
   file specification for the ZIP file(s) to be processed.  If no parameters 
   are supplied, ANSIKill will display a brief syntax help list.

   The syntax is as follows:

          ANSIKill [switches] [filespec1] [filespec2] ... [filespecN]

   switches  -  The switches may be placed in any order, but MUST be separated
                from each other by spaces and appear prior to any filespecs.

    /B            To tell ANSIKill that it is running on a Bulletin Board
                  System.  All (A)bort/(R)etry error messages will default to
                  the answer of (A)bort.  This prevents a BBS from hanging 
                  while unattended.
    
    /C<filespec>  To tell ANSIKill to write the ZIP file comments to the file
                  denoted by <filespec> any time ANSI codes which re-define 
                  the keyboard are removed.  This is intended for the use of 
                  BBS sysops.  Writes the complete path and name of the ZIP 
                  file on one line, followed by the first 255 characters of 
                  the comment on successive lines.

    /E            To use extended ERRORLEVEL processing.  With this option
                  set, ANSIKill reports the complete status of the ZIP files 
                  processed through the DOS ERRORLEVEL.

    /H            To reset (turn off) the Hidden flag of all Hidden files in 
                  the ZIP.

    /L<filespec>  To tell ANSIKill to write to the log file filespec any time
                  either file attributes are reset or ANSI codes which re-
                  define the keyboard are removed.  This is intended for the 
                  use of BBS sysops who wish to be alerted to possible user 
                  abuses.  Writes 1 line of the form:  
                  "ANSIKill:  <message> in <zipfile> at <time>"

    /N            To reset all (necessary) files within the ZIP to those of a
                  Normal file.  (System, Hidden, and ReadOnly turned off).

    /R            To reset (turn off) the ReadOnly flag of all ReadOnly files
                  in the ZIP.

    /S            To reset (turn off) the System flag of all System files in
                  the ZIP.  This will also turn off the Hidden flag.

   filespec  -  This is the name of the file the ZIP file(s) to be processed.
                It may include a drive and directory specification as well as
                DOS standard wildcards ("?" and "*").   If no file extension
                is specified, .ZIP is assumed.  Several filespecs can be 
                specified.

                EXAMPLES:   ANSIKill C:\DOWNLOAD\JUSTGOT.ZIP

                            ANSIKill \SA?.ZIP \B*.ZIP \DOWNLOAD\*.ZIP

                            ANSIKill /B /N /CC:\USERS\BADCMTS.DAT *.ZIP

                            ANSIKill /B /N /LC:\PCB\MAIN\CALLER *.ZIP



What is AKPARM?

   You may use the DOS SET command to establish a variable in your environment
   named AKPARM which specifies parameters to ANSIKill.  This function has 
   been given quite a bit of flexibility.  It is possible, for instance, to
   specify ALL parameters including the filespecs although it is not 
   recommended since it in effect disables using options on the command line
   (since all options must appear before the filespecs).

   However, the way that AKPARM works is that it is parsed directly onto the
   command line, as if it was specified directly.  If AKPARM is set to the 
   string "/N /B" then specifying "ANSIKill /N *.ZIP" would be equivalent to
   specifying "ANSIKill /N /B /N *.ZIP" if AKPARM was not set.  There is no
   harm in doing this, but you might want to be aware of it.  Please notice
   that AKPARM takes precedence over the options specified on the command
   line.  An examples follows:

        SET AKPARM=/N /E /LC:\PCB\MAIN\CALLER
        
        (The usage "ANSIKill *.ZIP" will be interpreted as
         "ANSIKill /N /E /LC:\PCB\MAIN\CALLER *.ZIP")



What is extended ERRORLEVEL reporting?

   Normally, ANSIKill returns a DOS ERRORLEVEL of 1 (and only 1) if an attempt
   to process a ZIP file is unsuccessful.  With extended ERRORLEVEL reporting,
   many more DOS ERRORLEVEL conditions are after ANSIKills completion.  If 
   more than one ZIP file is processed (due to wildcards), then the most 
   severe ERRORLEVEL is returned.  For example, if 5 ZIPs are processed at one
   time due to wildcards and the 1st, 2nd, and 4th ZIPs contained no comments
   but the 3rd contained a valid comment and the 5th contained keyboard
   re-defines, then the errorlevel for keyboard re-defines will be returned 
   since it is the most severe.  

   ERRORLEVELs returned upon completion:
    
                        1    No comment(s) found
                        2    Valid comment(s) found
                        3    ANSI sequences removed from comment(s)
                        4    File Attributes reset
                        5    ANSI keyboard re-define sequences removed
                        6    Unsuccessful processing

   ERRORLEVEL 1 is the lowest in severity and ERRORLEVEL 6 is the highest in
   severity.



Additional Notes

   I think that ANSIKill covers almost any case that you can think of.  If you
   disagree or find a problem, PLEASE call or write.

   ANSIKill starts by searching for the each ZIP file as it is specified on
   the ANSIKill command line, expanding all wildcards.  If no matching files
   can be found, a message will appear and program execution will halt.  Next,
   ANSIKill will attempt to read the ZIP file.  If the file cannot be opened
   or is not a valid ZIP file, a message will appear and the next matching
   file (if any) will be processed.

   If a fatal error occurs while processing a ZIP file, ANSIKill will prompt
   with the ever-familiar "(A)bort or (R)etry".  This includes disk read or
   write errors, write protect errors, and hardware errors.  If the /B switch
   was specified, (A)bort will be automatically chosen in the event of an
   error.

   ANSIKill will restore the original ZIP file date AND time upon completion
   processing.  A DOS file's date and time are updated each time that it is
   modified.  ANSIKill prevents having a ZIP file dated 12/25/87 changed to
   05/25/89 simply because its comments were updated.

   If extended ERRORLEVEL processing is NOT used and ANSIKill completes
   unsuccessfully, an ERRORLEVEL of 1 will be returned to DOS.  Please note
   that when specifying multiple filespecs or using wildcards, ANSIKill will
   return an ERRORLEVEL of 1 if ANY of the files have failed.  If 10 files
   are processed and 1 file fails, an ERRORLEVEL of 1 will be returned.



For PCBOARD Sysops

   For users of ProDoor 3.0 or later, the following is an extract from a
   sample PROUTEST.BAT file:

   rem -- remove ansi escape codes from all ZIP comments
   chkpath ANSIKill %0 >>%1
   ANSIKill /B /LC:\PCB\ABUSER.LOG /N /C:\PCB\COMMENT.LOG /E %2\*
   if errorlevel 5 proecho %3 ZIP contained keyboard re-defines!
   if errorlevel 4 proecho %3 ZIP contained HIDDEN, SYSTEM or READONLY files!



   Most sysops also perform a PKUNZIP -T afterwords to insure the archive's
   integrity.


   Recommendation:  Prohibit each user from uploading unless the user is
                    currently in ProDoor.  This insures that all ZIP file
                    uploads will be tested and tath potentially dangerous
                    comments will be neutralized by ANSIKill.



MANY Thanks...

   Many thanks to:

        Rob Rosenberger for an invaluable and interesting little piece of
           INLINE code.

        Rick Welshans of The Warped Board BBS for his infinite patience,
           numerous suggestions and comments, and beta testing.

        Irve Towers of The HUB BBS for his suggestions, comments, and beta
           testing.

        Mel Douglas of Houston, TX for pointing out the bug with improperly
           terminated ANSI sequences, which version 1.2 corrects.