COMMIX NETWORK SOFTWARE CABLE/MODEM VERSION FOR MS-DOS

                                 2 OCTOBER 1987

















                                      ITRON
                             A DIVISION OF INFOTRON
                                    SUITE 116
                                130 GAITHER DRIVE
                         MOUNT LAUREL, NEW JERSEY 08054
                                  (800)423-8044
                                  (609)722-5575






                                      INDEX

     1.   INTRODUCTION

          General Description
          CNS Functions
          Files
          Manual Outline

     2.   INSTALLING CNS ON YOUR PC

          Copying CNS to Your PC Boot Disk
          Modifying Autoexec.bat
          COMMIX Network Software Menu Structure
          Setting up a Modem
          Cabling PC's Back to Back

     3.   CONFIGURING CNS FOR YOUR NETWORK

          Configuration Sub-Menu
          Printer Setup
          File Transfer Method
          File Service Access
          Serial Port Configuration
          Terminal Emulation Destinations
          Save Configuration

     4.   USING COMMIX NETWORK SOFTWARE

          Introduction
          File Transfer
          File Service
          Printer Control
          Terminal Emulation

     5.   TROUBLESHOOTING



     Hayes is a trademark of Hayes Microcomputer Products Inc.
     VT100 is a trademark of of the Digital Equipment Corporation.
     COMMIX,  COMMIX  32  and  COMMIX  Network  Software  are  trademarks of
          Infotron Systems Corporation.
     Lotus 123 is a trademark of the Lotus Development Corporation
     WordPerfect is a trademark of the WordPerfect Corporation
     IBM and IBM PC  are trademarks  of the  International Business Machines
          Corporation.
     MS-DOS is a trademark of the Microsoft Corporation.
     Leading Edge is a trademark of Leading Edge Hardware Products, Inc.
     Sidekick is a trademark of Borland International,






                                    SECTION 1
                                  INTRODUCTION


     GENERAL DESCRIPTION

     COMMIX Network Software (CNS) permanently resides in the memory of a PC
     and provides seamless and transparent COMMIX and Hayes-compatible modem
     functionality to  PC users.  CNS transfers files, manages printers, and
     performs terminal  emulation. CNS  is normally  used with  one of three
     hardware configurations:

          1)   HARDWIRE. Two PC's are directly cabled together through their
               serial communications  ports. A  printer may  be connected to
               the PC  via a  serial connection. CNS allows software written
               to communicate with parallel  printers  to  work  with serial
               printers using XON/XOFF flow control.

          2)   MODEM. A  PC communicates  with another  PC, printer, or host
               computer via a modem connection.

          3)   COMMIX 32. Several PC's, modems, printers, and host ports are
               cabled to COMMIX 32 ports. (The file READ.ME on this diskette
               will tell you more about the COMMIX 32.)

               In a  COMMIX  network,  CNS  automatically  makes  and breaks
               connections through  COMMIX to provide these services. COMMIX
               Network Software works across  COMMIX Ethernet  Links as well
               as within a single COMMIX node.

     COMMIX Network  Software resides  in the  background memory of a PC and
     will not interfere with most other PC application software. A  user can
     be working  with Lotus 123(c) or WordPerfect(c) at the same time CNS is
     transferring a database.

     COMMIX Network Software is controlled and  set  up  via  a  pop-up menu
     system. The  menus can  be accessed at any time by pressing the ALT and
     period key at the  same  time.  This  is  known  as  a  "hot  key." For
     example,  a  user  in  the  middle  of working on a spreadsheet, simply
     presses ALT-period and the  menu appears.  When the  user is  done, the
     screen and application are completely restored.

     As  menu  options  are  chosen,  new  menus  overlay previous ones. The
     ESCape key moves to previous  menus.  Pressing  ESCape  at  the initial
     menu returns to an application or DOS prompt.

     CNS FUNCTIONS

     FILE TRANSFER  -- user selects a system from the pop-up menu and a file
          to send  or receive  from that  system. CNS  makes the connection,
          transfers  the  file,  then  breaks  the  connection. The transfer
          happens in background so the user can work  on other  tasks during

                                       1-1




          the transfer. The File Server capabilities allow a user to do file
          transfers with no user intervention on the remote system.

     FILE SERVICE -- sets up your PC to permit easy file transfer  access to
          other users.  Several directories  can be set up with combinations
          of READ, CREATE, OVERWRITE,  or  NO  access.  The  actual transfer
          itself is initiated by a user on the network via the File Transfer
          options of CNS. CNS is a two-way street; it can both initiate file
          transfers and respond to transfer requests from a distant machine.

     PRINTING --  redirects all  print jobs from a parallel port to a serial
          port. If required, CNS can make a connection  through COMMIX  to a
          printer or  dial a  call to  a printer  through a modem (the modem
          must be configured for  auto-answer). It  initializes the printer,
          prints the job, then breaks the connection. The pop-up menu allows
          the user to select  from six  different printers,  each with their
          own set of configuration parameters. 

          If less  than six  printers are used, the same printer can be used
          as  several  logical  printers,  each   with   its   own   set  of
          characteristics. For example, printers DRAFT and LETTER can be the
          same  dot  matrix  printer.  When  printer  DRAFT  is  chosen, the
          initialization string  causes the  printer to  work in draft print
          mode, printer LETTER tells it  to  print  in  near  letter quality
          mode.

     TERMINAL  EMULATION  --  pops  up  an  ASCII terminal and automatically
          makes a connection through COMMIX or dials a call through a modem.
          Four predefined  destinations can  be chosen.  User can also start
          terminal emulation without making a connection or a call. 


     FILES

     There are four files on this diskette:

     CNSMC.COM --   The COMMIX Network Software program.
     CNS.CFG --     Configuration file for CNS.
     CNS.DOC --     The users manual for CNS
     READ.ME --     An quick introduction to CNS and this diskette,  as well
                    as an  introduction to  ITRON's COMMIX 32 office network
                    system.

     Section two of this manual will tell you how to install CNS on your PC.









                                       1-2





     MANUAL ADDENDUM OUTLINE

     This manual addendum is divided into five parts:

          INTRODUCTION
          INSTALLING CNS ON YOUR PC
          CONFIGURING CNS FOR YOUR NETWORK
          USING CNS consisting of information on
               File Transfer
               File Service
               Printer Control
               Terminal Emulation
          TROUBLESHOOTING







































                                       1-3




                                    SECTION 2
                            INSTALLING CNS ON YOUR PC


     There are four phases of installing COMMIX Network Software on your PC:

     1)   Copying the  software from the ITRON distribution diskette to your
          hard disk, or the floppy from which you boot your system.

     2)   Placing commands in your AUTOEXEC.BAT  file  which  places  CNS in
          memory whenever you boot your system.

     3)   Learning the CNS menu structure.


     COPYING CNS TO YOUR PC BOOT DISK

     To copy  the files  on to your hard drive or floppy from which you boot
     your PC, place the ITRON CNS  distribution disk  in one  of your floppy
     disk drives.  Then set your default directory to the directory you wish
     the CNS  files to  reside. It  doesn't matter  where you  place the CNS
     files, so  put them in a directory which suits your needs. Finally, use
     the DOS COPY command  to copy  the files  named CNS.COM  and CNS.CFG to
     the hard drive or boot disk.

     For example, to install CNS in a directory called \SYS\COMMAND on drive
     C:, place  the  ITRON  distribution  disk  in  drive  A:  and  type the
     following commands at the DOS prompt:

          C:
          MD \SYS\COMMAND     (unless directory already exists)
          CD \SYS\COMMAND
          COPY CNS.*


     MODIFYING AUTOEXEC.BAT

     Once the  CNS files  have been placed on your boot disk, you should add
     the following commands to a file called AUTOEXEC.BAT:

          CD \SYS\COMMAND
          CNS
          PATH \SYS\COMMAND

     These commands  will  place  COMMIX  Network  Software  into  your PC's
     memory whenever you start your system.

     Once installed,  COMMIX Network  Software is ready to serve you. Simply
     press the ALT-period "hot key" to activate the pop-up menu.




                                       2-1





     COMMIX NETWORK SOFTWARE MENU STRUCTURE

     The main menu shows several options.  To select  an option,  use the up
     and down arrows to move to highlight bar to the desired option. You may
     also type the first letter of the option to select it. Once  the option
     is selected,  press the  RETURN or  ENTER key  to activate it. The FILE
     SERVICE option  allows you  to enable  or disable  a feature. Selecting
     the other  features will  take you into sub-menus. Sub-menu options are
     selected and chosen in the same manner as they are in the main menu.

     To leave a sub-menu and return to a higher level menu, press the ESCape
     key. To  return to  DOS or  your application  from the main menu, press
     ESCape. If you select  an option  by mistake,  simply press  ESCape and
     you'll go  back to  the menu  from which  you selected  the option. The
     COMMIX Network Software menus and their functions are discussed in more
     detail in the next two sections of this manual.


     DOS AND MACHINE COMPATIBILITY

     The CNS  software should  operate correctly  with all 99% IBM PC clones
     running PC-DOS or  MS-DOS  version  2.0  or  later.  The  software will
     automatically support  monochrome, Hercules,  CGA, EGA and VGA displays
     while in text mode.

     The software is known to operate correctly on the following machines:
          
          IBM PC:        XT, AT, ATX
          IBM PS/2:      30, 50, 60
          Amstrad:       1512, 1640 (mouse driver not installed)
          Zenith:        Z-181, Z-183
          Leading Edge:  Model D


     The CNS software will not run  correctly if  the machines  system clock
     "tick" is  not 18.2 per second. For example CNS will not work correctly
     with the Amstrad range of machines if the mouse driver is installed.

     The software  will  NOT  normally  operate  with  the  "DOS compatible"
     operating  systems  because  the  program  may be swapped out of memory
     while communicating in the background, or the screen may be in graphics
     mode. (For  the same  reasons CNS should NEVER be swapped out of memory
     using some TSR program selectors as CNS may have a file open and serial
     data being transmitted).

     Systems to avoid include:

          PC-MOS 386
          DosMerge 386
          Microsoft Windows (1.x or 2.x)
          OS/2.

                                       2-2





     Alternate versions  of CNS  will be  available to support some of these
     other operating systems in the future. 

      
     INTERACTION WITH OTHER PROGRAMS

     The CNS software occupies less  than  40K  of  memory  when  loaded and
     provides all  the functions  outlined in  section 1.  The whole package
     must be loaded, it is not possible to selectively load functions. 

     During file transfers the CHKDSK command  must be  avoided. The program
     assumes that  no files  are currently  being accessed,  and will report
     any partially written file from CNS an error. 

          * NEVER RUN CHKDSK/F WITH CNS ACTIVE. *

     If a file is "typed" and the scroll  lock or  CONTROL-S entered  in the
     middle of  the file,  then any  current file  transfer may  fail due to
     timeouts. This will only  occur if  the screen  is held  stationary for
     more than 60 seconds.

     The CNS  software may  be loaded  with Borland's Sidekick. Sidekick, as
     usual, must be loaded last. 

     The CNS software should  coexist with  most other  popup software which
     does not access the selected serial port.


     SETTING UP A MODEM

     If you  are using  COMMIX Network Software with a modem, the modem must
     be configured to hang up the call when your PC  drops DTR.  You'll need
     to  consult  your  modem  documentation  to  see how this is done. Some
     modems (such as the Hayes 1200) require you to set  hardware switchs on
     the modem,  others (like  the Hayes 2400) allow you to set this through
     software.

     On a Hayes 2400 or full compatible you would use CNS to  enter terminal
     emulation without  dialing a  call (see section 4 for details). You can
     now enter "AT" commands directly to the modem. Then type:

          AT&D2&W <RETURN>

     This will set the modem. Then  press FUNCTION  KEY 9  to leave terminal
     emulation.


     CABLING PC'S BACK TO BACK

     If you  are connecting two PC's back to back you must use what is known
     as  a  "cross-over"  cable.   This  can   be  purchased   from  a  data

                                       2-3




     communications equipment  distributor or computer store. If you wish to
     make your own cable see the use the following instructions:

               DB-25 CONNECTOR

          Pin  3    to pin2
          Pin  2    to pin3
          Pin  7    to pin7
          Pin  6    to pin20
          Pin  20   to pin6

               DB-9 CONNECTOR

          Pin  2    to pin3
          Pin  3    to pin2
          Pin  5    to pin5
          Pin  1    to pin6
          Pin  6    to pin1



































                                       2-4




                                    SECTION 3
              CONFIGURING COMMIX NETWORK SOFTWARE FOR YOUR NETWORK


     Once you have installed CNS software on your PC, you'll  need to tailor
     CNS to  your particular network. In many instances the default settings
     will be sufficient for  your  network.  You  can  make  a  standard CNS
     configuration and  distribute it to your PC users, or you can configure
     CNS separately on each PC.

     There are seven steps to properly configuring COMMIX Network Software:

          1)   Enter the  configuration  sub-menu  of  CNS  and  perform the
               following seven steps.
          2)   Set  up  printer  name,  telephone number or COMMIX port, and
               initialization strings for each printer.
          3)   Define file transfer method.
          4)   Define file service access.
          5)   Set serial port number and speed.
          6)   Define four predefined terminal emulation destinations.
          7)   Save all  configuration settings  to a  configuration file so
               that the  settings will  be active  when you turn on or reset
               your PC.


     CONFIGURATION SUB-MENU

     Once you have drawn your  network,  you  are  ready  to  begin software
     configuration. Press ALT-period to bring up the COMMIX Network Software
     menu. Use the arrow key, or  press "C"  to select  configuration. Press
     RETURN and you'll see the configuration menu.

     Once in  the Configuration sub-menu, use the arrow keys or first letter
     of the option to select the option. Press  RETURN to  go into  the sub-
     menu for that particular configuration option.

     Once  you  are  done  configuring  select  SAVE  CONFIGURATION from the
     configuration  sub-menu  to  save  all  configuration   settings  to  a
     configuration file so that the settings will be active when you turn on
     or reset your PC.


     PRINTER SETUP

     Use the arrow key,  or press  "P" to  select PRINTER.  Press RETURN and
     you'll  see  the  printer  configuration.  For each of the six possible
     printers, there are three options to be set:

          1)   The printer name which appears in the printer sub-menu. 

          2)   The printer destination. If the printer is cabled directly to
               your PC,  leave this blank. If you are communicating with the

                                       3-1




               printer through a modem, this should be the  telephone number
               of the  modem to  which the  printer is  attached. If you are
               networking through a COMMIX 32,  this  should  be  the COMMIX
               port number or name to which the printer is attached.

          3)   The initialization  string to be sent to the printer whenever
               a print job is sent. Consult the documentation  supplied with
               the printer  to see  what these  codes are, as they vary with
               printer. Control characters  can  be  included  by  using the
               tilde (^) character before a letter. For example control-O is
               represented as ^O. The escape character is ^[.


     One physical printer can serve as several CNS printers. For  example, a
     Star(c) printer  could be  cabled to COMMIX port 12 with a port name of
     "STAR" . You could then configure two CNS printers, "STAR  DRAFT" which
     prints  on  the  Star  printer  in  draft mode, and "STAR LETTER" which
     prints in letter quality mode. Both CNS printers would send  print jobs
     to  the  same  COMMIX  port,  but  would  send different initialization
     strings to the printer.

     To select a printer to configure  enter the  number of  the printer, or
     use the  arrow to  move the  highlight bar. Press RETURN and you'll see
     the configuration options for that printer. Select an  option by typing
     its first  letter or  using the  arrows, then  press enter. You can now
     type the printer name shown on the menu,  the printer  destination, and
     the  initialization  string.  Press  RETURN  when  finished typing each
     option.

     Besides setting  up six  printers, you  can also  write a  banner to be
     printed with  each printout.  A good  idea would  be to have the banner
     different for each PC so that  printouts can  be easily  distributed to
     the requesters.  Type "B" or use the arrow to move the highlight to the
     banner option.  Press RETURN  and type  the banner  followed by another
     RETURN. If no banner is specified, then the banner page is not printed.


     FILE TRANSFER METHOD

     COMMIX Network  Software allows  you to  exchange files with another PC
     using CNS, or with another system (including PC) using the  Kermit file
     transfer protocol. You will need to configure CNS accordingly.

     Selecting FILE  TRANSFER OPTION  from the configuration menu allows you
     to set to options:

          1)   Whether to use seven or eight bit bytes during file transfer.
               If  you  are  using  a  modem  which  only  passes  seven bit
               characters, choose seven bits; otherwise, use eight bits.

          2)   Default directory for file transfers. This  is only important
               if Kermit  is calling  CNS. Since  Kermit can  not change the

                                       3-2




               remote directory, you must pre-set it in CNS.

               With CNS to  CNS  file  transfers,  you  can  set  the remote
               subdirectory with local CNS.

     Use of  Kermit programs  and terminal  emulations not  written by ITRON
     with the CNS file service is not supported and is done at  the your own
     risk.      

     Select FILE  TRANSFER OPTION  SELECTION from  the Configuration menu to
     change these settings. To  change  the  number  of  bits  select HI-BIT
     CONTROL and press RETURN to toggle between seven and eight bits.

     To  change  the  default  directory  select  DEFAULT DIRECTORY from the
     Configuration menu, press  RETURN,  type  the  default  directory, then
     press RETURN.


     FILE SERVICE ACCESS

     File Service  Access Control allows you set file transfer access to DOS
     subdirectories on your PC. This controls the access  of users  on other
     PCs. COMMIX  Network Software  will not  interfere with  your access to
     files on your PC.

     You can set access  for up  to seven  subdirectories. You  can also set
     default access  for the remaining subdirectories not specifically given
     access.  A  password  prevents  unauthorized  people   from  seeing  or
     modifying your file service access settings.

     Four levels of access can be granted:

          1)   READ ONLY  -- remote  users may  only receive files from that
               subdirectory. They cannot send to it.

          2)   WRITE ONLY -- users can send  files to  the subdirectory, but
               cannot receive for it.

          3)   READ/WRITE --  users can both send and receive files from the
               subdirectory.

          4)   NO ACCESS -- users  can neither  send nor  receive files from
               the subdirectory.

     The configuration  options for file service access is split between two
     sub-menus within the configuration menu. Menu one sets  access for four
     subdirectories; menu  two sets  access for  three menus, as well as the
     default access and the password for using the File Service  Access sub-
     menus.

     To  view  or  modify  file  service  access  select File Service Access
     Control 1 or 2 from the configuration sub-menu. After you  press RETURN

                                       3-3




     you  will  be  asked  for  a  password.  The  initial password on a new
     installation of CNS is "ITRON." You  may  change  the  password  in the
     File Service Access Control 2 menu. After entering the correct password
     you'll see File Service Access Control menu.

     To add or modify a subdirectory, select a directory, press RETURN, type
     the subdirectory name, then press RETURN. To remove a subdirectory from
     the list, select it, press RETURN, and press the space  bar followed by
     another RETURN.

     To modify  access, select  the access  option for the subdirectory, and
     press RETURN until the access you desire is displayed.

     The password for the File Service Access Control menus can  be modified
     in  the  File  Service  Access  Control  2 menu. Select Password, press
     RETURN, type the new password, and again press RETURN.

     Since the access list is always scanned from  entry 1  to entry  7, and
     the scanning  stops at  the first  match, a  very powerful file control
     system can be setup.

     For example if a user wished  to exclude  access to  all of  drive 'C:'
     except for a directory "\external" where users may read files, and
     a directory  "\external\write" where  users might read and write files,
     the following setup would be used:

          C:\external\write            Read/write access
          C:\external                  Read only
          C:                           No access

     The order is important. If the entry for "C:" was first then  the whole
     disk would be protected.


     SERIAL PORT CONFIGURATION

     The  serial  communications  port,  speed  and  dialing  used by COMMIX
     Network Software is set in the  COM PORT  SELECTION AND  SPEED sub-menu
     of the Configuration menu.

     Select  COM  Port  used,  and  press RETURN to toggle between COM1: and
     COM2: of your PC. If you  do not  know which  COM: port  to use, you'll
     need to  consult with  the person who sold you your PC or installed the
     hardware. If your PC has one serial port it is most likely COM1:.

     Select Baud Rate Used, and press RETURN to choose a  speed between 1200
     and 19,200 bps.

     The dialing  method allows  you to  tailor CNS to the type of telephone
     service your modem uses. The following options are available:

          1)   Touch-tone for telephone circuits with that capability.

                                       3-4




          2)   Pulse Dialing for those without touch-tone capability.
          3)   COMMIX port name. This is used  when your  PC is  cabled to a
               COMMIX 32 unit rather than a modem or another PC.
          4)   Disabled when you don't wish CNS to place calls.

     To choose  a dialing  method, select DIALING and press RETURN until the
     desired setting is displayed.


     TERMINAL EMULATION DESTINATIONS

     The Terminal Emulation Destinations and Terminal  Type sub-menu  of the
     Configuration  menu  allows  you  to  set auto-dial destinations. These
     destinations can be telephone numbers if  your  PC  is  connected  to a
     modem, or  COMMIX port  names or  numbers if  your PC is connected to a
     COMMIX 32. You can set up  to  four  auto-dial  destinations.  When you
     choose Terminal Emulation in the main menu, these four destinations are
     shown. You  can  then  simply  choose  one  and  a  connection  will be
     automatically dialed  through your  modem or  made through COMMIX. This
     will be explained in greater detail in Section 4 of this manual.

     The auto-dial destinations are  set  by  selecting  one  of  the preset
     destinations  in  the  Terminal  Emulation  sub-menu,  pressing RETURN,
     typing a telephone number, or a COMMIX port  number or  name, and again
     pressing  RETURN.  To  remove  a  destination from the list, select the
     destination, press RETURN,  press  the  space  bar,  then  press RETURN
     again.


     SAVE CONFIGURATION

     Once  you  have  configured  your  CNS  system  it is active during the
     current session. If you  want the  information to  be active  after you
     reset your PC or toggle power, you must Save Configuration.

     ITRON RECOMMENDS  THAT YOU  SAVE CONFIGURATION WHENEVER YOU CHANGE YOUR
     CNS CONFIGURATION.

     To Save Configuration, simply select the Save Configuration option from
     the configuration sub-menu, and press RETURN.

     The configuration is kept in a file called CNS.CFG which is in the same
     directory as the CNS  program itself.  Do not  place them  in different
     subdirectories. When  you Save  Configuration you  DO NOT have to be in
     the directory  holding CNS.COM  and CNS.CFG.  When you  first load CNS,
     normally via  commands in  AUTOEXEC.BAT during system boot, the default
     directory must be set to the directory holding these files. See section
     2 of this manual for more details.





                                       3-5




                                    SECTION 4
                                    USING CNS


     INTRODUCTION

     Now that  you've configured  COMMIX Network  Software, you are ready to
     put CNS to work. When ever you wish to use CNS, simply press ALT-period
     key. The  CNS main  menu will  pop up on your screen as shown in figure
     4-1. It will not interfere with  whatever else  you are  doing. You can
     pop it  up while  using a  spreadsheet, a  word processor, or any other
     application. You can, of course, pop it up while at the DOS prompt.

     Throughout this section, we'll  talk about  "selecting" and "choosing."
     "Selecting" means  moving the highlight bar on a menu to an option. You
     can use the up or down arrows to move the  highlight bar.  You can also
     type the  first letter of the option and the highlight bar will jump to
     it. If more than one option start with the same  first letter,  you may
     have to press the letter more than once.

     "Choosing" means  pressing the  RETURN or  ENTER key when the highlight
     bar is on the desired option.  Depending on  the option,  choosing will
     either take  you to a sub-menu, toggle a setting, or cause an action to
     occur.


     FILE TRANSFER

     File Transfer allows you to send and receive files from another PC. The
     other PC  may be connected to a modem which CNS will dial, or it may be
     part of a COMMIX network to  which your  PC is  attached. You  can also
     transfer files  between two  PC's hard wired to each other. All control
     is from the PC on which  you are  working. We'll  refer to  this as the
     "local PC."  The other  PC will  be referred to as the "remote PC," and
     must have COMMIX Network Software installed.  File access  control must
     be set on the remote PC as discussed in section 3 of this manual.

     The start  file transfer, select and choose File Transfer from the main
     COMMIX Network Software menu and you'll see the  file transfer  menu as
     shown in  figure 4-2.  Before transferring a file you need to set three
     things:

          REMOTE MACHINE -- If your  PC is  cabled to  a modem,  this is the
                            telephone number of the remote machine. If it is
                            cabled to a COMMIX  32 this  is the  COMMIX port
                            name or number of the remote PC. If two PC's are
                            directly cabled to each other, no REMOTE MACHINE
                            should be specified.

          READ FILE --      The name  of the file to transmit. The read file
                            is on the local machine if you are  sending from
                            local to  remote. It is on the remote machine if

                                       4-1




                            you are receiving from the remote and sending to
                            local.

          WRITE FILE --     The  name  the  file  is  to  have on the target
                            machine.

     You can use the asterisk as a wildcard character just as you would with
     DOS. The  question mark  can also  be used  as a  wildcard for a single
     character as it is in DOS. 

     For example you wish  to send  all files  in the  \FINANCE directory of
     your  PC  with  a  file  extension  of  ".WKS"  to  another PC with the
     telephone  number  722-1234.  On  the  remote  machine  you'd  like the
     filenames  to   have  the  extension  ".BAK"  and  be  in  the  \BACKUP
     subdirectory. 

     Set the REMOTE MACHINE to "7221234" . Set READ FILE to "\FINANCE\*.WKS"
     and the WRITE FILE to "\BACKUP\*.BAK" .

     Now you're  ready to  transmit, that  is, to send from the local to the
     remote machine. To begin the transmission, select and  choose the field
     labelled:

          Send file(s) to remote:

     A status  screen will  automatically "pop up". This screen will let you
     see COMMIX trying to  establish the  connection to  the remote machine.
     The status  screen provides  a field at the bottom that allows users to
     cancel the dial attempt. 

     Once the connection is established, a new pop-up will appear to let you
     know how  the file  transfer itself is taking place. This file transfer
     status screen will also allow  users  to  abort  the  file  transfer if
     necessary.

     When the  transfer is  complete, a  final pop-up  will appear to verify
     that the transfer was successful.

     You can receive files from the remote machine in much the same  way. To
     begin the transfer from the remote machine, select and choose the field
     labelled:

          Receive file(s) from remote:

     Again, a set of pop-up screens will appear to keep you informed  of the
     status of your transfer. 


     FILE SERVICE

     When setting up the configuration menu of CNS as described in section 3
     of  this  manual,  you  were  able  to  establish  a  series  of access

                                       4-2




     privileges (read  only, write  only, read  and write, no access) to the
     files on your PC.

     While  the  configuration  menu   allowed   you   to   establish  these
     parameters,  CNS  does  not  automatically implement them. These access
     parameters are implemented only when the File Service  field is  set to
     ENABLED. Select  this field  and press RETURN to toggle between ENABLED
     and DISABLED.

     If File Service is DISABLED,  there  will  be  no  access  available to
     remote users for files on the local PC.


     PRINTER

     The Printer  option of  CNS allows  users to  divert a printout request
     from a  parallel printer  port (LPT1,  LPT2 or  LPT3) to  a serial port
     which  could   be  connected  directly  to  a  printer  with  a  serial
     interface, to a modem which will dial a  connection to  a printer  at a
     remote location, or connected to a COMMIX 32 network.

     The printer field of the CNS menu allows users to do the following:

     1.   Define the parallel printer port (LPT1, LPT2 or LPT3) to which the
          PC typically directs printer output. 

     2.   Choose from one of  a  maximum  of  six  printers  defined  in the
          Printer Setup  field. As  explained in  the configuration section,
          the six choices can be  different  printers,  or  several printers
          with different logical names to define initialization strings that
          set different print modes or any combination of the above. 

     CNS will divert the  printed output  from the  designated parallel port
     and to divert it to the serial port named in the COM PORT SELECTION AND
     SPEED field of the Configuration menu.

     To define the parallel port from which CNS will divert data, select the
     PRINTOUT FROM:  field of the Printer menu screen. The RETURN key allows
     you to select LPT1, LPT2 or LPT3. If you want  to keep  CNS active, but
     disable the printout diversion, choose DISABLE.

     If the  feature is enabled, select and choose the logical printer name,
     from the list of six, to which you want CNS  to redirect  the printout.
     Once users  choose the  printer, the DIVERTED TO: field should indicate
     the change. To double check that CNS recognized the change,  go back to
     the Main  CNS screen.  The PRINTOUT  FROM: and  the DIVERTED TO: fields
     should show the same selections as the printer menu screen. 

     The COMMIX Network Software printer setup required is simpler than that
     for DOS (no need to use the DOS MODE command). Only three wires need be
     used: transmit and receive data and ground. None  of the  control lines
     need be  connected on  the IBM,  and the  printer should  be set up for

                                       4-3




     XON/XOFF (DC1/DC3) software flow control.


     TERMINAL EMULATION

     The terminal emulation menu causes  your  PC  to  emulate  a  DEC VT100
     terminal via one of three services:

     1.   Select  one  of  the  four destination addresses that were entered
          into the  program  in  the  Preset  Dial  Numbers  section  of the
          Configuration menu. 

     2.   Define and connect to a temporary destination address. 

     3.   Have  your  PC  enter  terminal  mode  with  no preset destination
          address.

     To access the Terminal Emulation menu,  select and  choose the TERMINAL
     option of the main CNS menu. The Terminal menu screen will appear. This
     screen will display the destination addresses (up to  4) stored  in the
     configuration menu. This screen will also display the fields that allow
     you to define and  connect to  a temporary  destination and  to go into
     terminal emulation mode without defining a destination.

     To connect  to one  of the  stored destinations, just select and choose
     the destination address to which you  would like  to connect.  CNS will
     display another  pop-up screen which will display status information as
     CNS attempts to make the connection. The display  allows you  to cancel
     the connection request simply by entering RETURN.

     The CNS program allows users to define a temporary destination address.
     This feature is when you  want  to  request  connection  to  a specific
     destination several  times during  the course  of a day but will not be
     connecting to the destination often enough  to warrant  it being placed
     in the CNS configuration file. 

     To  enter  the  temporary  destination,  select  and  choose  the  TEMP
     DESTINATION field of  the  Terminal  Emulation  pop-up.  CNS  will then
     display a  window that allows users to enter the temporary destination.
     The destination may be a maximum of 18 alphanumeric characters and is a
     telephone number or COMMIX port name.

     Once the  temporary address  is placed in CNS, you can connect to it by
     selecting and choosing the Connect to  Temp field.  Once this  field is
     chosen, CNS  will deal  with the connection request in exactly the same
     way as it does for permanently stored destinations. 

     You can also turn your PC  into  a  VT100  compatible  terminal without
     connecting to  a pre-defined  destination by selecting and choosing the
     Direct Terminal (No Dial) field. 

     Once your PC is  in terminal  emulation mode,  the monitor  screen will

                                       4-4




     clear and  a bar will appear across the bottom of the screen giving you
     three special options:

     1.   DISCONNECT AND  EXIT. Pressing  Function Key  9 causes  a modem or
          COMMIX 32  connection to  be broken, CNS leaves terminal emulation
          and returns to the main CNS menu.

     2.   Break the  connection  but  stay  in  terminal  emulation  mode by
          pressing Function Key 10.

     3.   Hold. Pressing  Function Key  5 will  toggle between screen scroll
          and no screen scroll.

     You PC's keys will act like those of a VT100 in the following manner:

          VT100 KEYPAD KEYS             PC KEYS

          1 through 9                   Keypad 1 through 9

          Function keys 1 through 4     Function keys 1 through 4.

          Arrows                        Arrows

          Minus                         Minus

          Comma                         Keypad asterisk

          Period                        Period

          Enter                         Keypad Plus























                                       4-5




                                    SECTION 5
                                 TROUBLESHOOTING


     GENERAL CONCERNS

     This section will describe several potential difficulties you  may have
     using COMMIX Network Software and will tell you how to solve them. Most
     often these problems are caused by improper configuration of CNS.

     Here are some general settings you should check before going  into more
     detailed troubleshooting:

     1)   Make sure  that CNS is set to the proper speed for the devices you
          are using, such as printer or modem (COM Port Selection  and Speed
          sub-menu of the configuration menu). 

     2)   Verify that  CNS is  using the  proper COM port of you PC, such as
          COM1: or COM2: (COM  Port  Selection  and  Speed  sub-menu  of the
          configuration menu).

     3)   If you  are communicating  with another  PC verify that it is also
          using a properly configured CNS.

     4)   If you are cabled directly to another PC,  use a  cross-over cable
          as discussed in section 2 of this PC.

     5)   Verify that  your modem is a Hayes-compatible modem using the "AT"
          commands and is properly configured to operate with  your PC. (See
          modem documentation.)


     MENU DOESN'T POPUP WHEN YOU PRESS ALT-PERIOD

     Check your AUTOEXEC.BAT file. The first set of commands should load CNS
     as described in section  2 of  this manual.  CNS should  be loaded into
     your system before any other memory resident utilities.

     If CNS  'beeps' when you press alt-period then CNS is correctly loaded,
     but is  unable to  popup. There  are two  common reasons  for this: the
     operating system  is busy  (e.g. a  disk format), or graphics are being
     displayed.


     WON'T DIAL CALLS

     Verify the dialing procedure  is correct  for your  application (touch-
     tone,  pulse,  COMMIX  port  name).  See  section  3 of this manual for
     details.

     Verify that your modem is configured properly for  your PC.  Check your
     modem documentation for more details.

                                       5-1






     GARBAGE PRINTED ON PRINTER

     If operating via direct wire or modem, verify that CNS and your printer
     are operating at the same speed, and that the printer is set  for eight
     bits, no  parity, 1 stop bit. If you are going through COMMIX 32, speed
     and parity conversion will be performed. 

     Consult your printer manual to see if any special initialization string
     must be  sent to  the printer.  If this is so, place this string in the
     INIT STRING printer parameter of CNS as described in section  3 of this
     manual.


     WON'T TRANSFER FILES

     CNS must  be operating  in both  PC's. If  you are  operating through a
     modem, the REMOTE MACHINE NAME must  be  the  telephone  number  of the
     modem cabled to the remote machine.


     NOTHING HAPPENS OR MUTILATED DATA IN TERMINAL EMULATION

     If operating  via direct  wire or  modem, verify  that CNS and the host
     machine are operating at the same speed, and  that the  host machine is
     set for  eight bits,  no parity,  1 stop  bit. If you are going through
     COMMIX 32, speed and parity conversion will be performed. 


     LARGE LETTERS FAIL TO APPEAR ON PRINTER BANNER

     If the printer banner appears as six lines of your banner text in small
     letters then CNS has failed to find the character generator tables used
     by the machines. This should only happen on poor "clones" of the IBM PC.


















                                       5-2