DDDDSSSSZZZZ((((1111))))                XXXXEEEENNNNIIIIXXXX SSSSyyyysssstttteeeemmmm VVVV ((((OOOOMMMMEEEENNNN))))                DDDDSSSSZZZZ((((1111))))



     NNNNAAAAMMMMEEEE
          dsz - YMODEM, ZMODEM PC-DOS file transfer subprogram

     SSSSYYYYNNNNOOOOPPPPSSSSIIIISSSS
          ddddsssszzzz [CCCCOOOONNNN] [ppppoooorrrrtttt NNNN] [ssssppppeeeeeeeedddd SSSS] [dddd] [rrrreeeessssttttrrrriiiicccctttt] _c_o_m_m_a_n_d

     DDDDEEEESSSSCCCCRRRRIIIIPPPPTTTTIIIIOOOONNNN
          _D_s_z uses the YMODEM or ZMODEM error correcting batch
          protocol to transfer files over a serial port with a variety
          of programs.  _D_s_z is designed to be called from a
          communications program or bulletin board to perform file
          transfers.

          _D_s_z uses its own modem I/O.  The original interrupt vector,
          UART interrupt configuration, and 8259 interrupt mask are
          restored on exit.  The March 1987 version buffers both
          transmitted and received data, providing enhanced throughput
          with multi taksing systems such as DESQview.

          _D_s_z uses DOS standard output for messages, it does not write
          directly to the screen.  _D_s_z expects its standard output to
          point to the console, a logging file, or NULL, not the modem
          port.  It may be redirected to the console device with the
          CCCCOOOONNNN command.

          _D_s_z exits with 0 status for successful transfers, 1 if the
          file transfer failed.

          The available commands are:

          CCCCOOOONNNN  Redirect message output to the DOS "CON" (console)
               device, overriding any previous redirections.
          ppppoooorrrrtttt NNNN
               select port N (n = 1,2,3 or 4) Default is port 1 (COM1)
               or read from the DDDDSSSSZZZZPPPPOOOORRRRTTTT dos environment variable.
          ssssppppeeeeeeeedddd SSSS
               Set specified speed, default is the port's current
               speed.
          dddd    Disables carrier dropout monitoring, for modems that do
               not properly drive the "Data Carrier Detect" input on
               the PC.
          LLLLAAAARRRRGGGG Convert AAAARRRRGGGG to lowercase, then parse aaaarrrrgggg....
          ppppxxxxNNNN  Set a numeric parameter xxxx to N.  These parameters
               correspond to the Pro-YAM or ZCOMM "zmodem" parameters
               and rarely need changing.  These parameters assume
               their defaults each time _d_s_z is called.
          rrrreeeessssttttrrrriiiicccctttt
               Restrict pathnames to current disk and directory tree.
          sssszzzz   [-Vabnpr+y] [PREFIX=p | ONAME=n] afn ...
          ssssbbbb   [-Vk] [PREFIX=p | ONAME=n] afn ...
          rrrrzzzz   [-Vabnpr+y]
          rrrrzzzz   [-Vabnpr+y] file1 file2 ...  (filename override)



     Page 1                                          (printed 3/15/87)






     DDDDSSSSZZZZ((((1111))))                XXXXEEEENNNNIIIIXXXX SSSSyyyysssstttteeeemmmm VVVV ((((OOOOMMMMEEEENNNN))))                DDDDSSSSZZZZ((((1111))))



          rrrrbbbb   [-Vab+y]
          rrrrbbbb   [-Vab+y] file1 file2 ...  (filename override)
          ----VVVV   Dsiplay debugging information.  More V's give more
               detailed information.

     EEEEXXXXAAAAMMMMPPPPLLLLEEEESSSS
          dsz sz -r b:zcom*.arc c:foo.bar

          dsz port 2 speed 19200 restrict rz

          dsz  rz  -y newprog.arc   (single file with pathname
          override)
          DSZ LRZ L-Y NEWPROG.ARC   (command line forced to upper
          case)

     SSSSEEEEEEEE AAAALLLLSSSSOOOO
          Consult the Professional-YAM or ZCOMM manual chapter
          "Options for File Transfers" for option meanings.  The "File
          Transfer Basics" chapter explains the relative merits of the
          XMODEM, YMODEM, and ZMODEM protocols.  The "Main Commands"
          chapter describes the rb, rz, sb, and sz commands.

     NNNNOOOOTTTTEEEESSSS
          _D_s_z sets the UART shift register to 8 bits no parity; the
          original parity setting (if different) is not restored on
          exit.

          32 bit CRC code courtesy Gary S. Brown.

     FFFFIIIILLLLEEEESSSS
          ZCOMMDOC.ARC, ZCOMMEXE.ARC, ZCOMMHLP.ARC, ZMODEM.ARC

     LLLLIIIICCCCEEEENNNNSSSSEEEE
          _D_s_z is written by Chuck Forsberg.  _D_s_z may be freely used
          and copied, but not modified or sold without the written
          permission of Omen Technology Inc.  As a courtesy to the
          author, bulletin board systems using _d_s_z are requested to
          feature the ZCOMM files (ZCOMMEXE.ARC, ZCOMMDOC.ARC,
          ZCOMMHLP.ARC) for unrestricted downloading.
















     Page 2                                          (printed 3/15/87)