TALKCOM

INTRODUCTION - 

   TALKCOM   is  a communications program  that   can   transmit, 
 receive,  and  capture received data for saving on a disk  file.  
 It  will  function  in both attended  and  unattended  modes  of 
 operation.

   TALKCOM  accepts  command  input from  the  keyboard  or  from         
 previously set up macro files. This allows repeated execution of 
 processes by simply executing the macro file.
 
   TALKCOM  macro  files are "keypressed" files for  the  TALKCOM 
 program.  Macro  files may contain menu  selections,  send  file 
 commands  and data to be sent to the modem.  They may be started 
 from the DOS command line by passing the macro file name as  the 
 first parameter or by the X menu selection.


FEATURES.

     - Menu driven.
     - Execution of TALKCOM macro files.
     - Send / receive either ASCII or XMODEM files.
     - Terminal emulations including user defined.
     - Execute DOS commands from within TALKCOM.
     - Set the time of day to execute.
     - Flow / timing control of send files. 
     - Host mode for remote dial in.

FILES INCLUDED ON THE DISTRIBUTION DISKETTE.

     TALKCOM.EXE    TALKCOM program file.
     SCRLOOK.COM    Support program for using screen input forms.
     TALKCOM.DOC    documentation file (this file).
     INCOLOR.EXE    program  which allows the user to change  the 
                    background   and  foreground  colors  of  the 
                    TALKCOM program.
     *.EMU          All  files  ending with a file  extension  of 
                    EMU  are  terminal  emulation  files.  Files 
                    included are:
                     VT52     - Digital Equipment VT52.
                     VT100    - Digital Equipment VT100.
                     DG210    - Data General Dasher 210.
                     DP8220   - Data Point 8220.
                     CDC75X   - Control Data 752 x/y positioning
                     DUMMY    - TTY mode.

GETTING STARTED.

     1. Make  a work copy of the TALKCOM  distribution  diskette. 
        This  can  be  done  using  "DISKCOPY".   Refer  to  your 
        operating system manual on the use of "DISKCOPY".


     2. To start TALKCOM type:
         
          A>TALKCOM(cr)

       This will bring up the TALKCOM command screen shown on the 
       next page,  for a definition of each of TALKCOM's commands 
       refer to the TALKCOM command section of this document.

       If you do not like TALKCOM's screen colors,  then you can 
       change them using INCOLOR. Refer to the INCOLOR section of 
       this document for instructions in the use of INCOLOR. 

     The simplest way to use TALKCOM is by running TALKCOM in TTY 
     terminal mode. 

          1. Set the baud rate,  if necessary.  (Default is  1200 
             baud, 8 data bits, no parity, com port 1).
          2. Connect to host system. 
          3. Enter terminal mode. (TALKCOM command option T).

     Refer  to  the reference section for additional  information 
     about terminal mode operations.



                        TALKCOM SCREEN
________________________________________________________________
|                    TALKCOM  VERSION X.XX                      |
|                                                               |
|    File  Selections              Execution  Selections        |
|                                                               |
| S  Send a File                X  Execute Batch Command File   |
|                                                               |
| R  Receive a File             T  Terminal Mode                |
|                                                               |
| P  Print a File               V  View Flag           FALSE    |
|                                                               |
| O  Open Terminal Save File    B  Set Baud Rate                |
|                                                               |
| C  Close Receive/Save File    D  Use Auto Dial Modem          |
|                                                               |
| Y  Erase A File               M  Enter Emulation Mode         |
|                                                               |
|    Misc Selections            U  Run DOS Command Line         |
|                                                               |
| F  Add Form Feed to Save File H  Enter Host Mode              |
|                                                               |
| I  Set Time of Day to Delay to                                |
|                                                               |
|                                                               |
| E  Return to DOS(Reset Modem) N  Return to DOS(No Modem Reset)|
|                                                               |
|_______________________________________________________________|


TALKCOM MENU COMMAND SET. 

  Each  of the menu commands are invoked by specifying  a  single 
character i.e., S for send, R for receive.
  
1. File Commands.

   a. Send a File.
    
     S - Send  a file to the connected host system.  This command 
         requests  a file name  be specified,  and type  of  file 
         transfer  to  use  (XMODEM,   XMODEM  - CRC,   ASCII  or 
         INCLUDE).   TALKCOM's  INCLUDE  files  are  ASCII  files 
         included  in a TALKCOM macro file.  If ASCII or  INCLUDE 
         transfer type is selected, then the data lines (a string 
         of  characters  terminated by a carriage return  /  line 
         feed)  may  be sent under control of TALKCOM 's  control 
         characters. TALKCOM control characters are the following 
         special characters placed in column 1.

                                  *** note ***

         Send  file  control characters \  (BACKSLASH),  {  (LEFT 
         BRACE)   and   ~  (TILDE)  are   included   for   upward 
         compatibility  from  TALKCOM  version 1.  All  of  their 
         control  functions  may be accomplished by  |  (VERTICAL 
         LINE) procedures.

          '\' - The    BACKSLASH    character   tells  the   send 
                procedure   to close  the current  terminal  save 
                file.    If   the  BACKSLASH  is  followed  by  a 
                character string,  a new terminal save file  will 
                be   opened  with  the  name  specified  by   the 
                character string.

                  \(cr) Close the open terminal save file.
                  \file.abc(cr)  Close  the open save  file,  and  
                                 open "file.abc".

                These control functions may also be  accomplished 
                by  |MENU  C  and |MENU Ofile name vertical  line 
                procedures.

          '{' - The   LEFT  BRACE   character   tells  the   send 
                procedure  to  change  the  pace  string  to  the 
                character(s)   following  the  BRACE.   The  pace 
                string  is the character string the PC will  wait 
                for  before  executing the next line of the  send 
                file.  Everything between the  LEFT BRACE and the 
                terminating carriage return are part of the  pace 
                string you are specifying.

                  {:  (cr)  Change  the pace  string to
                            COLON-SPACE-SPACE 
                  {?(cr)    Change  the  pace string  to  ?
                  {//(cr)   Change   the  pace  string   to 
                            SLASH-SLASH. 

                This control function may also be accomplished by 
                |REPEAT WAIT string.

          '~' - The   TILDE  character  encountered in your  send 
                file  tells  TALKCOM to save a special  character 
                string  to the terminal save file.  This  may  be 
                useful  in  controlling  printer  functions.  The 
                following  example  will  cause the  text  to  be 
                printed in enlarged print on an Epson printer :

                  ~14 "MY NAME" 13 10

                  The 14 specifies enlarged print.
                  The  "MY  NAME"  specifies the text  string  to  
                  print. The quotes are required.
                  The 13 specifies a carriage return.
                  The 10 specifies a line feed.

                This control function may also be accomplished by 
                |WRITENR  or |WRITE n "string" n n.  The  example 
                above would look like :

                  |WRITENR 14 "MY NAME" 13 10
                           OR
                  |WRITE 14 "MY NAME" 
              
          '|' - The VERTICAL LINE character indicates to  TALKCOM 
                that  a  standard  send file  procedure  will  be 
                executed. Vertical line procedures should be used 
                in  favor of the special characters listed above. 
                Future releases of TALKCOM will not support those 
                other characters.

                For  a  detailed  description of each  of  the  | 
                VERTICAL  LINE procedures refer to the SEND  FILE 
                section below.

   b. RECEIVE.

      R - Receive a file  from the connected system. This command 
          requests  a  file  name   be  specified,  and  type  of 
          protocol to use (XMODEM - CRC,  XMODEM or ASCII),  then 
          opens the  file at  the PC.

            If the file transfer protocol was specified as ASCII, 
          then the receive command will wait a number of  seconds 
          before starting the time-out counter. If no   character 
          is  received in a given amount of  time from the  host, 
          the receive command is  terminated.  The receiving file 
          stays open at the  PC. The file may be closed by a  'C' 
          (CLOSE)  command, a '\' (BACKSLASH) within a send  file 
          or  returning  to  DOS. By leaving  the  receive  open, 
          multiple  system  files may  be appended  to  the  same 
          ASCII file.

            If  XMODEM  file transfer was specified,  it  follows 
          XMODEM protocol by sending a NAK.  The XMODEM  protocol 
          uses a checksum for error checking.

           If XMODEM - CRC  file transfer was specified,  then it 
          follows  XMODEM - CRC protocol by sending a  "C".  This 
          protocol uses a 16 bit CRC for error checking.
           

   c. OPEN. 

      O - Open  a  terminal save  file.  This command requests  a 
          file  name and  then writes all characters sent  to  or 
          received  from the  connected host into the  file  name 
          specified.  This  terminal  save file is  used  by  the 
          RECEIVE, SEND and TERMINAL commands.  The terminal save 
          file stays open until  closed by a 'C' (CLOSE) command, 
          a '\' (BACKSLASH) is encountered in the send file or  a 
          return  to  DOS. Capture mode may be turned  on/off  in 
          terminal mode by pressing Ctrl Y.
     

   d. CLOSE. 

      C - Close  the  currently  open terminal  save  file.  This 
          command  writes  the  internal PC  buffer  holding  the 
          received data to the open disk file and then closes the 
          file.


   e. PRINT.

      P - Print a named file.   This command requests a file name 
          and  then  prints  the specified file(s)  on  the  line 
          printer.   DOS  "WILDCARD"  characters are  valid  when 
          specifying  the file name.  The print command sends  an 
          escape  sequence  of  "esc  C B esc N Ctrl  C"  to  the 
          printer first.  This escape sequence causes an EPSON or 
          compatible printer to sets the form length to 66  lines 
          and skip over perforation to 3 lines.


   f. ERASE. 

      Y - Erase  a named file.   This command erases a  specified 
          file(s)  from the disk.  DOS "WILDCARD" characters  are 
          valid when specifying the file name.


  2.  EXECUTION COMMANDS.

   a. BATCH EXECUTE COMMAND.

      X - Execute a macro command file.  This  command requests a 
          file name,  reads TALKCOM commands from the named file, 
          and  executes  them  as if they were  coming  from  the 
          keyboard.  Parameters  may be specified along with  the 
          file  name.  These parameters are loaded as if  entered 
          from  the  DOS command line.  In the case  of  multiple 
          command  files,  when command file 1 calls command file 
          2,  control  is  passed to command  file  2.  For  more 
          details  about  macro  files refer to the  MACRO  FILES 
          section below. 

   b. TERMINAL MODE.

      T - Enter  terminal mode.   This command puts  the PC  into 
          terminal  mode.   When  connected  to a  host,  the  PC  
          functions as a terminal,  either as an emulated type or 
          TTY if no emulation was specified. If there is an  open  
          terminal  save   file,  both  the   characters/commands  
          entered  from  the keyboard and the data received  from 
          the host system are saved in the file.

            If  the terminal mode is not an emulated  type,  then 
          there are special control codes enabled. They are :
               Ctrl A  - This aborts terminal mode and returns to 
                         the TALKCOM's main menu.  
               Ctrl C  - This aborts TALKCOM and returns to DOS. 

                                       *** NOTE ***
                         The Ctrl A and Ctrl C control codes work 
                         as   described   within   most   TALKCOM 
                         commands.

               Ctrl E  - Toggles echo to the screen on and off.    
               Ctrl K  - Sends a break to the connected system.
               Ctrl L  - Clears the local display screen.
               Ctrl O  - Allows  any character to be sent to  the 
                         connected system.  In example, to send a 
                         Ctrl  A to the connected  system,  first 
                         you must press Ctrl O then Ctrl A.
               Ctrl P  - Toggles  parallel  print  to  the  local 
                         printer on and off.
               Ctrl Y  - Toggles capture mode on and off.

            If  the terminal mode is not an emulated  type,  then 
          the command stack and line editor are also in  enabled. 
          The  command  stack  contains  the  last  ten  commands 
          entered  from  the keyboard. They may  be  recalled  by 
          pressing  the down arrow or up arrow cursor  keys.  The 
          commands   recalled  may  be  edited  before   pressing 
          carriage  return.  The edit keys are  Home,  End,  left 
          arrow, right arrow, back space, insert and delete.
   c. VIEW FLAG. 

      V - Toggle the view flag.   This command sets the view flag 
          to  either  TRUE or FALSE.   The view flag is  used  in 
          conjunction  with  the 'S' and 'R' (SEND  and  RECEIVE)  
          commands.  When the flag  is  TRUE  and 'R' is  active, 
          then  all received  characters  are  displayed as  they 
          are  received.  When  the flag is TRUE and 'S'  active,  
          all   characters both sent and received are  displayed. 
          The view flag only applies to ASCII file transfers.

   d. BAUD RATE.

      B - Set   baud   rate.   This  command will ask  for  modem 
          parameters to be entered. Selections available are :

           1.  300 baud,   7 bits,  1 stop bit, even parity, echo  
               on,  com port 1.
           2.  1200 baud, 8 bits, 1 stop bit, no parity, echo on,          
               com port 1.
           3.  Manual selections of baud rate, parity, stop bits, 
               echo, and com port. 
           4.  2400 baud, 8 bits, 1 stop bit, no parity, echo on,          
               com port 1.
 
   e. AUTO-DIAL.

      D - Dial  a  HAYES  or  compatible  auto-dial  modem.  This 
          command  requests a  modem command  line which will  be  
          sent to the HAYES SMARTMODEM.  Refer to the HAYES modem 
          handbook   for  more  detail on  the  specific  command 
          structure. If a "NO CARRIER" is detected, then the DIAL 
          command will retry the modem command line until  either 
          "CONNECTED"  is detected or you abort the retry process 
          with  a Ctrl-A.  The DIAL command forces a modem  reset 
          before  dialing.  You  should set  the  DTR  signal  to 
          "following", not "forced".

   f. TERMINAL EMULATION MODE.

      M - Prepare for terminal emulation mode. TALKCOM's terminal 
          emulation  works  through lookup tables.  The  terminal 
          emulation  files are values which are read  into  these 
          lookup tables.  There are four lookup tables,  they are 
          called receive,  receive-escape, send, and send-escape. 

          For more details about the structure of emulation files 
          refer to the section EMULATION FILES below.

   g. RUN DOS COMMAND LINE.

      U - TALKCOM requests and executes a DOS command line.  This 
          command  line  may  be almost any command that  can  be 
          entered  from  the DOS command prompt.  There  must  be 
          enough  memory  available  for  both  TALKCOM  and  the 
          program requested to coexist.

   h. ENTER HOST MODE.

      H - Place TALKCOM into Host mode. Host mode allows a remote 
          PC or terminal to dial in and execute functions on  the 
          Host mode machine. These functions are :

           (E)xecute  - Execute  a DOS command line.  This can be 
                        any   DOS  command  line  which  can   be 
                        redirected  using DOS's  I/O  redirection 
                        features.

           (F)iles   - Display  files menu.  Functions  from  the 
                       files menu are :

                        (T)ype     - display a file.
                        (L)ist     - display  a list of files  on  
                                     current log disk.
                        (D)ownload - Send a file to the remote PC 
                                     using either XMODEM or ASCII 
                                     protocol.  Must  have 8 data 
                                     bits set to use XMODEM.
                        (U)pload   - Receive  a  file  from   the 
                                     remote   PC   using   either 
                                     XMODEM or ASCII protocol.

           (L)og off - Terminate  the session.  Log off Host  and 
                       free up telephone line for next caller.

           (M)essage - Send  a  message  to  Host  operator.  The 
                       message is displayed on the Host console.

          To execute a Host function from the remote PC, type the 
          letter shown in () parentheses.  

          TALKCOM  Host mode will request a file name to be  used 
          as  a log file of all transactions done by remote PC's. 
          If you enter a legal file name then a log will be kept. 
          If just a carriage return is entered,  then no log file 
          will be kept.  If a ",time" is appended to the log file 
          name  then  HOST mode will end execution at the  "time" 
          specified.  This is only true if no one is logged in at 
          that time.
            
            013186.TCL,03:00
            LOGFILE.TCL,03

          Both examples above would try to end HOST mode at 3  in 
          the  morning.  If someone was logged in at 03:00,  then 
          the  first example would not complete.  In  the  second 
          example execution would end if someone was logged in at 
          03:00  but  logged off by 04:00.  This is  because  the 
          "time" is specified as a mask.

          There  must  be a file by the name of "TALKCOM.USR"  on 
          the current logged directory when a remote PC dials in. 
          A user name,  password will be requested of the  remote 
          user.  This  is a single line entry and may be anything 
          from 1 to 80 characters.  The line of the file and  the 
          line entered must match exactly including cases.  
 

 3.  MISCELLANEOUS COMMANDS.

   a. FORM FEED.

      F - Save a form feed  character.    This allows a form feed 
          or  top-of-form  character  to  be  inserted  into  the 
          terminal save file.

   b. TIME-OF-DAY.

      I - Set   time-of-day   delay  to   specified   time.  This  
          command    requests  the   time  of  day  to   continue  
          processing   this   command  file.  Execution  of  this 
          command  file   will be suspended until the   specified 
          time  of  day  is equal to the   system  time.   It  is 
          important for the system  time to be  correct for  this 
          command to function properly.

   d. END.

      E - End  TALKCOM  and return to DOS.   This command flushes 
          the  PC buffer to the current save file and resets  the 
          modem before returning to DOS.  

   e. END.

      N - End TALKCOM and return to DOS without a modem reset. If 
          the modem in on-line it will remain so if this  command 
          is use.

      Z - Special command used to turn off the menu displays when 
          executing  from  a macro file.  The first time a  Z  is 
          encountered   in  a  macro  file  all   menu   displays 
          requesting  operator  input will be turned  off.  If  a 
          second Z is encountered in a macro file,  then the menu 
          displays will be turned back on.  Reaching the end of a 
          macro  file  will also turn the menu displays back  on. 
          The  Z  command is the only macro command that  is  not 
          also a main menu command.  If Z is the first command in 
          a  macro  file,  then it is possible to run  a  TALKCOM 
          macro  file and never have any screen activity with the 
          user.  

TALKCOM's Variables, Expressions and Standard Functions.

1. Variables.
   
   a. String Variables

      There  are 32 (%0 thru %31) string variables available  for 
      use  within a TALKCOM session.  They are  initially  loaded 
      from  the the DOS command line in the same manner as  DOS's 
      batch  command files.  These variables may be set using the 
      "|SET" send file procedure or on the file name line of menu 
      selection X. The variables are identified in a TALKCOM send 
      file as "%g", where g is a number from 0 to 31.

      These  string variables may be used anywhere in a  send  or 
      macro  file,  except as a label identifier in the  "|LABEL" 
      statement. |LABEL |%2 would not be a useful statement.


   b. Counter Variables

      TALKCOM  has 32 counter variables(C0 thru C31).  These  are 
      integer variables and may be used as counters or numbers in 
      an integer expression.  The send file procedure |SET Cx may 
      be used to change the counter's value. The counters are set 
      to zero when TALKCOM is loaded. 


2. Expressions.

     TALKCOM  expressions  are operands combined by operators  to 
     give a integer result.  All operands must be integer.  Valid 
     operators include +,  -,  *,  /, OR and AND. Parentheses and 
     precedence are observed. The final integer result must be in 
     a   range  of  between  32767   and   -32767.   Intermediate 
     calculations are done with real numbers, so integer overflow 
     is  not  a problem.  All division operations are  done  with 
     integer  division.  This  includes intermediate  operations. 
     Division results will be the largest integer value.

     Examples 
       3+5*7 = 38
       (3+5)*7 = 105
       123 + 255 = 378
       123 - 23 = 100
       132 * 4 = 528
       123 / 4 =  30 
      -123 / 4 = -30
       127 OR 128 = 255
       127 AND 128 = 0


3. Standard Functions.

   a. Description.

      When  a  line  is read from either a TALKCOM send  file  or 
      macro  file,  the  line is checked for the function  symbol 
      (|%),  this  may be read as "the value  of".  The  function 
      symbol  and  function  identifier will be replaced  by  the 
      result of the function. Functions may be called recursively 
      and are evaluated from right to left.


   b. Standard Function Syntax.

      |%n

      This function returns the value of string variable n.  N is 
      a integer value.
       
        |SET %29=1234SX
        |ECHO %29 EQUALS |%29.
        

      |%Cn

      This function returns the value of counter variable n. N is 
      a integer value.
        
        |SET  C1 = 1
        |ECHO C1 = |%C1
        |SET  C1 = (|%C1 * 8) + 1
        |ECHO C1 SHOULD EQUAL 9. C1 = |%C1.
       

      |%|%

      This function recursively calls the function  parser.  This 
      function  may  be  used  to indirectly  identify  a  string 
      variable, as shown below. 

        |SET C1=31
        |LABEL TOP OF LOOP
        | ECHO STRING VARIABLE |%C1 = |%|%C1.
        |LOOP C1 NE 0 TOP OF LOOP

      The  example  above  would  display  the  value  of  string 
      variables 31 thru 1.


      |%ADDR

      ADDR  returns  a  string  containing  the  starting  memory 
      address of the variable block.  The format of the string is 
      segment: offset. Segment and offset are decimal values. The 
      variable block is laid out : 

         string  variables 0 thru 31
         counter variables 0 thru 31

      The  ADDR  function's  primary use  is  to  allow  external 
      programs to accept and return variables from a TALKCOM send 
      file.

      Below  is  a Turbo Pascal program that demonstrates how  to 
      access the variable block.

      PROGRAM USE_ADDR;
      TYPE
       STR255 = STRING[255];
      VAR
       W1,W2    : STRING[5];
       X1,X2    : REAL;
       RESULT,J,
       REG_SEG,
       REG_OFS  : INTEGER;
       STRPARMS : ^STR255;
       COUNTER  : ^INTEGER;
       W        : STR255;

      FUNCTION CONVERT_DECIMAL(X : REAL) : INTEGER;
      BEGIN
       IF X > 32767.0 THEN
       BEGIN
        X := X + $8000;
        CONVERT_DECIMAL := TRUNC(X) - $8000;
       END
       ELSE CONVERT_DECIMAL := TRUNC(X);
      END;

      BEGIN
       J  := POS(':',PARAMSTR(1));
       W1 := COPY(PARAMSTR(1),1,J-1) + '.0';
       W2 := COPY(PARAMSTR(1),J+1,5) + '.0';
       VAL(W1,X1,RESULT);
       VAL(W2,X2,J);
       REG_SEG  := CONVERT_DECIMAL(X1);
       REG_OFS  := CONVERT_DECIMAL(X2);
       RESULT   := (RESULT + J);
       IF RESULT = 0 THEN
       BEGIN
        STRPARMS := PTR(REG_SEG,REG_OFS);
        COUNTER  := PTR(REG_SEG,REG_OFS + (32*256));
        WRITELN(REG_SEG,':',REG_OFS);
        WRITELN('PARM    0 = ',STRPARMS^);
        WRITELN('COUNTER 0 = ',COUNTER^);
        STRPARMS^ := 'THE COMES FROM THE ADD PROGRAM';
       END;
      END.

      If  the program above was compiled to USEADDR.COM,  then  a 
      send file that would access this program would look like :

        |SET %0 =THIS IS A TEST LINE.
        |SET C0 =(5 + 3)*(8 /2)
        |MENU UUSEADDR |%ADDR
        |ECHO |%0   

      |%BUFFER

      BUFFER  returns  the contents of the  receive  buffer.  The 
      receive  buffer  is a string of 200  characters  containing 
      characters received from the modem.  The receive buffer  is 
      reset  at the beginning of each WAIT,  REPEAT WAIT or  CASE 
      send  file procedure.  Carriage return and line  feeds  are 
      thrown  away,  so  all string functions and procedures  are 
      available to use on the BUFFER.

        |TIMEOUT 60
        |ON TIMEOUT ERR TIMEOUT
        |ECHO Going to wait for SIGN ON ---
        |WAIT SIGN ON ---
        KMY
        |GOTO END
        |LABEL ERR TIMEOUT
        |  ECHO A timeout error occurred.
        |  ECHO The BUFFER =
        |  ECHO |%BUFFER
        |LABEL END
       
      The example above, waits 60 seconds for the phrase "SIGN ON 
      ---"  to be received from the modem.  If the phrase is  not 
      received in 60 seconds, then control is passed to the label 
      ERR TIMEOUT and the receive buffer will be displayed.

       
      |%COPY("str",x,y)
         str = string expression
           x = starting position
           y = number of characters to copy  

      COPY  returns  a  substring of str which  is  y  number  of 
      characters  in  length and starts at position x.  Str is  a 
      string expression and x and y are both integer expressions.

        |ECHO |%COPY("ABCDEF",2,3)
        |SET C1 = 0
        |SET %2 =ABCD
        |ECHO |%COPY("|%2",|%C1+2,3)
        |ECHO |%COPY("ABCDE",(3+4)-5,(4 + 20)/8)
        |ECHO |%COPY("|%COPY("ABCDEF",2,3)",1,3)

      The example above displays "BCD" four times.

      |%DAY

      DAY returns a eight character string containing the day  of 
      the  week.  The  format is (  Monday,  Tuesday,  Wednesday, 
      Thursday, Friday, Saturday or Sunday ).

        |ECHO Today is |%DAY


      |%DATE

      DATE returns an eight character string containing the date. 
      The format is MM/DD/YY. (i.e. "01/28/86").

        |ECHO Today is |%DAY  |%DATE.


      |%DECM(e)

      DECM returns the decimal equivalent for hex character 
      string e.

        |ECHO Hex 1E is equal to |%DECM(1E) decimal (30).
        |ECHO I/O port 3FE contains |%PORT[|%DECM(3FE)].


      |%EVAR(str)
         str = string expression

      EVAR  returns the string assigned to  environment  variable 
      str.  If str is not found, then a null string is  returned. 
      Str is a string expression.

        |ECHO |%EVAR(U)

      If  the  environment  variable U is  equal  GFC,  then  the 
      example above displays "GFC".


      |%HEX(x)

      HEX returns the hex equivalent for the decimal integer 
      expression x.

        |ECHO 30 decimal is equal to |%HEX(30) hex (1E).
        |ECHO Port 3FE contains |%HEX(|%PORT[|%DECM(3FE)]) hex.


      |%LENGTH(str)

      LENGTH  returns the number of characters within the  string 
      expression specified.
       
        |ECHO The length of ABCDE should be 5.
        |ECHO The length of ABCDE is |%LENGTH(ABCDE).


      |%MEM[x:y]

      MEM returns the value of memory location segment:offset 
      x:y. X and y are integer expressions.

        |ECHO Memory  0:30 hex contains |%MEM[0:|%DECM(30)].
        |ECHO Address 0:30 hex = |%HEX(|%MEM[0:|%DECM(30)]) hex.


      |%PORT[x]

      PORT returns the value of I/O port x. X is an integer 
      expression.

        |ECHO Port 3FE contains |%HEX(|%PORT[|%DECM(3FE)]) hex.


      |%POS("obj",target)
        obj      = string to look for
        target   = string to look at

      POS  returns  the  first position  of  target  string  that 
      matches  the object string.  If there is no match then  POS 
      returns  a 0.  Obj and target are string  expressions.  Pos 
      returns an integer value.  
        
        |SET %2 =THIS IS A TEST LINE
        |ECHO |%POS("TEST",|%2) is the position of TEST
        |ECHO in string variable 2.

      In the example above, the POS would return a value of 11.

      |%READBUF

      READBUF is special variable that allows the user to by pass 
      the function parser. This is useful when listing or sending 
      one send file from another.

        |INFILE OPEN TEST.SF
        |LABEL READ LOOP
        |  INFILE READ %READBUF
        |  ECHO |%READBUF
        |  IF(EOF(TEST.SF)) THEN |GOTO END
        |GOTO READ LOOP
        |LABEL END
          
      The example above will list the send file named TEST.SF.


      |%TIME

      TIME  returns a string containing the current system clock. 
      The format is HH:MM:SS. (i.e. 17:35:32 ).

        |ECHO The current time is |%TIME 


      |%VER

      VER  returns  a  string containing the version  of  TALKCOM 
      which is running the send file. 

        |ECHO Your version of TALKCOM is |%VER.
        |IF "|%VER" LT "2.3" THEN 
        |  ECHO Your version of TALKCOM is too old.
        |ENDIF 


TALKCOM's Directive Files.

1. Macro Files.

   a. Description.

      TALKCOM  macro files may contain  menu  commands,  standard 
      functions and send files in INCLUDE format. Macro files may 
      be called from the DOS command line,  the menu, a send file 
      or  from another  macro file.  Only one macro file  may  be 
      open at a time. If a new macro file is called, then the old 
      macro  file is closed and control of the session is  passed 
      to the new macro file. If the Z command option is the first 
      letter  in a macro file called from the DOS  command  line, 
      then  the TALKCOM session will execute  without  disturbing 
      the display screen.


   b. Syntax of macro file lines.

      Macro  file lines contain the letter options from the menu. 
      These  letters may be strung together on a single  line  or 
      placed on different lines. Some of the menu command options 
      require  string  arguments,  these must be terminated by  a 
      carriage return line feed.  

      Below  are  three  examples of  TALKCOM  macro  files.  The 
      comments out to the right (following the *) are not part of 
      the  macro file.  They are there as an explanation of  what 
      the macro files is doing.

      Macro file 1.
       Y*.OUT                 *Erases all files with OUT ext.
       B2VDATDT9,521-0510     *Sets baud, view flag, dial phone
       SYLOGON.SF             *Calls send file LOGON.SF
       T                      *Enters terminal mode
       E                      *Exits TALKCOM and reset modem

      Macro  file  2 and 3 do the same thing.  Macro file 2  uses 
      only  macro  commands.  Macro  file 3 uses  the  send  file 
      INCLUDE format.
       
      Macro file 2.
       Y*.SDM                 *Erases all files with ext ".SDM"
       B2VDATDT9,521-0510     *Sets baud,view flag and dial phone
       OCDCMAIL.SDM           *Opens save file "CDCMAIL.SDM"
       SYCDCMSEND.TXT         *Sends file "CDCMSEND.TXT"     
       CPCDCMAIL.SDM          *Closes and prints "CDCMAIL.SDM"
       E                      *Reset modem and exit TALKCOM

      Macro file 3.
       SI
       |NO DATA
       *   Erase all files with ext ".SDM"
        MENU Y *.SDM          *Or "|MENU U DEL *.SDM"
       *  Set the baud rate to 1200   
        MENU B2               *The default was already 1200
       *  Toggle view flag  
        MENU V
       *  Dial the phone
        MENU D ATDT9,521-0510 *Or the ATDT could be sent as data 
       *  Open a save (capture) file named CDCMAIL.SDM
        MENU O CDCMAIL.SDM
       *  Send file CDCMSEND.TXT using ASCII format.
        MENU SY CDCMSEND.TXT  *This file contains send file procs
       *  Return from send file
       *  Close save (capture) file.
        MENU C
       *  Print the save (capture) file.
        MENU P CDCMAIL.SDM    *Or "|MENU U COPY CDCMAIL.SDM PRN"
       *  End send file INCLUDE format and exist TALKCOM.
       |EOF                   *End send file INCLUDE format
       E                      *End TALKCOM and reset modem

2. Send Files.

   a. Description.

      TALKCOM  send  files are ASCII files that may contain  send 
      file procedures, TALKCOM standard functions, and data lines 
      to  be  sent  to  the  modem.   Send  file  procedures  are 
      identified  by  a  | VERTICAL LINE  in  column  1.  TALKCOM 
      standard  functions are identified by the  function  symbol 
      (|%)  followed  by a function identifier.  Data  lines  are 
      identified by the absence of the | VERTICAL LINE or special 
      characters  ('\','{'  or '~') in column 1.  Send files  may 
      pure data files,  sub programs for a larger TALKCOM session 
      or control the current session.  The choice is yours.  Send 
      files may be called from a macro file,  the menu or another 
      send file. In each case control is returned to the caller.


   b. Send File Procedure Line Syntax.

      The | VERTICAL LINE in column 1 may be followed by extra 
      spaces for all procedure identifiers except EOF, ENDCASE 
      and LABEL. Any  VERTICAL LINE identifier that is not valid 
      will be treated as a comment line. All keywords and 
      identifier must be in upper case.

       |   THESE  LINES WOULD BE COMMENTS BECAUSE  "THESE" 
       |   AND "AND" ARE NOT VALID TALKCOM PROCEDURE IDS 
       data line 1
       data line 2  
       |   CLS
       |   cls
       |   LABEL BAD LABEL NAME
       |LABEL GO LABEL NAME

      The  first CLS above is valid TALKCOM  syntax.  The  second 
      will be treated as a comment.  The first LABEL statement is 
      not valid because of leading spaces. 

      The | VERTICAL LINE procedures are : 

      Command          Syntax
      --------      ----------------------
        BEEP       |BEEP   

                   Sends a beep to the CPU speaker.

      BEGDATA      |BEGDATA

                   Signals  the start of a data block.  Lines  in 
                   the data block are to be sent to the modem  as 
is and are not to be interpreted as commands. ENDDATA  terminates 
the data block.

        BREAK      |BREAK  

                   Sends a hardware break signal to the connected 
                   CPU.

      CHRPACE      |CHRPACE x

                   Sets  a  delay  of  x  micro  seconds  between 
                   character send using the SEND procedure. Stays 
                   in effect until you exit TALKCOM. Set it to 0, 
                   if you no longer require the delay.

        CASE       |CASE
                   pace string1=label1
                   pace string2=label2
                   |ENDCASE

                   This  procedure waits for one of a set of pace    
                   strings.  When  there is a pace string  match, 
                   then execution is passed to the label  defined 
                   in the pace strings=label combination.  If the 
                   timeout   value  is  reached  before  a  match 
                   occurs,  then a timeout error will be set  and 
                   the CASE procedure is ended.
                           
                    |CASE(cr)
                    HI THERE=GREETINGS(cr)
                    STOP=END EXECUTION(cr) 
                    ABORT=SOMETHING WRONG(cr)
                    GUESS=|%3(cr)
                    |ENDCASE(cr)

                   The  above  example shows a case structure  of 
                   four  pace strings.  If the string  "STOP"  is 
                   received,  execution  of the send file will be 
                   passed  to label "END EXECUTION".  The  string 
                   variable  %3 would be replaced by  either  the 
                   command   line   entry  or  using   a   "|SET" 
                   procedure.   All  label and control words must 
                   be  in  upper  case,  pace  strings  are  case 
                   sensitive  (if you are looking for upper  case 
                   then  enter upper case).  No equal  signs  are 
                   allowed within the pace strings. 

        CLEAR      |CLEAR TOGGLES
                   |CLEAR Cx,Cy
                   |CLEAR %g,%h 
                   |CLEAR ALL
                   |CLEAR FIELDS

                   This  procedure  clears  variables,  counters, 
                   fields  or toggles. Toggles are the VIEW  FLAG 
                   and  the Z FLAG, they are set to FALSE when  a 
                   CLEAR  TOGGLES  procedure is  executed.  CLEAR 
                   Cx,Cy sets a range of counter variables from x 
                   to y to the value 0. CLEAR %g,%h sets a  range 
                   of  string  variables from g to h  to  a  null 
                   string value. CLEAR ALL clears the toggles and 
                   all counter and string variables. CLEAR FIELDS 
                   clears  all  fields variables  and  reset  any 
                   multiple  field  definition. CLEAR  FIELDS  is 
                   used  for  full screen input forms.  For  more 
                   information  on the use of full  screen  input 
                   forms refer to the SCRLOOK section.     G,  h, 
                   x and y are integer expressions.

                    |SET C1 = (1+2)*2
                    |LABEL LOOP1 
                    |  SET %|%C1 =THIS IS A STRING |%C1
                    |  ECHO |%|%C1
                    |LOOP C1 NE 0 LOOP1
                    |CLEAR %2,%4
                    |SET C1 = 6
                    |LABEL LOOP2
                    |  ECHO |%|%C1
                    |LOOP C1 NE 0 LOOP2

                   The example above sets and displays the string 
                   variables  1  through 6 to the value "THIS  IS 
                   STRING # x" where x is the present loop count. 
                   String variables 2 through 4 are cleared. Then 
                   the variables 1 through 6 are displayed again. 


        CLS        |CLS 

                   This   procedure   clears  the   display   and 
                   positions  the cursor to the upper  left  hand 
                   corner of the screen.

                    |CLS
                     
        DEC        |DEC Cn

                   This  procedure decreases the value of counter 
                   variable n by one. N is an integer value.

                    |SET C1=5
                    |ECHO C1 = |%C1 (SHOULD BE 5)
                    |DEC C1
                    |ECHO C1 = |%C1 (SHOULD BE 4)


        DELAY      |DELAY x 

                   Executes  a  delay of a  specified  number  of 
                   seconds before resuming send file execution. X 
                   is an integer expression.

                    |ECHO ALL OF THESE DELAY FOR 15 SECONDS
                    |DELAY 15(cr)
                    |DELAY (20-19)*5
                    |SET C1=10
                    |DELAY |%C1 + 5

                   Would   delay   15  seconds  for  each   DELAY 
                   procedure  then resume execution of  the  send 
                   file.


        DELETE     |DELETE %g,x,y

                   This  procedure removes y number of characters 
                   starting at position x from string variable g. 
                   G, x and y are integer expressions. 

                    |ECHO %1 will contain ABCDE
                    |SET %1=ABCDE
                    |SET C1 = 3
                    |DELETE %1,|%C1,5
                    |ECHO |%1

                   The  example above sets string variable  1  to 
                   "ABCDE". Sets counter variable 1 to 3. Deletes 
                   5  characters from string variable 1  starting 
                   at position 3.  Then displays "AB".  Since the 
                   delete  procedure  was  told  to  delete  more 
                   characters  than  were left to the end of  the 
                   string,  the delete procedure will delete  all 
                   characters up to the end of string.

        ECHO       |ECHO message
                   |ECHONR message
                   |ECHO ON
                   |ECHO OFF

                   This procedure displays message (the string of 
                   characters  following the first space  through 
                   the   terminating  carriage  return)  on   the 
                   display.  Form  one terminates with  a  CR/LF. 
                   Form  two leaves the cursor at the end of  the 
                   message.   The  last  two  forms  control  the 
                   display  of send file procedure  commands.  If 
                   ECHO is ON, then a dayfile named TALKCOM.DF is 
                   opened.  If  the  file  already  exists,  then 
                   TALKCOM.DF will be appended.  While ECHO is ON 
                   all  procedures are displayed and written to a 
                   dayfile before they are executed.  If ECHO  is 
                   OFF,   then   none   of  the  procedures   are 
                   displayed.  If TALKCOM.DF was opened by a ECHO 
                   ON,  then  it will be closed.  The default  is 
                   ECHO OFF. 

                    |ECHO Hi there sports fans.(cr)
                    |ECHONR Enter your choice : (cr) 

                   Would display  :

                    Hi there sports fans.
                    Enter your choice : 

                   leaving the cursor at the end of "choice : ".


        EOF        |EOF

                   Used in the send file INCLUDE format to signal 
                   the return to TALKCOM's main menu selections.

                    SI(cr)
                    |LABEL IN INCLUDE FILE(cr)
                    |EOF(cr)
                    E(cr)

                   Above is a macro file that starts a send  file 
                   in  INCLUDE format "SI(cr)",  makes a label of 
                   "IN  INCLUDE FILE",  then returns to the  main 
                   menu  and  executes a "E" option (exit to  DOS 
                   after resetting modem). 

        EXIT       |EXIT

                   Terminates  the sendfile. If in  send  include 
                   format,  then the macro file is positioned  to 
                   the |EOF.


       FIELD       |FIELD,x,y,s,n [,"str"]

                   This  procedure  defines  a field  of  a  full 
                   screen  input form.  X and y define the screen 
                   position (x=column and y=line) of the field. S 
                   equals  the number of characters  in  size.  N 
                   defines  the field number ( which is the  same 
                   as   the  string  variable  number).   Str  is 
                   optional  parameter  which  defines  the  help 
                   string. The help strings are displayed on line 
                   25 of the input form at data entry.

                     |FIELD,12,10,5,2,"Last 4 numbers of pager #"

                   In  the example above,  a field  5  characters 
                   wide  would  be  displayed on  the  screen  at 
                   column 12 line 10.  When the cursor is  placed 
                   on  this field the help string "Last 4 numbers 
                   of pager #" will be displayed on line 25.  The 
                   data  entered  into this field  will  go  into 
                   string variable 2.

                                    *** note ***
                   This procedure will be created by the  SCRLOOK 
                   program.  It  is  not likely you will  have  a 
                   reason  to  create  a  full  screen  form  one 
                   procedure at a time. Refer to SCRLOOK for more 
                   details regarding full screen input forms.  

        GET        |GET x %g or |GET x CHAR INTO %g
                   |GET LINE %g or |GET LINE INTO %g
 
                   GET x receives x number of characters from the 
                   modem and places them into the string variable 
                   g.  GET  LINE continues to receive  characters 
                   into  string  variable  g until  a  line  feed 
                   character  is received.  X and g  are  integer 
                   expressions. 

                    |ECHO Both GET 5 chars in string variable 5
                    |GET 5 CHARS INTO PARAMETER %5(cr)   
                    |SET C1=10
                    |GET |%C1 - 5 INTO %(|%C1 / 2)
                    |ECHO Receive a line into variable 6
                    |GET LINE INTO %6

                   As  you can see the procedure is free  format. 
                   The mandatory sections are the "|GET " and the 
                   "%X".   The  example  above  could  have  been 
                   expressed as "|GET 5 %5(cr)".  The rest of the 
                   procedure  can  be  expressed  other  ways  to 
                   improve its clarity.
        GOSUB      |GOSUB label

                   This  procedure calls a subroutine whose  name 
                   is  label.  Send file execution proceeds  from 
                   the  subroutine label to the  first  "|RETURN" 
                   procedure.   Send   file  execution  is   then 
                   returned  to  the  line following  the  |GOSUB 
                   procedure. 

                     |ECHO THIS IS MAIN
                     |GOSUB SUB1
                     |ECHO THIS MAIN AGAIN
                     |GOTO END
                     |LABEL SUB1
                     |  ECHO THIS IS SUB1
                     |RETURN
                     |LABEL END

                   The output from the send file above would look 
                   like:
                     THIS IS MAIN
                     THIS IS SUB1
                     THIS IS MAIN AGAIN


        GOTO       |GOTO label

                   Passes execution of the send file to the label 
                   specified.

                    |GOTO ALL DONE(cr)
                    |GOTO |%2(cr)

                   Send  file  execution is passed to  the  label 
                   "ALL  DONE"  in  example 1  and  whatever  the 
                   string  value  of  string  variable  2  is  in 
                   example  2.  If the label specified  with  the 
                   GOTO statement is a null, then the GOTO is not 
                   executed.  If  the GOTO statement appears in a 
                   send  INCLUDE file,  then the label  specified 
                   may  exist anywhere within the  TALKCOM  macro 
                   file.   This   may  be  used  to  bypass  menu 
                   selections in a macro file. 

        GOTOXY     |GOTOXY x,y

                   Position  cursor to column position x and line 
                   position y. X and y are integer expressions.
                    
                    |GOTOXY 40,10
                    |ECHO THIS IS COL 40 LINE 10
                    |SET C1=10
                    |GOTOXY (|%C1+10)*2,|%C10+10
                    |ECHO THIS IS COL 40 LINE 20


        HANGUP     |HANGUP

                   This procedure disconnects the telephone  line 
                   and resets the modem.
                     
        IDLE       |IDLE x

                   This   procedure   waits  for  a  modem   idle 
                   condition.  An  idle condition  is  determined 
                   when  no  activity is detected from the  modem 
                   for  x  amount of seconds.  X  is  an  integer 
                   expression.

                    |WAIT EMPLOYEE NUMBER : 
                    53688
                    |IDLE 10
                    |ECHO Going to terminal mode
                    |MENU T

                   The   example  above  waits  for  the   string 
                   "EMPLOYEE  NUMBER  :" to  be  received.  Sends 
                   "53688"  to  the  modem.  Waits for  IDLE  (10 
                   seconds  of no modem activity).  Displays  the 
                   message "Going to terminal mode". Executes the 
                   menu command for terminal mode.  

        IF   |IF [NOT] expression THEN procedure [ELSE procedure]
                             or
                   |IF [NOT] expression THEN 
                    procedure
                    procedure
                 [ |ELSE
                    procedure
                    procedure ]
                   |ENDIF
                   
                   valid expressions:
                   |IF EXIST(file name) THEN proc
                   |IF EOF(file name) THEN proc
                   |IF KEYPRESSED THEN proc
                   |IF COMIN THEN proc
                   |IF "str" operation "str" THEN proc 
                   |IF x operation y THEN proc

                   "str" = any string value
                   x, y  = any valid integer expression
                   (parentheses and order observed)

                   valid relational operations:
                   EQ - equal to
                   LT - less then
                   GT - greater then
                   NE - not equal to

                   This    procedure   checks   the    relational 
                   expression  for a true conditions.  If a  true 
                   condition  is determined,  then the  procedure 
                   specified   is  executed.   If  there  is   no 
                   procedure  specified  following  the  reserved 
                   word  THEN,  the multiple line syntax of IF is 
                   assumed. 

                   In a multiple line IF,  all procedures between 
                   the  IF and ENDIF (or ELSE if  specified)  are 
                   executed  on  a true condition.  An  ENDIF  is 
                   required to terminate the multiple line IF.  

                   If  the relational expression is false and the 
                   optional  ELSE clause is specified,  then  the 
                   procedure following the ELSE is executed. In a 
                   multiple line syntax,  all procedures  between 
                   the ELSE and the ENDIF are executed.

                   The  EOF  is  true  if  the  file  pointer  is 
                   positioned  beyond  the last component of  the 
                   specified  INFILE.  

                   The  EXIST(file name) is true if file name  is 
                   found in the directory. 

                   KEYPRESSED is true if a key on the keyboard is 
                   pressed. 

                   COMIN  is  true if there is still data in  the 
                   communication buffer. The communication buffer 
                   holds  data  that has been received  from  the 
                   modem.

                     |IF EXIST(MY.FLE) THEN |ECHO FOUND 

                   If  the file named "MY.FLE" exists,  then  the 
                   procedure "|ECHO FOUND" would be executed. 

                     |IF |%C1 LT 3 THEN |ECHO C1 LESS THAN 3

                   If  counter 1 is less than 3,  then the  |ECHO 
                   procedure would be executed. 

                     |IF "|%1" EQ "|%2" THEN |CLS ELSE |BEEP

                   If  string  variable  1  is  equal  to  string 
                   variable   2,   then   a  |CLS  procedure   is 
                   executed, else the BEEP is executed.

                     |IF NOT EOF(|%0) THEN |GOTO READLOOP

                   If the input file specified in string variable 
                   0  is  not at the end of file,  then  a  |GOTO 
                   procedure would be executed. 

                     |IF |%C1 LT |%C13 - 5 THEN |GOSUB WRONG DATA 

                   If  counter variable 1 is less than the  value 
                   in  counter  variable 13 minus  5,  then  goto 
                   subroutine "WRONG DATA".

                  |IF 1 EQ 1 THEN |IF 2 EQ 2 THEN |CLS ELSE |BEEP 

                 The example above shows a nested IF structure in 
                 the  single  line  syntax.   If  either  of  the 
                 expressions (1 EQ 1 or 2 EQ 2) were false,  then 
                 the the BEEP would be executed.

                     |IF |%C1 EQ |%C2 THEN
                     | ECHO C1 AND C2 ARE EQUAL
                     | GOSUB CLEAR DATA
                     | IF |%C1 GT 3 THEN 
                     |  ECHO C1 GT 3
                     |  GOSUB SET UP FILES
                     | ENDIF
                     |ENDIF
      
                   If counter variable 1 is less than counter  2, 
                   then  the  procedures between the IF  and  the 
                   last ENDIF are executed.  If the nested IF (C1 
                   GT  3) is false,  then none of the  procedures 
                   between  it  and  the  first  ENDIF  will   be 
                   executed.   Leading  spaces  are  ignored  and 
                   should  be  used  to show which IF  gets  what 
                   ENDIF.

                    |NO DATA
                     IF 0 EQ 1 THEN 
                      ECHO P3
                     ELSE
                      IF 0 EQ 1 THEN |ECHO P3ST ELSE |ECHO P3SF
                      IF 0 EQ 2 THEN
                       ECHO P4
                       ECHO P5
                      ELSE
                       ECHO P6
                       ECHO P7
                      ENDIF
                      ECHO P8
                      ECHO P9
                     ENDIF
                    |EOF
                    
                   The example above would display :
                    P3SF
                    P6
                    P7
                    P8 
                    P9


        INC        |INC Cn

                   This  procedure increases the value of counter 
                   variable n by one. N is an integer value.

                    |SET C1=5
                    |ECHO C1 = |%C1 (SHOULD BE 5)
                    |INC C1
                    |ECHO C1 = |%C1 (SHOULD BE 6)


        INFILE     |INFILE OPEN file name
                   |INFILE CLOSE file name
                   |INFILE READ %g
                   |INFILE READ %READBUF

                   This procedure works with an input  file.  The 
                   input  file  must be opened before a  read  is 
                   performed.  The  input file should  be  closed 
                   when it is no longer needed. The "|IF(EOF(file 
                   name))"  procedure  should  be used  to  avoid 
                   reading past the end of the file.  INFILE READ 
                   %g reads a line into string variable g  or the 
                   special  variable  READBUF.  G is  an  integer 
                   expression.

                     SI
                     |NO DATA
                      CLS
                     |LABEL GET NAME
                        ECHO Enter file name to display
                        READKBD %0
                        IF EXIST(|%0) THEN |GOTO FILE NAME OK
                        ECHO File |%0 does not exist.
                      GOTO GET NAME
                     |LABEL FILE NAME OK
                        INFILE OPEN |%0
                     |LABEL READ LOOP
                        INFILE READ %1
                        ECHO |%1
                        IF NOT EOF(|%0) THEN |GOTO READ LOOP
                        INFILE CLOSE |%0 
                        ECHONR Display another file (Y/N)  
                        READKBDC %9
                        IF "|%9" EQ "Y"  THEN |GOTO GET NAME
                     |EOF

                   The  above example requests a  file  name.  If 
                   that file does not exist,  it tells you so and 
                   asks again.  If that file does exist, then the 
                   file  is opened.  A line is read from the file 
                   into  string variable 1 then displayed on  the 
                   screen. This is repeated until the end of file 
                   is  reached.  When the end of file is  reached 
                   the  file is closed.  It then asks if  another 
                   file is to be displayed. 


        INSERT     |INSERT str,%g,x

                   INSERT  returns  a new string variable g  with 
                   the value of str inserted at position  x.  Str 
                   is  a string expression.  X and g are  integer 
                   expressions.

                    |SET C1=1
                    |SET %5=ABCDEF
                    |SET %6=|%5
                    |INSERT XX,%|%C1+4,|%C1 + 3
                    |INSERT XX,%6,4
                    |ECHO |%5 is the same as |%6

                   The  example above sets counter variable 1  to 
                   1.  Sets string variables 5 and 6 to "ABCDEF". 
                   Inserts  "XX" into string variables 5 and 6 at 
                   position 4. Then displays the line : 

                    "ABCXXDEF is the  same as ABCXXDEF"                    


        LABEL      |LABEL label

                   This procedure defines a line position to pass 
                   execution to.
            
                     |LABEL SOME LABEL(cr)

                   The  label  identifier equals  the  string  of 
                   characters  following  the first space to  the 
                   terminating  carriage  return.  In  the  above 
                   example, "SOME LABEL" is the label.

        LOOP       |LOOP Cx NE y label
                   |LOOP Cx DOWNTO y label
                   |LOOP Cx TO y label

                   The NE and DOWNTO operators work the same. The 
                   LOOP  procedure  checks the counter  x  for  a 
                   value of y.  If the counter is not equal to y, 
                   then it is decreased by one and control of the 
                   send  file is transferred to the line  defined 
                   as  label.  The  operator TO works  the  same, 
                   except the counter value is increased by one. 

                   The  levels deep a loop may be nested  is  the 
                   number  of  counter  variables.  X and  y  are 
                   integer expressions.

                    |SET C1=0
                    |LABEL LOOP1
                    |  SET C2=2
                    |LABEL LOOP2
                    |    ECHO THIS IS THE INNER LOOP.
                    |LOOP C2 NE 0 LOOP2
                    |  ECHO THIS IS THE OUTER LOOP.
                    |LOOP C1 TO 2 LOOP1


        MENU       |MENU str

                   Allows  execution of a main menu command  from 
                   within   a  send  file.   Str  is   a   string 
                   expression.
                    
                    |MENU DATDT9,123-4567(cr)
                    |MENU RXJUNK.FLE(cr)
                    |MENU SX|%3(cr)

                   In   the  examples  above,   a  DIAL   command 
                   (DATDT9,123-4567),     a    RECEIVE    command 
                   (RXJUNK.FLE)  and  a SEND command (SX|%3)  are 
                   executed.  The MENU procedure can only execute 
                   one menu command per call.

         MULTIF    |MULTIF,x,"str" 

                   This  procedure  loads the field table x  with 
                   the  information  in str.  It  indicates  that 
                   field  x contain several  preset  values.  The 
                   first  MULTIF  procedure defined for  field  x 
                   will be the default value.


                                    *** note ***
                   This procedure will be created by the  SCRLOOK 
                   program.  It  is  not likely you will  have  a 
                   reason  to  create  a  full  screen  form  one 
                   procedure at a time. Refer to SCRLOOK for more 
                   details regarding full screen input forms.  

                      
          NO DATA  |NO DATA

                   This  procedure sets the NO DATA flag.  The NO 
                   DATA flag indicates to the send file processor 
                   that  all of the lines following the |NO  DATA 
                   procedure are send file procedure  lines.  Any 
                   line  that is not a valid send file  procedure 
                   will be treated as a comment line. 
 

                     |NO DATA
                       CLS
                       ECHO | are not needed after the NO DATA.
                       ECHO except for |LABEL and |EOF
                      |LABEL label_one
                     |EOF

                   Notice that the |LABEL procedure does not have 
                   to start in column 1, but the |NO DATA and the 
                   |EOF procedure do.

        ON TIMEOUT |ON TIMEOUT label

                   Specifies  a label to which the  execution  of 
                   the  send  file  is passed in the event  of  a 
                   timeout error.

                    |ON TIMEOUT ERROR1(cr)
                    |GOTO START(cr)
                    |LABEL ERROR1(cr)
                    BYE(cr)
                    |GOTO DONE(cr)
                    |LABEL START(cr)
                    |WAIT ENTER USERID : (cr)
                    FIRST USERS(cr)
                    |WAIT ENTER PASSWORD : (cr)
                    FIRST PW(cr)
                    |LABEL DONE(cr)

                   In  the example above,  if the send  procedure 
                   gets a timeout error waiting for either "ENTER 
                   USERID :  " or "ENTER PASSWORD :  " , then the 
                   next  send file line to be processed  will  be 
                   the   line  "|LABEL  ERROR1(cr)".   The  label 
                   specification may be a replaceable  parameter. 
                   The  ON  TIMEOUT statement works as  an  event 
                   driven GOTO statement. Once a ON TIMEOUT is in 
                   effect,  it stays in effect until the label is 
                   changed  by another ON TIMEOUT statement or it 
                   is disabled by the line: 

                    |ON TIMEOUT(cr)  

        PACE       |PACE x

                   Executes  a delay of x seconds before each  of 
                   the  data  line  are sent.  X  is  an  integer 
                   expression.

                    |PACE 2(cr)
                    |WAIT WAIT(cr)
                    SEND LINE 1(cr)
                    |WAIT WAIT FOR SOMETHING ELSE(cr)
                    SEND LINE 2(cr)
                    |PACE (|%C1 * 2) + 5

                   Would  cause  a  delay  of  2  seconds  before 
                   sending  "SEND  LINE 1" and another  2  second 
                   delay before sending "SEND LINE 2".  The  last 
                   line  sets  a new pace amount of the value  in 
                   counter 1 times 2 plus 5 seconds.

        PAD        |PAD %g,d,x

                   Inserts spaces in variable g.  If d equals "L" 
                   then spaces are inserted at the beginning.  If 
                   d equals "R" then spaces are added to the end. 
                   X indicates the maximum length of variable g.

                     |SET %1=PAD
                     |PAD %1,L,5
                     |ECHO [|%1]

                   The example sets variable 1 to "PAD".  Inserts 
                   2 spaces. Displays "[  PAD]" on the screen.
 

        POP        |POP Cx
                   |POP %g

                   This  procedure  will return either a  counter 
                   variable or a string variable,  POP Cx or  POP 
                   %x respectively,   from the local stack. These 
                   variables  must  have been  previously  PUSHED 
                   onto  the  stack.  Two uses of this  procedure 
                   would be to extend the number of variables and 
                   to  save variables between sub program or  sub 
                   routine   calls.   X   and   g   are   integer 
                   expressions.

                    |SET C1 = |%C1 * 3
                    |SET %3 =THIS IS NOT FUNNY
                    |PUSH C1
                    |PUSH %3
                    |CLEAR ALL
                    |MENU SYSUBPRG.SF
                    |POP C1
                    |POP %3

                   The  example above sets counter variable 1  to 
                   the  value  of counter 1 times  3.  Then  sets 
                   string  variable  3 to "THIS  IS  NOT  FUNNY". 
                   Pushes these values onto the stack, clears all 
                   toggles  and variables then calls sub  program 
                   "SUBPRG.SF".  When  "SUBPRG.SF" finishes,  the 
                   example  pops counter 1 and string 3 to  their 
                   values before the call to "SUBPRG.SF".

        PUSH       |PUSH Cx
                   |PUSH %g

                   This  procedure  pushes counter  variables  or 
                   string  variables   onto their   local  stack, 
                   PUSH  Cx  or PUSH  %x  respectively.  If  this 
                   procedure   is  not  executed  before  a   POP 
                   procedure,  then an error will occur.  X and g 
                   are integer expressions.
                    
                    |NO DATA
                     SET C1 = 31
                    |LABEL LOOP1
                      PUSH C|%C1
                     LOOP C1 NE 0 LOOP1
                     ECHO ALL COUNTERS SAVED.
                     SET C1 = 1
                    |LABEL LOOP2
                      POP C|%C1
                     LOOP C1 TO 31 LOOP2
                     ECHO ALL COUNTERS RESTORED.  

                   The  example above saves (pushes) all  counter 
                   variables  onto the stack,  displays the  line 
                   "ALL  COUNTERS  SAVED.",  restores (pops)  all 
                   counters  from the stack,  then  displays  the 
                   line "ALL COUNTERS RESTORED." 


        READKBD    |READKBD %g
                   |READKBDC %g

                   This procedure displays a question mark on the 
                   screen  then  accepts a character or a  string 
                   characters from the keyboard. The character or 
                   characters   are   place  in   the   parameter 
                   specified.   Form  one  accepts  a  string  of 
                   characters  terminated by a  carriage  return. 
                   Form  two accepts only a single character  and 
                   does  not require a carriage return.  G is  an 
                   integer expression.

                    |READKBD %3
                    |READKBDC %4

                   Would  read  characters from the keyboard  and 
                   place them into string variable 3, then read a 
                   single character from the keyboard a place  it 
                   into string variable 4.
                      
        READSCR    |READSCR

                   This procedure activates the full screen entry 
                   handler.  The  screen display and entry fields 
                   should  have  been  previously  set  up.  This 
                   procedure  accepts  keyboard input  into  each 
                   field  start from the top of the screen.  Full 
                   cursor  control is available and data entry is 
                   completed  by  pressing  the  F10  key.   

                                    *** note ***
                   This procedure will be created by the  SCRLOOK 
                   program.  It  is  not likely you will  have  a 
                   reason  to  create  a  full  screen  form  one 
                   procedure at a time. Refer to SCRLOOK for more 
                   details regarding full screen input forms.  

                      
      REPEAT WAIT |REPEAT WAIT str

                   Waits   for  a  string  of  characters  to  be 
                   received from the modem  that match the string 
                   defined. If no match occurs before the timeout 
                   value is reached then a timeout error  occurs. 
                   Once the REPEAT WAIT procedure is set,  a WAIT 
                   string  is done before each line of data to be 
                   sent. This procedure is equivalent in function 
                   to the { (LEFT BRACE).
                    
                    |REPEAT WAIT ?
                    LINE 1
                    LINE 2
                    |REPEAT WAIT
                    BYE

                   This  example  will wait for a  question  mark 
                   before sending "LINE 1" and then again  before 
                   sending  "LINE  2".  The REPEAT WAIT  with  no 
                   string  following,   resets  the  REPEAT  WAIT 
                   procedure.

       RETURN     |RETURN

                   This  procedure returns execution of the  send 
                   file  to  the line following  the  last  GOSUB 
                   procedure executed.
                     
                    |ECHO MAIN
                    |GOSUB SUB1
                    |ECHO RETURN FROM SUB1
                    |GOTO END
                    |LABEL SUB1
                    | ECHO SUB1
                    | GOSUB SUB2
                    | ECHO RETURN FROM SUB2
                    |RETURN
                    |LABEL SUB2
                    |  ECHO SUB2
                    |RETURN
                    |LABEL END

                   The display from the example above would be :
                     MAIN
                     SUB1
                     SUB2
                     RETURN FROM SUB2
                     RETURN FROM SUB1

        SEND       |SEND "str" n n
                   |SENDNR "str" n n

                   This  procedure sends a string  of  characters 
                   (str  +  character  n + character  n)  to  the 
                   modem.  SEND  finishes with a carriage  return 
                   line feed,  SENDNR does not.   Str is a string 
                   expression. N is a decimal integer value. 

                    |SEND "ATZ"
                    |WAIT OK
                    |ECHO
                    |DELAY 2
                    |SENDNR "AT"  "S0" "?" 13 10
                    |WAIT OK

                   The  example above would send the line ATZ  to 
                   the modem,  wait for an OK,  delay 2  seconds, 
                   send line ATS0? then wait for a final OK. 

        SET        |SET Cx=y
                   |SET %g=str
                   |SET MEM[x:y] = z
                   |SET PORT[x] = y
                   |SET RC=y

                   Form  one  sets  counter  variable  x  to  the 
                   integer  value of expression y.  

                   Form  two  sets the string variable g  to  the 
                   value of string expression str.  

                   Form  three  sets memory location  segment  x: 
                   offset y to the integer value of expression z.

                   Form four sets I/O port x to the integer value 
                   of expression y.
  
                   Form five sets DOS return code (ERRORLEVEL) to 
                   the integer value of expression y.

                    |SET C1= 3 + 4 * 5
                    |SET %1=VALUE FOR PARM 1(cr)
                    |SET MEM[|%DECM(40):|%DECM(49)] = 7
                    |SET PORT[|%DECM(3F8)] = |%DECM(FF)
                    |SET RC=1

                   Example one sets counter variable 1 to a value 
                   of 23. 

                   Example two would set string variable 1 to the 
                   value "VALUE FOR PARM 1".

                   Example  three sets hex memory location  40:49 
                   to a value of 7. 

                   Example  four sends a 255 (FF hex) to port 3F8 
                   hex.  

                   Example  five sets the DOS return code  to  1, 
                   when TALKCOM is ended. This return code may be 
                   checked  using  the  batch  file  command   IF 
                   ERRORLEVEL.  

        TIMEOUT    |TIMEOUT x

                   Sets  the  timeout  counter to  the  value  of 
                   integer  expression  x  seconds.  The  timeout 
                   counter  is  the  length  of  time  the   send 
                   procedure  will wait for a pace string  before 
                   setting a timeout error.

                    |TIMEOUT 3 * 10(cr)
                    |WAIT WAIT(cr)
                    SEND HELLO(cr)

                   Would set the timeout value to 30 seconds.  If 
                   30  seconds pass and the pace string "WAIT" is 
                   not seen then a timeout error would occur.

                              *** note ***
                   The  maximum number of seconds allowed by  the 
                   DELAY, PACE or TIMEOUT procedure is 32767.


        TRIM       |TRIM %g,d,x

                   Trims spaces from variable g.  If d equals "L" 
                   then spaces are deleted from the beginning. If 
                   d equals "R" then spaces are deleted from  the 
                   end.   X   indicates  the  minimum  length  of 
                   variable g.

                     |SET %1=   PAD
                     |TRIM %1,L,5
                     |ECHO [|%1]

                   The  example  sets  variable 1  to  "    PAD". 
                   Deletes  1  space.  Displays "[  PAD]" on  the 
                   screen.


        UPSTR      |UPSTR %g

                   This procedure converts the string variable  g 
                   to  upper  case  letters.   G  is  an  integer 
                   expression.
                    
                     |SET %31=lower case
                     |ECHO |%31
                     |UPSTR %31
                     |ECHO |%31

                   The example above would display :
                     lower case
                     LOWER CASE

        WAIT       |WAIT str 

                   Waits   for  a  string  of  characters  to  be 
                   received from the modem  that match the string 
                   defined. If no match occurs before the timeout 
                   value is reached then a timeout error occurs.

                   |WAIT //
                    
                   |WAIT SYSTEM--
                   KMY

                   The  example  above,  waits  for  "//"  to  be 
                   received from the modem. Then sends a carriage 
                   return  to the modem.  Waits  for  "SYSTEM--", 
                   then sends KMY.


        WRITE      |WRITE "str" n n 
                   |WRITENR "str" n n

                   Writes a character string to the terminal save 
                   file. Form two terminates the character string 
                   with  a  carriage return line  feed  sequence. 
                   This  may  be  useful in  controlling  printer 
                   functions or saving information about an error 
                   condition  in  a disk file.  Str is  a  string 
                   expression. N is an integer value.  

                    |LABEL ERROR
                    |SET C1=3
                    |WRITE 13 10 "ERROR C1 = |%C1" 
                    |MENU C

                   The  last line of the terminal save file  will 
                   be "ERROR C1 = 3".

     Below is an example of a TALKCOM macro file,  called  DEBUG, 
which  uses the send file INCLUDE format.  This macro file may be 
called into execution by either typing TALKCOM DEBUG [file  name] 
from  the DOS command line or selecting menu option X then typing 
DEBUG  [file  name].  File name is  an  optional  parameter.  The 
comments  out  to the side (following the *) are not part of  the 
macro  file and are included as an explanation of what the  macro 
file is doing.


 ZSI                        *Call send file include format    
 |NO DATA                   *set NO DATA flag on
  CLS                       *Clear display screen
  ECHO OFF                  *Turn off procedure line display 
 |LABEL MAIN                *Setting label MAIN
   SET %30=|%2              *Moving the file name parm to %30
   GOSUB CHECK FILE NAME    *Calling CHECK FILE NAME
 |LABEL LOOP                *Setting label LOOP
   GOSUB MENU               *Calling the menu display
   IF "|%31" EQ "E" THEN |GOSUB EXECUTE
   IF "|%31" EQ "G" THEN |GOSUB GO
   IF "|%31" EQ "L" THEN |GOSUB LIST
   IF "|%31" EQ "N" THEN |GOSUB NEW NAME
   IF "|%31" EQ "Q" THEN |GOTO END
   IF "|%31" EQ "?" THEN |GOSUB DISPLAY HELP
  GOTO LOOP                 *The IF's above decode keyboard input
 |LABEL MENU                *The menu routine displays menu and  
   ECHONR Enter letter (E,G,L,N,Q,?) > 
   READKBDC %31                       *requests a character input
  RETURN                    *Return to caller
 |LABEL PAUSE               *Routine to pause for a return
   ECHO
   ECHO Press <return> to continue.
   READKBD %0
  RETURN
 |LABEL CHECK FILE NAME     *Routine to check for valid file name
   IF "|%30" EQ "" THEN |GOSUB GET NAME
   IF "|%30" NE "" THEN
    IF NOT EXIST(|%30) THEN
     ECHO File name |%30 was not found on disk.
     ECHO Please enter file name again.
     SET %30=                  *Clear invalid file name
     GOTO CHECK FILE NAME      *Goto ask for new file name
    ENDIF
   ENDIF
  RETURN
 |LABEL GET NAME            *Routine to ask for a file name
   ECHONR Enter file name to debug or <return>  
   READKBD %30
   ECHO
  RETURN
 |LABEL EXECUTE             *Routine to execute a line entered 
   ECHO Enter send file command (i.e. |SET %30=FILE NAME)
   READKBD %31
   |%31                     *Execute line as a send file proc
   SET %31=                 *Clear entry
  RETURN                    *Return to caller
 |LABEL MORE                *Routine to pause after 22 lines
   GOSUB PAUSE
   CLS
   SET C31=1                *Reset line counter to 1
  RETURN
 |LABEL LIST                *Routine  to  list  a  file
   IF EXIST(|%30) THEN |GOTO FILE NAME OK
  RETURN                    *Make sure file still exists
 |LABEL FILE NAME OK
   INFILE OPEN |%30         *Open file to list
   SET C31=1                *Set line count to 1
 |LABEL READ FILE           *Start of read loop
   INFILE READ %READBUF     *Read line into special read variable
   ECHO |%READBUF           *Display line read in.
   INC C31                  *Increase line count
   IF |%C31 GT 22 THEN |GOSUB MORE        *Check line cnt > 22
   IF NOT EOF(|%30) THEN |GOTO READ FILE  *Check for end of file
   ECHO === END OF FILE ===
   INFILE CLOSE |%30        *Close file name in string var 30
  RETURN
 |LABEL GO                  *Routine to call another send file 
   PUSH %30                 *Save file name
   CLEAR ALL                *Clear all variables
   POP %1                   *Move the file name string var 1
   PUSH %1                  *Save file name
   MENU SY|%1               *Call send file in string var 1
   CLEAR ALL                *Return from send file. Clear vars 
   POP %30                  *Get file name back in var 30
  RETURN
 |LABEL NEW NAME            *Routine to change file names
   SET %30=
   GOSUB CHECK FILE NAME
  RETURN
 |LABEL DISPLAY HELP        *Routine to display help screen
   ECHO E  Execute. Execute a command entered from the keyboard.
   ECHO G  Go.      Execute the current file name.
   ECHO L  List.    List the current file name.
   ECHO N  Name.    Allows a new file name to be entered.
   ECHO Q  Quit.    Exits the DEBUG send file.
   ECHO ?  Help.    Displays this menu.
  RETURN
 |LABEL END
 |EOF

  The  following  is  an example of a TALKCOM macro  file  called 
LOGON.  It  uses send file INCLUDE format.  This macro file  also 
uses  the Z command to turn off the menu displays.  The  comments 
out  to the side (following the *) are not part of the macro file 
and  are  included as an explanation of what the  macro  file  is 
doing.

 ZSI                        *Turn off menu and call send file
 |NO DATA                   *Turn on NO DATA flag.      
  SET %3=TERMINAL MODE      *Set string var 3 to TERMINAL MODE
  CLS                       *Clear screen
  ECHO Dialing the phone.
  GOTO |%2                  *Goto label passed on parm line
 |LABEL KMY                 *Routine for KMY login
 *                     -- KMY PROCEDURE FILE  *comment line
  MENU D ATDT9,521-0510     *Dial phone number
  MENU V                    *Toggle VIEW FLAG 
  ECHO Phone line connected.
  ECHO Processing login for |%2.
  WAIT //                     *Wait for a "//" from modem
  SEND ""                     *Send a carriage return to modem
  WAIT --                     *Wait for a "--" from modem
  SEND "KMY"                  *Send "KMY"
  WAIT :                      *Wait for ":" 
  SEND "KMY,CLEVLND"          *Send "KMY,CLEVLND"
  WAIT #######                *Wait for "#######"
  SEND "PASSW,TF639BN,*CAMS*" *Send line
  WAIT :                    
  SEND "12345"
  ECHO Logged in going to terminal mode.
  ECHO
  *                -- END OF THE KMY PROCEDURE
  GOTO |%3                  *Goto label in string var 3
 |LABEL DG                  *Routine for login Data General
  SEND "ATDT9,1-612-123-4567" *Send ATDT command to modem
  MENU M3D:DG210.EMU        *Load emulation file D:DG210.EMU
  MENU B3400300             *Set baud rate com port options
  GOTO |%3                  *Goto label in string var 3
 *END OF THE DG PROCEDURE   *comment line  
 |LABEL OFFICE              *Routine for login TALKCOM HOST 
  MENU B3400300             *Use menu procedure for baud rate
  MENU D ATDT9,123-4567     *Use menu procedure for dialing
 |LABEL TERMINAL MODE       *Make label TERMINAL MODE
 |EOF                       *End INCLUDE format
 TZ                         *Macro menu commands for terminal 
                            *mode and toggle menu display 

     This  TALKCOM  macro file may be brought into  execution  by 
either of two ways.

     1. Typing TALKCOM LOGON KMY(cr),  for the KMY system, at the 
        DOS command line.
     2. Using the X command of the main menu and typing 
        LOGON DG(cr), for the DG system.
3. EMULATION FILES.

   a. Description.

      TALKCOM's  emulation files contain information loaded  into 
      the emulation look up tables. They have a file extension of 
      ".EMU". 
   
   b. Emulation File Line Syntax.

         The emulation loader requires the emulation files be set 
      to a definite structure. This structure contains flag codes 
      which  have  a value of 128 and above.  Each of these  flag 
      codes  indicates  to  the emulation  loader  what  type  of 
      information is to follow.  All values, except the emulation 
      name, are decimal values.     
       
        128 CDC75X
        129 32
        130 25
        131 22  0 24  1 25 8 14  6 15  7 
            23 15 27 10  3 9 21 11 26 13
            31  9 18  9 12 9
        132 49  4
        133 0
        134 1
        255

      Above  is  an  example of an emulation  file.  It  actually 
      emulates a CDC 752 terminal in X/Y position mode.  In  this 
      emulation file all values above 128 are flag codes.


       The different flag codes are :

      Function
       code                Definition
       ----- ------------------------------------
        128  Used  to name the emulation file.  One line of  text 
             per flag code.  It may also be used as a remark line 
             anywhere in the file.

        129  The value following will become the bias  added 
             to the received XY positioning values.

        130  The value following indicates the number of lines on 
             the screen to use for terminal emulation.

        131  Indicates that the values following are to be loaded 
             into  the  receive  table.  The  format  is  receive 
             character  code SPACE function code.  In the example 
             above,  a  receive character of 22 decimal (Ctrl  V) 
             would  cause  function code 0  (Clear  from  current 
             column to end of line) to executed.

        132  Indicates that the values following are to be loaded 
             into the receive-escape table. The format is receive 
             character  code SPACE function code.  In the example 
             above,  if  a receive sequence of 27 41 X Y  (ESC  1 
             colX rowY) was received,  then function code 4 (Goto 
             XY position) would be executed.

        133  The  following value is used to indicate to  TALKCOM 
             that  no character has been received since the  last 
             com  port  poll.  Default is 00.  This may become  a 
             problem  in  some terminal emulations.  Use  133  to 
             change this value. 

        134  Advance after high intensity. Some terminals advance 
             the  cursor  after the receipt of a  high  intensity 
             command. If the emulation loader sees a 134, TALKCOM 
             will also.

        135  Indicates that the values following are to be loaded 
             into  the  send  table.   The  format  is   keyboard 
             character code SPACE send character code.

        136  Indicates that the values following are to be loaded 
             into  the send-escape table.  The format is keyboard 
             character  code  SPACE the string of  characters  to 
             send.

        137  Indicates  that the Y coordinate is given  first  in 
             the position XY cursor command. 


        138  Indicates  the  following value is to be used  as  a 
             "super-shift"  character.  "Super-shift" can be used 
             when  a  terminal  emulation  needs  more  then  ten 
             function keys (i.e.  a "super-shift" F1 may indicate 
             a F11, etc.).

        139  Indicates  to the loader to immediately execute  the 
             following value as a emulation function code. 

        255  Indicates to the loader that the emulation file load 
             loop is over.

        The  receive  lookup  table is mostly used  for  checking 
      single  character control codes.  It contains values  which 
      are matched against the characters received.  If there is a 
      match  then the corresponding "function code" is  executed. 
      Function codes are a set of pre-declared functions existing 
      in TALKCOM. They are:

      Function
       code                Definition
       ----- ------------------------------------
          0   Clear from current column to end of line.
          1   Clear screen place cursor at top of screen.
          2   Delete current line. Scroll lines up one.
          3   Insert a line. Scroll lines down one.
          4   Goto  XY position.  Positions cursor to  the  given     
              X, Y position. This function expects the X position 
              (a  column  value  between 1 and 80)   to  be  send 
              first,  then  the Y (a row value between 1 and 25). 
              If this is not the way the terminal emulated  works 
              then  the "bias" and Y first must be  defined.  The 
              upper  left hand corner of the screen is column  1, 
              row 1.
          5   Clear to end of screen.  Clears from current cursor 
              position  to  the end of the  screen.  The  current 
              cursor position remains the same.
          6   Start  high  intensity.  High intensity remains  in 
              effect until a low intensity is received.
          7   Start  low  intensity.  Turns  off  high  intensity 
              field.
          8   Home. Moves cursor to position 1,1.
          9   NOP.  Throws the receive character away.
         10   Escape Load.  Check next character in the  receive-
              escape table.
         11   Cursor right.  Moves cursor right one position.  No 
              wrap at right margin.   
         12   Cursor  left.  Moves cursor left one  position.  No 
              wrap at left margin.
         13   Cursor up. Moves cursor up one line.
         14   Cursor down. Moves cursor down one line.  
         15   Start blink mode.  Turn on blink mode. Reset by low 
              intensity.  
         16   Turn local printer off. Reset parallel print.
         17   Turn local printer on. Sets parallel print option.
         18   Display CR/LF sequence. 
         19   Where X/Y. Returns the current X/Y positions.
         20   VT100  assist.  This  function  handles  the  VT100 
              format  of  parameters and commands and  translates 
              them into the function codes listed above.
         21   Auto-wrap on. This turns wrap at column 80 on (this 
              is the default).  
         22   Auto-wrap off. This turns wrap at column 80 off.

      As in the CDC 752 example,  you can see that loading of the 
      receive  table (loader flag 131) can continue onto the next 
      line  and will continue to load until a value greater  then 
      127 is read.

       The  receive-escape  lookup  table  is  used  when  a  two 
      character  function  is required  for  emulation.  This  is 
      normally  an escape followed by a second  character.   Only 
      the  second receive character is matched against the table. 
      The escape character is indicated in the receive table with 
      function  code  10.  The receive-escape  lookup   table  is 
      loaded using loader flag 132.  In the CDC 752 example,  the 
      escape  code is 27(indicated by function code 10) and a "1" 
      (decimal value 49) is the receive-escape table entry.  When 
      an  "ESC  1"   (decimal values 27  49)  are  received  then 
      function code 4 (goto xy) will be executed.    

       The  send  lookup  table  is used to  translate  a  single 
      keyboard  character to a different character which will  be 
      sent  to the connected system.  As with the receive  lookup 
      table  loading  can continue onto the next  line  and  will 
      terminate  when a value greater then 127 is read.  The send 
      lookup  table is loaded using loader flag 135.  All  values 
      contained  in the emulation file are decimal values of  the 
      character to translate or send.

       The  send-escape  lookup  table is  used  when  an  escape 
      sequence  from  the  keyboard needs to be translated  to  a 
      different  character  sequence  that will be  sent  to  the 
      connected system.  TALKCOM was written in TURBO PASCAL,  so 
      function,  cursor, and ALT keys return escape sequences. If 
      you  do  not  know what codes TURBO  assigns  you  can  use 
      TALKCOM to display them. Enter terminal mode (T) then press 
      an F(unction) key.  Pressing F10,  for example,  you should 
      see a left arrow followed by a D (decimal values 27 68).
       
         136 59 27 82

      To use F1 to send an escape R to the connected system,  the 
      above  line  would be entered into the  emulation  file.  A 
      sequence of up to six characters may be sent from the send-
      escape table.  The send-escape table is loaded using loader 
      flag 136.

             128 VT52
             129 32
             130 24
             137
             131 27 10 
             132 65 13 66 14 67 11 68 12 
                 72  8 74  5 75  0 89  4 
                 61  9 62  9
             133 127
             134 0
             135 11 10
             135 8 127
             135 12 10
             136 59 27 82
             136 60 27 65
             136 61 27 63 121
             136 62 27 66
             136 63 27 63 118
             136 64 27 67
             136 65 27 63 115
             136 66 27 68
             136 67 27 63 110
             136 68 27 63 77
             136 72 27 65
             136 75 27 68
             136 77 27 67
             136 80 27 66
             136 83 127
             136 84 27 80
             136 85 27 81
             136 86 27 63 119
             136 87 27 63 120
             136 88 27 63 116
             136 89 27 63 117
             136 90 27 63 113
             136 91 27 63 114
             136 92 27 63 112
             136 93 27 63 112
             255

      The above is an example of DEC VT52 emulation.


      Emulation files included are :

         CDC  75X
         DEC VT52
         DEC VT100
         DP  8220
         DG   210


TALKCOM MENU COMMAND SET     - Command Summary -

                            TALKCOM Menu Commands

File Commands -
     S -  Send a file to the connected system.
     R -  Receive a file from the connected system.
     O -  Open a terminal save file ( capture file ).
     C -  Close terminal save or receive file.
     P -  Print file(s). File name can include "wildcards".
     Y -  Erase file(s). File name can include "wildcards".

Execution Commands -
     X -  Execute TALKCOM batch file.
     T -  Enter terminal mode.
     V -  Toggle view flag
     B -  Set baud rate.( default = 1200 baud,8 bits, no parity)
     D -  Send entered string to COM port.          
     M -  Load and enable terminal emulation mode. 
     U -  Request and run DOS command line. 
     H -  Becomes a host machine for remote PC access.

Misc. Commands -
     F -  Saves a forms feed character in the terminal save file.
     I -  Delay to given time of day.

     E -  Exit to DOS, reset modem before leaving.
     N -  Exit to DOS, no reset of the modem.
     Z -  Special  command to turn off menu displays during macro 
          files. Does not appear on menu.
 Summary of TALKCOM Standard Functions and Send File Procedures 

     Functions  are  designated  by a |% (the  value  of)  symbol 
proceeding the identifier.  Procedures are designated by having a 
|  VERTICAL LINE in column 1.  A line having a | VERTICAL LINE in 
column  1,  but not being one of the standard procedures will  be 
treated as a comment line. 

     Str, target, label, help and message are string expressions. 

     X, y, z, g and h are integer expressions. Integer operations 
     include  addition(+),   subtraction(-),   multiplication(*), 
     division(/), OR(OR) and AND(AND).

     e is a hex value.

     N and f are integer values.

     Label id is a string of characters terminated by a  carriage 
     return. 

     File  name is a legal DOS file name.  Drive letters but  not 
     paths may be specified.  

     Operation is relational operators EQ, LT, GT and NE.  
 



COMMUNICATIONS RELATED
  Functions  - 
     |%BUFFER

  Procedures -
     |BREAK  
     |CASE
     str1=label1
     str2=label2
     |ENDCASE
     |CHRPACE x
     |GET x %g or |GET x CHAR INTO %g
     |GET LINE %g or |GET LINE INTO %g
     |HANGUP
     |IDLE x
     |IF COMIN THEN proc
     |ON TIMEOUT label
     |PACE x
     |REPEAT WAIT str
     |SEND "str" n n
     |SENDNR "str" n n
     |TIMEOUT x
     |WAIT str 

FILE INPUT AND OUTPUT
  Functions -
     |%READBUF

  Procedures -
     |EOF
     |IF EXIST(file name) THEN proc
     |IF EOF(file name) THEN proc
     |INFILE OPEN file name
     |INFILE CLOSE file name
     |INFILE READ %g
     |INFILE READ %READBUF
     |WRITE "str" n n 
     |WRITENR "str" n n


VARIABLE RELATED
  Functions -
     |%n
     |%Cn
     |%|%
     |%COPY("str",x,y)
     |%LENGTH(str)
     |%POS("str",target)

  Procedures - 
     |CLEAR ALL
     |CLEAR TOGGLES
     |CLEAR Cx,Cy
     |CLEAR %g,%h
     |DEC(Cn)
     |DELETE(%g,x,y)
     |INC(Cn)
     |INSERT(str,%g,x)
     |PAD %g,d,x     (d="L" for pad left or "R" for right) 
     |POP Cx
     |POP %g
     |PUSH Cx
     |PUSH %g
     |SET Cx=y
     |SET %g=str
     |TRIM %g,d,x    (d="L" for trim left or "R" for right) 
     |UPSTR %g

SCREEN / KEYBOARD RELATED PROCEDURES

     |BEEP
     |CLEAR FIELDS
     |CLS 
     |ECHO message
     |ECHONR message
     |FIELD,x,y,n,f,j,"help"
     |GOTOXY(x,y)
     |IF KEYPRESSED THEN proc
     |MULTIF,f,"str"
     |READKBD %g
     |READKBDC %g
     |READSCR

SEND FILE FLOW CONTROL PROCEDURES

     |EXIT
     |GOSUB label
     |GOTO label
     |IF "str" operation "str" THEN proc [ ELSE proc ]
     |IF x operation y THEN proc [ ELSE proc ]
     |LABEL label id
     |LOOP Cx NE 0 label
     |LOOP Cx TO y label
     |LOOP Cx DOWNTO y label
     |RETURN


MISCELLANEOUS PROCEDURES AND FUNCTIONS 
  Functions -
     |%ADDR
     |%DAY
     |%DATE
     |%DECM(e)
     |%EVAR(str)
     |%HEX(x)
     |%MEM[x:y]
     |%PORT[x]
     |%TIME
     |%VER

  Procedures - 
     |DELAY x 
     |ECHO ON
     |ECHO OFF
     |MENU str
     |NO DATA
     |SET MEM[x:y] = z
     |SET PORT[x] = y
     |SET RC=x

SCRLOOK.

     The  SCRLOOK program creates a TALKCOM macro file to be used 
for  a full screen input form.  It receives input from  an  input 
file name SCR.INP and a series of keyboard prompts.  For example, 
let  us assume that you would like to use the input form as shown 
below.

  _____________________________________________________________
 |                  Employee Input Form                        |
 |                                                             |
 | Enter employee's last name  : _______________               |
 |                                                             |
 | Enter employee number       : _____                         |
 |                                                             |
 | Enter employee's work shift : _______                       |
 |                                                             |
 |                                                             |
 |                                                             |
 |                                                             |
 |            Additional employees ( Y/N ) ? _                 |
 |_____________________________________________________________|


     The following steps would be done.

1. Create  form  using any ASCII text editor,  such as FSEDIT  or 
   WordStar non-document mode.  Save it as file name SCR.INP. The  
   underscore  character ( _ ) is used to define the position and 
   length of the input fields.

2. Type "SCRLOOK" (cr). 
    
   The following screen will be displayed.

  _____________________________________________________________
 |SCRLOOK Version X.XX             Data field options screen   |
 |Enter output file name :                                     |
 |                                                             |
 |                                                             |
 |_____________________________________________________________|

3. Enter an output file name. For example, SCR.OUT.

4. The  following set of prompts will be displayed.  One  set  of 
   prompts for each input field define in SCR.INP .
  _____________________________________________________________
 |SCRLOOK Version X.XX             Data field options screen   |
 |Enter output file name : scr.out                             |
 |20 Characters preceding field (loyee's last name  :)         |
 |Field Number = 1                                             |
 |Justified    = L                                             |
 |Help Line    =                                               |
 |OK ? y                                                       |
 |                                                             |
 |_____________________________________________________________|

   The field number is assigned from top to bottom left to  right 
   starting with 1.  This field number corresponds to the TALKCOM 
   string  variable number to use.  The field data can be  either 
   left  or  right justified within the field's width and  spaces 
   are added if needed.  The help line is a character string  (40 
   characters  max.)  that will be displayed on line 25 when  the 
   cursor is positioned to that field. 

   If  you  answer "y" or (cr) to the OK prompt,  then the  field 
   options displayed will be used.  If you answer "n" or anything 
   else, then you will be prompted for each field option as shown 
   below. 

  _____________________________________________________________
 |SCRLOOK Version X.XX             Data field options screen   |
 |Enter output file name : scr.out                             |
 |20 Characters preceding field (loyee's last name  :)         |
 |Field Number = 1                                             |
 |Justified    = L                                             |
 |Help Line    =                                               |
 |OK ? n                                                       |
 |Field Number : 15                                            |
 |L for left justified or R for right : l                      |
 |Help line (40 characters max) : Use last name only.          |
 |                                                             |
 |_____________________________________________________________|

5. Answer the multiple definition prompt. 
  _____________________________________________________________
 |SCRLOOK Version X.XX             Data field options screen   |
 |Enter output file name : scr.out                             |
 |20 Characters preceding field ( employees (Y/N) ? :)         |
 |Field Number = 4                                             |
 |Justified    = L                                             |
 |Help Line    =                                               |
 |OK ? y                                                       |
 |                                                             |
 |Any multiple definition fields ( Y / N ) ? y                 |
 |Enter field number. Blank line to end input. 3               |
 |Enter field data : days                                      |
 |Enter field number. Blank line to end input. 3               |
 |Enter field data : swings                                    |
 |Enter field number. Blank line to end input. 3               |
 |Enter field data : mids                                      |
 |Enter field number. Blank line to end input.                 |
 |_____________________________________________________________|

   If  you  answer  "y" (yes) that there is  multiple  definition 
   fields,  then   you will be prompted for the field number  and 
   field data. 

   Multiple  field  definitions are used to preset  and  limit  a 
   field  with  certain values.  In the example  above,  field  3 
   defined  work shifts and the only possible responses you would 
   like  are "days","swings" or "mids".  The "days" value is  the 
   default. 

   At  data  entry time,  field 3's value would be  toggled  from 
   "days", "swings" and "mids" using the + and - keys. This field 
   would not require a case check or a valid entry check since it 
   can only contain one of the three preset values.

6. Use  the  SCRLOOK output file.  The file may be included  into 
   your TALKCOM macro file or used as a building block.  Below is 
   the SCRLOOK output file (SCR.OUT) from the examples above.

     ZSI
     |NO DATA
      CLS
      CLEAR FIELDS
      FIELD,31,4,15,1,L
      FIELD,31,6,5,2,L
      FIELD,31,8,7,3,L
      FIELD,44,13,1,4,L
      MULTIF,3,"days"
      MULTIF,3,"swings"
      MULTIF,3,"mids"
      GOTOXY(18,2)
      ECHO Employee Input Form
      GOTOXY(1,4)
      ECHO Enter employee's last name  :
      GOTOXY(1,6)
      ECHO Enter employee number       :
      GOTOXY(1,8)
      ECHO Enter employee's work shift :
      GOTOXY(13,13)
      ECHO Additional employees ( Y/N ) ?
      READSCR
     |EOF
     Z

INCOLOR.

     This program allows the user to specify which foreground and 
     which  background  colors  they prefer to use  when  in  the 
     TALKCOM  program.  At the DOS command prompt,  enter INCOLOR 
     (cr). Follow the prompts to specify which program to set the 
     colors into,  and then which colors to set into the  program 
     specified.  The color selections are shown as each option is 
     selected  so the user can tailor the screen colors to  their 
     particular preference.
 
                             ***  NOTE  ***
     INCOLOR  is  a general purpose program and used  with  other 
     programs.
________________________________________________________________
|                                                              |
|           COLOR INSTALL PROGRAM VERSION X.X                  |
|                                                              |
|           E     CHANGE ENTERED FILE NAME                     |
|                                                              |
|           F     CHANGE FSEDIT                                |
|                                                              |
|           I     CHANGE INCOLOR                               |
|                                                              |
|           T     CHANGE TALKCOM                               |
|                                                              |
|           ENTER YOUR CHOICE   :                              |
|                                                              |
|______________________________________________________________| 


     After  making a program selection,  a second menu screen  is 
     brought  up allowing selection of background,  normal  text, 
     and  highlight  text colors for both the screen  and  status 
     lines. The function keys make the color selections. Function 
     key F10 makes the color choices permanent in the program you 
     have selected.

                        USER COMMENT FORM
                       ------------------
 Your  comments  assist  us in improving the  usefulness  of  our 
systems,  please  fill out the following form.  This  information 
will  be used to alert you of any future releases.

Your Name __________________________________   Facility ________

Product or system's name   TALKCOM             Version 2.4A3      

HARDWARE

1. Type of computer program being run on.

 _ a.IBM PC _ b.Z150 _ c.Columbia _ d.Other(specify) ____________  

2. Type of modem being used.

 _ a.HAYES  _ b.UDS _ c.Multitech _ d.Other(specify) ____________

SOFTWARE
                                         poor       excellent
3. How would you rate the software.         
   a. For ease of use                       1 2 3 4 5
   b. For completeness                      1 2 3 4 5
      (Doing what is documented)
   c. For accuracy                          1 2 3 4 5
      (Number of errors or bugs)                   

4. How would you rate the documentation.
   a. For ease of use                       1 2 3 4 5
   b. For completeness                      1 2 3 4 5
   c. For accuracy                          1 2 3 4 5

OTHER

5. Brief description of old method of doing this task.
   ______________________________________________________________ 
   ______________________________________________________________

6. Comments
   ______________________________________________________________
   ______________________________________________________________
   ______________________________________________________________ 
   ______________________________________________________________
   ______________________________________________________________
   ______________________________________________________________

         PLEASE RETURN TO:    CONTROL DATA CORP.
                              6701 ROCKSIDE RD.
                              INDEPENDENCE, OHIO  44131
                        ATTN: GARY CURTIS  FAC. CODE: CLEASO

 RD.
                              INDEPENDENCE, OHIO  44131