Zmodem-T Console Receiver

        RT.BAT  = DSZ.COM port 1 speed 2400 d pB8192 t -y8g

        enter RT to go on-line and ALT-X to go off-line (the DOS prompt).



                        Zmodem-Z Console Transceiver

        SZ.BAT  = DSZ.COM port 1 speed 2400 D pB8192 sz -Zty8g %1 %2 %3

        enter SZ Filespecs at the DOS prompt and use CTRL-Break to abort.


        after sending Files  the Transmitter  becomes a Console Receiver.
        enter ALT-X to go off-line (the DOS prompt) and RT to go on-line.



____________________________________________________________________________



       PROGRAM:         DSZ.COM   Zmodem Driver, Borland Turbo-C Version

       PROGRAM:         DSZ.EXE   Zmodem Driver, Microsoft-C LIB Version



       PURPOSE:         High-performance File Transfer Engines



   DESCRIPTION:         DSZ is a State-of-the-Art File Transfer Engine
                        that functions as a  DOS Console Terminal  or,
                        as an  External Transfer Protocol Driver  for
                        sending and receiving Files.



      FEATURES:     T   Zmodem Batch-T  DOS Telecommunications Console

                    A   Zmodem Batch-Z  with RLE compression for  ASCII
                    W   Zmodem Batch-W  with sliding window for TELENET
                    R   Zmodem Batch-R  with automatic  Crash  Recovery

                    Z   Zmodem Batch with 32-bit CRC  error correction
                    B   Ymodem Batch with 16-bit CRC  error correction
                    Y   Xmodem-1k /CRC /CheckSum /-G  error correction
                    X   Xmodem    /CRC /CheckSum /-O  error correction

                    G   Ymodem Batch-G  for hardware  error correction





   PERFORMANCE:         Observed Throughput  ( avg ARC File Size = 48 Kb )



                        CCITT V.22 2400 Baud STD Modem

        228 ñ 5 c.p.s.  ZMODEM-Z transfer ARC Files, direct CONNECT 2400

        213 ñ 5 c.p.s.  ZMODEM-Z transfer ARC Files through Telenet 2400

        108 ñ 5 c.p.s.  ZMODEM-Z transfer ARC Files through Telenet 1200



                        CCITT V.22 2400 Baud MNP Modem

        278 ñ 5 c.p.s.  YMODEM-G transfer ARC Files, direct CONNECT 2400 MNP

        223 ñ 5 c.p.s.  YMODEM-G transfer ARC Files through Telenet 2400 MNP

        113 ñ 5 c.p.s.  YMODEM-G transfer ARC Files through Telenet 1200 MNP



                        CCITT V.29 9600 Baud HST Modem

       1148 ñ 5 c.p.s.  YMODEM-G transfer ARC Files, direct CONNECT 9600 HST

       1048 ñ 5 c.p.s.  ZMODEM-Z transfer ARC Files, direct CONNECT 9600 HST






                CHARACTERISTICS



      DSZ.COM :         Compiled with Borland Turbo-C run-time Library.

                        the COM Driver uses less memory than EXE Driver

                        the COM Driver executes when both are on d:\path



      DSZ.EXE :         Cross-compiled using the Microsoft "C" Library.

                        the EXE Driver does not support a pB8192 buffer

                        the EXE Driver does not support  MS-DOS "SHARE"


                        the EXE Driver uses table-driven lookup of CRCs

                        the EXE Driver uses different run-time routines

                        the EXE Driver provides more throughput at 9600







____________________________________________________________________________



        AUTHOR:         Chuck Forsberg, Omen Technology, Inc


       ADDRESS:         17505-V Northwest Sauvie Island Road
                        Portland, Oregon  USA  97231


  REGISTRATION:         Enables advanced features of DSZ, and provides
                        the author with funding for new development.

                        For VISA/MC Registrations, call (503) 621-3406


        U.S.A.:         Mail $20.00 to  Omen Technology Inc
                                        P.O. Box 4681
                                        Portland, Oregon USA 97208


        CANADA:         Mail $20.00 to  Dynamis Productivity Software Ltd
                                        P.O. Box 5008, Station B
                                        Victoria, BC  V8R  6N3


      OVERSEAS:         Mail $25.00 to  Omen Technology Inc
                                        P.O. Box 4681
                                        Portland, Oregon USA 97208


____________________________________________________________________________



                              COMMAND  LINE  SYNTAX



        DSZ [parameters] [numeric parameters] command [-options] [File]


        SYNTAX:         The DSZ command line is lengthy, case sensitive
                        and position dependent. Although the parameters
        and options provide advanced features and enable operation with
        a variety of modems and transmission mediums, all configuration
        of the driver is done from the DOS command line or environment.

        To realize the full potential of DSZ, one must make Batch Files
        to act as receivers and transmitters.  Using numeric parameters
        and command -options, receivers and transmitters are fine tuned.



         USAGE:


    DSZ [port n] [speed s] [ha x] [est 0 b] [d/D] [pB8192] command [-options]


                        Use SET DSZLOG=d:\path\DSZ.LOG in AUTOEXEC.BAT
                        to create a Log File located on d:\path.  This
                        File is updated by DSZ after any File transfer.




                ENVIRONMENT  VARIABLES



        DIRRX=d:\path                   specifies a directory to receive to

        DIRRX=d:\path\                  specifies absolute receive directory

        DSZFILES=File1 File2 File3      specifies Filename(s) to send batch

        DSZLOG=d:\path\DSZ.LOG          specifies log File name and location

        DSZOPT=ty8g                     specifies global command line options

        DSZPORT=2                       specifies serial port for operations

        MAXBYTES=1024000                specifies maximum bytes per transfer

        ZONE=420                        specifies minutes behind GMT for PST






____________________________________________________________________________




                        COMMAND  LINE  PARAMETERS



        CON             specifies redirection to the DOS console  CON:

                        use this parameter when operating in CTTY mode

                        use this parameter for the  ProComm  HOST mode

                        alternatively, use  >CON  >PRN or >NUL  at the
                        end of a command line to redirect the display.

                        use  >filespec  to  "capture"  console data to
                        a disk File - press ALT-X (after RXD modem LED
                        stops glowing) to end capturing data.

                        the default device is CON:, unless re-directed


         NOTES:         The CON parameter must be the first parameter
                        on the command line when used.




        port n          specifies the COMn: serial communications port

                        n = 1,2,3,4  for IBM PC/XT and PC/AT computers

                        n = 10,11,12,13  for IBM PS/2 computer systems

                        alternatively,  SET DSZPORT=n  in AUTOEXEC.BAT

                        the default communications port n = 1 for COM1




        speed s         opens the COMn: serial port with Baud Rate = s

                        s =  300, 1200, 2400, 4800, 9600, 19200, 38000

                        or, use  MODE COMn:,s,N,8,1,-  in AUTOEXEC.BAT

                        the default Baud Rate is initialized by MS-DOS




        ha x            enables hardware and/or software handshaking x

                        ha bo   enables XON/XOFF and RTS/CTS handshake

                        ha on   specifies RTS/CTS hardware handshaking
                        ha slow specifies RTS/CTS, drops RTS for Disks

                        ha cts  specifies CTS (5) hardware handshaking
                        ha dsr  specifies DSR (6) hardware handshaking
                        ha dcd  specifies DCD (8) hardware handshaking

                        the default handshaking is XON/XOFF for Zmodem
                        and Ymodem Batch or, no handshaking for Xmodem




        est 0 b         estimates Batch Transfer times for Baud Rate b

                        Use this parameter to achieve better estimates
                        of Batch Transfer times when the port is setup
                        for a fixed speed and the modem Baud is lower.

                        syntax:         est filesize baudrate

                        the default estimate is based upon the speed s


         NOTES:         The estimate parameter must follow port, speed,
                        and handshake parameters, when used.




        d               disables checking DCD (8) for a CARRIER - this
                        is useful for operating in "tty" mode before a
                        CARRIER is present, and for direct connections.

                        the default check DCD (8) for a CARRIER is ON.

        D               enables  checking DCD (8) for a CARRIER and it
                        will drop DTR (20) if CARRIER is not detected:
                        useful for a BBS or other HOST installation.




        pB8192          creates an 8 Kilobyte Disk Buffer for DSZ.COM

                        Use this parameter to minimize Disk Read/Write
                        activity for operations at or below 2400 Baud.

                        the default Disk Buffer is 1 Kilobyte for DSZ

         NOTES:         The pB8192 parameter is not applicable to the
                        DSZ.EXE Driver, or recommended above 2400 bps.



____________________________________________________________________________




                        COMMAND  LINE  NUMERIC  PARAMETERS



                        The Driver is rich with timing adjustments and
                        alternative configuration options.


        p               Use  DSZ d p t  to display numeric paramerters

        z p             Use  DSZ d z p t  to display  "zmodem"  params

        p z p           Use  DSZ d p z p t  to display all DSZ numeric
                        parameters and their default values.


         NOTES:         Numeric parameters are specified by p_ values,
                        and "zmodem" numeric parameters by  z p_ .

                        Numeric parameters are generally specified at
                        the end of a parameter list, before a command.

                        To get an accurate report of parameters on the
                        command line, use  p  or  z p  last, as in:

       EXAMPLE:         DSZ.COM D pB8192 p z pL1024 pw4096 p sz -k *.*

                        which displays an accurate report of the  pB_
                        numeric parameter and the pL_ and pw_ "zmodem"
                        numeric parameters.






                p_      NUMERIC PARAMETERS




        pB8192          creates an 8 Kilobyte Disk Buffer for DSZ.COM

                        Use this parameter to minimize Disk Read/Write
                        activity for operations at or below 2400 Baud.

                        the default Disk Buffer is 1 Kilobyte for DSZ


         NOTES:         The pB8192 parameter is not applicable to the
                        DSZ.EXE Driver, or recommended above 2400 bps.





        pO0             controls Xmodem "OverThruster" File transfers



                EXAMPLES OF OVERTHRUSTER CONFIGURATION



        pO-512  CompuServe XMODEM-Ovth  DSZ pO-512 ro Filename.ext

                Negative numbers up to a system dependent value less
                than the protocol block size increase throughput.

                Tune the  pO_  parameter for a specific Host computer.

                Try  pO-512  for  CompuServe  as the standard setting.

                Retry 0:  Received dup Sector - reduce parameter pO_ .



        pO60    XMODEM/-1k/-Ovth        DSZ pO60 rx -o Filename.ext

                Positive numbers up to a system dependent value less
                than the protocol block size increase throughput.

                Tune the  pO_  parameter for a specific Host computer.

                Try  pO60  for 2400 Baud MNP as the standard settting.

                Retry 0:  Received dup Sector - reduce parameter pO_ .



        pO60    YMODEM/-1k/-Ovth        DSZ pO60 rb -o

                Parameter pO_ is useful for tuning a CRC-16 receiver to
                one  particular  Host  and  transmission  medium.


         NOTES:

                The idea behind -Ovth is for the receiver to transmit an
                ACK for Block a few ticks before all 1,024 bytes come in.
                Fiddling with the pO_ parameter, positive/negative values
                show different effects with different modems and mediums.

                "OverThruster" is an  "advance ACK"  configured receiver.
                Varying the  pO_ parameter  eeks out the last few  c.p.s.
                possible for CRC-16 based, Xmodem/-1k and Ymodem-K Batch.
                This is when you get down to configuring a receiver for a
                particular Host... like, she's gotta have it.

                Because  -o closes the "artificial window" between sender
                and receiver, re-synchronization is unlikely after error.

                Whenever hardware error correction is available, the -g
                Gonzomode is the fastest way to receive compressed Files.





        pQ1             errorlevel returned to DOS when transfer fails




        pS15            timeout in seconds to wait after receiving the
                        XOFF (CTRL-S) character or, after CTS went low.

                        the default wait for handshake is  15  seconds.


         NOTES:         Use CTRL-Break to unlock Receiver Console after
                        receiving an XOFF (CTRL-S).





        pW0             timeout in seconds to wait before exiting upon
                        File transfer error.





        pa2000          CPU calibration for Xmodem and Ymodem  8088-05

        pa4000          CPU calibration for Xmodem and Ymodem  8086-08

        pa6000          CPU calibration for Xmodem and Ymodem 80286-08/1

        pa8000          CPU calibration for Xmodem and Ymodem 80286-10/1

        pa10000         CPU calibration for Xmodem and Ymodem 80386-16/1

        pa12000         CPU calibration for Xmodem and Ymodem 80386-20/1


         NOTES:         the default pa_ timing is 2000 for a PC/XT i.d.

                        the default pa_ timing is 6000 for a PC/AT i.d.





        pd1             enables sending  File Date Header information,
                        the default Batch transfer timestamp method.

        pd0             disables sending File Date Header information,
                        and uses current (receiver) date for new Files.





        pv0             disables DSZ "trace" mode, the default setting

        pv1             rings console BEL at the end of File transfers

        pv2             enables DSZ "trace" mode, displays Sector info





        pz0             timezone in minutes behind GMT world standard

        pz300           timezone in minutes behind GMT for  EST  Zone

        pz360           timezone in minutes behind GMT for  CST  Zone

        pz420           timezone in minutes behind GMT for  PST  Zone

                        alternatively, SET ZONE=420  in  AUTOEXEC.BAT





              z p_      ZMODEM NUMERIC PARAMETERS




      z pb0             disable sending of BREAK upon transfer error

      z pb1             enable sending of BREAK upon transfer error,
                        useful for clearing some high-speed modems.





      z pB2             duration in tenths of a second of the BREAK
                        signal - default is 200 milliseconds.





      z pC11            number of repetitions of a ZCOMMAND request

                        see ZCOMMDOC for more information...





      z pe0             disables escape of ASCII control characters,
                        the default setting.

      z pe1             enables  escape of ASCII control characters,
                        useful on certain networks.





      z pl0             disables wait for ACK for each Zmodem sector,
                        the default setting (free flowing).

      z pl4096          enables  wait for ACK after every 4096 Bytes,
                        transforms Zmodem to -4K Block, CRC-32 Batch.





      z pL0             enables auto-config of  Zmodem  Sub-Packets

      z pL128           configures Zmodem for  128 Byte Sub-Packets

      z pL256           configures Zmodem for  256 Byte Sub-Packets

      z pL384           configures Zmodem for  384 Byte Sub-Packets

      z pL512           configures Zmodem for  512 Byte Sub-Packets

      z pL1024          configures Zmodem for 1024 Byte Sub-Packets


         NOTES:         Larger Zmodem Sub-Packet sizes give better
                        performance on clear transmission lines.

                        Smaller Zmodem Sub-Packet sizes give better
                        performance on noisy transmission lines.

                        it is convenient to set sub-packet sizes to
                        one-fourth the effective Zmodem "window", as:

                                DSZ z pL256 pw1024 sz Filespecs

                                DSZ z pL384 pw1536 sz Filespecs

                                DSZ z pL512 pw2048 sz Filespecs

                                DSZ z pL1024 pw4096 sz Filespecs





      z pn0             defines the number of ASCII NULL characters
                        sent before each  ZDATA  frame - useful for
                        FastLink modems.





      z pp50            timeout in tenths of a second for a receiver
                        to wait for gaps within a packet. The default
                        wait is  5  seconds.





      z pP2             the default  z pP_  value is 2





      z pr0             disables removal of incomplete Files received,
                        the default setting.

      z pr1             enables  removal of incomplete Files received,
                        useful for Host systems:  DSZ z pr1 rz -p





      z ps15            timeout in seconds to wait after receiving the
                        XOFF (CTRL-S) character or, after CTS went low.

                        the default wait for handshake is  15  seconds.


         NOTES:         Use CTRL-Break to unlock Receiver Console after
                        receiving an XOFF (CTRL-S).





      z pt100           timeout in tenths of a second for a receiver
                        to wait for a packet or acknowledgement from
                        the sender.  The default is  10  seconds.





      z pT600           timeout in tenths of a second for the sender
                        to wait for a packet or acknowledgement from
                        the receiver.  The default is  60  seconds.





      z pw0             disable "window"  flowing  ACK from receiver,
                        the default setting (free-flowing).

      z pw2048          enable  "window"  2 Kb for Telenet 1200 Baud,
                        requesting the receiver to send an ACK every
                        512 Bytes received.

      z pw4096          enable  "window"  4 Kb for Telenet 2400 Baud,
                        requesting the receiver to send an ACK every
                        1024 Bytes received.


         NOTES:         Larger Zmodem "windows" increase performance
                        but may cause excessive XOFF delays or loss
                        of data inside the network - to minimize the
                        frequency of XOFFs on Telenet, use:

                                SET? 0:33,35:10,41:1,64:4 <cr>

                        at the outdial PAD before transmitting Files.

                        the   z pw_   parameter is applicable to the
                        Zmodem sender, as in:  DSZ z pw4096 sz Files.

                        the  -wN option over-rides "z pw_" parameter.





      z pW1400          defines the number of characters the  Zmodem
                        receiver will eat when looking for the start
                        of a new frame.


         NOTES:         Increase  z pW_  to tune error recovery  for
                        networks with a large "window" of in-transit
                        packets.  "Garbage Count Exceeded" indicates
                        z pW_ is too low.





      z pZ0             the number of minutes to adjust a File date
                        when using  TELINK  or  CLINK  protocols to
                        transfer a File between time zones.








____________________________________________________________________________



                        TRANSFER  PROTOCOL  CONFIGURATIONS



        COMMANDS        TRANSMITTERS


        sz File(s)      Send Zmodem Batch the Filespecs to a Receiver.


        sz @D:FILES.LST Send Zmodem Batch the Filespecs specified with
                        the ASCII File "FILES.LST" located on Drive D:
                        to a Receiver.  Valid delimiters for Filespecs
                        within "FILES.LST" are a SPACE, TAB, or CR/LF

                        Alternatively, Files can be specified by using
                        SET DSZFILES=d:\path\FILE1.ARC FILE2.ARC (etc)
                        in the AUTOEXEC.BAT File.


        sz -Z File(s)   Send Zmodem Batch the Filespecs to a Receiver,
                        using "RLE" compression. This reduces the time
                        required to transmit ASCII Files; there is not
                        much benefit when sending ARC type Files.


        sz -w File(s)   Send Zmodem Batch the Filespecs to a Receiver,
                        using a  "sliding window" - forcing a Receiver
                        to transmit an  acknowledgement  to the Sender
                        every window ö 4 bytes. This feature is useful
                        for sending Files over Telenet.


        sz -k File(s)   Send Zmodem Batch the Filespecs to a Receiver,
                        using 1,024 byte packets instead of auto-shift.



        sb -k File(s)   Send Ymodem-1K or Ymodem-1K-G the Filespecs to
                        a Receiver.  The Receiver determines CRC or -G
                        error correction method. The Sender determines
                        128 byte or 1,024 byte (-1K) packet size.



        sx -k File      Send Xmodem-1k or Xmodem-1k-G the Filespec to
                        a Receiver.  The Receiver determines CRC, Sum,
                        or -G error correction method. The Sender sets
                        the Xmodem packet size.  Xmodem-1K-C  is often
                        called  Ymodem/CRC .


        sx File         Send Xmodem/CRC or Xmodem/Sum the Filespec to
                        a Receiver.  The Receiver determines CRC, Sum,
                        or -O error correction method.



        COMMANDS        RECEIVERS


        rz -y           Receive Zmodem Batch and overwrite an existing
                        File with the same name.


        rz -y d:\path   Receive Zmodem Batch and overwrite an existing
                        File with the same name on directrory d:\path

                        Alternatively, a Receive pathspec is specified
                        by using  SET DIRRX=d:\path  in  AUTOEXEC.BAT


        rz -r           Receive Zmodem Batch and overwrite an existing
                        File with the same name - starting at the last
                        byte of the existing File ( Crash Recovery )


        rb -y           Receive Ymodem Batch and overwrite an existing
                        File with the same name.


        rc -y File      Receive Xmodem/CRC or Xmodem/Sum or Xmodem-1k,
                        overwriting "File" if it already exists.



         NOTES:         ZMODEM uses 32-Bit Cyclical Redunancy Checking

                        YMODEM uses 16-Bit Cyclical Redunancy Checking

                        XMODEM uses 16-Bit CRC and falls back CheckSum




        COMMANDS        RECEIVERS  -  High Speed MNP, V29, V32  Modems


        rb -gy          Receive Ymodem Batch-G  and overwrite existing
                        File with the same name - use with MNP modems-
                        ...the fastest transfer protocol in use today.


        rc -gy File     Receive Xmodem-1k-G  and overwrite an existing
                        File with the same name - use with MNP modems-
                        ...compatible with Friel's "Ymodem-G".


        ro -y File      Receive Xmodem-O  "Overthruster" and overwrite
                        an existing File.  Useful for GEnie Downloads,
                        and Compuserve XMODEM Downloads.





____________________________________________________________________________



                        COMMAND  LINE  OPTIONS



        TRANSMITTER OPTIONS


                sz [-ZwNfkt8g]  [PREFIX=p] [ONAME=n]  Filespecs

                sb [-fkt8g]  [PREFIX=p] [ONAME=n]  Filespecs

                sx [-kt8g]  Filespec



        -Z      enables ZMODEM 12-Bit Lempel-Ziv compression of File contents.
                ...this is the fastest way to transmit ASCII and/or EXE Files.

        -wN     Configure a Zmodem "window" of N bytes, over-riding a ZMODEM
                z pw_ numeric parameter if also present.  The default window
                is 3072 Bytes for the -w option.

        -f      enables (Batch) send Files to specified  d:\path  of receiver.

        -k      enables 1 Kb XMODEM or YMODEM Blocks or Zmodem initial packet.






        RECEIVER OPTIONS


                rz [-r+npyt8g]  [d:\pathspec]  [Filesoecs]

                rb [-go+npyt8g]  [d:\pathspec]  [Filespecs]

                rc [-gyt8g]  Filespec

                ro [-yt8g]  Filespec



        -r      enables automatic Crash Recovery for Zmodem File transfers.

        -g      enables full-flowing XMODEM or, YMODEM-1K-G File transfers.

        -o      enables "OverThruster" mode for YMODEM-1K-O File transfers.





        CONSOLE TERMINAL OPTION for TRANSMITTERS and RECEIVERS


        -yt8g           This option will return the Sender or Reciver
                        to "tty" mode after a File Transfer. Add this
                        option to Transmitter/Receiver command line or,

                        Use  SET DSZOPT=yt8g  in AUTOEXEC.BAT to make
                        all transfer commands return to the "tty" mode
                        after Receiving or Sending File(s).

                        Use  SET DSZOPT=rt8g  in AUTOEXEC.BAT to make
                        all transfer commands return to the "tty" mode
                        after Receiving or Sending File(s) with Crash
                        Recovery enabled.





        FILE HANDLING OPTIONS



        -p      transfer File if and only if it does not exist on d:\path .


        -r      receiver:  recover data to an existing File

        -r      sender:  command receiver to recover data to existing File


        -+      receiver:  append data to an existing File

        -+      sender:  command receiver to append data to an existing File

                sz -+ ONAME=MASTER.LOG *.LOG   transmits all .LOG Files from
                the sender's directory and appends them to File  MASTER.LOG
                on the receiver's directory.


        -f      transmit a full pathspec with the filespec to the receiver.

                sz -f \path\Filespec    sends File to \path\ on remote Dir.

                sz -y PREFIX=\path\ *.LOG   transmits all .LOG Files from
                the sender's directory and overwrites on remote's \path\ .


        -n      transfer File if newer or non-existant on remote directory.

        -N      transfer File if newer or longer or non-existant on remote.


        -y      receiver:  overwrite data to an existing File

        -y      sender:  command receiver to overwrite data to existing File


        -Y      transfer File if and only if it exists on remote directory.





        MISCELLANEOUS OPTIONS



        -a      requests the receiver to adjust Files to ASCII standards.

        -b      inhibits the receiver from altering binary information.

        -e      inhibits Zmodem sender from transmitting control characters.

        -S      interrogates the receiver for DSZ serial number.

        -s      logs "questionable" aborts from a Zmodem receiver.

        -u      deletes the Filespec(s) sent after transfer is completed.

        -v      enables viewing of data being received during a transfer.

        -q      disables XMODEM and YMODEM "block" status line displays.

        -zT     specify T minutes behind GMT (Greenwich Mean Time) in place
                of pz parameter value, if also present.






____________________________________________________________________________



                        CONSOLE  TERMINAL  CONFIGURATION



        COMMANDS


        t -y8g          DSZ "tty"  8-N-1  Terminal Mode with automatic
                        Zmodem Batch Downloading -  Files received are
                        written to the current directory and overwrite
                        an existing File with the same name.

        t -r8g          DSZ "tty"  8-N-1  Terminal Mode with automatic
                        Zmodem Batch Downloading -  Files received are
                        written to the current directory and overwrite
                        an existing File with automatic Crash Recovery.

        t -gy8g         DSZ "tty"  8-N-1  Gonzole Receiver with Zmodem
                        Downloading -  Files received are overwritten,
                        hit F3 to begin Ymodem-1K-G Batch Downloading.



         NOTES:         Use  DEVICE=ANSI.SYS  in  CONFIG.SYS  to make
                        a DOS ANSI Console DEVICE.

                        Use ANSI.COM in AUTOEXEC.BAT to make PC Mag's
                        ANSI-IBM Console RESIDENT.

                        Use DEVICE=FCONSOLE.DEV in CONFIG.SYS to make
                        a FANSI-ZMODEM Console Receiver.  This DEVICE
                        provides a scroll-back screen buffer that can
                        be saved to disk, enhanced keyboard and video
                        performance, and full ANSI X3.64 emulation.




        CONTROLS


                        Fkey-1       -  exits to DOS (not Shell), with
                                        no loss of CARRIER.

                        Fkey-3       -  begin to receive Ymodem Batch;
                                        Zmodem receive is automatic.

         NOTES:         Use  DSZ t -gy8g  to enable YMODEM-1K-G  auto
                        downloading via Fkey-3.


                         ALT-X       -  exits to DOS (not Shell), with
                                        no loss of CARRIER.

                         ALT-N       -  aborts DSZ and returns to DOS,
                                        but does not drop the CARRIER.

                         ALT-P       -  toggles 8th bit parity off/on,
                                        note 8g is required for ANSI.

                         ALT-H       -  toggles local echo on, autoLF,
                                        and echo/LF off (default). Use
                                        this for PC to PC connections.

                         ALT-F       -  cancels a File being received;
                                        a Batch Transfer continues.

                         ALT-B       -  cancels a Batch of Files being
                                        received, returns to terminal.

                        CTRL-S       -  (XOFF) suspends receiving data

                        CTRL-Q       -  (XON)  resumes  receiving data

                        CTRL-X       -  (CAN)  cancels  receiving data

                        CTRL-Break   -  cancels any File Transfer then
                                        returns to terminal mode.  Use
                                        to unlock the local console if
                                        an XOFF (CTRL-S) is received.

                       SHIFT-PtScr   -  sends screen display to printer

                        CTRL-PtScr   -  trace console display on printer



      EXAMPLES:


                        Zmodem-T Console Receiver

        RT.BAT  = DSZ.COM port 1 speed 2400 d pB8192 t -y8g


                        Zmodem-R Console Receiver

        RZ.BAT  = DSZ.COM port 1 speed 2400 d pB8192 t -r8g


                        Zmodem-Z Console Transceiver

        SZ.BAT  = DSZ.COM port 1 speed 2400 D pB8192 sz -Zty8g %1 %2 %3


                        Zmodem-W Console Transceiver

        SW.BAT  = DSZ.COM port 1 speed 2400 D pB8192 sz -Zwty8g %1 %2 %3





                        CONSOLE  TERMINAL  OPERATION



        enter RT to go on-line and ALT-X to go off-line (the DOS prompt).

        enter RZ to go on-line with Zmodem CRC-32 Crash Recovery enabled.

        enter SZ Filespecs at the DOS prompt and use CTRL-Break to abort.

        enter SW Filespecs at the DOS prompt to transmit "window" Zmodem.


        Upon completion of a transfer the console is returned to terminal
        mode, acting effectively as a "transceiver".  Loading the program
        from a virtual (RAM) disk, the transition from DOS console to TTY
        is so fast that it feels as if "RT" is a DOS "RTTY" mode.

        To dial enter ATDT1234567 <cr>. To hang up enter three "+++" then
        wait for your modem's "OK" to appear and type  ATH <cr>.

        There is no software dialer inside DSZ.  With hardware dialing it
        really sings.  Software dialing is available from many integrated
        communications packages:  the DSZ "console transceiver" is closer
        to the DOS console and the Modem device than integrated packages.
        Rather like a Formula II car with no fenders or bumpers but with
        a very powerful Zmodem engine behind you.

        A DSZ console transceiver operator should be aware that his modem
        responds to typed commands beginning with the prefix "AT" and his
        console (display / keyboard) responds to "escape sequences", thus
        "emulating" an American National Standards Institute terminal.

        With FANSI CONSOLE installed, RT delivers efficient displays and
        a screen recall buffer.  With CED installed, operations from the
        DOS prompt are facilitated.  RT.BAT and associated receivers and
        transmitters can be fully integrated with DOS by using "CED syn".

        To capture data enter  RT >capture.dat   and punch  ALT-X  after
        your modem RXD light stops glowing ( no display during capture ).

        enter  RT >>capture.dat  to append data to an existing File.




                        CONSOLE STATUS DISPLAY



             enter  DSZ.COM d pv2 p z p t  for a detailed console display.


  DSZ (TurboC) Copyright 01-08-89 by Omen Technology INC
           "The High Reliability Software"
  B =   1024   O =      0   Q =      1   S =     15   W =      0   a =   6000
  d =      1   v =      2   z =      0
  b =      0   B =      2   C =     11   e =      0   l =      0   L =      0
  n =      0   p =     50   P =      2   r =      0   s =     15   t =    100
  T =    600   w =      0   W =   1400   Z =      0   
  COM1 2400 bps  Carrier Detect DISABLED  Handshake Off S/N 7890
  DSZOPT = 'Zyt8g' Command line = 'd pv2 p z p t '
  Talking 8g. Type F1 to exit.



        STATUS:         the NUMERIC PARAMETERS and ZMODEM PARAMETERS
                        are listed by  letter = value.

                        the pv2 parameter enables detail during xfers,
                        including status of Zmodem-W "window" pacing.

                        the port  COM1:  device was opened by default.

                        the "d" parameter used above has DISABLED the
                        check for DCD (pin 8) Carrier Detect.

                        the hardware Handshake (RTS/CTS) is disabled,
                        XON/XOFF handshaking is in effect for Zmodem
                        and Ymodem Batch transfers by default.

                        environment options DSZOPT=Zyt8g are present.

                        DSZ Terminal mode was invoked with  -y option
                        from the environment enabling File over-write.

                        DSZ Terminal mode was invoked with -8g option
                        from the environment enabling high ASCII (the
                        default "parity" of  8n  "none" is equivalent
                        to a high-ASCII display filter).




                        CONSOLE INDICATORS



        2048 ZMODEM CRC-32  XOFF

                        indicates that the sender has received an XOFF
                        from the receiver or a network medium through
                        which he is transmitting.


        Sector 280 35k YMODEM-1k-g  FLOW


                        indicates that CTS (pin 5) is low, suspending
                        transmission to the modem or device until the
                        line goes high.


        Output Restraint RELEASED


                        indicates that the sender or receiver has not
                        received an XON or CTS (8) high in 15 seconds.


         NOTES:         Use the NUMERIC PARAMETERS pS15 and z ps15 to
                        change the default 15 second timeout for XOFF.

                        Use the NUMERIC PARAMETERS pS15 and z ps15 to
                        change the default 15 second timeout for FLOW.




        ERROR RECOVERY

                        indicates that sender and receiver are trying
                        to continue the File transfer after an error.


        ZMODEM Crash Recovery at

                        indicates that the "-r" option was active and
                        the receiver is recovering data in a Filespec.


        Not allowed to overwrite

                        indicates that the "-y" option was not active
                        and the receiver has attempted to  over-write
                        an existing Filespec.


        File skipped by receiver request

                        indicates that the "-y" option was not active
                        for the receiver and the sender has attempted
                        to transfer an existing Filespec.


        No such file or directory

                        indicates that the Path/File specified on the
                        command line was nonexistant.




        Unknown Machine Type XX

                        indicates the pa6000 timing parameter may need
                        to be manually set for your computer.


        Garbage Count Exceeded

                        indicates the z pW1400 timing parameter should
                        be manually set for this transmission medium.




        Serial Input Error: Line Status Register XX


                        indicates a general communications failure, as:

                01      receive buffer full - remote not responding to
                        XOFF software or RTS hardware flow control.

                02      data overrun - receiving errors were caused by
                        interrupt latency effects.  Upgrade to a 16550
                        UART and/or eliminate TSRs and DEVICEs.

                08      framing error - indicates Baud/Parity mismatch
                        or very high line noise.

                10      break interrupt - also a Baud/Parity mismatch
                        or very high line noise.




        No Carrier Detect

                        indicates that the ENABLED check for a CARRIER
                        on DCD (pin 8) has found NO CARRIER present.



        DSZ FINISHED! exit code = 0

                        indicates the errorlevel returned to DOS after
                        exit from Terminal Mode or completion of File
                        transfer.  Errorlevel = 1 for abnormal exit.






____________________________________________________________________________



                        TRANSMITTER  CONFIGURATIONS  FOR  TELENET




                        Send Zmodem Batch-W  Telenet 2400 (CONNECT 2400)

        SW.BAT  = DSZ.COM port 1 speed 2400 pB8192 sz -Zw4096 %1 %2 %3

                        use this command when you are connected 2400
                        to your local PAD and a Host is CONNECT 2400
                        from the 2400 out-dial PAD.



                        Send Zmodem Batch-W  Telenet 2400 (CONNECT 1200)

   S3.BAT  = DSZ.COM port 1 speed 2400 est 0 1200 pB8192 sz -Zw3072 %1 %2 %3

                        use this command when you are connected 2400
                        to your local PAD and a Host is CONNECT 1200
                        from the (2400 or 1200) out-dial PAD.



                        Send Zmodem Batch-W  Telenet 1200 (CONNECT 1200)

        S2.BAT  = DSZ.COM port 1 speed 1200 pB8192 sz -Zw2048 %1 %2 %3

                        use this command when you are connected 1200
                        to your local PAD and a Host is CONNECT 1200
                        from the 1200 out-dial PAD.



       NOTES:           Larger Zwindows increase transfer performance but
                        may cause excessive XOFF delays from the network.

                        Downloading is more efficient than uploading and
                        Host systems can usually transmit without "-w".





                        TELENET  CONFIGURATION  PROCEDURES



   PROCEDURE:           to configure Telenet for ZMODEM CRC-32 Batch


                1)      ATDT7780825 <cr>        dial local Telenet PAD
                2)      @D <cr>                 link 8-N-1 Telenet PAD
                3)      D3 <cr>                 TERMINAL= buffered 12:1
                4)      C D/TXHOU/24,id,pw      request remote PAD link
                5)      ATZ <cr>                clear   out-dial modem
                6)      @ <cr>                  request Telenet command mode
                7)      SET? 5:1 <cr>           enable  XOFF from PAD to you
                8)      RST? 5:1 <cr>           enable  XOFF from PAD to host
                9)      CONT <cr>               return  to out-dial modem
               10)      AT*E1 <cr>              enable  auto-MNP seeking
               11)      ATDT9611604 <cr>        execute auto-dial of number



       NOTES:           ZMODEM "escapes" network commands and can compress
                        data before sending in a continuous flow.  Packets
                        adjust in size depending upon baud and error rates.

                        The receiver checks each packet with a 32-bit CRC,
                        and requests re-transmission of data from an exact
                        point should an error occur.

                        When an error does occur, a receiver discards the
                        data flowing in until the requested frame start is
                        found.  This "garbage count" is set to 1400 bytes
                        by default and can be made larger if required.

                        When sending, the network will accept a continuous
                        stream of data until an artificial "window" fills,
                        at which time it sends an XOFF (CTRL-S) to stop or
                        slow down (pace) the transmitter.

                        The frequency of XOFF delays is a function of the
                        network loading and the size of the real "window".

                        Zmodem-W File transfers are free-flowing however,
                        the receiver must return an acknowledgment after
                        every  window ö 4  bytes.  When the Zmodem window
                        is equal to the real network window, fewer  XOFF
                        delays and over-run errors are experienced.

                        The idea behind ZMODEM-W is for the receiver and
                        transmitter to pace themselves rather than having
                        the network set the pace by causing XOFF delays.

                        The Zmodem "-w" option configures a File transfer
                        for a 3 Kb "window" (by default) and can be reset
                        up  -w4096  or down  -w2048  for precision pacing.

                        A "window" ò  -w4096  usually indicates that free
                        flowing (no -w option) is possible.





   PROCEDURE:           to configure Telenet for YMODEM/-1K/CRC/-G Batch


                1)      ATDT7780825 <cr>        dial local Telenet PAD
                2)      @D <cr>                 link 8-N-1 Telenet PAD
                3)      D3 <cr>                 TERMINAL= buffered 12:1
                4)      C D/TXHOU/24,id,pw      request remote PAD link
                5)      ATZ <cr>                clear   out-dial modem
                6)      @ <cr>                  request Telenet command mode
                7)      SET? 5:1 <cr>           enable  XOFF from PAD to you
                8)      RST? 5:1 <cr>           enable  XOFF from PAD to host
                9)      SET? 0:33,35:10,64:4    increase artificial window
               10)      CONT <cr>               return  to out-dial modem
               11)      AT*E1 <cr>              enable  auto-MNP seeking
               12)      ATDT9611604 <cr>        execute auto-dial of number



       NOTES:           YMODEM sends binary data in 128 byte or 1K blocks,
                        and uses a Filespec Header for  Batch  capability.

                        The YMODEM receiver performs a 16-bit CRC test for
                        each data block, returning an ACK or NAK code to a
                        sender after each block is received and tested.

                        When  -w4096  is possible there is  YMODEM-1K-G to
                        consider.  This is a balls-out protocol, no checks,
                        designed for MNP type modems.  Telenet features MNP
                        on all 2400 Baud Lines.  Even if your modem is not 
                        MNP, enabling  the  outdial  modem's  MNP  provides
                        hardware error correction whenever a Host uses MNP.

                        Achieving a RELIABLE connect with a Host will often
                        enable his high-speed "-G" protocols.  But even so,
                        just firing up a  YMODEM-G Receive  in response to
                        a YMODEM-1K Sender causes him to go into "-G" mode.

                        From a  DSZ t -g  Gonzole Receiver, just punch F3.

                        Without error-correction on one or both (PAD) ends,
                        using YMODEM-G can be risky.  To be sure, one line
                        hit or extraneous character in the data stream will
                        cause a transfer to abort ( often spectacularly ).

                        Using  YMODEM-G  pushes the ability of the network
                        to process continuous data at high speeds. Setting
                        SET 0:33,35:10  (equivalent to SET 4:10)  commands
                        the network to accumulate data into larger bundles
                        before sending them on. This reduces the frequency
                        of XOFF flow control delays when you upload... but
                        there are unpleasant side-effects on your console.

                        Parameter 0:33,35:2 can be SET from 35:1 to 35:80

                        Parameter 0:33,64:0 can be SET from 64:0 to 64:8

                        Parameter 64:4 is called "advance ACK" and defines
                        an "artificial window".  Changing the default 64:0
                        to increase the artificial window size may improve
                        efficiency... but there is some risk of data loss.

                        Tweaking the Telenet default  SET?  0:33,35:2,64:0
                        affects Zmodem-W and Ymodem-G transfer performance.
                        Note that any SET? commands can always be modified
                        after the out-dial modem has established a CONNECT.


     CAUTION:           Note that the RST? command should not be attempted
                        after the out-dial modem has established a CONNECT.






   PROCEDURE:           to configure Telenet for XMODEM/-1K/CRC/Sum/-G


                1)      ATDT7780825 <cr>        dial local Telenet PAD
                2)      @D <cr>                 link 8-N-1 Telenet PAD
                3)      D1 <cr>                 TERMINAL= video display
                4)      C D/TXHOU/24,id,pw      request remote PAD link
                5)      ATZ <cr>                clear   out-dial modem
                6)      @ <cr>                  request Telenet command mode
                7)      SET? 1:0,7:8 <cr>       change  <cr>@<cr> to BREAK
                8)      CONT <cr>               return  to out-dial modem
                9)      AT*E1 <cr>              enable  auto-MNP seeking
               10)      ATDT9611604 <cr>        execute auto-dial of number



       NOTES:           XMODEM sends pure binary data in 128 byte or 1 Kb
                        packets.  The XMODEM receiver performs a checksum
                        or 16-bit CRC test for each data block, returning
                        an ACK or NAK code to the waiting sender.

                        Because the network medium causes a delay between
                        sender and receiver, the turnaround time required
                        to process an ACK or NAK is considerable.  XMODEM
                        with 1 Kb packets (often called Ymodem/CRC), uses
                        7 less ACK/NAK delays for every 1,024 bytes sent.

                        As in YMODEM-G, the XMODEM-G receiver requests an
                        XMODEM/-1K sender to transmit free-flow.  However
                        unlike YMODEM-G, XMODEM does not support XON/XOFF
                        and can garble data by blowing it into Telenet.


     CAUTION:           Because the network command <cr>@<cr> in any data
                        stream would cause an escape to net command mode,
                        change the <cr>@<cr> to a break signal to prevent
                        accidental abort of an XMODEM File transfer.

                        Note further that unless  CTRL-Break "send BREAK"
                        functions on your console, using SET 1:0,7:8 will
                        prevent subsequent access to net command mode!







   PROCEDURE:           to configure out-dial Racal-Vadic Modem for MNP


                1)      ATZ <cr>                clear   out-dial modem
                2)      CTRL-E <cr>             request Racal-Vadic mode
                3)      O <cr>                  request Option Groups menu
                4)      2 <cr>                  request Option Group 2 menu
                5)      19 <cr>                 request Option 19 menu
                6)      1 <cr>                  enable  auto-MNP seeking
                7)      0 <cr>                  request Option Group 2 menu
                8)      0 <cr>                  request Option Groups menu
                9)      4 <cr>                  execute changed options
               10)      D9611604 <cr>           execute auto-dial of number
               11)      R9 <cr>                 execute auto-redial of number



       NOTES:           Telenet's  Racal-Vadic mode presents menus in place
                        of "AT" commands. They are useful for exploring the
                        capabilities of out-dial hardware and for using the
                        built-in auto-dialer.

                        The R-V auto-dialer is faster than the "Hayes" ATDT
                        dialer and provides more information about the call.
                        The R-V hardware redialer will make up to 9 redials.

                        MNP seeking remains enabled until a CONNECT or ATZ.

                        Whether using the above procedure for "Racal-Vadic"
                        or simply using  AT*E1  from the "Hayes" mode, note
                        that MNP must be re-enabled after completing a call.

                        Note some 1200 Baud out-dial modems do not have MNP.




   PROCEDURE:           to disconnect from TeleNet and turn off all timers


                1)      I <cr>                  request Hayes mode
                2)      ATZ <cr>                clear   out-dial modem
                3)      @ <cr>                  request Telenet command mode
                4)      D <cr>                  request remote PAD unlink
                5)      +++                     request modem command mode
                6)      ATH <cr>                disable carrier









____________________________________________________________________________




        EXAMPLES of DSZ.COM USAGE with CCITT V.22 STANDARD 2400 MODEMS



                          Zmodem Console Receiver

        RT.BAT  = DSZ.COM port 1 speed 2400 d pB8192 t -8g


                        Zmodem-Z Console Transmitter

        ST.BAT  = DSZ.COM port 1 speed 2400 sz -Zt8g %1 %2 %3



        Standard 2400 Baud CCITT V.22 Modems can achieve 228 ñ 5 c.p.s.
        throughput on ARC Files using the DSZ Zmodem Driver.



        TRANSMITTERS

                        Send Zmodem Batch CRC-32/RLE

                SZ.BAT  = DSZ.COM port 1 speed 2400 pB8192 sz -Z %1 %2 %3



                        Send Ymodem Batch/CRC-16

                SB.BAT  = DSZ.COM port 1 speed 2400 pB8192 sb -k %1 %2 %3



                        Send Xmodem-1k/CRC/Sum

                SY.BAT  = DSZ.COM port 1 speed 2400 pB8192 sx -k %1



                        Send Xmodem/CRC/Sum

                SX.BAT  = DSZ.COM port 1 speed 2400 pB8192 sx %1



        RECEIVERS

                        Receive Zmodem Batch CRC-32

                RZ.BAT  = DSZ.COM port 1 speed 2400 pB8192 rz



                        Receive Ymodem Batch/CRC-16

                RB.BAT  = DSZ.COM port 1 speed 2400 pB8192 rb



                        Receive Xmodem/-1k/CRC/Sum

                RY.BAT  = DSZ.COM port 1 speed 2400 pB8192 rc %1




         NOTES:         Use  SET DSZOPT=y  in AUTOEXEC.BAT to enable
                        overwriting existing Files when received.

                        Use  SET DSZOPT=r  in AUTOEXEC.BAT to enable
                        Crash Recovery of existing Files.

                        Use  SET DSZOPT=yt8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        after Receiving or Sending File(s).

                        Use  SET DSZOPT=rt8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        with Crash Recovery enabled.




____________________________________________________________________________




        EXAMPLES of DSZ.EXE USAGE with CCITT V.22  MNP LEVEL 5 MODEMS



                          Zmodem Console Receiver

        RT.BAT  = DSZ.EXE port 1 speed 9600 ha bo est 0 2400 d t -g8g


                        Zmodem-Z Console Transmitter

    ST.BAT  = DSZ.EXE port 1 speed 9600 ha bo est 0 2400 sz -Zktg8g %1 %2 %3


                        Ymodem-G Console Transmitter

    SB.BAT  = DSZ.EXE port 1 speed 9600 ha bo est 0 2400 sb -ktg8g %1 %2 %3




        The MultiTech MT224EH is a CCITT V.22 MNP Level 5 Modem that's
        capable of 280 ñ 5 c.p.s. throughput for ARC Files using  DSZ.

        The 224E should be configured to disable "compression" for ARC
        File transfers; use  AT&E14&W0  to do this.  Note that RTS/CTS
        handshaking should be ENABLED -- and that XON/XOFF handshaking
        is DISABLED (to "flow through") for proper Modem operation.

        This Modem features "speed conversion".  The serial port UART
        is "locked" at 9,600 Baud and the 224E adjusts  automatically
        to a 1200 or 2400 Baud Host (with or without MNP).

        Owners of MT224EH Modems should replace their  8250  or 16450
        UART chip with a  NS16550AN  UART to achieve best performance.



        TRANSMITTERS

                        Send Zmodem Batch CRC-32/RLE

        SZ.BAT  = DSZ.EXE port 1 speed 9600 ha bo est 0 2400 sz -Z %1 %2 %3



                        Send Ymodem Batch/CRC-16/-G

        SB.BAT  = DSZ.EXE port 1 speed 9600 ha bo est 0 2400 sb -k %1 %2 %3



                        Send Xmodem-1k/CRC/Sum/-G

        SY.BAT  = DSZ.EXE port 1 speed 9600 ha on sx -k %1



                        Send Xmodem/CRC/Sum/-O

        SX.BAT  = DSZ.EXE port 1 speed 9600 ha on sx %1



        RECEIVERS

                        Receive Zmodem Batch CRC-32

        RZ.BAT  = DSZ.EXE port 1 speed 9600 ha bo est 0 2400 rz



                        Receive Ymodem Batch/CRC-16

        RB.BAT  = DSZ.EXE port 1 speed 9600 ha bo est 0 2400 rb



                        Receive Ymodem Batch-G

        RGB.BAT = DSZ.EXE port 1 speed 9600 ha bo est 0 2400 rb -g



                        Receive Xmodem/-1k/CRC/Sum

        RY.BAT  = DSZ.EXE port 1 speed 9600 ha on rc %1



                        Receive Xmodem/-1k/-G

        RG.BAT  = DSZ.EXE port 1 speed 9600 ha on rc -g %1



                        Receive Xmodem/-1k/-O

        RO.BAT  = DSZ.EXE port 1 speed 9600 ha on pO60 ro %1




         NOTES:         Use  SET DSZOPT=y  in AUTOEXEC.BAT to enable
                        overwriting existing Files when received.

                        Use  SET DSZOPT=r  in AUTOEXEC.BAT to enable
                        Crash Recovery of existing Files.

                        Use  SET DSZOPT=ytg8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        after Receiving or Sending File(s).

                        Use  SET DSZOPT=rtg8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        after Receiving or Sending File(s) with Crash
                        Recovery enabled.




____________________________________________________________________________




        EXAMPLES of DSZ.EXE USAGE with CCITT V.29  MNP LEVEL 6 MODEMS



                          Zmodem Console Receiver

        RT.BAT  = DSZ.EXE port 1 speed 19200 ha bo est 0 9600 d t -g8g


                        Zmodem-Z Console Transmitter

    ST.BAT  = DSZ.EXE port 1 speed 19200 ha bo est 0 9600 sz -Zktg8g %1 %2 %3


                        Ymodem-G Console Transmitter

    SB.BAT  = DSZ.EXE port 1 speed 19200 ha bo est 0 9600 sb -ktg8g %1 %2 %3




        The USR 9600 HST is a CCITT V.29 "pseudo-duplex" Modem that's
        capable of 1150 ñ 5 c.p.s. throughput of ARC Files using DSZ.

        The HST should be configured to disable "compression" for ARC
        File transfers.  Use  AT&K0&W  to do this.  Note that RTS/CTS
        handshaking should be ENABLED - and that XON/XOFF handshaking
        should be DISABLED for proper Modem operation.

        This Modem features "speed conversion".  The serial port UART
        is "locked" at 19,200 Baud and the HST adjusts  automatically
        to a 1200 or 2400 Baud Host (with or without MNP) and to 9600
        Baud when another HST modem is detected.

        Owners of USR HST Modems must replace their  8250  or  16450
        UART chip with a  NS16550AN  UART to achieve high performance.




        TRANSMITTERS

                        Send Zmodem Batch CRC-32/RLE

        SZ.BAT  = DSZ.EXE port 1 speed 19200 ha bo est 0 9600 sz -Z %1 %2 %3



                        Send Ymodem Batch/CRC-16/-G

        SB.BAT  = DSZ.EXE port 1 speed 19200 ha bo est 0 9600 sb -k %1 %2 %3



                        Send Xmodem-1k/CRC/Sum/-G

        SY.BAT  = DSZ.EXE port 1 speed 19200 ha on sx -k %1



                        Send Xmodem/CRC/Sum/-O

        SX.BAT  = DSZ.EXE port 1 speed 19200 ha on sx %1



        RECEIVERS

                        Receive Zmodem Batch CRC-32

        RZ.BAT  = DSZ.EXE port 1 speed 19200 ha bo est 0 9600 rz



                        Receive Ymodem Batch/CRC-16

        RB.BAT  = DSZ.EXE port 1 speed 19200 ha bo est 0 9600 rb



                        Receive Ymodem Batch-G

        RGB.BAT = DSZ.EXE port 1 speed 19200 ha bo est 0 9600 rb -g



                        Receive Xmodem/-1k/CRC/Sum

        RY.BAT  = DSZ.EXE port 1 speed 19200 ha on rc %1



                        Receive Xmodem/-1k/-G

        RG.BAT  = DSZ.EXE port 1 speed 19200 ha on rc -g %1



                        Receive Xmodem/-1k/-O

        RO.BAT  = DSZ.EXE port 1 speed 19200 ha on pO60 ro %1




       NOTES:           Use  SET DSZOPT=y  in AUTOEXEC.BAT to enable
                        overwriting existing Files when received.

                        Use  SET DSZOPT=r  in AUTOEXEC.BAT to enable
                        Crash Recovery of existing Files.

                        Use  SET DSZOPT=ytg8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        after Receiving or Sending File(s).

                        Use  SET DSZOPT=rtg8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        after Receiving or Sending File(s) with Crash
                        Recovery enabled.




____________________________________________________________________________




        EXAMPLES of DSZ.EXE USAGE with EIA RS232-C  DIRECT CONNECIONS



                          Zmodem Console Receiver

        RT.BAT  = DSZ.EXE port 1 speed 38400 ha bo d t -yg8g


                        Zmodem-Z Console Transmitter

        ST.BAT  = DSZ.EXE port 1 speed 38400 ha bo d sz -Zktyg8g %1 %2 %3


                        Ymodem-G Console Transmitter

        SB.BAT  = DSZ.EXE port 1 speed 38400 ha bo d sb -ktyg8g %1 %2 %3



        Direct connection between computers creates an RS232 "network"
        by which two operators can communicate at very high speed.

        PC -to- PC  File transfers are useful when two computers have
        dis-similar removable media or, when they are far apart.

        By using an appropriate Null Modem Cable between serial ports,
        two MS-DOS machines can transfer Files at 38,400 Baud or more.




                IBM PC SERIAL PORT  UART SPECIFICATIONS


             8250       The PC/XT 8250 Universal Asynchronous Receiver
                        Transmitter (UART) provides nine of the RS232C
                        lines from a  DB-25p  (25-pin, male) connector.
                        This is the standard PC serial port controller.

            16450       The "AT" 16450 Universal Asynchronous Receiver
                        Transmitter (UART) provides nine of the RS232C
                        lines from a  DB-9p (9-pin, male) connector or,
                        from a  DB-25p (25-pin, male) connector. It is
                        capable of operating at higher speeds.

            16550       The PS/2 16550 Universal Asynchronous Receiver
                        Transmitter (UART) provides nine of the RS232C
                        lines from a DB-9p (9-pin, male) connector and
                        features a 16-byte FIFO port buffer.


       NOTES:           UART 40-pin DIP devices are pin-compatible and
                        can be upgraded - the NS16550AN is recommended
                        for any MS-DOS computer running the DSZ Driver.




                IBM PC SERIAL PORT  PLUG SPECIFICATIONS


                        The Serial Port is configured as RS232-C Data
                        Terminal Equipment (DTE) :


                        pin    DTE direction     signal

                       ( 1)    CHS    nul    chasis ground
                       ( 2)    TXD    out    transmit data
                       ( 3)    RXD    inp    receive data
                       ( 4)    RTS    out    request to send
                       ( 5)    CTS    inp    clear to send
                       ( 6)    DSR    inp    data set ready
                       ( 7)    GND    nul    signal ground
                       ( 8)    DCD    inp    data carrier detect
                      (9/20)   DTR    out    data terminal ready



       NOTES:           The Data Terminal Ready DTR signal is on pin 9
                        of DB-9p Male connectors and pin 20 of DB-25p.





                IBM PC to MODEM CABLE CONFIGURATION: STANDARD DTE-DCE


              signal        pin    DTE     pin    DCE        signal

         chassis ground    ( 1)    CHS    ( 1)    CHS    chasis ground
          transmit data    ( 2)    TXD    ( 2)    TXD    transmit data
           receive data    ( 3)    RXD    ( 3)    RXD    receive data
        request to send    ( 4)    RTS    ( 4)    RTS    request to send
          clear to send    ( 5)    CTS    ( 5)    CTS    clear to send
         data set ready    ( 6)    DSR    ( 6)    DSR    data set ready
          signal ground    ( 7)    GND    ( 7)    GND    signal ground
    data carrier detect    ( 8)    DCD    ( 8)    DCD    data carrier detect
    data terminal ready   (9/20)   DTR   (9/20)   DTR    data terminal ready



       NOTES:           Connecting a Modem or other  Data Communications
                        Equipment device requires a shielded, nine-wire,
                        straight connect cable, with one DB25p Male plug
                        for the device and either a DB9s or DB25s Female
                        socket for the computer.





                IBM PC to PC CABLE CONFIGURATION:  NULL MODEM DTE-DTE


              signal        pin    DTE     pin    DTE        signal

         chassis ground    ( 1)    CHS    ( 1)    CHS    chasis ground
          transmit data    ( 2)    TXD    ( 3)    RXD    receive data
           receive data    ( 3)    RXD    ( 2)    TXD    transmit data
        request to send    ( 4)    RTS    ( 5)    CTS    clear to send
          clear to send    ( 5)    CTS    ( 4)    RTS    request to send
         data set ready    ( 6)    DSR   (9/20)   DTR    data terminal ready
          signal ground    ( 7)    GND    ( 7)    GND    signal ground
    data terminal ready   (9/20)   DTR    ( 6)    DSR    data set ready

                                          ( 8)    DCD    data carrier detect
                                          ( 6)    DSR    data set ready
    data carrier detect    ( 8)    DCD
         data set ready    ( 6)    DSR



       NOTES:           Connecting a  Computer  or other  Data  Terminal
                        Equipment device requires a shielded, nine-wire,
                        "null modem" cable with  DB9s  or  DB25s  Female
                        sockets for the two computers.

                        Standard Practice  to make a null modem cable is
                        to modify straight-wired cable with an extracor/
                        insertion tool, switching:  2x3,  4x5,  and  6x9
                        (or 6x20 for DB25) on one end.  then...

                        Cut the DCD wire  2" from pin 8 on both ends, and
                        "strap" it to DSR pin 6 by soldering on both ends.
                        Take out the old DCD wire from the cable assembly.

                        ...alternatively the state of Data Carrier on pin
                        eight is ignored by using the  "d"  parameter.





____________________________________________________________________________




        EXAMPLES of DSZ.EXE CONFIGURATION for PCBOARD with 9600 HST



                    N   None Specified   ( always prompts )
                    X   Xmodem/CRC/Sum   ( 80% efficiency )
                    Y   Xmodem/-1K/CRC   ( 90% efficiency )
                    O   Xmodem/-1K/y-G   ( 99% efficiency )
                    B   Ymodem Batch-K   ( 90% efficiency )
                    G   Ymodem Batch-G   ( 99% efficiency )
                    Z   Zmodem Batch-Z   ( 94% efficiency )




                UPLOADING


                        PCBOARD  FILE  PCBRX.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha on D rc %3
        if errorlevel 1 goto bad
        if not exist %3 goto bad
        pkunpak.exe -t %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on

                        PCBOARD  FILE  PCBRY.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha on D rc %3
        if errorlevel 1 goto bad
        if not exist %3 goto bad
        pkunpak.exe -t %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on

                        PCBOARD  FILE  PCBRO.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha on D rc -g %3
        if errorlevel 1 goto bad
        if not exist %3 goto bad
        pkunpak.exe -t %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on

                        PCBOARD  FILE  PCBRB.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha bo est 0 2400 D rb -p %3
        if errorlevel 1 goto bad
        if not exist %3 goto bad
        pkunpak.exe -t %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on

                        PCBOARD  FILE  PCBRG.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha bo est 0 9600 D rb -gp %3
        if errorlevel 1 goto bad
        if not exist %3 goto bad
        pkunpak.exe -t %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on

                        PCBOARD  FILE  PCBRZ.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha bo est 0 2400 D z pr1 rz -p %3
        if errorlevel 1 goto bad
        if not exist %3 goto bad
        pkunpak.exe -t %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on



       NOTES:           The above receivers process Files with PKUNPAK
                        before posting Uploads to the Board.



                DOWNLOADING


                        PCBOARD  FILE  PCBSX.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha on D sx %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on

                        PCBOARD  FILE  PCBSY.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha on D sx -k %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on

                        PCBOARD  FILE  PCBSO.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha on D sx -k %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on

                        PCBOARD  FILE  PCBSB.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha bo est 0 2400 D sb -k %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on

                        PCBOARD  FILE  PCBSG.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha bo est 0 9600 D sb -k %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on

                        PCBOARD  FILE  PCBSZ.BAT

        @echo off
        if exist pcberr.fil del pcberr.fil >nul
        dsz.exe port 1 speed 19200 ha bo est 0 2400 D sz -Z %3
        if errorlevel 1 goto bad
        goto end
        :bad
        copy pcberr.old pcberr.fil >nul
        :end
        @echo on



       NOTES:           The Xmodem transmitter automatically detects
                        a CRC-16 or CheckSum receiver and adapts.

                        These receivers and transmitters drop DTR if
                        the carrier is lost during a transfer.




                PCBOARD  FILE  PCBPROT.DAT


        N,I,0,None Specified   ( always prompts )
        X,S,128,Xmodem/CRC/Sum   ( 80% efficiency )
        Y,S,1024,Xmodem-1K/-CRC   ( 90% efficiency )
        O,S,1024,Xmodem/-1K/y-G   ( 99% efficiency )
        B,S,1024,Ymodem Batch-K   ( 90% efficiency )
        G,S,1024,Ymodem Batch-G   ( 99% efficiency )
        Z,S,1024,Zmodem Batch-Z   ( 94% efficiency )







____________________________________________________________________________




        EXAMPLES of DSZ.EXE CONFIGURATION for PRODOOR with 9600 HST




        ;
        ;       EXTERNAL PROTOCOL CONFIGURATIONS
        ;
        ;       X  Xmodem/CRC/Sum  (80%)          B  Ymodem Batch-K  (90%)
        ;       Y  Xmodem/-1K/CRC  (90%)          G  Ymodem Batch-G  (99%)
        ;       O  Xmodem/-1K/y-G  (99%)          Z  Zmodem Batch-Z  (94%)
        ;
        ;
        ;       UPLOADING
        ;
        80 X 0 R 1 Xmodem/CRC/Sum
        DSZ.EXE port $N$ speed 19200 ha on D rc
        ;
        90 B 0 R 0 Ymodem Batch-K
        DSZ.EXE port $N$ speed 19200 ha bo est 0 2400 D rb -p
        ;
        90 Y 0 R 1 Xmodem/-1K/CRC
        DSZ.EXE port $N$ speed 19200 ha on D rc
        ;
        99 G 1 R 0 Ymodem Batch-G
        DSZ.EXE port $N$ speed 19200 ha bo est 0 9600 D rb -gp
        ;
        99 O 1 R 1 Xmodem/-1K/y-G
        DSZ.EXE port $N$ speed 19200 ha on D rc -g
        ;
        94 Z 0 R 0 Zmodem Batch-Z
        DSZ.EXE port $N$ speed 19200 ha bo est 0 2400 D z pr1 rz -p
        ;
        ;       DOWNLOADING
        ;
        80 X 0 T 1 Xmodem/CRC/Sum
        DSZ.EXE port $N$ speed 19200 ha on D sx
        ;
        90 B 0 T 20 Ymodem Batch-K
        DSZ.EXE port $N$ speed 19200 ha bo est 0 2400 D sb -k $@$
        ;
        90 Y 0 T 1 Xmodem/-1K/CRC
        DSZ.EXE port $N$ speed 19200 ha on D sx -k
        ;
        99 G 1 T 20 Ymodem Batch-G
        DSZ.EXE port $N$ speed 19200 ha bo est 0 9600 D sb -k $@$
        ;
        99 O 1 T 1 Xmodem/-1K/y-G
        DSZ.EXE port $N$ speed 19200 ha on D sx -k
        ;
        94 Z 0 T 20 Zmodem Batch-Z
        DSZ.EXE port $N$ speed 19200 ha bo est 0 2400 D sz -Z $@$
        ;
        ;       END OF FILE



       NOTES:           ProDoor provides a Batch Transfer interface to
                        the DSZ Driver and enhances  PCBoard's Message
                        and Conference capabilities.

                        ProDoor 2.9á implements the "RZ" Command which
                        initiates a Zmodem Batch Receive.

                        Because DSZ sends an  rz <cr>  to the Receiver
                        at the beginning of a Zmodem Upload, users can
                        Upload Zmodem to the ProDoor Command Prompt.





____________________________________________________________________________




        EXAMPLES of DSZ.EXE CONFIGURATION for DOS CTTY with 9600 HST


                  RX  SX  Xmodem/CRC/Sum   ( 80% efficiency )
                  RY  SY  Xmodem/-1K/CRC   ( 90% efficiency )
                  RO  SO  Xmodem/-1K/y-G   ( 99% efficiency )
                  RB  SB  Ymodem Batch-K   ( 90% efficiency )
                  RG  SG  Ymodem Batch-G   ( 99% efficiency )
                  RZ  SZ  Zmodem Batch-Z   ( 94% efficiency )


        It is useful for a Remote Sysop to have File Transfer capability
        from the  DOS  "Shell"  CTTY  Mode.  Place these DSZ Batch Files
        "on the path" of the HOST computer to achieve this.


                        RECEIVERS

        RX.BAT  = DSZ.EXE CON port 1 speed 19200 ha on D rc -y %1
        RY.BAT  = DSZ.EXE CON port 1 speed 19200 ha on D rc -y %1
        RO.BAT  = DSZ.EXE CON port 1 speed 19200 ha on D rc -gy %1
        RB.BAT  = DSZ.EXE CON port 1 speed 19200 ha bo D rb -y
        RG.BAT  = DSZ.EXE CON port 1 speed 19200 ha bo D rb -gy
        RZ.BAT  = DSZ.EXE CON port 1 speed 19200 ha bo D rz -y


                        TRANSMITTERS

        SX.BAT  = DSZ.EXE CON port 1 speed 19200 ha on D sx %1
        SY.BAT  = DSZ.EXE CON port 1 speed 19200 ha on D sx -k %1
        SO.BAT  = DSZ.EXE CON port 1 speed 19200 ha on D sx -k %1
        SB.BAT  = DSZ.EXE CON port 1 speed 19200 ha bo D sb -k %1 %2 %3
        SG.BAT  = DSZ.EXE CON port 1 speed 19200 ha bo D sb -k %1 %2 %3
        SZ.BAT  = DSZ.EXE CON port 1 speed 19200 ha bo D sz -Z %1 %2 %3



       NOTES:           The DSZ 'CON' Parameter re-directs the display
                        to the  DOS CON: device  for  CTTY  operations.

                        Alternatively, use  >NUL  at the end of a line.

                        Because DSZ sends an  rz <cr>  to the Receiver
                        at the beginning of a Zmodem Upload, Files can
                        be uploaded to the DOS Prompt with SZ Filespec
                        from the Remote Sysop's Console Transmitter.





____________________________________________________________________________



                        PRO-YAM HOST  TeleGodzilla  BULLETIN BOARD


       CONNECT:         (503) 621-3746  1200 & 2400 (MNP) 8-N-1
                                        19,200 Baud TeleBit PEP
                                        1200 Telenet D/ORPOR/12


     DIRECTORY:     Enter DIRD at the Pro-Yam Host prompt to list Files


      DOWNLOAD:      sz DSZ.ARC  -  DSZ.COM and DSZ.DOC Fileset

      DOWNLOAD:      sz DSZEXE.ZOO  -  DSZ.EXE Driver File

      DOWNLOAD:      sz ZCOMMDOC.ARC  -  Zmodem Communications Reference

      DOWNLOAD:      sz YZMODEM.ZOO  -  Ymodem and Zmodem Protocol Reference

      DOWNLOAD:      sz RZSZ.ZOO  -  Zmodem Source Code in "C" Language



____________________________________________________________________________


         Prepared by:   Steve Shelton    co-Sysop of Sands PCBoard

                        with the help of the Sands PCBoard members


      (713) 961-1604:   9600 HST / 2400 MNP Level 5 / Telenet 2400 MNP

____________________________________________________________________________