CoreAids Macro Assembler Subroutine Library Utilities
                    Copyright 1987, CoreTechs

You are free to use, copy and distribute CoreAids providing that:
        NO FEE IS CHARGED FOR USE, COPYING OR DISTRIBUTION.
        IT IS NOT MODIFIED IN ANY WAY.

These subroutines are provided AS IS without any warranty,
expressed or implied, including but not limited to fitness for a
particular purpose.

Please send comments, suggestions and contributions to:

                            CoreTechs
                          P.O. Box 6207
                     Silver Spring, MD 20906


           SECTION I. ROUTINES LISTED ALPHABETICALLY

ALOC_CHG.ASM         6/25/87       902
        DESC:   Modifies Allocated memory block size                 V1.00
        IN:     *{BLOCK} segment address of memory block to be modified
                *{PARA} new requested block size in paragraphs {ie multiples
                 of 16 bytes}
        SAMPLE: Callm   ALOC_CHG,<BLOCK,PARA>,

ATRB_WRT.ASM         6/25/87      2268
        DESC:   Writes character attributes to the screen            V1.00
        IN:     *{PAGE} page number (0-3) 4 available pages in 80 column mode
                *{ROWCOL} row(0-24),col(0-79) (ie 0345 indicating fourth row,
                 46th column)
                *{ATRB} attribute (see technical reference manual for
                 information on color graphics adapter)
                *{NUM_CHARS} # of chars to be affected
        SAMPLE: Callm   ATRB_WRT,<PAGE,ROWCOL,ATRB,NUM_CHARS>,

CHAR_GET.ASM         6/25/87       771
        DESC:   gets a character from the keyboard                   V1.00
        IN:     *{REQ_TYPE} (0:get character,1:see if character
                 is there,2:get shift status)
        OUT:    *{CHAR} character ( high byte is shift status,
                 low byte is char.)
        SAMPLE: Callm   CHAR_GET,<REQ_TYPE>,<CHAR>

CHG_DIR.ASM          6/25/87       821
        DESC:   Changes to a new directory using the path provided   V1.00
        IN:     *{SEG_VAL} segment  and
                *{OFFSET} offset of path string
        SAMPLE: Callm   CHG_DIR,<SEG_VAL,OFFSET>,

CHG_MOD.ASM          6/25/87      1211
        DESC:   Changes the mode of a file                           V1.00
                (ie archived, hidden, system)
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of filename
                *{FUNC_CODE} function code(1:set mode,0:get mode)
                *{FILE_MODE} mode of file (1:read only,2:hidden file,
                 4:system file,8:volume label,10H:sub-directory,
                 20H:archived file
        OUT:    *{CMODE} mode of file after completions of call
        SAMPLE: Callm   CHG_MOD,<SEG_VAL,OFFSET,FUNC_CODE,FILE_MODE>,<CMODE>

CLEAR.ASM            6/25/87       524
        DESC:   Clears the screen                                    V1.00
        SAMPLE: Callm   CLEAR,,

CLOSE.ASM            6/25/87       693
        DESC:   Closes a file handle                                 V1.00
        IN:     *{INHNDL} handle of file to be closed
        SAMPLE: Callm   CLOSE,<INHNDL>,

COPY.ASM             6/25/87      2768
        DESC:   Copies existing file to new or existing file         V1.00
                using complete path names
        IN:     *{OUT_SEG_VAL} segment and
                *{OUT_OFFSET} offset of new filename
                *{IN_SEG_VAL} segment and
                *{IN_OFFSET} offset of old filename
        SAMPLE: Callm   COPY,<OUT_SEG_VAL,OUT_OFFSET,IN_SEG_VAL,IN_OFFSET>,

CREATE.ASM           6/25/87      1009
        DESC:   Creates a new data file                              V1.00
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of filename to be created as ASCIIZ string
                *{ATRB} attribute or mode of file as listed in CHG_MOD
                 command
        OUT:    *{OUTHNDL} handle of file created
        SAMPLE: Callm   CREATE,<SEG_VAL,OFFSET,ATRB>,<OUTHNDL>

CURS_GET.ASM         6/25/87       938
        DESC:   Gets Cursor Position                                 V1.00
        IN:     *{PAGE_NUM} page number (0-7) in 40 character mode
                 or (0-3) in 80 character mode (i.e. 0003) is page 4
        OUT:    *{ROWCOL} row (0-24),col (0-79)  (i.e. 0104)
                 1st row, 5th column
                *{CURS_MODE} cursor mode (see manual for description)
        SAMPLE: Callm   CURS_GET,<PAGE_NUM>,<ROWCOL,CURS_MODE>

CURS_SET.ASM         6/25/87       883
        DESC:   Sets Cursor Position                                 V1.01
        IN:     *{ROWCOL} row and column to postion cursor
                 row (0-24),col (0-79)  (i.e. 0104)
                 1st row, 5th column
                *{PAGE_NUM} page number (0-7) in 40 character mode and (0-3)
                 in 80 character mode (i.e. 0003) is page 4
        SAMPLE: Callm   CURS_SET,<ROWCOL,PAGE_NUM>,

DATE_GET.ASM         6/25/87      1482
        DESC:   Gets the system date                                 V1.00
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of system date in format MM/DD/YY
        SAMPLE: Callm   DATE_GET,<SEG_VAL,OFFSET>,

DELETE.ASM           6/25/87       822
        DESC:   Deletes a file                                       V1.00
        IN:     *{SEG_VAL} segment
                *{OFFSET} offset of filename to be deleted
        SAMPLE: Callm   DELETE,<SEG_VAL,OFFSET>,

ERRORMSG.ASM         6/25/87      5589
        DESC:   Prints DOS error messages 1-18 and additional user   V1.01
                 supplied messages from 19 up. If the value of ERR_NUM is
                 0 control returns to the calling program with no effect.
                 If ERR_NUM is greater than the value of the maximum error
                 message then the message "No Error for This Value" is
                 displayed and control returns to DOS. If an error code is
                 displayed then control also returns to DOS. The memory
                 address where the error occured is displayed on exit.
        IN:     *{ERR_NUM} error number where the possible legal values are:
                 1......Invalid Function Number
                 2......File Not Found
                 3......Path Not Found
                 4......Too Many Open Files (no handles left)
                 5......Access Denied
                 6......Invalid Handle
                 7......Memory Control Blocks Destroyed
                 8......Insufficient Memory
                 9......Invalid Memory Block Address
                10......Invalid Environment
                11......Invalid Format
                12......Invalid Access Code
                13......Invalid Data
                14......This Error Does Not Exist
                15......Invalid Drive Was Specified
                16......Attempted To Remove The Current Directory
                17......Not Same Device
                18......No More Files
                19......No Room For File(s) On Target Disk
                20......No Filename(s) Specified
                21......No Volume Label On Disk
                22......Wrong Number of Parameters
                >22.....No Error for This Value
        SAMPLE: Callm   ERRORMSG,<ERR_NUM>,

EXECUTE.ASM          6/25/87      2336
        DESC:   Loads and Executes another program                   V1.00
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of filename to run including extension
                *{PAR_HI} high word and
                *{PAR_LO} low word of pointer to command line
                 to be passed to new program. Command line should be in the
                 form N,' ',PARAM,0DH where N is the length of PARAM+1, and is
                 followed by a space. PARAM is the command line and 0DH is
                 a carriage return ending the line.
                *{MEMBLK} segment value of last memory control block 
                 segment is typically the value of DS at entry to the main
                 program.
                *{SIZE} size of main calling program in segment form
        SAMPLE: Callm   EXECUTE,<SEG_VAL,OFFSET,PAR_HI,PAR_LO,MEMBLK,SIZE>,

FILEDATE.ASM         6/25/87      1891
        DESC:   Converts Bit-Mapped file date to ASCII format        V1.00
        IN :        *file date in form yyyyyyymmmmmddddd
                where mm is the month 1-12
                      dd is the day 1-31
                      yy is the year 0-119 (1980-2099)
        OUT :        *segment and
                *offset of the file date in the form
                mm/dd/yy
        SAMPLE: Callm   FILEDATE,<DATE>,<ES,BX>

GET_DIR.ASM          6/25/87      1038
        DESC:   gets the current directory path string in the form   V1.00
                dir1\dir2\dir3...
        IN:     *{DRIVE} drive number of the drive to operate on where
                 0 is the default, 1 is A, etc.
                *{SEG_VAL} segment and
                *{OFFSET} offset of 64 byte user are where resultant string
                 will be placed ending with a byte containing 0
        SAMPLE: Callm   GET_DIR,<DRIVE,SEG_VAL,OFFSET>,

GET_DSK.ASM          6/25/87       679
        DESC:   returns the disk transfer address                    V1.00
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of DTA
        SAMPLE: Callm   GET_DSK,,<SEG_VAL,OFFSET>

GET_TEXT.ASM         6/25/87      1333
        DESC:   gets a line of text from the keyboard                V1.00
        IN:     *{MAX_CHARS} maximum # of characters to get from keyboard
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of text buffer
                *{LENGTH} length of text
        SAMPLE: Callm   GET_CHAR,<MAX_CHARS>,<SEG_VAL,OFFSET,LENGTH>

HELP.ASM             6/25/87      3269
        DESC:   Provides help to the user for all programs           V1.03
                linking to the help module and following the
                specified format
        IN:     *{DS} value passed to data segment at start of main program
                *{HELP} location of help data
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of parameter string
                *{LENGTH} length of parameter string
        SAMPLE: Callm   HELP,<DS,HELP>,<SEG_VAL,OFFSET,LENGTH>

HEXDSPLY.ASM         6/25/87      1855
        DESC:   Displays hexadecimal codes as ASCII values           V1.00
        IN:     *{HEX_WORD} hex word (0000 - FFFF)
        OUT:    *{ASC_HI} first two characters of result (i.e EF from EFAB)
                *{ASC_LO} second two characters of result (i.e. AB from EFAB)
        SAMPLE: Callm   HEXDSPLY,<HEX_WORD>,<ASC_HI,ASC_LO>

HEX_ASC.ASM          6/25/87      3724
        DESC:   Convert Hex numbers to decimal in ASCII format       V1.03
        IN:     *{HI_HEX} High order word of 4 byte hexadecimal number
                *{LO_HEX} Low order word of 4 byte hexadecimal number
        OUT:    *{ASC_1} five words from MSB to LSB with leading
                *{ASC_2} zeros stripped
                *{ASC_3}
                *{ASC_4}
                *{ASC_5}
        SAMPLE: Callm   HEX_ASC,<HI_HEX,LO_HEX>,
                                <ASC_1,ASC_2,ASC_3,ASC_4,ASC_5>

MOVE_BYT.ASM         6/25/87       912
        DESC:   Moves a source buffer to a dest. buffer              V1.00
        IN:     *{SEG_VAL1} segment and
                *{OFFSET1} offset of input buffer
                *{SEG_VAL2} segment and
                *{OFFSET2} offset of output buffer
                *{NUM_CHARS} # of chars to move
        SAMPLE: Callm   MOVE_BYT,<SEG_VAL1,OFFSET1,SEG_VAL2,OFFSET2,
                                 NUM_CHARS>,

MOV_PTR.ASM          6/25/87      1195
        DESC:   Moves the file read/write pointer                    V1.00
        IN:     *{METH_VAL} Method value
                 (0:ofst,1:ofst+cloc,2:eof+offset)
                *{HANDLE} handle
                *{MSW} most significant word of offset
                *{LSW} least significant word of offset
        OUT:    *{OMSW} most significant word of pointer location
                *{OLSW} least significant word of pointer location
        SAMPLE: Callm   MOV_PTR,<METH_VAL,HANDLE,MSW,LSW>,<OMSW,OLSW>

OPEN.ASM             6/25/87       967
        DESC:   Opens a file                                         V1.00
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of filename as ASCIIZ strng
                *{ACC_CODE} access code of file (0:read,1:write,2:read write)
        OUT:    *{HANDLE} handle of file
        SAMPLE: Callm   OPEN,<SEG_VAL,OFFSET,ACC_CODE>,<HANDLE>

PARM_BRK.ASM         6/25/87      1843
        DESC:   Takes in parameter string retrieved from DOS level   V1.00
                and breaks the string into separate elements using
                commas and the end of line as the only breaks.
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of parameter string
                *{LENGTH} length of parameter string
        OUT:    *{N} n is the number of sets of segment,offset  and length
                 groups returned, which indicates the number of total
                 parameters passed to the program.
                *{OSEG_VAL,OOFFSET,OLENGTH} repeated N times
                 and returned in reverse order (i.e. P3, P2 , P1)
        SAMPLE: Callm   PARM_BRK,<SEG_VAL,OFFSET,LENGTH>,
                                 <N,<OSEG_VAL,OOFFSET,OLENGTH>>

PARM_GET.ASM         6/25/87      1127
        DESC:   Gets parameters passed to program from DOS level     V1.00
                at DS+80H
        IN:     *{DS} value passed to data segment at start of main program
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of parameter string
                *{LENGTH} length of parameter string
        SAMPLE: Callm   PARM_GET,<DS>,<SEG_VAL,OFFSET,LENGTH>

POPALL.ASM           6/25/87      1190
        DESC:   Pop all registers (SI,DI,BP,ES,DS,DX,CX,BX,AX)       V1.00
        SAMPLE: POPALL

PUSHALL.ASM          6/25/87      1277
        DESC:   Push all registers (AX,BX,CX,DX,DS,ES,BP,DI,SI)      V1.00
        SAMPLE: PUSHALL

READ.ASM             6/25/87      1008
        DESC:   Reads data from a file                               V1.00
        IN:     *{HANDLE} handle of file
                *{NUM_BYTES} number of bytes requested to read from file
                *{SEG_VAL} segment and
                *{OFFSET} offset of buffer
        OUT:    *{NUM_READ} number of bytes actually read
        SAMPLE: Callm   READ,<HANDLE,NUM_BYTES,SEG_VAL,OFFSET>,<NUM_READ>

REPLACE.ASM          6/25/87      1640
        DESC:   Replaces an occurence of a string with another       V1.00
                string
        IN:     *{RSTRNG} segment and
                *{ROFF} offset of replacement string (must be same length)
                *{DIR} direction of search (0:forward,1-FFFF:reverse)
                *{SEG_VAL} segment and
                *{OFFSET} offset of buffer to search
                *{LENGTH} length of search string
                *{SSTRNG} segment and
                *{OSTRNG} offset of search string
        OUT:    *{OSEG} segment and
                *{OOFF} offset of replacement (both zero if not replaced)
        SAMPLE: Callm   REPLACE,<RSTRNG,ROFF,DIR,SEG_VAL,OFFSET,LENGTH,
                        SSTRNG,OSTRNG>,<OSEG,OOFF>

SCAN_BYT.ASM         6/25/87      2716
        DESC:   Scans a source buffer for given characters           V1.01
                and returns the character and location of the closest
                matching character

        ***        SCAN_BYT performs forward and reverse searches. The CLD
                assembler command must be used before calling the procedure
                to perform a forward search. The STD command must be used
                before calling to perform a reverse search.     ***

        IN:     *{MATCH2N} 2nd and additional matches
                *{SEG_VAL} segment and
                *{OFFSET} offset of buffer to scan
                *{MATCH1} 1st of N number of possible matching sequences
                *{N} number of matching sequences passed in
        OUT:    *{MATCH_VAL} value of matching character
                *{MATCH_LOC} location of offset in match segment where
                 matching value was found
        SAMPLE: Callm   SCAN_BYT,<MATCH2N,SEG_VAL,OFFSET,MATCH1,N>,
                                 <MATCH_VAL,MATCH_LOC>

SCRN_RST.ASM         6/25/87       780
        DESC:   Restores 16K screen to video memory                  V1.00
        SAMPLE: SCRN_RST

SCRN_SAV.ASM         6/25/87       834
        DESC:   Saves 16K screen from video memory                   V1.00
        SAMPLE: SCRN_SAV

SCRN_TYP.ASM         6/25/87       899
        DESC:   Returns the address of the video memory buffer       V1.00
        OUT:    *{VIDEO} segment address of start of video memory area
                 Useful only with MDA and CGA graphics. B&W area is at B000H
                 while color area is at B800H
        SAMPLE: Callm   SCRN_TYP,,<VIDEO>

SEARCH.ASM           6/25/87      2078
        DESC:   Searches for a string in the indicated buffer        V1.02
        IN:     *{DIR} direction of search (0:forward,1-FFFF:reverse)
                *{SEG_VAL} segment and
                *{OFFSET} offset of buffer to search
                *{LENGTH} length of search string
                *{SSTRNG} segment and
                *{OSTRNG} offset of search string
        OUT:    *{OSEG} segment and
                *{OOFF} of search string (both zero if not found)
        SAMPLE: Callm   SEARCH,<DIR,SEG_VAL,OFFSET,LENGTH,SSTRNG,OSTRNG>,
                               <OSEG,OOFF>

SET_DSK.ASM          6/25/87       681
        DESC:   sets the disk transfer address                       V1.00
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of DTA
        SAMPLE: Callm   SET_DSK,<SEG_VAL,OFFSET>,

SRCH_FIL.ASM         6/25/87      2791
        DESC:   search for the first of a set of matching filenames  V1.00

        ***        CX must be loaded with the appropriate file attribute
                to search on (1:read only,2:hidden file,
                 4:system file,8:volume label,10H:sub-directory,
                 20H:archived file).                              ***

        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of search string
        OUT:    *{TIME} time file last written
                *{DATE} date file last written
                *{SIZE_LO} low word of file size
                *{SIZE_HI} high word of file size
                *{OUT_SEG} segment and
                *{OUT_OFF} offset of first matching filename
                *{LENGTH} length of filename found, 0 if not found
        SAMPLE: SRCH_FIL,<SEG_VAL,OFFSET>,
                         <TIME,DATE,SIZE_LO,SIZE_HI,OUT_SEG,OUT_OFF,LENGTH>

SRCH_NXT.ASM         6/25/87      2791
        DESC:   search for the next of a set of matching filenames   V1.00

        ***        CX must be loaded with the appropriate file attribute
                to search on (1:read only,2:hidden file,
                 4:system file,8:volume label,10H:sub-directory,
                 20H:archived file).                              ***

        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of search string
        OUT:    *{TIME} time file last written
                *{DATE} date file last written
                *{SIZE_LO} low word of file size
                *{SIZE_HI} high word of file size
                *{OUT_SEG} segment and
                *{OUT_OFF} offset of first matching filename
                *{LENGTH} length of filename found, 0 if not found
        SAMPLE: SRCH_NXT,<SEG_VAL,OFFSET>,
                         <TIME,DATE,SIZE_LO,SIZE_HI,OUT_SEG,OUT_OFF,LENGTH>

SRCH_PRE.ASM         6/25/87      2440
        DESC:   search for the previous file of a set of filenames   V1.00

        ***        CX must be loaded with the appropriate file attribute
                to search on (1:read only,2:hidden file,
                 4:system file,8:volume label,10H:sub-directory,
                 20H:archived file).                              ***

        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of search string
        OUT:    *{TIME} time file last written
                *{DATE} date file last written
                *{SIZE_LO} low word of file size
                *{SIZE_HI} high word of file size
                *{OUT_SEG} segment and
                *{OUT_OFF} offset of first matching filename
                *{LENGTH} length of filename found, 0 if not found
        SAMPLE: SRCH_PRE,<SEG_VAL,OFFSET>,
                         <TIME,DATE,SIZE_LO,SIZE_HI,OUT_SEG,OUT_OFF,LENGTH>

SRCH_VOL.ASM         6/25/87      1483
        DESC:   Search for a volume name                             V1.00
        IN:     *{DRIVE} drive number (0:default,1:A,2:B,etc...)
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of volume name
                *{FLAG} has a value of 0 if a volume label is found
        SAMPLE: Callm,<DRIVE>,<SEG_VAL,OFFSET,FLAG>

STK_STOP.ASM         6/25/87       685
        DESC:   return from the user stack to the system stack       V1.00
        SAMPLE: STK_STOP

STK_STRT.ASM         6/25/87       742
        DESC:   start a user stack                                   V1.00
        SAMPLE: STK_STRT

TEXT_RD.ASM          6/25/87      2204
        DESC:   Reads text from the screen                           V1.00
        IN:     *{PAGE} page number of screen (0-3)
                *{ROWCOL} row(0-24), col(0-79) (i.e. 0345) at which to
                 begin reading from screen
                *{NUM_CHARS} # of chars to read
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of string read
        SAMPLE: Callm   TEXT_RD,<PAGE,ROWCOL,NUM_CHARS>,<SEG_VAL,OFFSET>

TEXT_WRT.ASM         6/25/87      3181
        DESC:   Writes text to screen                                V1.02
        IN:     *{ATTRIB_PAGE} attribute used to display text (00-FFH),
                 page number to write on (0-3)
                *{ROWCOL} row(0-24), col(0-79) row and column to start writing
                 at.
                *{SEG_VAL} segment of text and
                *{OFFSET} offset of text
                *{END_OFF} offset end text
        SAMPLE: Callm   TEXT_WRT,<PAGE,ROWCOL,SEG_VAL,OFFSET,END_OFF>,

TIME_GET.ASM         6/25/87      1546
        DESC:   Gets the system time                                 V1.00
        OUT:    *{SEG_VAL} segment address and
                *{OFFSET} offset within segment of time in ASCII printable
                 format. Time is in format HH:MM:SS.XX
        SAMPLE: Callm   TIME_GET,,<SEG_VAL,OFFSET>

WRITE.ASM            6/25/87       995
        DESC:   Writes to a data file                                V1.00
        IN:     *{HANDLE} handle of file
                *{NUM_BYTES} number of bytes to write
                *{SEG_VAL} segment and
                *{OFFSET} offset of buffer
        OUT:    *{OUT_BYTES} number of bytes actually written
        SAMPLE: Callm   WRITE,<HANDLE,NUM_BYTES,SEG_VAL,OFFSET>,<OUT_BYTES>


       SECTION II. ROUTINES LISTED BY FUNCTIONAL AREA

                        BUFFER OPERATIONS

HEXDSPLY.ASM         6/25/87      1855
        DESC:   Displays hexadecimal codes as ASCII values           V1.00
        IN:     *{HEX_WORD} hex word (0000 - FFFF)
        OUT:    *{ASC_HI} first two characters of result (i.e EF from EFAB)
                *{ASC_LO} second two characters of result (i.e. AB from EFAB)
        SAMPLE: Callm   HEXDSPLY,<HEX_WORD>,<ASC_HI,ASC_LO>

HEX_ASC.ASM          6/25/87      3724
        DESC:   Convert Hex numbers to decimal in ASCII format       V1.03
        IN:     *{HI_HEX} High order word of 4 byte hexadecimal number
                *{LO_HEX} Low order word of 4 byte hexadecimal number
        OUT:    *{ASC_1} five words from MSB to LSB with leading
                *{ASC_2} zeros stripped
                *{ASC_3}
                *{ASC_4}
                *{ASC_5}
        SAMPLE: Callm   HEX_ASC,<HI_HEX,LO_HEX>,
                                <ASC_1,ASC_2,ASC_3,ASC_4,ASC_5>

MOVE_BYT.ASM         6/25/87       912
        DESC:   Moves a source buffer to a dest. buffer              V1.00
        IN:     *{SEG_VAL1} segment and
                *{OFFSET1} offset of input buffer
                *{SEG_VAL2} segment and
                *{OFFSET2} offset of output buffer
                *{NUM_CHARS} # of chars to move
        SAMPLE: Callm   MOVE_BYT,<SEG_VAL1,OFFSET1,SEG_VAL2,OFFSET2,
                                 NUM_CHARS>,

REPLACE.ASM          6/25/87      1640
        DESC:   Replaces an occurence of a string with another       V1.00
                string
        IN:     *{RSTRNG} segment and
                *{ROFF} offset of replacement string (must be same length)
                *{DIR} direction of search (0:forward,1-FFFF:reverse)
                *{SEG_VAL} segment and
                *{OFFSET} offset of buffer to search
                *{LENGTH} length of search string
                *{SSTRNG} segment and
                *{OSTRNG} offset of search string
        OUT:    *{OSEG} segment and
                *{OOFF} offset of replacement (both zero if not replaced)
        SAMPLE: Callm   REPLACE,<RSTRNG,ROFF,DIR,SEG_VAL,OFFSET,LENGTH,
                        SSTRNG,OSTRNG>,<OSEG,OOFF>

SCAN_BYT.ASM         6/25/87      2716
        DESC:   Scans a source buffer for given characters           V1.01
                and returns the character and location of the closest
                matching character

        ***        SCAN_BYT performs forward and reverse searches. The CLD
                assembler command must be used before calling the procedure
                to perform a forward search. The STD command must be used
                before calling to perform a reverse search.     ***

        IN:     *{MATCH2N} 2nd and additional matches
                *{SEG_VAL} segment and
                *{OFFSET} offset of buffer to scan
                *{MATCH1} 1st of N number of possible matching sequences
                *{N} number of matching sequences passed in
        OUT:    *{MATCH_VAL} value of matching character
                *{MATCH_LOC} location of offset in match segment where
                 matching value was found
        SAMPLE: Callm   SCAN_BYT,<MATCH2N,SEG_VAL,OFFSET,MATCH1,N>,
                                 <MATCH_VAL,MATCH_LOC>

SEARCH.ASM           6/25/87      2078
        DESC:   Searches for a string in the indicated buffer        V1.02
        IN:     *{DIR} direction of search (0:forward,1-FFFF:reverse)
                *{SEG_VAL} segment and
                *{OFFSET} offset of buffer to search
                *{LENGTH} length of search string
                *{SSTRNG} segment and
                *{OSTRNG} offset of search string
        OUT:    *{OSEG} segment and
                *{OOFF} of search string (both zero if not found)
        SAMPLE: Callm   SEARCH,<DIR,SEG_VAL,OFFSET,LENGTH,SSTRNG,OSTRNG>,
                               <OSEG,OOFF>


                           DOS CONTROL

ALOC_CHG.ASM         6/25/87       902
        DESC:   Modifies Allocated memory block size                 V1.00
        IN:     *{BLOCK} segment address of memory block to be modified
                *{PARA} new requested block size in paragraphs {ie multiples
                 of 16 bytes}
        SAMPLE: Callm   ALOC_CHG,<BLOCK,PARA>,

CHG_DIR.ASM          6/25/87       821
        DESC:   Changes to a new directory using the path provided   V1.00
        IN:     *{SEG_VAL} segment  and
                *{OFFSET} offset of path string
        SAMPLE: Callm   CHG_DIR,<SEG_VAL,OFFSET>,

EXECUTE.ASM          6/25/87      2336
        DESC:   Loads and Executes another program                   V1.00
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of filename to run including extension
                *{PAR_HI} high word and
                *{PAR_LO} low word of pointer to command line
                 to be passed to new program. Command line should be in the
                 form N,' ',PARAM,0DH where N is the length of PARAM+1, and is
                 followed by a space. PARAM is the command line and 0DH is
                 a carriage return ending the line.
                *{MEMBLK} segment value of last memory control block 
                 segment is typically the value of DS at entry to the main
                 program.
                *{SIZE} size of main calling program in segment form
        SAMPLE: Callm   EXECUTE,<SEG_VAL,OFFSET,PAR_HI,PAR_LO,MEMBLK,SIZE>,

GET_DIR.ASM          6/25/87      1038
        DESC:   gets the current directory path string in the form   V1.00
                dir1\dir2\dir3...
        IN:     *{DRIVE} drive number of the drive to operate on where
                 0 is the default, 1 is A, etc.
                *{SEG_VAL} segment and
                *{OFFSET} offset of 64 byte user are where resultant string
                 will be placed ending with a byte containing 0
        SAMPLE: Callm   GET_DIR,<DRIVE,SEG_VAL,OFFSET>,

PARM_BRK.ASM         6/25/87      1843
        DESC:   Takes in parameter string retrieved from DOS level   V1.00
                and breaks the string into separate elements using
                commas and the end of line as the only breaks.
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of parameter string
                *{LENGTH} length of parameter string
        OUT:    *{N} n is the number of sets of segment,offset  and length
                 groups returned, which indicates the number of total
                 parameters passed to the program.
                *{OSEG_VAL,OOFFSET,OLENGTH} repeated N times
                 and returned in reverse order (i.e. P3, P2 , P1)
        SAMPLE: Callm   PARM_BRK,<SEG_VAL,OFFSET,LENGTH>,
                                 <N,<OSEG_VAL,OOFFSET,OLENGTH>>

PARM_GET.ASM         6/25/87      1127
        DESC:   Gets parameters passed to program from DOS level     V1.00
                at DS+80H
        IN:     *{DS} value passed to data segment at start of main program
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of parameter string
                *{LENGTH} length of parameter string
        SAMPLE: Callm   PARM_GET,<DS>,<SEG_VAL,OFFSET,LENGTH>

POPALL.ASM           6/25/87      1190
        DESC:   Pop all registers (SI,DI,BP,ES,DS,DX,CX,BX,AX)       V1.00
        SAMPLE: POPALL

PUSHALL.ASM          6/25/87      1277
        DESC:   Push all registers (AX,BX,CX,DX,DS,ES,BP,DI,SI)      V1.00
        SAMPLE: PUSHALL

SET_DSK.ASM          6/25/87       681
        DESC:   sets the disk transfer address                       V1.00
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of DTA
        SAMPLE: Callm   SET_DSK,<SEG_VAL,OFFSET>,

STK_STOP.ASM         6/25/87       685
        DESC:   return from the user stack to the system stack       V1.00
        SAMPLE: STK_STOP

STK_STRT.ASM         6/25/87       742
        DESC:   start a user stack                                   V1.00
        SAMPLE: STK_STRT


                        FILE MANIPULATION

CHG_MOD.ASM          6/25/87      1211
        DESC:   Changes the mode of a file                           V1.00
                (ie archived, hidden, system)
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of filename
                *{FUNC_CODE} function code(1:set mode,0:get mode)
                *{FILE_MODE} mode of file (1:read only,2:hidden file,
                 4:system file,8:volume label,10H:sub-directory,
                 20H:archived file
        OUT:    *{CMODE} mode of file after completions of call
        SAMPLE: Callm   CHG_MOD,<SEG_VAL,OFFSET,FUNC_CODE,FILE_MODE>,<CMODE>

CLOSE.ASM            6/25/87       693
        DESC:   Closes a file handle                                 V1.00
        IN:     *{INHNDL} handle of file to be closed
        SAMPLE: Callm   CLOSE,<INHNDL>,

COPY.ASM             6/25/87      2768
        DESC:   Copies existing file to new or existing file         V1.00
                using complete path names
        IN:     *{OUT_SEG_VAL} segment and
                *{OUT_OFFSET} offset of new filename
                *{IN_SEG_VAL} segment and
                *{IN_OFFSET} offset of old filename
        SAMPLE: Callm   COPY,<OUT_SEG_VAL,OUT_OFFSET,IN_SEG_VAL,IN_OFFSET>,

CREATE.ASM           6/25/87      1009
        DESC:   Creates a new data file                              V1.00
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of filename to be created as ASCIIZ string
                *{ATRB} attribute or mode of file as listed in CHG_MOD
                 command
        OUT:    *{OUTHNDL} handle of file created
        SAMPLE: Callm   CREATE,<SEG_VAL,OFFSET,ATRB>,<OUTHNDL>

DELETE.ASM           6/25/87       822
        DESC:   Deletes a file                                       V1.00
        IN:     *{SEG_VAL} segment
                *{OFFSET} offset of filename to be deleted
        SAMPLE: Callm   DELETE,<SEG_VAL,OFFSET>,

MOV_PTR.ASM          6/25/87      1195
        DESC:   Moves the file read/write pointer                    V1.00
        IN:     *{METH_VAL} Method value
                 (0:ofst,1:ofst+cloc,2:eof+offset)
                *{HANDLE} handle
                *{MSW} most significant word of offset
                *{LSW} least significant word of offset
        OUT:    *{OMSW} most significant word of pointer location
                *{OLSW} least significant word of pointer location
        SAMPLE: Callm   MOV_PTR,<METH_VAL,HANDLE,MSW,LSW>,<OMSW,OLSW>

OPEN.ASM             6/25/87       967
        DESC:   Opens a file                                         V1.00
        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of filename as ASCIIZ strng
                *{ACC_CODE} access code of file (0:read,1:write,2:read write)
        OUT:    *{HANDLE} handle of file
        SAMPLE: Callm   OPEN,<SEG_VAL,OFFSET,ACC_CODE>,<HANDLE>

READ.ASM             6/25/87      1008
        DESC:   Reads data from a file                               V1.00
        IN:     *{HANDLE} handle of file
                *{NUM_BYTES} number of bytes requested to read from file
                *{SEG_VAL} segment and
                *{OFFSET} offset of buffer
        OUT:    *{NUM_READ} number of bytes actually read
        SAMPLE: Callm   READ,<HANDLE,NUM_BYTES,SEG_VAL,OFFSET>,<NUM_READ>

SRCH_FIL.ASM         6/25/87      2791
        DESC:   search for the first of a set of matching filenames  V1.00

        ***        CX must be loaded with the appropriate file attribute
                to search on (1:read only,2:hidden file,
                 4:system file,8:volume label,10H:sub-directory,
                 20H:archived file).                              ***

        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of search string
        OUT:    *{TIME} time file last written
                *{DATE} date file last written
                *{SIZE_LO} low word of file size
                *{SIZE_HI} high word of file size
                *{OUT_SEG} segment and
                *{OUT_OFF} offset of first matching filename
                *{LENGTH} length of filename found, 0 if not found
        SAMPLE: SRCH_FIL,<SEG_VAL,OFFSET>,
                         <TIME,DATE,SIZE_LO,SIZE_HI,OUT_SEG,OUT_OFF,LENGTH>

SRCH_NXT.ASM         6/25/87      2791
        DESC:   search for the next of a set of matching filenames   V1.00

        ***        CX must be loaded with the appropriate file attribute
                to search on (1:read only,2:hidden file,
                 4:system file,8:volume label,10H:sub-directory,
                 20H:archived file).                              ***

        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of search string
        OUT:    *{TIME} time file last written
                *{DATE} date file last written
                *{SIZE_LO} low word of file size
                *{SIZE_HI} high word of file size
                *{OUT_SEG} segment and
                *{OUT_OFF} offset of first matching filename
                *{LENGTH} length of filename found, 0 if not found
        SAMPLE: SRCH_NXT,<SEG_VAL,OFFSET>,
                         <TIME,DATE,SIZE_LO,SIZE_HI,OUT_SEG,OUT_OFF,LENGTH>

SRCH_PRE.ASM         6/25/87      2440
        DESC:   search for the previous file of a set of filenames   V1.00

        ***        CX must be loaded with the appropriate file attribute
                to search on (1:read only,2:hidden file,
                 4:system file,8:volume label,10H:sub-directory,
                 20H:archived file).                              ***

        IN:     *{SEG_VAL} segment and
                *{OFFSET} offset of search string
        OUT:    *{TIME} time file last written
                *{DATE} date file last written
                *{SIZE_LO} low word of file size
                *{SIZE_HI} high word of file size
                *{OUT_SEG} segment and
                *{OUT_OFF} offset of first matching filename
                *{LENGTH} length of filename found, 0 if not found
        SAMPLE: SRCH_PRE,<SEG_VAL,OFFSET>,
                         <TIME,DATE,SIZE_LO,SIZE_HI,OUT_SEG,OUT_OFF,LENGTH>

SRCH_VOL.ASM         6/25/87      1483
        DESC:   Search for a volume name                             V1.00
        IN:     *{DRIVE} drive number (0:default,1:A,2:B,etc...)
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of volume name
                *{FLAG} has a value of 0 if a volume label is found
        SAMPLE: Callm,<DRIVE>,<SEG_VAL,OFFSET,FLAG>

WRITE.ASM            6/25/87       995
        DESC:   Writes to a data file                                V1.00
        IN:     *{HANDLE} handle of file
                *{NUM_BYTES} number of bytes to write
                *{SEG_VAL} segment and
                *{OFFSET} offset of buffer
        OUT:    *{OUT_BYTES} number of bytes actually written
        SAMPLE: Callm   WRITE,<HANDLE,NUM_BYTES,SEG_VAL,OFFSET>,<OUT_BYTES>


                          I/O ROUTINES

CHAR_GET.ASM         6/25/87       771
        DESC:   gets a character from the keyboard                   V1.00
        IN:     *{REQ_TYPE} (0:get character,1:see if character
                 is there,2:get shift status)
        OUT:    *{CHAR} character ( high byte is shift status,
                 low byte is char.)
        SAMPLE: Callm   CHAR_GET,<REQ_TYPE>,<CHAR>

GET_TEXT.ASM         6/25/87      1333
        DESC:   gets a line of text from the keyboard                V1.00
        IN:     *{MAX_CHARS} maximum # of characters to get from keyboard
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of text buffer
                *{LENGTH} length of text
        SAMPLE: Callm   GET_CHAR,<MAX_CHARS>,<SEG_VAL,OFFSET,LENGTH>


                       PROGRAM INFORMATION

ERRORMSG.ASM         6/25/87      5589
        DESC:   Prints DOS error messages 1-18 and additional user   V1.01
                 supplied messages from 19 up. If the value of ERR_NUM is
                 0 control returns to the calling program with no effect.
                 If ERR_NUM is greater than the value of the maximum error
                 message then the message "No Error for This Value" is
                 displayed and control returns to DOS. If an error code is
                 displayed then control also returns to DOS. The memory
                 address where the error occured is displayed on exit.
        IN:     *{ERR_NUM} error number where the possible legal values are:
                 1......Invalid Function Number
                 2......File Not Found
                 3......Path Not Found
                 4......Too Many Open Files (no handles left)
                 5......Access Denied
                 6......Invalid Handle
                 7......Memory Control Blocks Destroyed
                 8......Insufficient Memory
                 9......Invalid Memory Block Address
                10......Invalid Environment
                11......Invalid Format
                12......Invalid Access Code
                13......Invalid Data
                14......This Error Does Not Exist
                15......Invalid Drive Was Specified
                16......Attempted To Remove The Current Directory
                17......Not Same Device
                18......No More Files
                19......No Room For File(s) On Target Disk
                20......No Filename(s) Specified
                21......No Volume Label On Disk
                22......Wrong Number of Parameters
                >22.....No Error for This Value
        SAMPLE: Callm   ERRORMSG,<ERR_NUM>,

GET_DSK.ASM          6/25/87       679
        DESC:   returns the disk transfer address                    V1.00
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of DTA
        SAMPLE: Callm   GET_DSK,,<SEG_VAL,OFFSET>


                       SCREEN MANIPULATION

ATRB_WRT.ASM         6/25/87      2268
        DESC:   Writes character attributes to the screen            V1.00
        IN:     *{PAGE} page number (0-3) 4 available pages in 80 column mode
                *{ROWCOL} row(0-24),col(0-79) (ie 0345 indicating fourth row,
                 46th column)
                *{ATRB} attribute (see technical reference manual for
                 information on color graphics adapter)
                *{NUM_CHARS} # of chars to be affected
        SAMPLE: Callm   ATRB_WRT,<PAGE,ROWCOL,ATRB,NUM_CHARS>,

CLEAR.ASM            6/25/87       524
        DESC:   Clears the screen                                    V1.00
        SAMPLE: Callm   CLEAR,,

CURS_GET.ASM         6/25/87       938
        DESC:   Gets Cursor Position                                 V1.00
        IN:     *{PAGE_NUM} page number (0-7) in 40 character mode
                 or (0-3) in 80 character mode (i.e. 0003) is page 4
        OUT:    *{ROWCOL} row (0-24),col (0-79)  (i.e. 0104)
                 1st row, 5th column
                *{CURS_MODE} cursor mode (see manual for description)
        SAMPLE: Callm   CURS_GET,<PAGE_NUM>,<ROWCOL,CURS_MODE>

CURS_SET.ASM         6/25/87       883
        DESC:   Sets Cursor Position                                 V1.01
        IN:     *{ROWCOL} row and column to postion cursor
                 row (0-24),col (0-79)  (i.e. 0104)
                 1st row, 5th column
                *{PAGE_NUM} page number (0-7) in 40 character mode and (0-3)
                 in 80 character mode (i.e. 0003) is page 4
        SAMPLE: Callm   CURS_SET,<ROWCOL,PAGE_NUM>,

SCRN_RST.ASM         6/25/87       780
        DESC:   Restores 16K screen to video memory                  V1.00
        SAMPLE: SCRN_RST

SCRN_SAV.ASM         6/25/87       834
        DESC:   Saves 16K screen from video memory                   V1.00
        SAMPLE: SCRN_SAV

SCRN_TYP.ASM         6/25/87       899
        DESC:   Returns the address of the video memory buffer       V1.00
        OUT:    *{VIDEO} segment address of start of video memory area
                 Useful only with MDA and CGA graphics. B&W area is at B000H
                 while color area is at B800H
        SAMPLE: Callm   SCRN_TYP,,<VIDEO>

TEXT_RD.ASM          6/25/87      2204
        DESC:   Reads text from the screen                           V1.00
        IN:     *{PAGE} page number of screen (0-3)
                *{ROWCOL} row(0-24), col(0-79) (i.e. 0345) at which to
                 begin reading from screen
                *{NUM_CHARS} # of chars to read
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of string read
        SAMPLE: Callm   TEXT_RD,<PAGE,ROWCOL,NUM_CHARS>,<SEG_VAL,OFFSET>

TEXT_WRT.ASM         6/25/87      3181
        DESC:   Writes text to screen                                V1.02
        IN:     *{ATTRIB_PAGE} attribute used to display text (00-FFH),
                 page number to write on (0-3)
                *{ROWCOL} row(0-24), col(0-79) row and column to start writing
                 at.
                *{SEG_VAL} segment of text and
                *{OFFSET} offset of text
                *{END_OFF} offset end text
        SAMPLE: Callm   TEXT_WRT,<PAGE,ROWCOL,SEG_VAL,OFFSET,END_OFF>,


                       SYSTEM INFORMATION

DATE_GET.ASM         6/25/87      1482
        DESC:   Gets the system date                                 V1.00
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of system date in format MM/DD/YY
        SAMPLE: Callm   DATE_GET,<SEG_VAL,OFFSET>,

FILEDATE.ASM         6/25/87      1891
        DESC:   Converts Bit-Mapped file date to ASCII format        V1.00
        IN :        *file date in form yyyyyyymmmmmddddd
                where mm is the month 1-12
                      dd is the day 1-31
                      yy is the year 0-119 (1980-2099)
        OUT :        *segment and
                *offset of the file date in the form
                mm/dd/yy
        SAMPLE: Callm   FILEDATE,<DATE>,<ES,BX>

HELP.ASM             6/25/87      3269
        DESC:   Provides help to the user for all programs           V1.03
                linking to the help module and following the
                specified format
        IN:     *{DS} value passed to data segment at start of main program
                *{HELP} location of help data
        OUT:    *{SEG_VAL} segment and
                *{OFFSET} offset of parameter string
                *{LENGTH} length of parameter string
        SAMPLE: Callm   HELP,<DS,HELP>,<SEG_VAL,OFFSET,LENGTH>

TIME_GET.ASM         6/25/87      1546
        DESC:   Gets the system time                                 V1.00
        OUT:    *{SEG_VAL} segment address and
                *{OFFSET} offset within segment of time in ASCII printable
                 format. Time is in format HH:MM:SS.XX
        SAMPLE: Callm   TIME_GET,,<SEG_VAL,OFFSET>