Skeleton Format for MASM Main Programs

;	DESC:	description of the program                           VX.XX

		where X.XX is the version number of the program

;	IN:	*input parameter1 (one to a line)
;		*input parameter2
;		.................
;		*input parametern
;	OUT:	*output parameter1 (one to a line)
;		*output parameter2
;		..................
;		*output parametern
;	SAMPLE:	Program name <input parameter1,ip2,...,ipn>,
;		             <output parameter1,op2,..,opn>
;	####################################################################


DSEG	Segment Para Public 'DATA'

		where DSEG is the program name with a 'D' appended to it.
		and the last letter of the program name is dropped if it
		is 8 characters.

		help block1 in the format of a call to TEXT_WRT (five words)
		help block2 (segment address of licence block, one word)

		DW	0			;help message.
		DW	0
		DD	MHELP
		DW	EHELP
MHELP		DB	'reiterate description as at top'
EHELP		DB	0

		additional program data

DSEG	Ends


		declaration of external procedures



CSEG	Segment Para Public 'CODE'

		where CSEG is the
		code segment in the same format as the data segment except
		with a 'C' in place as the 'D'.

	Assume CS:CSEG,DS:DESG

		macro calling program

	Include	CALLM.MAC			;macro file which allows
						;input and output of
						;parameters to subroutines.
		data area

	DW	0,0,0,180,0,0,0

		notice which must be 48 characters exactly and must be
		directly before the main program.

	DB	'program name - V1.00, Copyright 1987, CoreTechs   ',0DH,0AH

program	Proc	Far			;main procedure.

	where program is the name of the program

	Push	DS				;store return address.
	Xor	AX,AX
	Push	AX

		main program body

program	Endp
CSEG	Ends
	End	program