Quick Documentation for Terminal.Pas by Jim Nutt (76044,1155 or 71076,1434) Description: Terminal is a terminal emulation program supporting VIDTEX cursor control codes and CIS-A protocol uploads and downloads. It is written in Turbo Pascal and is placed in the public domain. Thanks to Charles McGuinness of the programmer's sig (PCS-158) for all the information there on CIS-A as well as some examples coded in C. Thanks to Scott Murphy and Alan Bishop for the routines to do interrupt driven serial I/O. This is a program under development, more features are yet to come, but hopefully this will whet your appetite a little bit. Startup: Terminal is set up to use com1:, anyone needing to use com2: will have to change the appropriate places in async.pas. (async.pas is a slightly modified version of ITRMPORT.INC by Scott Murphy, patches for it to work on com2: should work for Terminal as well). To start the program simply type 'terminal ', it will come up with the com parameters set to 1200 baud, 8 data bits, no parity, and 1 stop bit. To use it with CIS you must go to DEFALT and change your terminal type to VIDTEX, this will set the other parameters appropriately. Once this is done Terminal will be ready to go. Commands: Terminal has very few commands, yet. I am open for suggestions as to what commands are needed and how badly they are needed. The current command list is as follows: Buffer Commands: - Open RAM capture buffer. The capture buffer is 64k long. - Close RAM capture buffer. This is done automatically when the buffer files up. - Kill the capture buffer. Clears the buffer's contents. - Write the capture buffer to a file. Parameter Set Command: -

Set program and communications parameters. This command asks for a subcommand. These are specified in the form "subcommand,value". The following are legal subcommands: baud,value Sets the current baud rate to value word,value Sets the current word length to value stop,value Sets the current stop bits to value parity,value Sets the parity to value display Displays the current parameters file,filename Assigns the capture buffer file to filename. All subcommands may be abbreviated to a single letter followed by a parameter. In the case of display, no parameter is necessary. Miscellaneous commands: - Hangs up the modem (hopefully) by bringing DTR low. - Prompts for the number to be dialed. Currently only for Hayes(tm) compatible modems. - Exits terminal. Does not disconnect. Uploads/Downloads To upload and download using Terminal, first make sure that you have told DEFALT that you are using a vidtex compatible terminal emulator. Next just issue the normal commands to download without specifying a protocol. CIS will interrogate Terminal and ask what protocol to use, to which Terminal will reply 'CIS A, of course', (or something to that effect). CIS will then prompt you for a filename to use at your end, answer that prompt and the computers will do the rest. Cursor Positioning Terminal responds to all the Vidtex screen control commands except those dealing with color and graphics (coming soon!). It also does not allow CIS to open and close its ram buffer. The codes are listed in VID-12 on CIS. Key  to continue: Q allow CIS to open and close