TOPIC: NSS, NFS, and MODHEX Disabled Speed Switching - Differences

MODHEXing is functionally equivilant to NSS. What NSS does in addition
is actually remove the code from the source that handles speed switching.
MODHEX can only enable or disable speed switching, not remove code.
                                                                             
NFS will not floppy switch. However it will attempt speed switching if:
 1) CTRL-ALT + or - are pressed
 2) The speed switch routine is called
 3) Protected mode access is done

_________________________________________________________________________

TOPIC: Power On Self Test Numbers - 286 and 386 BIOS

These POST numbers are output to ports 80H and 300H during the POST. These are
valid for Award BIOSs 3.00 through 3.03 (as of 8-26-87). System will keep 
outputting POST sequence to DEBUG_PORT defined in ATBASE.INC if failure 
occurred during POST 6 to 24. After that the error message will be displayed 
on screen.

POST 1   1H   - Processor test 1 - processor status verification
                Output: infinite loop if failed, continue test if ok
                Registers: AX, BP
POST 2   2H   - Determine type of POST test
                Failed if keyboard interface buffer filled with data
                Output: infinite loop if failed, continue test if ok
                Registers: AX, BX, BP
POST 3   3H   - Clear 8042 interface
                Output: infinite loop if failed, continue test if ok
                Registers: AX, BX, BP
POST 4   4H   - reset 8042
                Input: none
                Registers: AX, BX, BP
POST 5   5H   - get 8042 manufacturing status
                Read input port via keyboard controller to determine 
                manufacturing or normal mode operation.
                Output: infinite loop if failed, continue test if ok
                Registers: AX, BX, BP
POST 6   6H   - Init chips (DMA, 8259'S, CMOS)
POST 7   7H   - Processor test #2
POST 8   8H   - Initialize CMOS chip
POST 9   9H   - Eprom checksum for 32 kbytes
POST 10  AH   - Initialize video interface
POST 11  BH   - Test 8254 channel 0
POST 12  CH   - Test 8254 channel 1
POST 13  DH   - Test 8254 channel 2
POST 14  EH   - Test CMOS date and timer
POST 15  FH   - Test CMOS shutdown byte
POST 16  10H  - Test DMA channel 0
POST 17  11H  - Test DMA channel 1
POST 18  12H  - Test DMA page registers
POST 19  13H  - Test 8741 keyboard controller
POST 20  14H  - Test meoory refresh toggle circuits
POST 21  15H  - Test 1st 64k bytes of system memory
POST 22  16H  - Setup interrupt vector table
POST 23  17H  - Setup video I/O operations
POST 24  18H  - Test video memory
POST 25  19H  - Test 8259 channel 1 mask bits
POST 26  1AH  - Test 8259 channel 2 mask bits
POST 27  1BH  - Test CMOS battery level
POST 28  1CH  - Test CMOS checksum
POST 29  1DH  - Setup configuration byte from CMOS
POST 30  1EH  - Sizing system memory & compare w/CMOS
POST 31  1FH  - Test found system memory
POST 32  20H  - Test stuck 8259'S interrupt bits
POST 33  21H  - Test stuck NMI (parity/IO chk) bits
POST 34  22H  - Test 8259 interrupt functionality
POST 35  23H  - Test protected mode and A20 gate
POST 36  24H  - Sizing extended memory above 1MB
POST 37  25H  - Test found system/extended memory
POST 38  26H  - Test exceptions in protected mode
POST 39  27H  - Reserved
POST 40  28H  - Reserved

286 N3.03 Extensions

POST 42  2AH  - POST_KEYBOARD, present during reset keyboard before boot, has
                no relationship to POST 19
POST 43  2BH  - POST_FLOPPY, present during init of floppy controller and
                drive(s)
POST 44  2CH  - POST_COMM, present during init of serial cards
POST 45  2DH  - POST_PRN, present during init of parallel cards
POST 46  2EH  - POST_DISK, present during init of hard disk controller and 
                drive(s)
POST 47  2FH  - POST_MATH, present during init of math co-processor. Result
                remains after DOS boot, left on the port 80 display
POST 48  30H  - POST_EXCEPTION, present during protected mode access, or when
                processor exceptions occur. A failure indicates that protected
                mode return was not possible
POST 204 CCH  - POST_NMI, present when selecting the F2 system halt option
          

Power On Self Test Numbers - 8088/86 BIOS

POST 1   1H   - Processor test 1 - processor status verification
                Output: infinite loop if failed, continue test if ok
                Registers: AX, BP
POST 2   2H   - Determine type of POST test
                Failed if keyboard interface buffer filled with data
                Output: infinite loop if failed, continue test if ok
                Registers: AX, BX, BP
POST 6   6H   - Init chips (DMA, 8259'S, CMOS)
POST 7   7H   - Processor test #2
POST 9   9H   - Eprom checksum for 32 kbytes
POST 10  AH   - Initialize video interface
POST 21  15H  - Test 1st 64k bytes of system memory
POST 22  16H  - Setup interrupt vector table
POST 23  17H  - Setup video I/O operations
POST 24  18H  - Test video memory
POST 25  19H  - Test 8259 channel 1 mask bits
POST 26  1AH  - Test 8259 channel 2 mask bits
POST 29  1DH  - Setup configuration byte from CMOS
POST 30  1EH  - Sizing system memory & compare w/CMOS
POST 31  1FH  - Test found system memory
POST 32  20H  - Test stuck 8259'S interrupt bits
POST 33  21H  - Test stuck NMI (parity/IO chk) bits
POST 34  22H  - Test 8259 interrupt functionality

_________________________________________________________________________

TOPIC: Award BIOS Messages/Beeps

 ______________________________

 AWARD BIOS 8086/88 VERSION 3.0
 ______________________________

 Message/Beep(s)                        Description

 1 long beep and 2 short beeps..........Video error

 2 short beeps followed by              
 PRESS F1 KEY TO CONTINUE...............Any non-fatal error
                                        
 1 short beep...........................No error during POST

 201 followed by:                       
 ERROR. PRESS F1 KEY TO CONTINUE........Memory test failed.

 301 followed by:                       Keyboard error, keyboard not
 ERROR. PRESS F1 KEY TO CONTINUE........present, or key stuck.

 601 followed by:                       Diskette power on diagnostic test
 ERROR. PRESS F1 KEY TO CONTINUE........failed.                            

 1801 followed by:                      I/O expansion unit failed power on
 ERROR. PRESS F1 KEY TO CONTINUE........diagnostic.                        

 PARITY CHECK 1.........................Parity error in system board
                                        memory. This is a fatal error.

 PARITY CHECK 2.........................Parity error in expansion unit
                                        memory. This is a fatal error.

 INSERT SYSTEM DISK IN DRIVE............This is a disk boot failure.
 A, AND PRESS ANY KEY

 XXX KB MEMORY GOOD.....................XXX KB memory tested good during
                                        memory test.                       
 _______________________________

 AWARD BIOS 286/386 VERSION 3.03
 _______________________________

 Message/Beep(s)                        Description

 1 long beep and 2 short beeps..........Video error              

 1 long beep and 3 short beeps..........Keyboard controller error
 followed by system halt.

 2 short beeps, followed by.............Any non-fatal error      
 PRESS F1 KEY TO CONTINUE

 1 short beep...........................No error during POST     

 REFRESH TIMING ERROR                   The refresh clock is not operating
 then PRESS F1 KEY TO CONTINUE..........as expected.                      
 OR CTRL-ALT ESC FOR SETUP...

 KEYBOARD ERROR OR NO         ..........Either there is a keyboard problem,
 KEYBOARD PRESENT                       or the keyboard is not attached.
 then PRESS F1 KEY TO CONTINUE
 OR CTRL-ALT ESC FOR SETUP...

 EQUIPMENT CONFIGURATION                The system configuration determined
 ERROR - RUN SETUP                      by POST is different from what was 
 then PRESS F1 KEY TO CONTINUE..........defined using SETUP.               
 OR CTRL-ALT ESC FOR SETUP...

 SYSTEM KEY IS IN LOCKED................The keyboard is physically locked
 POSITION - KEYBOARD IS                 out via the key on the system's
 LOCKED OUT TURN KEY TO                 front panel.     
 UNLOCKED POSITION AND
 then PRESS F1 KEY TO CONTINUE
 OR CTRL-ALT ESC FOR SETUP...
                                        
 MEMORY SIZE ERROR - RUN SETUP..........The amount of memory found by POST
 then PRESS F1 KEY TO CONTINUE          is different than the amount      
 OR CTRL-ALT ESC FOR SETUP...           defined using SETUP.              

 REAL TIME CLOCK ERROR - RUN SETUP......The real time clock is not        
 then PRESS F1 KEY TO CONTINUE          operating as expected.          
 OR CTRL-ALT ESC FOR SETUP...

 ERROR ENCOUNTERED INITIALIZING.........Reset of fixed disk fails.      
 HARD DRIVE then
 PRESS F1 KEY TO CONTINUE
 OR CTRL-ALT ESC FOR SETUP...

 ERROR INITIALIZING HARD DISK...........Fixed disk controller fails
 CONTROLLER then PRESS F1 KEY TO        internal diagnostic.
 CONTINUE OR CTRL-ALT ESC FOR SETUP...

 FLOPPY DISK CNTRLR ERROR OR NO.........The floppy disk controller is
 CNTRLR PRESENT then PRESS F1 KEY TO    failing its self test, or it is not
 CONTINUE OR CTRL-ALT ESC FOR SETUP...  present in the system.

 CMOS RAM ERROR, CHECK BATTERY/RUN......CMOS is invalid. This can be caused
 SETUP then PRESS F1 KEY TO             by the battery not operating
 CONTINUE OR CTRL-ALT ESC FOR SETUP...  correctly. SETUP must be run.

 PRESS A KEY TO REBOOT..................This occurs when a call has been
                                        made to ROM BASIC which is not
                                        present in the Award BIOS.

 MEMORY ADDRESSING ERROR AT XXXX........Memory errors. Values are as
 MEMORY ERROR AT XXXX                   close as possible.
 WROTE 0A5A5 BUT READ XXXX

 DISK BOOT FAILURE, INSERT..............The system is unable to load the
 SYSTEM DISK AND PRESS ENTER            system from the boot disk. Insert a
                                        working boot disk into drive A: and
                                        press ENTER.

 PARITY ERROR IN SEGMENT XXXX...........This fatal error occurs during POST
                                        memory test.

 MEMORY VERIFY ERROR....................POST error. AA is # of MBytes
 AA:SSSS:FFFF                           boundary; SSSS=segment FFFF=offset

 IO PARITY ERROR - SYSTEM HALTED........These errors occur after POST has
                                        finished and the system is
                                        operating correctly.
 RAM PARITY ERROR. CHECKING FOR                                            
 SEGMENT ADDRESS...
                                                                           
 They are then followed by either:                                         
 OFFENDING ADDRESS NOT FOUND
 or
 OFFENDING SEGMENT: XXXX
 and then system halt.

 XXXX KILOBYTES MEMORY GOOD

 __________________________

 AWARD EGA BIOS VERSION 1.6
 __________________________

 Message/Beep(s)                        Description

 1 long beep and 2 short beeps..........Video memory error

 1 long beep and 3 short beeps..........EGA memory error

_________________________________________________________________________

TOPIC: 8088/86 BIOS Version 3.0 Switch Settings

8088/86 BIOS Version 3.0 Switch Settings

                                      OFF            ON
The motherboard DIP                   ZDDDDDDDDDDDDDDD?
switch settings for                   3ZDDDDDDDDDDDDD?3
the 3.0 BIOS differ            Normal 33[[[[[[1      33 POST Loop
from previous vers.                   3CDDDDDDDDDDDDD43
                     Diskette 1   3+" 33      2[[[[[[33 5,"
                                      3CDDDDDDDDDDDDD43
                     Diskette 2   3+" 33      3[[[[[[33 5,"
                                      3CDDDDDDDDDDDD443
            Diskette Controller 16-bit33      4[[[[[[33 8-bit
                                      3CDDDDDDDDDDDDD43
                     Video Type       33[[[[[[5      33 EGA  5-on  6-on
                                      3CDDDDDDDDDDDDD43 CO80 5-on  6-off
                                      33[[[[[[6      33 CO40 5-off 6-on
                                      3CDDDDDDDDDDDDD43 MONO 5-off 6-off
        Number of Floppy Drives       33[[[[[[7      33
                                      3CDDDDDDDDDDDDD43 Qty 1  7-on  8-on
                                      33      8[[[[[[33 Qty 2  7-off 8-on
                                      3@DDDDDDDDDDDDDY3 Qty 3  7-on  8-off
                                      @DDDDDDDDDDDDDDDY Qty 4  7-off 8-off