EMS 4.0 Driver Test Program
 Preliminary release Version 1.02


 Written by Douglas Boling
 Copyright (c)1988 - Ziff Davis Publishing Co.




      Description

        The LIM EMS 4.0 Driver test program is designed to test the correct
        implimentation of the EMS 4.0 spec from the aspect of the documented
        software interface. Each of the functions of the EMS driver is called
        and the results of the function are verified with the expected result.
        When the test program detects an error, the tests for the function
        function currently being tested is stopped, and an error message is
        printed. Codes are printed with the error message to assist in the
        localization of the error.

        The tests in this program are based on information in the 'Lotus/
        Intel/Microsoft Expanded memory Specification version 4.0' dated
        October 1987.

        The error code is a 4 digit code that indicates the reason for
        the error message. The first two digits indicate the test routine
        currently being executed. The number matches the function being
        tested. For example, error code 1704 is an error in testing
        function 17. Some error codes do not coorspond to a specific
        functional test. Codes can also be the result of errors in the
        setup and initialization routines.

        When an error is detected in routines vitial to the continued
        testing of the driver, the test program prints the error message
        and program itself terminates without testing any other part of
        the driver.

        Two types of error messages are printed. The first type is printed
        when the EMS driver returns an error though its return code. The
        test program prints a message indicating that an EMS function
        has failed to execute. The return code from the EMS driver is
        included in the error message. It is important to note that
        testing of one function involves the use of other EMS functions.
        It is quite possible that an error will be returned on a function
        not being tested, but rather, a function being used to test some
        other part of the driver.

        The second type of error message is printed when the test program
        detects an error due to an unexpected result of a function. For
        example, if the test program mapped an EMS page to the page frame
        but the driver did not map the correct page. In this case an
        error code is printed indicating the reason for the failure.

        An index to the error codes is in this document. The codes are
        listed by functional tests. All error codes the test program
        prints should be in this index. Errors that cause the test
        program to terminate completely are indicated be the note
        'Terminal error.' For all other errors the test program will
        stop testing the function that failed. The other functions
        will be tested.


      Limitations and Exclusions

        The EMS 4.0 test program does not test parts of the LIM 4.0
        specification. A list of the untested functions is given
        below.
                Non volatile handles - Testing for this function
                        requires the rebooting of the computer.

                Function 25 - Get mappable page array - Since
                        the page array varies from machine to
                        machine there is no way to verify the
                        correctness of the information. The
                        function is called, but the data is
                        not interpeted.

                Function 26 - Get hardware information - Since
                        this information varies from driver to
                        driver, there is no way to verify the
                        correctness of the information. The
                        function is called, but the data is
                        not interpeted. Another progarm,
                        EMSINFO.COM is included with this
                        test program. The EMSINFO program
                        prints various information available
                        to software to the screen in an
                        organized manner.

                DMA alternate register sets. - The program does
                        not test this aspect of the LIM 4.0 spec.



 Error Code Reference for EMS 4.0 driver test.

        This refrence is composed of a section for each aspect of
        the test program. Each section contains a paragraph describing
        how the function is tested, along with a list of the possible
        error codes. Errors marked 'Termination error' cause the program
        to abort all testing and terminate.


      Search for EMS driver
         Driver is detected by the two recommended methods of detection,
         the 'Get interrupt technique' and the 'Open handle technique.'
         If the driver is not found by both methods, the test is terminated.
         Possible error codes:
          9900 : Driver could not be found by Get interrupt technique.
                (Termination error)
          9901 : Driver could not be found by Open handle technique.
                (Termination error)


      Function  01          ;Get status
         Function 1 is tested to assure a returned status of 0.
         Possible error codes:
          0000 : Return code not zero. (Termination error)


      Function  02          ;Get page frame segment address
        Function 2 is called to get the page frame address. The validity
        of the page frame is not tested, however, the remainder
        of the EMS tests depend on this address and will fail
        if the page frame returned is not accurate.
        Possible error codes:
                  0003 : Return code not zero. (Termination error)


      Function  03          ;Get unallocated page count
        Function 3 is called to get determine the number of unallocated
        pages in the system. The number of pages are checked
        to assure that there are enough free pages to complete
        the tests.
        Possible error codes:
        0004 : Return code not zero. (Termination error)
        0005 : Not enough free pages to complete test (Termination
                 error.)


      Function  04          ;Allocate pages
        Function 4 is called to allocate handles and pages for the test.
        Any error detected during the allocation of pages
        terminates the test.
        Possible error codes:
         0010 : Return code not zero during first handle allocation.
                  (Termination error)
         0013 : Return code not zero during handle 2 - 9 allocation.
                  (Termination error)


      Function  05          ;Map/unmap handle pages
        Function 5 is called to initially map the pages so they can be
        initialized. If an error occurs during this part of the
        test the test terminates.
        The function is tested for by mapping pages to physical
        pages in the page frame and comparing the data to the
        initialized data for the specific handle and logical
        page.
        Possible error codes:
         0011 : Return code not zero during map of first handle
                 pages. (Termination error)
         0013 : Return code not zero during map of handles 2 - 9
                 pages. (Termination error)
         0500 : Data in physical page 0 does not match expected data
         0501 : Data in physical page 1 does not match expected data
         0502 : Data in physical page 2 does not match expected data
         0503 : Data in physical page 3 does not match expected data


      Function  06          ;Deallocate pages



      Function  07          ;Get version
        Function 7 is tested to confirm version 4.0 or greater.
        Possible error codes:
         0001 : Return code not zero. (Termination error)
         0002 : EMM version less than 4.0. (Termination error)


      Function  08          ;Save page map
        Function 8 and 9 are tested in the same routine. Refer to function
        9 for error codes.


      Function  09          ;Restore page map
        Functions 8 and 9 are tested in the same routine. The page frame
        is initialized. Function 8 is called to save the mapping context.
        Different pages are mapped into the page frame. Function 9 is called
        to restore the original context. The pages are read to confirm the
        restoration.
        Possible error codes:
         0800 : Function 8 return code not zero.
         0801 : Function 9 return code not zero.
         0802 : Restored physical page 0 does not match expected data
         0803 : Restored physical page 1 does not match expected data
         0804 : Restored physical page 2 does not match expected data
         0805 : Restored physical page 3 does not match expected data


      Function  10          ;reserved
        Function 10 is not tested.


      Function  11          ;reserved
        Function 11 is not tested.


      Function  12          ;Get handle count
        Function 12 is called to get determine the number of unallocated
        handles in the system. The number of handles are checked
        to assure that there are enough free handles to complete
        the tests.
        The function is tested after the handles for the test
        have been allocated. The returned value is compared to
        the original value plus the number of handles requested
         by the test program.
        Possible error codes:
         0005 : Return code not zero. (Termination error)
         0006 : Not enough free handles to complete test (Termination
                  error.)
        1200 : Return code not zero on test.
        1201 : The handle count did not match expected number.


      Function  13          ;Get handle pages
        Function 13 is called to get the number of pages allocated to
        handle index 1 and handle index 2. The number of pages is compared
        to what is expected. (handle index 0 should have 8 pages allocated,
        handle index 1 should have 1 page allocated.
        Possible error codes:
         1300 : Function 13 return code not zero on call for
                  handle index 0.
         1301 : Number of pages returned does not match expected
                  number of pages for handle index 0.
         1302 : Function 13 return code not zero on call for
                  handle index 1.
         1303 : Number of pages returned does not match expected
                  number of pages for handle index 1.


      Function  14          ;Get all handle pages
        Function 14 is called the handle page array. The total number
        of open handles is compared to a maximum of 64. The 64 handle
        limit is due to the space allocated to the data area for the
        function 14 test. The total handles returned is compared to
        the expected number. The array is then searched for the handles
        allocated by the test. Each handle is searched for in the array,
        and the resulting page allocation is compared to what is expected.
        Possible error codes:
         1400 : Function 14 return code not zero.
         1401 : Number of open handles does not match expected.
         1402 : Handle index 0 page allocation does not match
                  expected value.
         1403 : Handle index 1 - 8 page allocations do not match
                  expected values.


      Function  15          ;Page map functions
        Function 15.3 is called to get the size of the save area needed.
        If the size is larger than 128 bytes the test is ended. The page
        frame is initialized by mapping pages to physical pages 0 through
        3. Function 15.0 Get page map is called. The page frame context
        is changed by mapping different pages into the frame. The new
        context is saved using a different save area. The page map is
        restored using function 15.1. The page frame data is checked to
        see if it matches the original context. Function 15.2, Get and
        Set page map is called. The page frame context is then tested
        for the restoration of the second mapping context. Function 15.1
        Set page map is called again using the saved context from the
        Get and Set function. The page map is checked to see if the
        original context is restored.
        Possible error codes:
         1500 : Function 15.3 return code not zero.
         1501 : Size of save array larger than 128 bytes.
         1502 : Function 15.0 return code not zero on first call.
         1503 : Function 15.0 return code not zero on second call.
         1504 : Function 15.1 return code not zero on first call.
         1505 : Set page 0 does not match expected data
         1506 : Set page 1 does not match expected data
         1507 : Set page 2 does not match expected data
         1508 : Set page 3 does not match expected data
         1509 : Function 15.2 return code not zero.
         1510 : Get and Set page 0 does not match expected data
         1511 : Get and Set page 1 does not match expected data
         1512 : Get and Set page 2 does not match expected data
         1513 : Get and Set page 3 does not match expected data
         1514 : Function 15.1 return code not zero on second call.
         1515 : Set page 0 does not match expected data
         1516 : Set page 1 does not match expected data
         1517 : Set page 2 does not match expected data
         1518 : Set page 3 does not match expected data


      Function  16          ;Partial page map functions
        Function 16.2 is called to get the size of the save area needed.
        If the size is larger than 128 bytes the test is ended. The page
        frame is initialized by mapping pages to physical pages 0 through
        3. The mapping structure is initialized using page frame segment.
        Function 16.0 Get partial page map is called to save mapping of
        physical pages 0 and 2. The page frame context is changed
        by mapping different pages into the frame. The original context
        is restored for pages 0 and 2 using function 16.1. The resulting
        context is checked to see if the result is a combination of the
        original context and of the modified context.
        Possible error codes:
         1600 : Function 16.2 return code not zero.
         1601 : Size of save array larger than 128 bytes.
         1602 : Function 16.0 return code not zero.
         1603 : Function 16.1 return code not zero.
         1604 : Restored page 0 does not match expected data
         1605 : Unchanged page 1 does not match expected data
         1606 : Restored page 2 does not match expected data
         1607 : Unchanged page 3 does not match expected data


      Function  17          ;Map/unmap multiple handle pages
        Function 17.0 is called to map the full four pages of the page
        frame. The mapping is checked to confirm it matches what is in
        the mapping structure. Segment addresses for the page frame
        physical pages are written into a second mapping structure.
        Function 16.1 is called to map the new pages into the page frame.
        The mapping is checked to see if it matches what is in the
        second mapping structure.
        Possible error codes:
         1700 : Function 17.0 return code not zero.
         1701 : Mapped page 0 does not match expected data
         1702 : Mapped page 1 does not match expected data
         1703 : Mapped page 2 does not match expected data
         1704 : Mapped page 3 does not match expected data
         1705 : Function 17.1 return code not zero.
         1706 : Mapped page 0 does not match expected data
         1707 : Mapped page 1 does not match expected data
         1708 : Mapped page 2 does not match expected data
         1709 : Mapped page 3 does not match expected data


      Function  18          ;Reallocate pages
        Function 18 is called to increase handle index 0 allocated
        pages from 8 to 10. The pages are initialized, then mapped
        to the page frame. The data for these new pages is checked.
        Function 13 is called to confirm that handle index 0 has
        10 pages allocated. Function 18 is called again to reduce
        the allocated pages for handle index 0 back to 8. An attempt
        to map pages 9 and 10 is made to confirm that the pages no
        longer exist.
        Possible error codes:
         1800 : Function 18 return code not zero on first call.
         1801 : New logical page 9 cannot be mapped and initialized.
         1802 : New logical page 10 cannot be mapped and initialized.
         1803 : New logical page 9 cannot be mapped to be read.
         1804 : New logical page 10 cannot be mapped to be read.
         1805 : Logical page 9 does not match expected data.
         1806 : Logical page 10 does not match expected data.
         1807 : Function 13 return code not zero.
         1808 : Number of pages for handle index 0 not correct.
         1809 : Function 18 return code not zero on second call.
         1810 : Accessing illegal page 9 does not cause illegal
                  page error.


      Function  19          ;Handle attribute
        Function 19.2 is called to see if nonvolatile handles are
        supported.
        if nonvolatile handles are not supported, function 19.0 get
        handle attribute is called to confirm that the function call
        causes a nonsupported return code. Function 19.1 is called
        to confirm that the function call returns a nonsupported
        return code.
        If nonvolatile handles are supported, function 19.0 get
        handle attribute is called. The returned attribute is tested
        to to see if valid type. Function 19.1 is called to set the
        attribute to volatile. Function 19.0 is called to confirm that
        the handle attribute is now volatile. Function 19.1 is called to
        set the attribute to nonvolatile. Function 19.0 is called to
        confirm that the attribute is now nonvolatile. Function 19.1
        is called with the illegal attribute value of 2 to confirm
        the return of an illegal attribute return code.
        Regardless of if volatile handles are supported or not, a message
        is printed to the screen indicating the driver support for this
        function.
        The test does not confirm that nonvolatile handles actually
        are nonvolatile.
        Possible error codes:
         1900 : Function 19.2 return code not zero.
         1901 : No unsupported return code for unsupported
                  function 19.0.
         1902 : No unsupported return code for unsupported
                  function 19.1.
         1903 : Function 19.0 return code not zero on first call.
         1904 : Illegal value for attribute for supported function.
         1905 : Function 19.1 return code not zero on first call.
         1906 : Function 19.0 return code not zero on second call.
         1907 : Supported attribute could not be set to 0.
         1908 : Function 19.1 return code not zero on second call.
         1909 : Function 19.0 return code not zero on third call.
         1910 : Supported attribute could not be set to 1.
         1911 : Illegal attribute return code not returned for
                  an attempted set to an illegal attribute.


      Function  20          ;Handle name
        Function 20.0 is called to see if a non-null handle name
        is set for a handle that has not has a name assigned. Function
        20.1 is called to assign a handle name. Function 20.0 is called
        to confirm the handle name just set. Function 6 is called to
        deallocate named handle. Function 4 is called to reallocate
        a handle to replace the handle. The new handle page is reinitialized.
        Function 20.0 is called to confirm that the new handle does not
        have a name assigned.
        Possible error codes:
         2000 : Function 20.0 return code not zero for first call.
         2001 : A non-null name is assigned to a new handle.
         2002 : Function 20.1 return code not zero for first call.
         2003 : Function 20.0 return code not zero for second call.
         2004 : Retrieved handle name does not match set handle name.
         2005 : Function 6 return code not zero.
         2006 : Function 4 return code not zero.
         2007 : Initialization of new handle page failed.
         2008 : Function 20.0 return code not zero on third call.
         2009 : Non_null name assigned to new handle.


      Function  21          ;Handle directory
        Function 21.2 is called to get the total number of handles
        supported by the driver. This number is checked to see if
        a minimum of 64 and a maximum of 255 handles are supported. Handle
        names for 2 handles are set using function 20.1. Function 21.0
        is called to get the handle directory. The returned directory is
        scanned to check for the two handle names just assigned. Function
        21.1 is called to search for the handle name of one of the handles
        just assigned a name. Function 21.1 is called again to search for
        a handle not in the directory. Function 21.1 is called for a third
        time to search for a handle with a null name.
        Possible error codes:
         2100 : Function 21.2 return code not zero.
         2101 : Less than 64 handles supported by driver
         2102 : More than 255 handles supported by driver.
         2103 : Number of open handles is not what is expected.
         2104 : Function 20.1 return code not zero for first call.
         2105 : Function 20.1 return code not zero for second call.
         2106 : Function 21.0 return code not zero.
         2107 : Active handle not found in handle directory.
         2108 : Handle name not correct for handle in directory.
         2109 : Function 21.1 return code not zero for first call.
         2110 : Search for handle name function returned wrong handle.
         2111 : Return code not 'not found' for search of a nonexistent
                  handle name.
         2112 : Return code not 'Null handle name' for search of a
                  null handle name.


      Function  22          ;Alter page map and jump
        The page frame is initialized. The function 22 data structure
        is initialized. The state of the stack pointer and the flags register
        is saved.  Function 22.0, Alter page map and jump is called.
        The state of the stack pointer and the flags register is compared
        to their states before the jump. The state of the page frame is
        compared to the expected mapping configuration.
        Possible error codes:
         2200 : Function 22.0 jump not taken.
         2201 : Function 22.0 return code not zero.
         2202 : Stack pointer corrupted across jump
         2203 : Flags register corrupted across jump
         2304 : Mapped page 0 does not match expected data
         2305 : Mapped page 1 does not match expected data
         2306 : Mapped page 2 does not match expected data
         2307 : Mapped page 3 does not match expected data


      Function  23          ;Alter page map and call
        The page frame is initialized. The function 23 data structure
        is initialized. The state of the stack pointer and the flags register
        is saved.  Function 23.0, Alter page map and call is called.
        In the called routine, a flag is set to indicate the routine
        has been called. The state of the page frame is checked.
        The state of the the flags register is saved. The called
        routine calls the EMS driver for the version number and returns
        using a far return. On return to the calling procedure,
        the state of the stack pointer is compared to its state before
        the call. The save states of the flags register are comared. The
        state of the page frame is compared to the expected mapping
        configuration.
        Possible error codes:
         2300 : Mapped page 0 does not match expected data for subroutine.
         2301 : Mapped page 1 does not match expected data for subroutine.
         2302 : Mapped page 2 does not match expected data for subroutine.
         2303 : Mapped page 3 does not match expected data for subroutine.
         2304 : Function 7 Get version failed when called from subroutine.
         2305 : Function 23.0 return code not zero.
         2306 : Subroutine not called by EMS driver.
         2307 : Stack pointer corrupted across call
         2308 : Flags register corrupted across call
         2309 : Original page 0 not restored on return from subroutine.
         2310 : Original page 1 not restored on return from subroutine.
         2311 : Original page 2 not restored on return from subroutine.
         2312 : Original page 3 not restored on return from subroutine.


      Function  24          ;move/exchange memory region
        The page frame is initialized. The function 24 data structure
        is initialized. Function 24.0 Move memory is called. The move
        is from expanded memory to conventional memory. The data
        read from the expanded memory is compared to twhat is expected.
        The page frame is checked to verify that the mapping context
        did not change during the move.
        Possible error codes:
         2400 : Function 24.0 return code not zero.
         2401 : First half of data moved from Expanded memory not accurate.
         2402 : Second half of data moved from Expanded memory not accurate.
         2403 : Original page 0 corrupted by move.
         2404 : Original page 1 corrupted by move.
         2405 : Original page 2 corrupted by move.
         2406 : Original page 3 corrupted by move.


      Function  25          ;Get mappable physical addr array
        Function 25.1 is called to get the size of the physical address
        page array. If the array is larger than 128 bytes the test is
        terminated. Functoin 25.0 is called to copy the page array into
        a data buffer. The number of entries retruned by functon 25.0
        is compared to the number returned in 25.1.
        Possible error codes:
         2500 : Function 25.1 return code not zero.
         2501 : Data from the physical page map will not fit in the
                test program buffer.
         2502 : Function 25.0 return code not zero.
         2502 : The number of pages returned by 25.1 is different than
                the number returned by 25.0.


      Function  26          ;Hardware configuration
        Function 26.0 is called to get the hardware configuration
        information. Function 26.1 is called to get the raw page
        count. The data is formatted so it can be printed, but the
        test progam print statement is disabled.
        Possible error codes:
         2600 : Function 26.0 return code not zero.
         2601 : Function 26.1 return code not zero.


      Function  27          ;Allocate standard pages
        Function 27.0 allocate standard pages with a requested
        page count of zero. Function 13 is called to confirm that
        no pages are allocated to the new handle. Function 6 is
        called to deallocate the new handle. Function 27.1 is
        called to allocate a handle with one raw page. Function 5
        is called to map the page to the page frame. Function 6
        is called to deallocate the page.
        Possible error codes:
         2700 : Function 27.0 return code not zero.
         2701 : Function 13.0 return code not zero.
         2702 : Handle count returned not equal to zero.
         2703 : Function 6 return code not zero.
         2704 : Function 27.1 return code not zero.
         2705 : Map of raw page failed, Function 5 return code not zero.
         2706 : Map of page to replace raw page failed, Function 5 return
                        code not zero.
         2707 : Deallocate of raw page failed, Function 6 return code not zero.


      Function  28          ;Alternate map register set
        The page frame is initialized. Function 28.2 is called to
        get the size of the save array. If the array is too large the
        test is terminated. Function 28.3 is called to allocate an
        alternate register set. If hardware register sets are not
        supported, the software emulation functon is tested. The
        page map is changed. Function 28.0 is called to get the
        current register set. Function 28.1 is called to invoke the
        alternate register set reserved earlier. The page map
        is checked. Functoin 28.1 is called to restore th orginal
        map register set. Function 28.4 is called to deallocate the
        alternate register set. The page frame is checked.
        For simulated register sets, Function 15.0 is called to
        initialize the save area. The page map is changed. Function
        28.1 is called to restore the page map. The page map is
        checked. The page map is modified. Function 28.0 is called
        to save the page map. The page map is modified. Function 28.1
        is called to restore the page map. The page map is checked.
        Possible error codes:
         2800 : Function 28.2 return code not zero.
         2801 : Save array size too large.
         2802 : Function 28.3 return code not zero.
         2803 : Function 28.0 return code not zero.
         2804 : Function 28.1 return code not zero.
         2805 : Original page 0 not restored by alt register map.
         2806 : Original page 1 not restored by alt register map.
         2807 : Original page 2 not restored by alt register map.
         2808 : Original page 3 not restored by alt register map.
         2809 : Restore of original reg set fail, Function 28.1
                        return code not zero.
         2810 : Function 28.4 return code not zero.
         2811 : Page 0 not restored by orginal register map.
         2812 : Page 1 not restored by orginal register map.
         2813 : Page 2 not restored by orginal register map.
         2814 : Page 3 not restored by orginal register map.
         2819 : Function 15.0 return code not zero.
         2820 : Function 28.1 return code not zero.
         2821 : Original page 0 not restored by alt register map.
         2822 : Original page 1 not restored by alt register map.
         2823 : Original page 2 not restored by alt register map.
         2824 : Original page 3 not restored by alt register map.
         2825 : Function 28.0 return code not zero.
         2826 : Function 28.1 return code not zero.
         2827 : Page 0 not restored by orginal register map.
         2828 : Page 1 not restored by orginal register map.
         2829 : Page 2 not restored by orginal register map.
         2830 : Page 3 not restored by orginal register map.


      Function  29          ;Warmboot preparation
        Function 29 is not tested.


      Function  30          ;OS/E functions
        Function 30.0 is called to get the OS/E password. Function
        30.0 is called again with a bad password. Function 30.1 is
        called to disable the OS/E function set. Function 26.2 is
        called to see if a disabled function can be accessed.
        Function 30.0 is called to enable the OS/E function set.
        Function 26.2 is called to access an OS/E function. Function
        30.2 is called with a bad password to return the password.
        Function 30.2 is called again with the correct password.
        Possible error codes:
         3000 : Function 30.0 return code not zero.
         3001 : Bad password return code not returned when Function 30.0
                        called with a bad password.
         3002 : Function 30.1 return code not zero.
         3003 : Function 26.2 did not return access denied return code
                        when disabled.
         3004 : Function 30.0 return code not zero.
         3005 : Function 26.2 return code not zero.
         3006 : Function 30.2 did not return bad password return code.
         3007 : Function 30.2 return code not zero.