The NEC V20 and V30 --- Replacements	for the	8088 and 8086



	Over  the  past	 few  years,   Intel  has  dominated  the  16-bit
	microprocessor	market	with a device that has become one of  the
	most popular microprocessors of	all time,  the 8086 family, which
	includes  the 8088/86/188/186/286 and the soon-to-come	80386,	a
	mythical beast which IBM seems to be considering as the	heart  of
	their  next  PC.  The 286 and 386 microprocessors are awesome  on
	their  own,  but it is just because of all that	 available  power
	that   many   hardware	and  software  manufacturers  are   still
	attempting  to	squeeze	 every	available  ounce  of  speed   and
	throughput  out	 of 8088/86 devices.  Too many people just  don't
	know  exactly  how  much  the  80286  can  do,	 and,  much  more
	importantly,  how to get the device to do it.  In so many  words,
	people	are  intimidated by these new and powerful  devices,  and
	they  have decided to wait in the wings	until someone figures  it
	all  out  and  decides to share	it with	 us.  In  the  meanwhile,
	software developers continue to	attempt	to squeeze their  devices
	for every clock	cycle they can get out of it.

	Picture	 this  scenario.  You are developing an	 interrupt-driven
	system for,  say,  a military avionics application, using a high-
	level  language	which until now	has been ideally suited	 for  the
	application,  PL/M-86.	The device is a	real-time terrain mapping
	system,	and the	update and refresh timing specifications are very
	tight,	20 milliseconds	per frame or so.  You have worked for the
	last  eight to ten months on developing	the code for this system,
	refining  it and optimizing it,	 and inserting assembly	 language
	code  in  key places to	give it	that extra "oomph"  to	meet  the
	timing	specifications.	 You process the code,	load it	into  the
	system,	 and begin checking your numbers to see	if those last few
	edits  did the job.  As	you make your calculations and pound that
	belligerent logic analyzer, it soon begins to dawn on you that no
	matter what you	do, you	just can't get the code	to fit the window
	between	 the  time your	first screen refresh data  comes  in  for
	processing,  and  the time three more sets of data are queued and
	waiting	 in the	wings.	The processor just can't handle	 the  job
	fast enough, and you're	not even working on worst-case situations
	yet. Now what...

	If  the	CPU in question	is either an 8088  or  8086,  relax,  our
	friends	 from  across the Pacific have come to	your  rescue.  It
	seems that someone in Japan actually though about the phrase "New
	and Improved",	so often found in our home TV sets,  and came  up
	with   a   new	and  improved  version	of  the	 8088  and   8086
	microprocessors. How new and improved, you may ask? How	does 100%
	throughput performance improvement sound?  Good? Well, that's not
	always the case,  but users of these new devices,  designated the
	V20 and	V30,  have reported such impressive numbers.  Too good to
	be true,  you say?  Lean back in your chair, and listen	to what	I
	have to	say here. If you are using the Intel devices now, it will
	be  a fresh of breath air for you,  but	if  you	 aren't,  proceed
	anyway,	 it's  fun reading,  and you just might	switch after  you
	finish it.

	The  company  is  NEC,	and the	name of	the game is  to	 make  it
	faster,	 better, and less power-hungry,	but still compatible with
	the old	ones.  (Sounds familiar, doesn't it...)	From the looks of
	it, it seems NEC has achieved just that	with their two new 16-bit
	microprocessors,  the 70108D and 70116D,  better known as the V20
	and  the V30.  These two devices are direct working  replacements
	for the	8088 and 8086,	respectively, and are available	in both	5
	and 8mhz speeds, but what NEC has come out with	is much	more than
	just  another  replacement  or	clone.	These  devices	are  high
	performance,  enhanced microprocessors that offer a lot	more than
	just  compatibility.  In  this	article,  we will  explore  these
	improvements and enhancements, and what	the implications of these
	are to those of	us still using the 8088, 8086, 80188 and 80186.

	First of all, the most obvious enhancement is the technology used
	to  actually make the device.  The V20 and the V30 both	are  CMOS
	devices,  which	 directly  translates to lower power  consumption
	(300mw active) and less	heat to	dissipate inside your system.  If
	you  have  ever	 opened	up your	 16-bit	 personal  computer,  you
	may  have noticed that the 8088	and 8086 both generate a  lot  of
	heat  and are very hot to the touch (if	you touch them soon after
	running	them for a while...). These new	devices	run significantly
	cooler,	 and since they	consume	less power, reduce the demands on
	your power supply.  Both of these chips	have standby modes  also.
	You  can  set the device into the standby mode,	 while	retaining
	interrupt service capability,  and during the period of	time  the
	device	is  in standby mode it will consume a tenth of the  power
	required  in full active mode.	This feature comes very	handy  in
	laptop	and portable computers,	 where power is	a  very	 precious
	commodity.

	Let's look a little deeper into	the processor design and see what
	new and	exciting things	we find.

	The  most obvious change that stands out upon an initial scan  of
	the  technical	specifications	is  that there	seem  to  be  new
	registers and different	names for the old ones.	 Here's	what they
	are:



	Mnemonic  Description			     8088/86 Equivalent
	--------  ---------------------------------- --------------------
	AW	  Accumulator (16-bit)		     AX
	AH	  High byte of AW		     AH
	AL	  Low byte of AW		     AL
	BW	  General register (16-bit)	     BX
	BH	  High byte of BW		     BH
	BL	  Low byte of BW		     BL
	CW	  General Register (16-bit)	     CX
	CH	  High byte of CW		     CH
	CL	  Low byte of CW		     CL
	DW	  General Register (16-bit)	     DX
	DH	  High Byte of DW		     DH
	DL	  Low byte of DW		     DL
	PC	  Program counter		     IP
	PS	  Program Segment register	     CS
	SS	  Stack	Segment	register	     SS
	DS0	  Data Segment 0		     DS
	DS1	  Data Segment 1		     ES
	PFP	  Pre-Fetch Pointer		     No	equivalent
	SP	  Stack	pointer			     SP
	BP	  Base Pointer			     BP
	IX	  Index	register (source)	     SI
	IY	  Index	register (destination)	     DI
	TA	  Temporary register A (internal)    No	equivalent
	TB	  Temporary register B (internal)    No	equivalent
	TC	  Temporary register C (internal)    No	equivalent
	PSW	  Program status word		     Flag Register

	The program status word	is further subdivided into the	following
	bit field definitions:

	Bit	  Description			     8088/86 Equivalent
	--------- ---------------------------------- ------------------
	0  : CY	  Status  flag - Carry		     CF
	1  : --	  reserved - pushed onto stack as 1  reserved
	2  : P	  Status  flag - Parity		     PF
	3  : --	  reserved - pushed onto stack as 0  reserved
	4  : AC	  Status  flag - Auxiliary Carry     AUX
	5  : --	  reserved - pushed onto stack as 0  reserved
	6  : Z	  Status  flag - Zero		     ZF
	7  : S	  Status  flag - Sign		     SF
	8  : BRK  Control flag - Break		     TF
	9  : IE	  Control flag - Interrupt Enable    IF
	10 : DIR  Control flag - Direction	     DF
	11 : V	  Status  flag - Overflow	     OF
	12 : --	  reserved - pushed onto stack as 1  reserved
	13 : --	  reserved - pushed onto stack as 1  reserved
	14 : --	  reserved - pushed onto stack as 1  reserved
	15 : MD	  Control flag - Mode		     no	equivalent/rsrvd



	The  last  flag	 has no	equivalent in  the  8088/86,  because  it
	controls a function that does not exist	in those microprocessors,
	8080 emulation mode.  Yes,  you	did read that correctly.  More on
	that later...

	The  first design change item that stands out is a dual	 internal
	bus,  versus a single internal bus on the 8088 and 8086. Now that
	integration  density  of  a  much higher order	of  magnitude  is
	possible,  it is relatively inexpensive	to integrate this feature
	into  the device,  which is exactly what NEC has  done.	 Internal
	data  transmission within the device is	now executed in	parallel,
	with both source and destination data traversing at the	same time
	on  the	 full  16-bit wide busses.  This decreases  the	 time  to
	execute	single instructions of any type.

	The  8088  and	8086  calculate	effective addresses  by	 using	a
	combination  of	 hardware and  microcode,  essentially	a  little
	program	 within	the device.  This process normally takes anywhere
	between	5 and 12 clock cycles.	NEC has	enhanced this part of the
	microprocessor,	replacing the microcode	with a dedicated hardware
	section	which will perform effective address calculations of  any
	type  in 2 clock cycles,  no more and no less.	Depending on  the
	operation, this	increases throughput in	this area from 150 to 600
	percent.

	A completely new item added to the design is a Pre Fetch Pointer,
	which works in conjunction with	the instruction	pointer.  The PFP
	always	points to the next instruction to be executed,	no matter
	how  close or far it may be from the  instruction  pointer.  This
	feature	 enhances  program  execution by allowing the  device  to
	always	have  the  next	 instruction  ready,  reducing	the  time
	required to execute jumps, calls, returns, etc.

	Three  new  16-bit  temporary registers	have been  added  to  the
	device,	 used strictly for multiplication,  division,  shift  and
	rotation  operation.  These  registers are NOT accessible by  the
	programmer  or the application,	 they are for internal use  only.
	The significance of this is not	fully realized until you actually
	perform	 some benchmarks,  and particularly when your  benchmarks
	are  obtained  using math-intensive software.  I personally  have
	performed  and witnessed some timing benchmarks	on the	V30  that
	were  absolutely  impressive.	Throughput  improvements  on  our
	benchmarks,  consisting	 of  math-intensive software  written  in
	PL/M-86,  ranged between 66 and	82% increases.	Considering  that
	the  only difference in	the tests were the replacement of the CPU
	in  the	system,	 from an 8086 to a V30,	 we were quite	impressed
	with  its  performance.	 In addition to	the temporary  registers,
	there  is a Loop Counter,  which is used to count the  number  of
	loops  for a primitive block transfer instruction and the  number
	of   shifts   that   will  be  performed  for  a   multiple   bit
	shift/rotation instruction.  This counter works	very closely with
	the  three  temporary registers,  and is a major  factor  in  the
	improvement of processing speed.

	The  V20 and V30 both implement	an impressive 101 instruction set
	which includes the 8088,  8086,	 80188 and 80186 instruction sets.
	In  addition,  it  also	contains some new instructions	which  by
	themselves  provide  tremendous	 power and  flexibility	 for  the
	programmer.  There's one more instruction set available, but I'll
	leave that for a little	later.	Watch for it. First of all, let's
	look  at the enhanced instructions that	are available on the  V20
	and V30.

	Enhanced stack operation instructions
	-------------------------------------

	PUSH imm
	--------
	Allows immediate data to be pushed onto	the stack

	PUSH R
	POP  R
	------
	These  two instructions	allow the programmer to	push the contents
	of the 8 general registers (yes, all of	them!) onto the	stack.

	Enhanced multiplication	instructions
	------------------------------------

	MUL reg16,imm16
	MUL mem16,imm16
	---------------
	These  instructions  allow the contents	of a register  or  memory
	location to be 16-bit multiplied by immediate data.

	Enhanced Shift and Rotate instructions
	--------------------------------------

	SHL reg,imm8
	SHR reg,imm8
	SHRA reg,imm8
	-------------
	These instructions allow the contents of a register to be shifted
	by the number of bits specified	in the immediate data operand.

	ROL reg,imm8
	ROR reg,imm8
	ROLC reg,imm8
	RORC reg,imm8
	-------------
	Allow  for the same type of operation as above,	 except	 rotation
	instead	of shifting.

	Check Array Boundary instruction
	--------------------------------

	CHKIND reg16,mem32
	------------------
	This  instruction is used to verify that index values pointing to
	the  elements of an array data structure are within  the  defined
	range.	The lower limit	of the array should be in memory location
	mem32,	the upper limit	in mem32 + 2. If the index value in reg16
	is not between these limits when CHKIND	is executed, a BRK 5 will
	occur.	This causes a jump to the location in interrupt	vector 5.
	This  instruction,  needless  to say,  is extremely powerful  and
	could be a big time saver for programmers, but it will definitely
	pose a problem for PC and compatible users, since their	interrupt
	5  executes  a	"print screen" routine.	 This  problem	was  also
	evident	in the 80286 and the AT.

	Block I/O instructions
	----------------------

	OUTM DW,src_block
	INM  dst_block,DW
	-----------------
	These  instructions  are used to input or output a string  to  or
	from  memory,  when preceded by	a repeat  prefix.  Very	 powerful
	stuff.

	Stack Frame instructions
	------------------------

	PREPARE	imm16,imm8
	------------------
	This instruction is used to generate the stack frames required by
	block-structured  languages,  such as PASCAL and Ada.  The  stack
	frame  consists	of two areas.  One area	has a pointer that points
	to  another frame which	has variables that the current frame  can
	access.	 The  other  is	 a local variable area	for  the  current
	procedure.

	DISPOSE
	-------
	This  instruction releases one from among the stack  frames  that
	have  been generated by	the PREPARE instruction.  It returns  the
	stack and base pointers	to the values they had before the prepare
	instruction  was  used	to call	a procedure.  Both this	 and  the
	PREPARE	 instruction  are  very	useful	to  compiler  developers,
	saving quite a bit of time from	having to code these functions.

	The V20	and V30	also have a set	of unique instructions which  are
	not  available on the 8088 and 8086.  These instructions are very
	powerful  and  useful in many  applications.  Support  for  these
	instructions  is  available in the form	of several compilers  and
	development tools available for	a variety of machines,	from  the
	IBM-PC to the DEC VAX line of mainframes.

	V20 - V30 Unique instructions
	-----------------------------

	Variable Length	Bit Field operation instructions
	------------------------------------------------

	This  category has two instructions,  INS (Insert bit field)  and
	EXT (Extract Bit Field).  These	instructions are highly	effective
	for computer graphics and high-level language applications.  They
	can,  for  example,  be	used for data structures such  as  packed
	arrays	and  record type data used in  PASCAL.	CAD/CAM	 software
	should	be  able  to benefit immensely from  these  instructions,
	which could quite easily reduce	code size by anywhere from 10  to
	30% and	increase performance tremendously.

	INS reg8,reg8
	INS reg8,imm4
	-------------
	These  instruction transfer low	bits from the 16-bit AW	 register
	(the  number  of bits is specified by the second operand) to  the
	memory location	specified by the segment base (DS register)  plus
	the  byte offset (IY) register.	 The starting bit position within
	this  byte  is specified as an offset by the lower 4-bits of  the
	first operand. After each complete data	transfer, the IY register
	and  the  register  specified by the lower 4 bits  of  the  first
	operand	 are  automatically updated to point to	 the  next  index
	field.	Either	immediate data or register may specify the number
	of  bits  transferred  (second	operand).   Because  the  maximum
	transferable bit length	is 16-bits,  only the lower 4 bits of the
	specified register (00H	to FFH)	will be	valid. Bit field data may
	overlap	the byte boundary of memory.

	EXT reg8,reg8
	EXT reg8,imm4
	-------------
	These  instructions  load to the AW register the bit  field  data
	whose  bit field length	is specified by	the second operand of the
	instruction from the memory location that is specified by the DS0
	segment	 register  (segment base),  the	IX index  register  (byte
	offset),  and the lower	4 bits of the first operand (bit offset).
	After the transfer is complete,	 the IX	register and the register
	specified  by  the  lower  4  bits  of	the  first  operand   are
	automatically  updated	to point to the	next  bit  field.  Either
	immediate  data	 or  a register	maybe specified	 for  the  second
	operand.  Because the maximum transferable bit length is 16 bits,
	however,  only	the lower 4 bits of the	specified register (0H to
	0FH) will be valid.  Bit field data may	overlap	the byte boundary
	of memory.

	Packed BCD Operation instructions
	---------------------------------

	These instructions provide the programmer with valuable	tools  to
	handle	packed binary-coded-decimal (BCD) operations  within  the
	application  being  developed.	The  BCD format	is most	 used  in
	business applications,	where numeric precision	is a requirement.
	The instructions described here	process	packed BCD data	either as
	strings	 (ADD4S,  SUB4S,  CPM4S) or byte-format	 operands  (ROR4,
	ROL4).	Note  that to perform string processing	for the	 rotation
	instructions,  the  programmer	must use the  macro  instructions
	ROR4S  and  ROL4S,  available with NEC's language  and	assembler
	support	software.

	ADD4S
	-----
	This  instruction adds the packed BCD string addressed by the  IX
	index register to the packed BCD string	addressed by the IY index
	register, and stores the result	in the string addressed	by the IY
	register.  The	length	of the string (number of BCD  digits)  is
	specified  by  the CL register,	 and the result	of the	operation
	will affect the	overflow flag (V),  the	carry flag (CY),  and the
	zero flag (Z).

	SUB4S
	-----
	This instruction subtracts the packed BCD string addressed by the
	IX  index register from	the packed BCD string addressed	by the IY
	register, and stores the result	in the string addressed	by the IY
	register.  The	length	of the string (number of BCD  digits)  is
	specified  by the Cl register,	and the	result of  the	operation
	will  affect the overflow flag (V),  the carry flag (CY) and  the
	zero flag.

	CPM4S
	-----
	This  instruction  performs the	same operation as  SUB4S,  except
	that  the result is not	stored,	 and only the overflow flag  (V),
	carry flag (CY)	and zero flag (Z) are affected.

	ROL4
	----
	This  instruction  treats  byte	data of	the  register  or  memory
	directly  specified by the instruction byte as BCD data	and  uses
	the  lower 4 bits of the AL register to	rotate that data one  BCD
	digit to the left.

	ROR4
	----
	This  instruction  works exactly like the ROL4,	 except	 the  end
	result is a shift of one BCD digit to the left.

	Bit Manipulation Instructions
	-----------------------------

	This  instructions  allow the programmer to  manipulate	 distinct
	bits within registers or memory	locations,  instead of having  to
	use  masks,  AND's,  OR's,  etc.  They are very	useful in bit-map
	graphics-oriented  and other similar applications.  Use	of  these
	instructions should decrease code size considerably.

	TEST1
	-----
	This  instruction  tests a specific bit	in a register  or  memory
	location.  If the bit is 1,  the Z flag	is reset to 0. If the bit
	is 0, the Z flag is set	to 1.

	NOT1
	----
	This  instruction inverts a specific bit in a register or  memory
	location.

	CLR1
	----
	This  instruction clears a specific bit	in a register  or  memory
	location.

	SET1
	----
	This  instruction  sets	 a specific bit	in a register  or  memory
	location.

	Repeat Prefix Instructions
	--------------------------

	These  instructions  allow for high speed block	 primitive  block
	transfers  to  be executed repeatedly based on the  status  of	a
	single flag, the CY flag.

	REPC
	----
	This   instructions  causes  the  microprocessor  to  repeat  the
	following primitive block transfer instruction until the CY  flag
	becomes	cleared.

	REPNC
	-----
	This   instruction  causes  the	 microprocessor	 to  repeat   the
	following  primitive block transfer instruction	until the CY flag
	becomes	set.

	Floating Point Operation Instructions
	-------------------------------------

	FPO1 fp-op,mem
	FPO2 fp-op,mem (new)
	--------------------
	These  instructions  are  used for the	external  floating  point
	processor. The floating	point operation	is passed to the floating
	point  processor when the CPU fetches one of these  instructions.
	From  this  point the CPU performs only	the  necessary	auxiliary
	processing (effective address calculation, generation of physical
	addresses, and start-up	of memory read cycle). The floating point
	processor  always  monitors the	instructions fetched by	the  CPU.
	When  it interprets one	as an instruction to itself  it	 performs
	the  appropriate  processing.  At this time,  the floating  point
	processor chip uses either the address alone or	both the  address
	and read data of the memory read cycle executed	by the CPU.  This
	difference   in	  the  data  used  depends  on	which  of   these
	instructions is	executed.

	Standby	Function
	---------------

	The  V20  and  V30  both  have a standby  mode	to  reduce  power
	consumption during wait	states,	 a mode	which comes in very handy
	when  designing	systems	that run on batteries or some other  type
	of limited power source. This mode is set by the HALT instruction
	in both	the native and emulation mode.	In the standby mode,  the
	internal  clock	 is supplied only to those  circuits  related  to
	functions  required  to	 release this mode and bus  hold  control
	functions.  As	a result,  power consumption can be  reduced   to
	1/10th the level of normal operational requirements in either the
	native	or  emulation  modes.  The standby mode	 is  released  by
	inputting  a RESET signal,  or an external interrupt (NMI,  INT).
	The bus	hold function is effective during standby mode.	 The  CPU
	returns	to standby mode	when the bus hold request is removed.

	Mode Operation Instruction
	--------------------------

	At  the	beginning of this article I made a few references to  the
	mode  flag,  an	emulation mode,	 and a few other items related to
	this subject.  All these references are	related	to a mode of this
	microprocessor which none of the Intel processors have.	 The  V20
	and   V30   are	 capable  of  fully  emulating	the  8080   8-bit
	microprocessor,	 including  its	full instruction set.  There  are
	four instructions directly related to this emulation mode.

	BRKEM imm8
	----------
	This  is the basic instruction used to start the  8080	emulation
	mode.  This  instruction  operates  exactly the	same as	 the  BRK
	instruction,  except  that BRKEM resets	the mode flag (MD) to  0.
	The PSW,  PS and PC registers are saved	onto the stack,	and MD is
	then reset and the interrupt vector specified by the operand imm8
	of this	command	is loaded into PS and PC.  The instruction  codes
	of  the	interrupt processing routine jumped to are then	 fetched.
	The CPU	then executes these codes as 8080 instructions.

	The registers and flags	of the 8080 are	mapped onto the	V20 - V30
	registers and flags as follows:

	8080 Register  V20 - V30 Register
	-------------  ------------------
	A	       AL
	B	       CH
	C	       CL
	D	       DH
	E	       DL
	H	       BH
	L	       BL
	SP	       BP
	PC	       PC

	8080 Flags     V20 - V30 Flag
	-------------  ------------------
	C	       CY
	Z	       Z
	S	       S
	P	       P
	AC	       AC

	The  use of independent	stack pointers (SP in native mode,  BP in
	emulation  mode)  allows separate stack	areas to be  defined  for
	each  mode  and	keeps the stack	of one of the  modes  from  being
	destroyed by stack operations in the other mode.

	The native-mode	SP,  IX,  IY and AH registers are not affected by
	any operations executed	during emulation mode.

	In the 8080 emulation mode,  the code segment register is defined
	by  the	 PS register (set by the interrupt vector) and	the  data
	segment	 register if defined by	the DS0	register.  This	last item
	must  be  set  by  the programmer  immediately	before	the  8080
	emulation mode is entered.

	RETEM
	-----
	When RETEM is executed in the 8080 emulation mode (interpreted by
	the CPU	as an 8080 instruction),  the CPU restores the PS, PC and
	PSW (just like if it were returning from an interrupt  processing
	routine),  and returns to the native mode.  At the same	time, the
	contents  of the mode flag (MD),  which	was saved to the stack by
	the BRKEM instruction,	is restored to a value of 1.  The CPU  is
	now  set to native mode,  and executes all following instructions
	as normal V20 -	V30 instructions.

	CALLN imm8
	----------
	This   instruction  makes  it  possible	 to  call   native   mode
	subroutines  while  in	8080 emulation mode.  To  return  from	a
	subroutine  to the 8080	emulation mode,	 the RETI instruction  is
	used.  In  this	 manner,  system  calls	that  would  normally  be
	serviced by 8080 subroutines in	a CP/M environment,  for example,
	can  be	rerouted to native mode	service	routines,  without having
	to develop more	code to	take care of these situations.	It  would
	require	a lot of ingenious programming,	 but the tools to do this
	are available here.

	The processing performed when this instruction is executed in the
	8080  emulation	 mode is similar to that performed when	a BRK  is
	executed  in  the  native mode.	 The imm8  operand  specifies  an
	interrupt  vector type.	 The contents of the PS,  PC and PSW  are
	pushed	onto the stack and an MD flag value of 0  is  saved.  The
	mode flag is set to 1,	and the	interrupt vector specified by the
	operand	is loaded into the PS and PC.

	RETI
	----
	This  is  a  general  purpose instruction  used	 to  return  from
	interrupt  routines  entered  by  the BRK instruction  or  by  an
	external interrupt in the native mode.	When this instruction  is
	executed at the	end of a subroutine entered by the execution of	a
	CALLN instruction, the operation that restores the PS, PC and PSW
	is restored,  however,	the 8080 emulation mode	value of the mode
	flag (MD) is restored, the CPU is set in emulation mode, and 8080
	emulation is resumed at	that point.


	As  you	 can see,  NEC has implemented very useful and	practical
	instructions  and added	them to	an already  powerful  instruction
	set. The instructions that they	have chosen to add and/or enhance
	can  be	 used to reduce	code and/or decrease processing	time  for
	just about any software	designed to run	on the 8086, 8088, 80188,
	80186, and even	the 8080 microprocessor.

	This  device has been installed	as a replacement to the	8088  and
	8086  in  many systems,	 ranging from single board  computers  to
	full-fledged mini- and microcomputers,	and it has worked fine so
	far.  For you IBM-PC and compatible users,  the	only problems  we
	have  encountered have been with software that is  copy-protected
	and  uses  exotic  schemes to determine	whether	or  not	 you  are
	running	 an authorized copy of the package,  or	whether	you  have
	your  key  disk	inserted in the	main floppy disk drive.	 In  some
	cases,	you  can  use the commercially	available  software  that
	allows you to bypass the check for the key disk	in drive A:. This
	is  NOT	an encouragement to bypass copy-protection,  it	is only	a
	suggestion  to	legal owners of	this type of software  who  might
	have  problems	of this	type.

	Purchase  of  this  device is an option	that  many  microcomputer
	owners might want to consider as an add-on that	will not take  up
	any  precious  expansion slots and will	enhance	 productivity  on
	their systems.	It is relatively easy to install in your machine,
	depending  on  the  type and  configuration,  and  is  relatively
	inexpensive (about $50 retail,	compared to anywhere from $800 to
	$1300  for a typical co-processor board).  Implementation of  the
	new and	enhanced instructions at an assembly language level could
	be achieved with the addition of a set of macros to automatically
	translate  the opcodes into the	machine	language the machine will
	understand.
									
	-----------------------------------------------------------------


	Additional NEC V20/V30 Information
	----------------------------------
		      

	#1	3-OCT-1985 08:27:02				     MAIL
	From:
	To:
	Subj:	V20 timing

	I haven't received the write-up  yet  but  here  is  some  timing
	measurements.

	Some random timing measurements on the IBM-PC of the 8088 and NEC
	V20 chips.

	test			  V20		  8088		% improve
							     (8088/V20)-1

	PASCAL sieve		 13.403 	 13.958 	 4.14
	PASCAL float		212.226 	219.820 	 3.57
	PASCAL real		453.858 	470.438 	 3.65
	PASCAL integer		 35.427 	 37.049 	 4.57
	PASCAL string		 46.480 	 81.355 	75.0
 
	C      sieve		 11.262 	 11.479 	 1.92
	C      float		278.039 	299.855 	 7.84
	C      fib		 68.841 	 70.748 	 2.77
	C      sort		191.832 	195.521 	 1.92
 
	lotus graph print	160.		163.		 1.8
 
	c compile (RAMDISK)	 31.		 28.		 9.6
    
	sq lcs.lib (RAMDISK)	 54.		 56.		 3.7
 
	123 re-calc		 72.		 80.		11.1
	123 create-extract	 93		131		43.9
 
	RBASE demo		141		144		 2.1
	RBASE demo1		 40		 42		 4.7

	-----------------------------------------------------------------