RESPRO.DOC v1.0
                            11/14/86
Eric Gans
French Department, UCLA
Los Angeles CA, 90024

     If  like most DOS users you have filled your RAM with memory 
resident  programs,  RESPRO  is for you.  RESPRO  allows  you  to 
disable and reactivate memory-resident programs at any time, from 
within  any application.  It also permits you to remove the  last 
program  loaded regardless of what it says in its user manual  or 
DOC  file.  This too can be done from within other  applications, 
but  memory errors may result if these are themselves dynamically 
requesting memory.

     RESPRO also includes an "uncrash" feature that allows you to 
exit  a "hung" program under most circumstances without having to 
reboot your computer.


              How Do Memory-Resident Programs Work?

     Memory-resident  programs are loaded like any  others;  they 
remain  resident  because  DOS allows them  to  keep  the  memory 
originally  allocated  to  them.  If you load a  series  of  such 
programs, they fill your RAM from the bottom up.

     But  residing  is only useful if these programs  can  remain 
active.  They  accomplish  this by capturing "interrupt  vectors" 
used  by  various  computing  activities.  Most  commonly,  these 
programs  look at one or both of the keyboard interrupts  (9  and 
16h)  to  see  if  you have typed  the  peculiar  combination  of 
characters   that  triggers  the  program.   Since  most  of  the 
characters  you type don't interest the resident  program,  after 
checking it passes on control to the next program down the  list, 
and  eventually  to  the BIOS that prints the  character  on  the 
screen.

                      How Does RESPRO Work

     RESPRO  itself operates by capturing interrupt  vectors  and 
using  its  time of control to record information concerning  the 
interrupts  used  by  other  memory  resident  programs.   RESPRO 
records  all  changes  that follow the loading  of  new  resident 
programs.  This  allows it to disable/reactivate  memory-resident 
programs   by   bypassing/restoring  these   programs'   captured 
interrupts.

                 Set-Up and Memory Requirements

     To  use RESPRO effectively,  you should load it  before  any 
other  memory-resident  programs (including those that  tell  you 
they  should  be loaded first).  RESPRO will only "see"  programs 
loaded  after  it;  it will always appear as #1 on  its  list  of 
memory-resident programs.Š
     RESPRO occupies about 10 K of memory, largely for buffers to 
hold  interrupt  data.  It requires DOS 2.0 or higher;  it  could 
probably be adapted for DOS 1, if anyone is still running it.

                        RESPRO Operation

     RESPRO  is  evoked  by  typing  Alt  `  (grave  accent).  On 
evocation,  and after any command,  it displays a list of memory-
resident programs,  their load addresses and the number of  bytes 
they occupy.

     The command line permits the following operations:
     
     (V)erbose  toggle:  Entering "v" toggles a mode that permits 
you  to see the interrupts captured by each resident program  and 
their  addresses  (segment:offset).  This  should be  of  use  to 
programmers.

     (R)emove  last:  This will remove the last resident  program 
from memory,  freeing the memory for other  applications.  RESPRO 
will  not  allow  you to perform this operation  from  within  an 
application  that has changed some of the interrupt vectors  used 
in  the  program(s) you wish to remove,  since on  exiting  these 
vectors  will  be reset to locations in the killed  program  that 
will  eventually be overwritten.  But because RESPRO cannot check 
for the future memory demands of your applications,  this command 
should always be used with caution from within other programs.

     (D)isable  #:  Entering "d3" will disable program  #3.  This 
operation may be performed without danger at any time,  since  it 
does not remove the program from memory.  A disabled program will 
not  use  processor  time or perform  any  other  function.   Any 
program thus disabled can be reactivated with the (A) command.

     (A)ctivate  #:  Enter  "a3" to reactivate  the  program  you 
disabled  with "d3".   This operation too can be performed safely 
at any time.

     Type <ESC> to exit. (No CR is necessary.)

     If you disable RESPRO it will remain in memory but no longer 
be  operative,  and  you will no longer be able to  call  up  its 
screen.  This is the one (obvious) exception to the rule that all 
disabled programs can be reactivated.

     You  can change the "`" character (scan code 41) by entering 
some  other  scan code at  location  103H.  (Technical  Reference 
manuals  and  the  like contain tables of these codes.)   DO  NOT 
enter the ASCII value of the new character!

     A  few  technically-oriented applications that  capture  the 
keyboard interrupts for themselves may not let you call up RESPRO 
while  they  are running.   This will not be the case for  normal 
user  programs  like  word-processors,   spreadsheets,   database Šprograms, or BASIC.

                         Uncrash Feature

     Since  RESPRO  keeps interrupt tables,  it can  handle  this 
function  more gracefully than other such programs.   If you  get 
caught in an endless loop but your keyboard is still  alive,  you 
can  exit  to  DOS  or the  "parent"  process  (e.g.,  DEBUG)  by 
simultaneously  pressing the CAPS LOCK and the SCROLL LOCK  keys.  
(This  operation  is independent of the current status  of  these 
keys.)  We can't absolutely guarantee that everything will be all 
right on exit,  but this feature may allow you to save files that 
would otherwise be lost.

     Please inform me if you have any problems using RESPRO.