"Z80MU" Z80 and CP/M 2.2 Emulator User's Guide                 "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide

                                       or

                   The Care and Feeding of Your Imaginary Z80                   The Care and Feeding of Your Imaginary Z80

                                       or

                         Fakeware For The Techie Masses!                         Fakeware For The Techie Masses!







                      A Guide to the Complete Z80 Emulator                      A Guide to the Complete Z80 Emulator

                         Z80MU.EXE version 3.10  3/14/86                         Z80MU.EXE version 3.10  3/14/86













     This document describes Z80MU, a software emulation of the Z80 and CP/M                             Z80MU
     2.2. The program was written by Joan Riff for Computerwise Consulting                                     Joan Riff
     Services.

     Placed in the public domain. No copyright notice. No legal mumbo-jumbo.
     No request for a financial contribution. No warrantee. Just a bunch of
     marvelous software magic.








     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 1
     INTRODUCTION













                                  INTRODUCTION                                  INTRODUCTION


     What is it?      ___________


     Z80MU is a software emulator of the ZILOG Z80 processor, which runs on
     the IBM PC. It also provides an emulation of Digital Research's CP/M
     version 2.2 operating system. 


     It includes the following facilities: 

          Complete emulation of Z80 object code, including all six
               active bits within the Z80 Flags Register. 
      
          Emulation of CP/M 2.2, with the exception of hardware-specific
               functions. 
      
          Advanced commands for debugging Z80 software (eliminating the
               need for DDT.COM), including: 
      
               Illegal Opcode control (treat 'em as FAULTs or NOPs). 
      
               BDOS function trace. 
      
               Instruction TRACE and NOTRACE, with Z80 PC traceback. 
      
               Breakpoints. 
      
               Dump CP/M memory in HEX and ASCII. 
      
               Patch CP/M memory in HEX, decimal, binary, ASCII charac-
                    ters, or ASCII strings. 
      
               Symbolic labels may be defined and used instead of CP/M
                    addresses. 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 2
     INTRODUCTION

      
               Z80 register and flag display and alter, including
                    alternate regs/flags and IFF1, IFF2, IMF, I, R regs.
      
               CP/M memory move and find. 
      
               Intel HEX files can be properly read into CP/M memory,
                    as well as created from CP/M memory. 
      
          An "emulated VT52 terminal" for full-screen CP/M applications.
      

          A full disassembler much like Ward Christensen's RESOURCE,
               built right in, with: 
      
               Symbolic addresses. 
      
               Control breakpoints for Instructions, Bytes (DB), Words
                    (DW), Table of Words (DW), and Storage (DS). 
      
               Automatic label generation. 
      
               Comments associated with Z80 addresses.
      
      
          Online help summaries. 
      
          Limited SUBMIT file support (built right in - no need for
               SUBMIT.COM).
      
          Access to all PCDOS programs and commands. 
      
          CP/M software reads and writes PCDOS files, and can be
               organized with the PCDOS directory structure (instead of
               using CP/M's "user number" idea). 
      

     Z80MU (from now on called "the Emulator") can be used quite transpar-
     ently to run CP/M applications on the IBM PC. It contains many advanced
     commands not found in CP/M, but there's no law that says that you have
     to use 'em all. By ignoring the advanced commands, you can run the
     emulated CP/M all day long and you'll swear that you're running CP/M. 
      
     You can also take advantage of the advanced commands and features, and
     have a user interface more powerful than that available with CP/M. 
      
     Advanced Z80 programmers can even ignore CP/M entirely and use the
     Emulator as a generic Z80 development tool for developing device
     controllers and other non-CP/M based Z80 code.

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 3
     INTRODUCTION

      
     At CCS, we use the Emulator to develop things like Z80-based hard disk
     controller card software, device-switching hardware, and even a few
     boring old standard CP/M applications. We have also used it to regen-
     erate the source code for the 32K ROM in the Radio Shack Model 100
     laptop computer, to figure out how it works. 
      
     The Emulator consists of a high-speed 8088 assembler subroutine (which
     does the actual Z80 emulation), and a 'C'-language main program which
     provides the CP/M-like interface to the user, the disassembler, the
     RESOURCE facility, and the rest of the advanced features. 


     Why Did We Do It?     _________________

     At CCS, we have quite an investment in CP/M software. Most of that
     software consists of fairly esoteric software development tools, things
     that are hard to find in the IBM PC world. Furthermore, we continue to
     develop software for the Z80. The old chip just won't die, although
     nowadays it is used more in controller boards than as a primary system
     processor.

     We wanted to keep these Z80 tools, yet apply our numerous IBM PC tools
     (especially some fantastic IBM PC editors) to our Z80 development
     process.

     We were also keenly interested in creating source code for some object-
     only Z80 applications, with a view to converting them to 8088 assembler
     source code for re-assembly as native IBM PC programs.

     We scouted around and discovered several software packages which sup-
     posedly allowed us to run CP/M programs on the IBM PC. Needless to say,
     they just couldn't cut it. The Heath User's Group (HUG) emulator, 80Mate
     by Vertex, and a host of similar packages (both public domain and
     commercial) were considered. There were many things that we were looking
     for, and every currently-available product flunked one or more tests:

          Speed of emulation: some packages performed the actual Z80          Speed of emulation
          emulation much slower than theoretical calculations said that
          they should have.

          Accuracy of the Emulation: many packages ignored one or more          Accuracy of the Emulation
          of the Z80 flag bits, especially the all-important overflow
          flag. And no available package accurately emulated CP/M's
          BDOS function calls. Most seemed to simply translate CP/M
          BDOS functions into their PCDOS equivalents, without allowing
          for the many differences in operation between the similar
          (but not identical) operating system calls.


     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 4
     INTRODUCTION

          User Interface: some packages didn't even try to provide a          User Interface
          user environment that looked like CP/M's CCP. Some, in fact,
          made you re-run their emulator with each CP/M program that you
          wanted to run.

          Special headers 'bound' to programs: some packages required          Special headers 'bound' to programs
          you to 'bind' a special header to the front of every CP/M
          .COM file that you wanted to run, and then made you run that
          program straight from PCDOS.

          Debug support and environment control: most of the packages          Debug support and environment control
          assumed that you would use DDT for whatever debugging needed
          to be done. They had nothing built in. And no package provided
          a proper interface to PCDOS commands or to the PCDOS environ-
          ment.

     Since we couldn't trust our software to any available Z80 emulators, we
     started thinking about developing our own. What's more, we kept bumping
     into folks who were in the business of Z80 development, and who kept
     badgering us to solve this problem "the right way" (whatever that
     means).

     At first, we were skeptical. On the surface, it appeared that a truly
     accurate software emulation of the Z80 would run "hundreds" of times
     slower on an IBM PC than on a real Z80. But then Joan Riff got involved,
     and started playing around with register assignments and a memory model
     that "just might work." By keeping images of most of the Z80 registers
     in 8088 registers (as opposed to memory), and by very careful main-
     tenance of the Z80's flags, Joan was able to hand-code a low-level Z80
     emulator which as far as we can tell is 100% accurate, and only four
     times slower than a 1 Mhz Z80.

     To this basic emulator we added the user interface (written in Lattice
     C) which did all of the control and debug operations that we needed.

     After six man-months of work, we had our Emulator. 














     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 5
     INTRODUCTION


     How Does It Work?     _________________
      
     When it runs under PCDOS, the Emulator looks like this: 
      
          +------------------------------------+ 
          | Z80MU 'C' main program             |             Z80MU 'C' main program
          |                                    | 
          | This is what you talk to, the guy  | 
          | that emulates CP/M Console Command | 
          | Processor.                         | 
          |                                    | 
          +------------------------------------+ 
          | Z80 Emulation 8088 Assembler Code  |             Z80 Emulation 8088 Assembler Code
          |                                    | 
          | Which actually emulates the Z80 as | 
          | it "executes" in the CP/M Segment. | 
          |                                    | 
          +------------------------------------+ 
          | 64K CP/M Segment                   |             64K CP/M Segment
          |                                    | 
          | In which the Z80 code is held as   | 
          | it executes. The size of the       | 
          | Transient Program Area is 65022    | 
          | bytes.                             | 
          |                                    | 
          |                                    | 
          |                                    | 
          |                                    | 
          |                                    | 
          |                                    | 
          |                                    | 
          | - - - - - - - - - - - - - - - - - -| 
          | BDOS and BIOS hooks                |             BDOS and BIOS hooks
          |                                    |
          | Which trap CP/M BIOS and BDOS      | 
          | calls, so that they can be         |
          | emulated.                          |
          |                                    |
          +------------------------------------+ 
      

     The main program accepts the user's commands, and processes them. When
     and if it comes time to run a Z80 program, the Z80 code is loaded into
     the CP/M Segment, and the 8088 assembler code which actually emulates
     the Z80 is called to run the program there.

     As the Z80 program executes, it accesses the outside world via calls to
     the BDOS and BIOS hooks. The code that is executed for a given BDOS or

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 6
     INTRODUCTION

     BIOS function actually resides within the 8088 assembler code that
     emulates the Z80.
      
      
     What Does It Require To Run?      ____________________________
      
     The Emulator runs on the IBM PC under PCDOS 2.x or above. The first
     thing that it does when it runs is allocate 64K to be used as CP/M
     memory (the "CP/M Segment"). Additionally, the various RESOURCE commands
     dynamically allocate memory for labels and comments. A safe rule to use
     is to allow an extra 64K for a large RESOURCE control table.

     In short, if a CHKDSK of your system shows at least 256K free memory
     bytes, then you have enough room to run the Emulator.
      
      
      
     How Accurate an Emulation Is It?      ________________________________
      
     There are two aspects to the accuracy of the Emulator: 
      
          1) How accurately it emulates the Z80 
          2) How accurately it emulates CP/M 2.2
      
     The Emulator emulates the Z80 almost perfectly, even down to an exact
     emulation of all six flag bits in the Flags Register. Even the untest-
     able Half-carry and Add/Subtract flag bits are emulated. For faster
     execution, the Emulator ignores the two unused bits in the Flags
     Register, so these will not act exactly as they would on a real Z80.

     Input/Output instructions (the IN's and OUT's) perform everything except
     the actual strobe of the I/O data lines. You can't very well have Z80
     code accessing I/O addresses that mean something entirely different on
     the IBM PC. So the actual data transfer has been disabled. But any
     setup, auto-increment of registers, and flag effects have been emulated
     even for the IN's and OUT's. 
      
     The Z80 HALT instruction is used as a hook to return control to the main
     'C' program, and as a call to the emulated CP/M BIOS and BDOS. 

     When it came to emulating CP/M 2.2, we took a less precise approach. We
     weren't interested in emulating the limitations of CP/M. We wanted to
     include many of the benefits of PCDOS. And we wanted to add many more
     "builtin" commands than were available with CP/M. We also demanded the
     largest possible TPA (Transient Program Area - the amount of memory
     available to be used by a Z80 program). Yet we wanted to keep the
     interface very close to CP/M's.
      


COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 7
     INTRODUCTION

     So we decided to support "standard" CP/M applications, ones that stood a
     good chance of executing on a wide variety of CP/M systems and thus were
     hardware independent. 
      
     This we have succeeded in doing. 
      
     The user interface is just like CP/M's, so that someone used to CP/M
     will feel right at home. 
      
     The program interface (via the BIOS and BDOS) is exactly the same as
     CP/M's. There are some BIOS and BDOS functions that are hardware-
     specific, or expect diskettes to have the CP/M format. These are in
     general not supported. The differences are explained in a later section.
     A tremendous amount of work has gone into translating CP/M BDOS func-
     tions into their PCDOS equivalents, and back again. Many folks assume
     that a given BDOS function can be emulated simply by calling PCDOS with
     the function in the 8088 AH register. This is not true. On the surface,
     PCDOS functions are similar to CP/M BDOS functions. In fact, there are a
     host of very small but very important differences, which are handled by
     the emulated CP/M within the Emulator.
      
     The handling of commands and command arguments (the command "tail")
     appears to the Z80 application exactly as it would on a real CP/M
     system. The default FCB at 5Ch is formatted with the filename implied by
     the first command-line argument, and the FCB at 6Ch with the second
     argument. The byte at 80h is set to the number of characters in the
     command tail, and is followed by an uppercase version of the command
     tail as typed by the user.
      
     We have achieved a TPA size of 65022 bytes. This is more than is
     available on almost all "real" CP/M systems, including the Baby Blue Z80
     add-on board (for the IBM PC) from MicroLog. 
      
     We have also built a fake VT52 terminal into the Emulator, since
     many CP/M applications (especially those doing full-screen editing)
     assume that they are being run from a serial ASCII terminal.

     All in all, the compatability of the Emulator is so good that we have
     been able to move all of our CP/M applications to the Emulator, and to
     have them run perfectly (although a tad slow). 
      
     Here is a partial list of CP/M applications that we have tested with the
     Emulator and found to run as they do on a "real" CP/M system: 
      
          ASM       LOAD      ED        DDT       DUMP
          PIP       M80       L80       LIB       MBASIC 
          LASM      MAC       dBase II 

          WORDSTAR 3.0 & 3.3 with MAILMERGE (but not SPELSTAR!) 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 8
     INTRODUCTION

          PMATE-80 rev. 3.02 
          Software Toolworks 'C' compiler
          Telecon 'C' compiler
          Chang Labs' MemoPlan 
          LU version 3.00
          S-BASIC Basic compiler v5.4b
          Target PlannerCalc spreadsheet



     This is more a list of the software that we happened to have on hand
     than an exhaustive list of software that will run under the Emulator.


     What WON'T Run Under the Emulator?     __________________________________

     There are some CP/M programs (like STAT.COM provided by Digital Re-
     search) which are hardware-specific. These cannot be run under the
     Emulator, or must be run "carefully" to avoid functions that look to the
     hardware. STAT, for instance, starts out by interrogating the physical
     layout of the diskette, and interpreting it as if it were formatted for
     CP/M. Since PCDOS disks aren't in CP/M format, this makes no sense. So
     this is unsupported under the Emulator, and STAT is immediately aborted
     by the Emulator. 

     WORDSTAR's SPELSTAR won't work, either. It tries to call CP/M's Console
     Command Processor (CCP) within the 64K CP/M segment. In the Emulator,
     however, there is no CCP in the CP/M segment. It's really quite sad.                    is no
     SPELSTAR goes to a lot of work to calculate just where in Z80 memory the
     CCP is located, relative to the BDOS address held in location 0005h.
     Then it calls that address. Unfortunately, there's nothing there...

     There are some CP/M programs which look too closely at the "reserved"
     fields of the FCB. These may have trouble. We have seen some products
     written by Microsoft which do this. They are thus highly release-
     dependent, and thus ought not to be emulatable at all. We have, however,
     added special code to the Emulator which keeps FCB+14 and FCB+15
     somewhat sensible, and that seems to have allowed these Microsoft
     programs to work.

      
      
     How Fast Is It?      _______________
      
     Aye, there's the rub. 
      
     Because the Z80 used by the Emulator is an imaginary one whose instruc-
     tions must be emulated in software, the effective speed of a Z80 program
     is considerably less than the speed of the IBM PC. One 12-cycle Z80

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 9
     INTRODUCTION

     instruction, for example, may take from 47 to over 100 IBM PC cycles
     (depending on the instruction, its addressing mode, etc). 
      
     For detail on the effective speed of the emulated Z80 and what it means,
     see the description of the "speed?" and "howfast?" Builtin Commands                                 speed?       howfast?
     later in this Guide. 
      
     We have not found the speed of the emulated Z80 to be entirely accept-
     able. Z80MU is the fastest software-based accurate Z80 emulator that                                               accurate
     we've seen for the IBM PC. Yet we would like to have something that
     would run the standard CP/M utilities on an IBM PC at an effective cpu
     speed of at least 1 MegaHertz, and still have all of the subtleties
     (like flag updating) performed with 100% accuracy. 
      
     The solution is to run the Emulator on an IBM PC/AT, Compaq DeskPro
     286, or similarly speedy CPU.
      


      
     How Do I Get My CP/M Programs Into The IBM PC?      ______________________________________________
      
     Assuming that you want to emulate some CP/M applications on the IBM PC,
     the first realization is that these CP/M files don't already reside on
     the PC. What's more, they currently exist (by definition) on disks
     formatted for CP/M, not for the IBM PC. So they can't be read by a
     vanilla IBM PC using PCDOS. They must be copied to standard PCDOS disk
     files. 
      
     We have used several approaches, all with excellent results. 
      
     The first approach is to transfer the CP/M files straight from the CP/M
     disks to PCDOS disks using a utility that runs on the IBM PC and is
     capable of reading the foreign CP/M format. Such utilities include:
      
          CONVERT  (from Selfware, Inc.  Fairfax, VA)           CONVERT
          XENOCOPY (from Vertex Systems, Inc.  L.A., Calif)           XENOCOPY
      

     This approach is nice, when it works. The major disadvantages are:

          Only certain CP/M formats are recognized by each of these
               utilities. Apple ][ and NorthStar Horizon CP/M disks, for
               example, cannot be read on the IBM PC without special
               hardware.

          You must have the CP/M disks at hand. 
      


COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 10
     INTRODUCTION

     Another approach is to transfer the CP/M files to the IBM PC via a
     communications line. This is Joan Riff's personal favorite. If the
     CP/M system is at hand, then the two machines are direct-connected and
     cranked up to 9600 baud. If the CP/M system is not handy, then the
     transfer is made over the phone at whatever speeds the respective modems
     can handle. In either case, the CP/M system running BYE and XMODEM is
     controlled by the IBM PC running Crosstalk VI version 3.5 (from Micro-
     Stuf) and Joan Riff's excellent XMODEM (with CRC) Crosstalk RUN command.

      
     When direct connected, files really fly across at 9600 baud. 
      
     The major advantages of this approach are: 
      
          Who cares what the CP/M disk format is? If the CP/M system can
               read its own files, then we can get them. This works very
               well when transferring Apple ][ and NorthStar Horizon
               CP/M files. 

          Public Domain CP/M software can be gathered just by dialing
               into a CP/M Bulletin Board or RCPM system. You need never
               know what hardware system is on the other end. 
      
      
     CP/M and PCDOS files are similar enough that we have never had to alter
     a file that was transferred using either of the above two approaches.
     We just download the files to the IBM PC and run 'em under the Emulator.
      
     The biggest problem is remembering which files are PCDOS files and
     which are CP/M files. If you transfer a CP/M file called DUMP.COM, for
     example, from a CP/M system to the IBM PC's disk, you really do want to
     remember that it is a CP/M file (to be run with the Emulator) and not an
     IBM PC .COM file. If you accidentally invoke DUMP.COM from PCDOS, you
     will be unpleasantly surprised. The CP/M DUMP.COM file contains Z80
     opcodes, which will be executed by the IBM PC as 8088 opcodes. Time to
     reach for the Big Red Switch... 
      
     You must run such CP/M command (.COM) files under the Emulator!          must
      
     At CCS, we keep things straight by storing CP/M files under separate
     PCDOS directories. The "Z80PATH" environment string (explained else-
     where) makes this particularly convenient. 
      
     The saving grace to this CP/M-to-PCDOS conversion is that it needs to be
     done only once for a given file. We spent quite a while transferring 10
     megabytes of CP/M files to the IBM PC. But we need never do it again.
     Now we just run everything on the IBM PC. 



     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 11
     INTRODUCTION


     How Do I Run It?      _________________
      
     The Emulator is just another PCDOS program. There are no arguments to
     give it. There is no syntax. Just type 
      
          Z80MU           Z80MU
      
     and bingo! - you're in CP/M.          bingo!
      
     To make things easier, you may want to copy Z80MU.EXE to one of your
     PCDOS "PATH" directories (if you have any). If you don't have any PATH
     directories set up, then just insert the floppy that holds Z80MU, start
     the program, and then remove the floppy. You don't need it until you
     want to run the Emulator again. 
      
     The next section ("The PCDOS Environment") describes the PCDOS environ-
     ment that applies to the Emulator. You may want to study it before you
     run the thing. 

      
      
     What Can Go Wrong?     __________________

     The Emulator is as safe a program as ever you'll find on the IBM PC.
     You will probably never experience any problem with it.

     There is one important thing to watch out for, however:

          If the Emulator itself is ever aborted, then you should          If the Emulator itself is ever aborted, then you should
          immediately reboot your IBM PC.          immediately reboot your IBM PC.

     Why? Because the Emulator must trap the IBM PC's BREAK interrupt. When
     the Emulator returns to PCDOS (i.e. - when you type the "exit" command),                                                              exit
     it restores this interrupt the way it was before. If the Emulator never
     gets a chance to exit gracefully, then it never gets a chance to restore
     this interrupt. The thing is left pointing to now-dead code somewhere in
     the IBM PC's memory. This is bad news for you, and good news for that
     big red switch on the side of your PC...











     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 12
     INTRODUCTION

     Why might the Emulator abort? Well, there is always the possibility of                                               is
     an Emulator bug that we haven't found. And we're not real confident of
     Lattice C and its flaky subroutine library, which once in a blue moon
     decides to abort for no apparent reason. But the most likely reason is a
     disk error that results in the familiar message:

                              Abort, Retry, Ignore?                              Abort, Retry, Ignore?

     If you select Abort, then you've just aborted the Emulator and left the                   Abort
     BREAK interrupt in limbo. So reboot to be safe.








































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 13
     THE PCDOS ENVIRONMENT













                             THE PCDOS ENVIRONMENT                              THE PCDOS ENVIRONMENT                                                    

     The Z80 Emulator runs as a normal application program under PCDOS
     (version 2.0 and above). There are a few things that you should keep in
     mind, in order to get the most out of the Emulator. 

      
     PCDOS's use of COMMAND.COM      __________________________

     Certain Emulator commands ("dir", "!xxxxxx", etc) are handled by calling                                 dir    !xxxxxx
     PCDOS to perform the associated operation. The first thing that PCDOS
     does when called in this way is reload its COMMAND.COM file from disk.
     To speed things up, you should make sure that PCDOS's COMMAND.COM file
     is in a RAMdisk, or on a hard disk. You can tell PCDOS where to find
     COMMAND.COM by using the "SET COMSPEC=" command in your AUTOEXEC.BAT
     file, or the "SHELL" command in your CONFIG.SYS file.
      
     Certain versions of PCDOS (2.0 and 2.1, and maybe others) have trouble
     obeying the "COMSPEC=" command. They try to reload COMMAND.COM from the
     boot disk, regardless of the current "COMSPEC=" parameter. If you use
     one of these versions of PCDOS, then you may avoid problems by keeping
     COMMAND.COM always available on the boot drive. Alternatively, you may
     apply one of the public domain COMZAP patches to fix your copy of PCDOS.

      
     The "Z80PATH=" Environment String     _________________________________

     The Emulator has a facility which is equivalent to the PCDOS "PATH"
     command. It allows you to tell the Emulator where to look for Z80
     command (.COM) files. 
      
     This facility is implemented by a new PCDOS environment string, called
     "Z80PATH". This string is a list of fully-qualified names of directories
     which are to be searched when the Emulator is looking for a .COM file to
     load and run. The various directory names must be separated with
     semicolon (";") characters, as follows: 
      

COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 14
     THE PCDOS ENVIRONMENT


          SET Z80PATH=c:\cpm;c:\z80\mystuff;c:\           SET Z80PATH=c:\cpm;c:\z80\mystuff;c:\

     This example tells the Emulator to search for Z80 programs first in the
     directory "CPM" on drive C:, and then (if not found there) in the
     directory "Z80\MYSTUFF" on drive C:, and finally (if still not found) in
     the root directory of drive C:. 
      
     A Z80PATH string should be defined in your AUTOEXEC.BAT file, so that
     it is always present when you run the Emulator.

     The trailing "\" character of each directory name is optional. If it is
     absent, a "\" character is automatically applied to the directory name
     before the name is used in the search.
      
     The Z80PATH search order is used whenever an "unqualified" program name
     is used as a command to the Emulator. An "unqualified" program name is a
     legal filename (up to 8 characters) which: 
      
          1) has no drive ID on the front of it (no ":" character), and
          2) has no directory names imbedded in it (no "\" characters), and 
          3) is not the name of an Emulator Builtin Command.

     For example, let's say that you give the following command to the
     Emulator: 
      
          Z80 A>asm dump.aaz                 asm dump.aaz

     The Emulator first checks to see if the command ("ASM") is one that it
     recognizes - a so-called Builtin Command (see the "Builtin Commands"
     section). If it is not, then the Emulator acts just like CP/M and
     attaches a .COM extension to the command, yielding "ASM.COM". It then
     looks in the current PCDOS directory on the current disk (in this case,
     drive A:) for a file by the name of ASM.COM. If it finds such a file,
     then it loads it into the CP/M Segment and runs it. 
      
     If the file is not found on the current drive, then the Emulator
     searches the various Z80PATH directories, looking for a file with the
     right name (ASM.COM). The directories are searched in the order that
     they appear in the Z80PATH string. The first ASM.COM file that is found
     is the one loaded and run. 
      
     If there is no Z80PATH string defined in the PCDOS environment, then the
     search stops with the current disk drive's current PCDOS directory. 
      
     If no matching filename is found after all of this, then the Emulator
     echos the command line

          asm? 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 15
     THE PCDOS ENVIRONMENT



     indicating that it doesn't know what you mean. 

     Note that no search takes place if the command is "qualified". A
     "qualified" command includes a drive ID or a pathname, such as:

          Z80 A>b:asm dump.aaz                b:asm dump.aaz
          Z80 A>\bin\asm dump.aaz                \bin\asm dump.aaz

     In such a case, the Emulator tries only once to open the Z80 .COM file,
     using the exact name given. If such a file cannot be found, then the
     command fails as mentioned above.



     The AUTOEXEC.Z80 File     _____________________

     When the Emulator first starts up, it automatically executes the
     following command:

          Z80 A>SUBMIT AUTOEXEC.Z80                SUBMIT AUTOEXEC.Z80

     If there is no file by the name of AUTOEXEC.Z80 in the current directory
     when the Emulator is run, then an error message is displayed and the
     Emulator just waits for you to enter commands from the keyboard.

     If there is such a file, however, then the Emulator reads its commands              is
     from that file, until EOF. See the "submit" builtin command for more                                         submit
     details about submit files.

     This is an easy way to automate the Emulator. At CCS, we use a different
     AUTOEXEC.Z80 file in each work directory in order to set up the parti-
     cular environment that we want to work with. The AUTOEXEC.Z80 file
     within the Radio Shack Model 100 directory, for example, automatically
     reads in the 64K Model 100 image from disk ("read 0 model100.mem"), and                                                  read 0 model100.mem
     the disassembler control file ("control read model100.ctl"). It also                                     control read model100.ctl
     sets up the disassembler format that we want ("list include A O"). So                                                    list include A O
     when we start up the Emulator while within that directory, the thing
     comes up ready to do real work.










     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 16
     THE PCDOS ENVIRONMENT


     I/O Redirection With The Emulator      _________________________________


          NOTE: The "terminal" builtin command has been enhanced to          NOTE:      terminal
          allow internal mapping of the builtin VT52 emulated terminal
          to respond to either CP/M BIOS or CP/M BDOS console I/O
          requests. This may thoroughly confuse the following discus-
          sion. So in the following text we assume the default condi-
          tion, in which the builtin VT52 terminal emulator only
          responds to CP/M BIOS console I/O requests.

      
     The Emulator writes its output to the standard output that is defined by
     PCDOS. So regular old PCDOS I/O redirection can be used when you start
     the Emulator. 
      
     For example, the following PCDOS command can be used to run the Emulator
     and capture all Emulator output to file OUTPUT.DOC: 

          Z80MU >OUTPUT.DOC           Z80MU >OUTPUT.DOC

     You may also append output to an existing file with:

          Z80MU >>OUTPUT.DOC           Z80MU >>OUTPUT.DOC

     This is perfect for automating the Emulator. Some of the samples
     displayed later in this document were captured by redirecting the
     Emulator's output to a file, and then editing that file into this
     document. 
      
     There are a few things to bear in mind, however. 
      
     First of all, remember that there are several parts of the Emulator:

      
          The main program, which reads your commands and in general          The main program
          acts like the CP/M CCP. It does all I/O via PCDOS, so it is
          subject to I/O redirection. 
       
          The actual Z80 emulator, which does no I/O at all.          The actual Z80 emulator
       
          The CP/M BIOS emulator. It does I/O at the IBM PC ROM BIOS          The CP/M BIOS emulator
          level, so PCDOS never sees what's going on. CP/M BIOS terminal
          I/O goes through the emulated "terminal" inside the Emulator,
          and then straight to the IBM PC screen. So I/O redirection
          does not apply there. 
      


COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 17
     THE PCDOS ENVIRONMENT


          The CP/M BDOS emulator. The BDOS emulator does its I/O via PCDOS,          The CP/M BDOS emulator
          so I/O redirection does apply to it, and to any Z80 programs that
          use BDOS functions for I/O. 


     Now the question arises: Will my CP/M application obey any I/O redirec-
     tion that I specify when I run the Emulator? 
      
     The answer, of course, depends on your application. 
      
     Most "standard" CP/M applications do their I/O via BDOS functions. So
     these will obey your I/O redirection. 
      
     Full-screen editors, in general, use the BIOS instead of the BDOS, for a
     lot of very good reasons. So these will automatically be exempt from
     your I/O redirection. 

      
     Please remember that all Emulator output is redirected at once. If you                          all
     redirect the output, meaning to enter commands from the keyboard, don't
     be real surprised if you can't see any of the Emulator's prompts. They
     are being written to the redirected output file, and not to the screen. 

          NOTE: When you redirect output to a disk file, your input
          keypresses are supposed to be sent to the output file (not to
          the screen). Some versions of PCDOS, however, contain a bug
          that causes your keypresses to appear on the screen instead.
          We have seen public domain patches to fix this bug floating
          around the Bulletin Boards, but can't vouch for any of them. 


      
     Using The Keyboard      __________________
      
     The Emulator reads its input from the standard input as defined by
     PCDOS. So if you don't use PCDOS input I/O redirection when you start
     the Emulator, then input comes from the keyboard. 
      
     The Emulator could have done its own direct keyboard and screen I/O.
     This would speed things up considerably. PCDOS is notoriously slow when
     it comes to writing to the screen. 
      
     We decided, however, not to circumvent PCDOS when writing to the screen
     and reading from the keyboard. The Emulator is slower as a result. But
     we gain a few conveniences as a result: 
      
          We achieve something closer to true CP/M emulation, 'cause


     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 18
     THE PCDOS ENVIRONMENT


          PCDOS automatically handles ^P and ^S/^Q in a manner close to
          CP/M's handling of them. 
      
          We get automatic I/O redirection. 
      
          We get PCDOS expanding macro keys and interpreting function
          keys. 
      
      
     The F3 key, for instance, can still be used to repeat the last command
     entered to the Emulator. The ESC key cancels the current input line. And
     F1 recreates the last command one character at a time. Other PCDOS
     keyboard conventions (like Ctrl-NumLock, Ctrl-PrtSc, and so on) are also
     handled by PCDOS in a way that we're all used to. 
      
     The addition of keyboard enhancers like CED and Sidekick can confuse
     things, so that the function keys don't act quite right. You'll just
     have to experiment with it.

     If you want to copy screen output to the printer, then press ^P or
     Ctrl-PrtSc. A second press will turn printer echo off. Remember that
     such PCDOS redirection applies to Emulator output (like dumps, disassem-
     blies, etc) as well as to the output of any CP/M applications being run
     under the Emulator that use BDOS functions for output.
      
     If text is scrolling off of the screen too fast to read (not real
     likely, with PCDOS being as slow as it is), you can pause and restart it
     with ^S/^Q, or Ctrl-NumLock. 

     The actions of ^S/^Q, ^P and Ctrl-PrtSc may vary, depending on the
     particular CP/M application being run. CP/M's BDOS function number 6
     (Direct Console I/O), for example, is handled by CP/M without it
     checking for ^S or ^P. The Emulator mimics this action.


     Filenames!     __________

     CP/M filenames may contain certain characters that PCDOS objects to. In
     general, don't use the "\" or "/" characters in filenames, or the I/O
     redirection characters ">" and "<", and so on.

     And watch out for PCDOS device names that are perfectly innocent
     filenames under CP/M. Things like "CON.ASM" will fool you.






     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 19
     THE CP/M ENVIRONMENT














                              THE CP/M ENVIRONMENT                              THE CP/M ENVIRONMENT


     This section describes the environment set up by the Emulator, under
     which your Z80 programs will run.



     Emulated Terminal     _________________


          NOTE: The "terminal" builtin command has been enhanced to          NOTE:      terminal
          allow internal mapping of the builtin VT52 emulated terminal
          to respond to either CP/M BIOS or CP/M BDOS console I/O
          requests. This may thoroughly confuse the following discus-
          sion. So in the following text we assume the default condi-
          tion, in which the builtin VT52 terminal emulator only
          responds to CP/M BIOS console I/O requests.

      
     When a Z80 program does character I/O by calling the emulated CP/M BIOS
     (not using BDOS functions, but BIOS calls), then it is communicating
     with an imaginary, emulated ASCII terminal which is maintained by the
     Emulator. The Emulator interprets ASCII codes that are sent to this
     "terminal", and translates them into appropriate calls to the IBM ROM to
     control the IBM's display. 
      
     Most ASCII characters that are sent to the emulated "terminal" are
     displayable characters - letters, numbers, and so on. They appear on the
     screen for the user to read. Other ASCII characters - called "control
     sequences" - are used not to display anything, but to cause the "ter-
     minal" to perform special functions like clearing the screen, switching
     between high- and low-intensity, and so on. 




     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 20
     THE CP/M ENVIRONMENT


     The builtin "terminal" obeys VT52 control sequences, which are the                                  VT52 control sequences
     same ones used by the Heath/Zenith H19 and H89 machines when in ZDS                           Heath/Zenith H19     H89
     mode. They are as follows:



          ESC H Homes cursor           ESC H

          ESC C Advances cursor 1 char to right. Stays on same line.           ESC C
      
          ESC D Backspaces cursor one char to left. Stays on same line.           ESC D

          ESC B Moves cursor down 1 line, staying in same column. Screen          ESC B
               is scrolled if necessary.
      
          ESC A Moves cursor up 1 line, staying in same column. No          ESC A
               scrolling occurs. 
      
          ESC I (uppercase letter "I", HEX 049h) Moves cursor up 1 line,          ESC I
               staying in same column. Scrolling occurs if cursor was on
               top line. 
      
          ESC n Causes current cursor position to be returned via          ESC n
               emulated "keyboard" as ESC Y line# column#. This control                                                           ____________
               sequence is ignored (not supported) by the Emulator.               ____________________________________________________
      
          ESC j Saves cursor position for later restore via ESC k.           ESC j
      
          ESC k Returns cursor to position that was saved via ESC j.           ESC k

          ESC Y line# column# Direct cursor addressing sequence. Screen          ESC Y line# column#
               lines are numbered 1 to 25. Screen columns are numbered 1
               to 80. Line# and column# args are obtained by adding 31
               (01Fh) to the desired line or column number. Alternative-
               ly, you may think of lines as being numbered from 0 to
               24, columns from 0 to 79, and the offset to add to each
               being 32 (020h).

               To position to line 5, column 10, for example, the
               following is sent: 
      
               ESC Y $ )                ESC Y $ )
      
               which is represented in HEX as 01Bh 059h 024h 029H and in                                              01Bh 059h 024h 029H
               decimal as 27 89 36 41. Note that the line# arg is                          27 89 36 41
               obtained by 5 + 31 = 36 (024h), and the column# arg by 10                                    36
               + 31 = 41 (029h).                       41
      

COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 21
     THE CP/M ENVIRONMENT


               Line# or column# args less than 32 default to 32 (i.e. -
               to line or column 1). An arg value that is too large
               defaults to the max legal value (25 for line, 80 for
               column). 

          ESC E Erases the entire screen and homes the cursor.           ESC E
      
          ESC b Erases from the start of the screen to the cursor,          ESC b
               including the cursor position. 
      
          ESC J Erases from the cursor to the end of the screen (inclu-          ESC J
               ding the cursor position). 
      
          ESC l (lowercase letter "L", HEX 06Ch) Erases the entire line          ESC l
               that the cursor is on, positions the cursor to the left
               edge of that line. 

          ESC o (lowercase letter "O", HEX 06Fh) Erases from the          ESC o
               beginning of the line to the cursor (including the cursor
               position). 
      
          ESC K Erases from the cursor to the end of the line (including          ESC K
               the cursor position). 
      
          ESC L Inserts a blank line before the line that the cursor is          ESC L
               on, shifts following lines (including the cursor line)
               down to make room. Cursor is moved to start of new blank
               line. 
      
          ESC M Deletes the line that the cursor is on, scrolls follow-          ESC M
               ing lines up to fill its place. Cursor moves to left edge
               of its line. 
      
          ESC N Deletes the character under the cursor, shifts remaining          ESC N
               text to left to cover it up. 
      
          ESC @ (At-sign character, HEX 040h) Enters Insert Mode.          ESC @
               Displayed characters cause others on the same line to be
               moved right to make room. This can be pretty pokey,
               thanks to the IBM ROM BIOS!

          ESC O (uppercase letter "O", HEX 04Fh) Exits Insert Mode.           ESC O

          ESC p Enters Reverse Video or Highlight mode.          ESC p

          ESC q Exits Reverse Video or Highlight mode.          ESC q

          BEL (decimal 7) Beeps bell.           BEL

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 22
     THE CP/M ENVIRONMENT


      
          BS (decimal 8) Backspaces cursor one character position.           BS

          HT (decimal 9) Tabs cursor to next mod-8 column boundary          HT

          LF (decimal 10, HEX 0Ah) Advances cursor to next line, same          LF
               column. 

          FF (decimal 12, HEX 0Ch) Clears screen and homes cursor.           FF

          CR (decimal 13, HEX 0Dh) Returns cursor to start of current          CR
               line. 


      
     The other standard ASCII control characters (below 032 or 20h) and those
     from 128 (80h) through 255 (FFh) display various graphic symbols. See
     the IBM Tech Ref Manual for details. 
      
     The emulated VT52 "terminal" also translates input from the IBM key-
     board. Most keypresses are returned to the Z80 program as single ASCII
     characters. The "extended" codes that are generated by IBM function
     keys, arrow keys, ALT keys, and so on, are translated into 2-byte
     keyboard sequences as follows: 

          The first byte is an ESCAPE character (Decimal 027, HEX 1Bh).                               ESCAPE

          The second byte is the keyboard scan code, as defined in the                                 keyboard scan code
          IBM Tech Ref Manual. 
      
     Additionally, the NUL extended code (CTRL-@) is translated into a                       NUL
     single ASCII character (Decimal 000). 
      
     For example, assume that the user presses the PgUp key on the IBM
     keyboard. The next time that the Z80 program calls the CP/M BIOS to read
     a keypress from the "terminal", an ESCAPE character will be returned.
     The time after that, a Decimal 073 (HEX 49h) will be returned. This is
     the scan code for the PgUp key. 
      
      
     The above information may be used to configure particular Z80 applica-
     tions for use with the Emulator's "terminal".  Remember that this
     emulated "terminal" only appears at the CP/M BIOS interface, unless you
     use the "terminal" command to alter this. Applications that do I/O via              terminal
     BDOS functions (which includes most of the standard CP/M utilities) do
     not see this behavior. 
      


COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 23
     THE CP/M ENVIRONMENT


     WORDSTAR, dBase II, Target Plannercalc  and PMATE, for example, do at
     least some of their terminal I/O via the CP/M BIOS, so they must be
     configured for the particular terminal being used. Refer to the above
     information when installing such applications for use under the Emula-
     tor, using this emulated VT52 "terminal". Please bear in mind, however,
     that things can get very confusing when one application (like dBase II)
     does terminal I/O via both the BIOS and the BDOS. Just experiment until
     you get something useful.

          NOTE: This emulated terminal facility may be controlled via
          the "terminal" builtin command, which is described in the               terminal
          "Builtin Commands" section.


      
     ^C and BREAK Handling      _____________________
      
     The ^C (Ctrl-C) and BREAK (Ctrl-Scroll Lock) keys are handled in a
     special way on the IBM PC. Under normal circumstances, these keypresses
     are trapped by PCDOS and cause the executing PCDOS program (in this
     case, the Emulator) to be aborted. 
      
     This is undesirable. 
      
     Additionally, CP/M includes an important assumption, to wit: ^C is a
     keypress like any other, and must be passed through all the way to the
     Z80 program for processing. Several standard CP/M programs (PIP.COM,
     M80.COM, WORDSTAR, etc) use ^C as a command, and must not be aborted                                                      must not
     when it is typed. 

     For this reason, the Emulator traps ^C and BREAK keypresses. It decides
     what to do with them as follows: 
      
          When not running a Z80 program (i.e. - when the Emulator is
               accepting commands), the BREAK key does nothing and the ^C
               keypress does various things depending on the mood of PCDOS. 
      
          When executing a Z80 program, pressing ^C causes a ^C character
               (Decimal 003) to be queued as keyboard input. Pressing BREAK
               causes the Z80 to be stopped (with an appropriate message),
               and a return to the Emulator awaiting your command.


     When the Emulator stops ("aborts") a Z80 program due to a BREAK key-
     press, it displays a message to that effect. It suspends the Z80 in
     perfect order, maintaining all registers, flags, etc. It then accepts
     Emulator commands. 
      

COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 24
     THE CP/M ENVIRONMENT


     At this point you may inspect registers, run another Z80 program, or
     whatever. You may also continue execution of the aborted program with
     the "go" command.           go
      
     This is a very powerful tool for debugging, which is not available with
     true (hardware) Z80 systems. You may in effect interrupt the Z80 at any                                                                         any
     point, actually pausing it between Z80 instructions. 
      
     This also maintains compatability with existing CP/M programs (like
     WORDSTAR) that want to read the ^C character.
      

          NOTE: When running PCDOS commands like type, dir, and so on                                                 type  dir
          from within the Emulator, the BREAK key may be unavailable to
          you. If you want to interrupt the output from such programs
          that are run "underneath" the Emulator, you may have to use
          the ^C key.
      
      
          
     Common PCDOS and CP/M File System      _________________________________
      
     The Emulator goes to great lengths to allow CP/M programs to read and
     write PCDOS files. Thus the PCDOS file system serves as a common
     environment for both PCDOS and CP/M files. This allows you to use your
     favorite IBM PC editor, for example, to edit source files that are then
     compiled within CP/M (using the Emulator) with ASM.COM, M80.COM,
     F80.COM, or whatever. 
      
     CP/M's "User Number" concept, however, is primitive compared to the
     directory structure available with PCDOS. So although the emulated BDOS
     supports the setting of a user number, the user number is ignored by the
     Emulator when it comes time to actually access files. 
      
     Likewise, the concept of a Read-Only disk drive is not necessary under
     the Emulator. And the fatal CP/M flaw that crops up when you change
     disks and forget to type ^C to Warm Boot the system has been virtually
     eliminated by PCDOS. 


     CP/M and its CCP (or lack of same)      __________________________________
      
     One thing that we did in order to achieve such a large TPA size (65022
     bytes) and such fast emulation was remove the console command part of
     CP/M (the Console Command Processor, or CCP) from the CP/M Segment. In
     fact, we did away with CP/M entirely. 
      


COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 25
     THE CP/M ENVIRONMENT


     The CCP is the part of a normal CP/M system which accepts commands from
     the user and processes them. The Digital Research CCP that comes with
     CP/M 2.2 is fairly limited in its power. 
      
     In the Emulator, it is the main Z80MU 'C'-language program which
     contains all of the functions of CP/M's CCP, and does a whole lot more.
     In fact, it is this program which emulates all of CP/M (with a lot of
     help from PCDOS). 

     For this reason, there are certain CP/M enhancements (like ZCPR) which
     will have a whole lot of trouble working under the Emulator. The good
     news is that they are largely irrelevant under the Emulator, as the
     Emulator itself provides a powerful increase in console power even
     without ZCPR. 
      
     So if you have dreams of running ZCPR (or any CP/M enhancement which
     counts on patching CP/M), you ought to forget about it. When using the
     Emulator, there's no CP/M for such programs to patch. It's all fakeware,
     invisible to Z80 programs. 
      
     Stick with CP/M programs which interact with the outside world via the
     standard, unmodified BIOS and BDOS interfaces. 
      
      

     CP/M 2.2 BIOS and BDOS Emulation      ________________________________
      
     The Emulator tries very hard to look to Z80 programs like CP/M version
     2.2, at least in terms of its BIOS calls and BDOS support functions.
     Most Z80 programs that are run under the Emulator will have no idea that
     they aren't being run on a Z80 machine running Digital Research's CP/M.
      
     There are some hardware-specific aspects of CP/M, however, that make no
     sense on a PCDOS system. 
      
     Many CP/M BIOS calls, for example, deal with the physical layout and
     operation of the floppy disk. Some of these are ignored. Others cause a
     fault of the Z80 program, with the display of a message to the effect
     that the program invoked an unsupported BIOS call. 
      
     There are a few BDOS functions which likewise are irrelevant, and which
     cause the Z80 program to be aborted. 
      
     The following is a list of the various BIOS calls that are supported by
     CP/M 2.2, and their effects under the Emulator. Calls that are marked
     "unsupported" cause the Z80 program to be aborted.



     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 26
     THE CP/M ENVIRONMENT


     The addresses listed are absolute addresses within the CP/M Segment.
     Note that when the CP/M segment is Cold Booted, CP/M's location zero is
     set to JMP BIOS+3 (FF03h - the Warm Boot vector). The only safe way for                                                                safe
     a Z80 program to locate this BIOS jump table in any CP/M system (not
     just the Emulator) is to look at address 0001 within CP/M's memory.

          BIOS          BIOS
          Address          Address   Function                     Function

          FF00h     Cold Start CP/M segment
          FF03h     Warm Start CP/M segment 
          FF06h     Set A-reg to FFh if Emulated VT52 Terminal has keypress
                         to be read, 00h if not
          FF09h     Get keypress from Emulated VT52 Terminal to A-reg, via
                         IBM's ROM BIOS 
          FF0Ch     Output C-reg to Emulated VT52 Terminal via IBM's ROM BIOS
          FF0Fh     Output C-reg to LPT1: via IBM's ROM BIOS
          FF12h     Output C-reg to COM1: via IBM's ROM BIOS 
          FF15h     Get char from COM1: to A-reg via IBM's ROM BIOS 
          FF18h     Home Disk (unsupported) 
          FF1Bh     Select Disk (unsupported) 
          FF1Eh     Set Track (unsupported) 
          FF21h     Set Sector (unsupported) 
          FF24h     Set DMA address (unsupported) 
          FF27h     Read Sector (unsupported) 
          FF2Ah     Write Sector (unsupported) 
          FF2Dh     Set A-reg to FFh if LPT1: ready for output, 00h if not,
                         as reported by IBM's ROM BIOS
          FF30h     Sector Translate (unsupported) 
       
      
     Similarly, here is a table of the various BDOS functions (in Decimal/-
     HEX), and their actions under the Emulator. Note that a CP/M BDOS
     function is invoked by loading the function number into C-reg, and
     doing a CALL 0005h. See standard CP/M documentation for detailed
     calling conventions.

          BDOS          BDOS
          Function          Function  Action                    Action
      
          00/00h    Warm Boot. Returns to accept more Emulator commands. Does
                         not alter memory in the CP/M Segment.                          not
          01/01h    Read char from PCDOS standard input to A-reg. 
          02/02h    Send E-reg to PCDOS standard output. 
          03/03h    Read char from PCDOS AUX: device into A-reg. 
          04/04h    Send E-reg to PCDOS AUX: device 
          05/05h    Send E-reg to PCDOS PRN device 


     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 27
     THE CP/M ENVIRONMENT


          06/06h    If E-reg on entry = FFh, then return in A-reg next char
                         from PCDOS standard input, or 00h if none available
                         at this instant. 
                    If E-reg on entry <> FFh, then send E-reg to PCDOS
                         standard output. 
          07/07h    Get IOBYTE to A-reg. 
          08/08h    Store E-reg into IOBYTE. 
          09/09h    Output string at (DE) to PCDOS standard output. 
          10/0Ah    Input line from PCDOS standard input to (DE). See Note 1
                         below. 
          11/0Bh    Set A-reg to FFh if char from PCDOS standard input is
                         ready to be read, or 00h if not. 
          12/0Ch    Return CP/M version to HL. Sets reg L to 22h (for CP/M
                         version 2.2), and reg H to 00h.
          13/0Dh    Reset disk system. Sets DMA to 80h. Does not change                                                             not
                         selected drive to A: (like CP/M does), as this is
                         not necessary with PCDOS. 
          14/0Eh    Set default drive to E-reg. 
          15/0Fh    Open file whose FCB is at (DE). Sets A-reg to 00h if
                         successful, else to FFh. 
          16/10h    Close file whose FCB is at (DE).  Sets A-reg to 00h if
                         successful, else to FFh. 
          17/11h    Search for first file that matches pattern in FCB at
                         (DE).  Sets A-reg to 00h if successful, else to FFh.
          18/12h    Search for next file that matches last pattern used. 
                         Sets A-reg to 00h if successful, else to FFh. 
          19/13h    Delete file(s) represented by FCB is at (DE).  Sets A-reg
                         to 00h if successful, else to FFh. 

          20/14h    Read next sequential record from file whose FCB is
                         at (DE). Sets A-reg to status as follows:
      
                         0 = successful 
                         1 = reading unwritten data (EOF) 
                         FFh = PCDOS returned error # 2: "No room in DTA for
                              record" 

                    Note that a short record is filled out by the Emulator
                         with ^Z (eof) characters. 










     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 28
     THE CP/M ENVIRONMENT


          21/15h    Write next sequential record to file whose FCB is at
                         (DE). Returns status in A-reg as follows: 
      
                         0 = successful 
                         5 = diskette full 
                         6 = PCDOS returned error # 2: "No room in DTA for
                              record" 
      
          22/16h    Create (and open) file whose FCB is at (DE).  Sets A-reg
                         to 00h if successful, else to FFh. 
          23/17h    Rename file(s) per special FCB at (DE).  Sets A-reg to
                         00h if successful, else to FFh. 
          24/18h    Return login vector (bitmap of known disks) to HL. Calls
                         PCDOS to discover number of available drives. 
          25/19h    Return default drive number in A-reg. 
          26/1Ah    Set DMA to DE. 
          27/1Bh    Return allocation information (unsupported - aborts Z80
                         program). See Note 2 below. 
          28/1Ch    Write-protect drive (ignored). 
          29/1Dh    Return write-protect vector (bitmap of $R/O drives) to
                         HL. Sets HL to zero (nobody's write-protected).
          30/1Eh    Set file attributes (ignored, but returns A-reg of 00h to
                         indicate success). 
          31/1Fh    Return physical disk information (unsupported - aborts
                         Z80 program). See Note 2 below. 

          32/20h    If E-reg on entry is FFh, then current user number is
                         returned in A-reg. 
      
                    If E-reg on entry <> FFh, then current user number is set
                         to E-reg MOD 32. 
      
                    This only updates the byte at CP/M address 4. The
                         Emulator ignores this byte when accessing files. 
      
          33/21h    Read random record from file whose FCB is at (DE).
                         Returns A-reg status as follows: 

                         0 = successful 
                         1 = reading unwritten data 
                         3 = (CP/M "Cannot close current extent" error):
                              PCDOS returned error # 2: "No space in DTA for
                              record" 
      
                    Note that a partial record is filled out by the Emulator
                         with ^Z (eof) characters. 
      


COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 29
     THE CP/M ENVIRONMENT


          34/22h    Write random record to file whose FCB is at (DE). Returns
                         A-reg status as follows: 
      
                         0 = successful 
                         3 = (CP/M "Cannot close current extent" error):
                              PCDOS returned error # 2: "No space in DTA for
                              record" 
                         5 = (CP/M "Directory Overflow" error): Diskette full

      
          35/23h    Compute file size for file whose FCB is at (DE). Result
                         goes into random record field of FCB. 
          36/24h    Set random record field per FCB at (DE). 
          37/25h    Reset drive (accepted but ignored) 
          38/26h    (unsupported - aborts Z80 program) 
          39/27h    (unsupported - aborts Z80 program) 
          40/28h    Write random record with zero fill. In the Emulator, this
                         is translated to a function 34/22h (above). 

          NOTE 1: Function 10/0Ah is now done manually by the Z80
          engine, instead of calling PCDOS. It now works much more like
          CP/M, except that ^R, ^E, ^U are data characters instead of
          editing controls.

          NOTE 2: If someone will kindly provide us with a coherent
          writeup of the disk parameter block and allocation information
          as returned by BDOS functions 31/1Fh and 27/1Bh above, then
          we will gladly emulate these functions in the next release.

      
     In CP/M the BDOS routines call the BIOS routines. This is not true in
     the Emulator. The Emulator's BDOS functions in general invoke the
     corresponding PCDOS functions, and the Emulator's BIOS routines call the
     IBM PC ROM BIOS routines. The "terminal" builtin command (q.v.) controls                                    terminal
     what actually happens, at least as far as CP/M's console character BDOS
     and BIOS requests are concerned.













     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 30
     EMULATOR BUILTIN COMMANDS













                                BUILTIN COMMANDS                                 BUILTIN COMMANDS                                                  

     This section describes those commands that are recognized and acted
     upon by the Emulator itself. Such commands do not involve a search of
     the disk for a corresponding .COM file, since the Emulator recognizes
     them as special commands which are to be handled within the Emulator
     itself. This process is roughly equivalent to the handling of CP/M's CCP
     commands.


     Command Name Conflicts     ______________________

     You may have a .COM (Z80 command) file that has the same name as one of
     these Builtin Commands. How do you tell the Emulator to run your .COM
     file, instead of doing its corresponding Builtin Command? All that you
     have to do is convince the Emulator that your command is indeed a disk
     file. This can be done by including a drive ID or pathname as part of
     your command:

          Z80 A>a:dump foobar.asc                a:dump foobar.asc
          Z80 A>b:\bin\dump foobar.asc                b:\bin\dump foobar.asc
          Z80 A>\mystuff\dump foobar.asc                \mystuff\dump foobar.asc

     Alternatively, you may want to rename your .COM file so that it no
     longer conflicts with an Emulator Builtin Command name.



     Numeric Arguments      _________________
      
     Some Builtin Commands accept numeric arguments. These may represent
     addresses to be dumped, the number of pages to save, or whatever.                     dump                           save
      
     A numeric argument may be entered in any of several ways: 
      
          As a HEX number. No prefix is required in this case, as this is
               the default numeric radix. 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 31
     EMULATOR BUILTIN COMMANDS


      
               Examples: ffff  0  7F  -5  +3FF 

          As a decimal number, prefixed by a period ("."). 

               Examples: .10  .0  -.1  +.256  .65022 
      
          As a binary number, prefixed with the percent sign ("%"). 

               Examples: %0  %1010101011110000  -%1 
      
          As an ASCII character, prefixed by the apostrophe ("'"). 

               Examples: 'A  '"  '0  -'Z
      
          As an ASCII escape sequence, prefixed by an apostrophe and back-
               slash ("'\"). 

               Examples: 

                    '\\            (single "\" char) 
                    '\0            (NUL byte) 
                    '\b or '\B     (Backspace char) 
                    '\t or '\T     (TAB char) 
                    '\n or '\N     (LINEFEED char) 
                    '\r or '\R     (CARRIAGE RETURN char) 
                    '\'            (single apostrophe ("'") char) 
                    '\"            (single double-quote char ) 
                    '\xFF or '\XFF (byte with HEX value of FF) 
      
          As a label which has been defined with the "label" builtin command.                                                      label

               Examples: fcb1  program_start  BDOS  -reserved 
      
          As two or more of the above entries, connected with "+" or "-"
               operators. 

               Examples: 

                    fcb1+5 
                    program_end-table_length 
                    'A-40+'a 
                    table-5+offset 
      
      




COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 32
     EMULATOR BUILTIN COMMANDS



     The Builtin Commands are presented by functional grouping:

          - The PCDOS pass-through command prefix
          - CP/M Builtins that are emulated
          - Emulator Builtins that are similar to CP/M's
          - General Emulator commands
          - Emulator DEBUG commands
          - CP/M Environment and file control commands
          - RESOURCE commands







































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 33
     BUILTIN COMMANDS: PCDOS PASS-THROUGH


      
     Builtin:     ________  !xxxxxx               !xxxxxx
      
     Passes command xxxxxx to PCDOS. This gives you a way to use the usual
     PCDOS utilities from within the emulator, without having them interpret-
     ed as CP/M commands. Everything after the "!" character is passed as a
     command to PCDOS. 
      
     This command requires the reloading (by PCDOS) of the PCDOS COMMAND.COM
     file from disk. See the section on "The PCDOS Environment" for more
     detail on this subject. 
      
     Since PCDOS handles the command (and any command arguments that may be
     present), the standard PCDOS "PATH" environment string may apply. So may
     all other PCDOS conventions, like I/O redirection, wildcards, PCDOS
     device names, etc. 
      
     The given command is executed above the Emulator's memory. This implies
     that there had better be enough memory available above the Emulator to
     run the given command. 
      
     You may use this facility to "drop into" PCDOS for a while (perhaps to
     use a PCDOS screen editor on a CP/M source file), and then return to the
     Emulator. Use "!command" to drop into DOS, and "exit" to leave PCDOS and                    !command                         exit
     return to the Emulator. Make sure that COMMAND.COM is in your PCDOS PATH
     search list if you want to try this.
      
     This is also the primary way to take advantage of PCDOS's directory
     structure while within CP/M. You may issue "CHDIR", "MKDIR", and other
     directory-related commands directly to PCDOS. The effect of such
     commands carries over to the Emulator. 


















     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 34
     BUILTIN COMMANDS: PCDOS PASS-THROUGH



     Example (from an actual session):
      
          Z80 A>!cd \foo                 !cd \foo
          Z80 A>!cd \                 !cd \
          Z80 A>!rd \foo                !rd \foo
          Z80 A>!chkdsk b:                 !chkdsk b:
      
      
             362496 bytes total disk space 
               1024 bytes in 1 directories 
             272384 bytes in 10 user files 
              89088 bytes available on disk 
      
             423936 bytes total memory 
             152384 bytes free 
      
          Z80 A>!md foo                 !md foo
          Z80 A>!cd foo                 !cd foo
          Z80 A>stat *.*                 stat *.*
      
      
               Volume in drive A has no label 
               Directory of  A:\foo 
      
               .         <DIR>     11-19-85   1:15a 
               ..        <DIR>     11-19-85   1:15a 
               2 File(s)    144384 bytes free 
      
          Z80 A>!command                 !command
       
      
          The IBM Personal Computer DOS 
          Version 2.00 (C)Copyright IBM Corp 1981, 1982, 1983 
      
          Tue 11-19-1985 1:16:00.18 
          A:>chkdsk              chkdsk
      
      
             362496 bytes total disk space 
               1024 bytes in 1 directories 
             217088 bytes in 17 user files 
             144384 bytes available on disk 
      
             423936 bytes total memory 
             149264 bytes free 
      
      

COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 35
     BUILTIN COMMANDS: PCDOS PASS-THROUGH


          Tue 11-19-1985 1:16:16.17 
          A:>exit              exit

          Z80 A>!format a:                 !format a:













































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 36
     BUILTIN COMMANDS: EMULATED CP/M BUILTIN'S


      
     Builtin:     ________  d:                d:

          Changes the default disk drive to the drive whose letter name is
     represented by the "d" character. The command prompt will change to

          Z80 d>

     to reflect the new default. Drive d's current PCDOS directory will
     then be the first directory searched for Z80 command (.COM) files,
     unless explicitly overridden by a drive prefix or pathname. Data files
     that are created will default to that drive and its current directory.
     Data files that are read will be searched for only in that drive and
     directory, unless explicitly overridden by the Z80 program. 
      
     Example (from an actual session): 

          Z80 A>stat b:*.*                 stat b:*.*
      
      
                Volume in drive B has no label 
                Directory of  B:\ 
      
               WORDSTAR     <DIR>     11-02-85   4:19a 
                    1 File(s)     89088 bytes free 
      
          Z80 A>dir b:\wordstar\ws*.*                 dir b:\wordstar\ws*.*
      
      
                Volume in drive B has no label 
                Directory of  B:\wordstar 
      
               WSMSGS   OVR   27904  11-06-85   6:27p 
               WSOVLY1  OVR   34048  11-06-85   6:30p 
               WSU      COM   15872  11-06-85   6:32p 
               WS       COM   15872  11-06-85   6:37p 
                    4 File(s)     89088 bytes free 
      
          Z80 A>b:                 b:
      
          Z80 B>dir                 dir
      
      
                Volume in drive B has no label 
                Directory of  B:\ 
      
               WORDSTAR     <DIR>     11-02-85   4:19a 
                    1 File(s)     89088 bytes free 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 37
     BUILTIN COMMANDS: EMULATED CP/M BUILTIN'S


      
          Z80 B>stat a:\*.exe                 stat a:\*.exe
      
      
                Volume in drive A has no label 
                Directory of  A:\ 
      
               Z80MU    EXE   94976  11-18-85   3:31p 
                    1 File(s)    142336 bytes free 
      







































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 38
     BUILTIN COMMANDS: EMULATED CP/M BUILTIN'S


      
     Builtin:  del <pattern>                del <pattern>      ________
               era <pattern>                era <pattern> 
               delete <pattern>                delete <pattern> 
               erase <pattern>                erase <pattern>

     These are identical commands. All cause the invocation of the PCDOS
     "DEL" command to delete files that match <pattern>. 

     See the PCDOS manual for details of <pattern>. 

     We have created several synonyms for the same command in order to make
     life easier for CP/M folks who are used to saying "ERA", and PCDOS
     folks who are used to saying "DEL" or whatever. 

     These commands cause PCDOS to reload COMMAND.COM, so see "The PCDOS
     Environment" section for further detail on that subject. 

     Example:
      
          Z80 A>erase b:*.asm                 erase b:*.asm
          Z80 A>del *.*                 del *.*
               Are you sure? y                              y
          Z80 A>delete c:\backup\foo.*                 delete c:\backup\foo.*
          Z80 A>era foo.asm                era foo.asm
























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 39
     BUILTIN COMMANDS: EMULATED CP/M BUILTIN'S


      
     Builtin:  dir <pattern>                dir <pattern>      ________
               stat <pattern>                stat <pattern>
      
     Shows a directory of files matching <pattern>. This invokes the PCDOS
     "DIR" command, so remember about COMMAND.COM (see "The PCDOS Environ-
     ment" section). 

     <pattern> is passed directly to PCDOS. So see the PCDOS manual if you
     want to know what's legal.
      
     The CP/M STAT command (STAT.COM) cannot be emulated, because the
     first thing that Digital Research's STAT.COM does is invoke a hardware-
     specific CP/M function that means nothing on the IBM PC, and is there-
     fore illegal within the Emulator. But the most common function of
     STAT.COM - displaying filenames and file sizes with "STAT *.*" or
     whatever - can be done with PCDOS's "DIR" command. So STAT and DIR have
     been made to do the same thing. If you're used to typing "STAT *.*" in
     CP/M, then you'll be able to do the same thing under the Emulator. 

     Example (from an actual session):

          Z80 A>stat b:*.*                 stat b:*.*
      
      
                Volume in drive B has no label 
                Directory of  B:\ 
      
               WORDSTAR     <DIR>     11-02-85   4:19a 
                    1 File(s)     89088 bytes free 
      
          Z80 A>dir b:\wordstar\ws*.*                 dir b:\wordstar\ws*.*
      
      
                Volume in drive B has no label 
                Directory of  B:\wordstar 
      
               WSMSGS   OVR   27904  11-06-85   6:27p 
               WSOVLY1  OVR   34048  11-06-85   6:30p 
               WSU      COM   15872  11-06-85   6:32p 
               WS       COM   15872  11-06-85   6:37p 
                    4 File(s)     89088 bytes free 
      
          Z80 A>b:                 b:
      
          Z80 B>dir                 dir
      
      

COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 40
     BUILTIN COMMANDS: EMULATED CP/M BUILTIN'S


                Volume in drive B has no label 
                Directory of  B:\ 
      
               WORDSTAR     <DIR>     11-02-85   4:19a 
                    1 File(s)     89088 bytes free 
      
          Z80 B>stat a:\*.exe                 stat a:\*.exe
      
      
                Volume in drive A has no label 
                Directory of  A:\ 
      
               Z80MU    EXE   94976  11-18-85   3:31p 
                    1 File(s)    142336 bytes free 



































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 41
     BUILTIN COMMANDS: EMULATED CP/M BUILTIN'S



     Builtin:  type <filename.typ>                type <filename.typ>      ________
               ty <filename.typ>                ty <filename.typ>
      
     This command is the equivalent of the CP/M "TYPE" command. The specified
     file is displayed on the standard output (normally the screen). 
      
     The display may be paused with either the CP/M convention of ^S/^Q or
     the PCDOS convention of CTRL-NUMLOCK. It may be aborted with ^C or
     CTRL-BREAK. 

     This command causes PCDOS to reload COMMAND.COM, so see "The PCDOS
     Environment" section for further detail on that subject. 
      
     Example: 

          Z80 A>ty b:foo.asm                 ty b:foo.asm
          Z80 A>type \source\backup\foo.doc                 type \source\backup\foo.doc
          Z80 A>ty ctest.err                 ty ctest.err






























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 42
     BUILTIN COMMANDS: SIMILAR TO CP/M'S



     Builtin:  rename <oldpath> <newpath>                rename <oldpath> <newpath>      ________
               ren <oldpath> <newpath>                ren <oldpath> <newpath>
      
     Renames the file specified by <oldpath> to the name given by <newpath>.

          NOTE: This is not the same syntax used by the CP/M equivalent,                        not
          which is "REN <newname>=<oldname>". 
      
     This command causes PCDOS to reload COMMAND.COM, so see "The PCDOS
     Environment" section for further detail on that subject. 
      
     This command invokes the PCDOS "RENAME" command. See the PCDOS manual
     for details.

     Example: 

          Z80 A>rename dbase.exe dbase.xxx                 rename dbase.exe dbase.xxx































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 43
     BUILTIN COMMANDS: SIMILAR TO CP/M'S



     Builtin:  save n <filename.typ>                save n <filename.typ>      ________
               sa n <filename.typ>                sa n <filename.typ>
      
     Saves n 256-byte pages of CP/M memory (starting at address 0100h) to the
     specified file. The data written to the file is a simple memory image.
     No translation is done, even if a .HEX extension is given in the
     filename. If you want to write a true Intel HEX file, use the write                                                                   write
     Builtin. 
      
          NOTE: This is close to the CP/M equivalent, except that the
          default radix for n is HEX, not decimal as with CP/M. 
      
     Example (from an actual session):

          Z80 A>save 3 820init2.com                 save 3 820init2.com
      
               Writing 3 pages (768 bytes) to file '820INIT2.COM' 
      
          Z80 A>save 0 continue.com                 save 0 continue.com
      
               Writing 0 pages (0 bytes) to file 'CONTINUE.COM' 



























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 44
     BUILTIN COMMANDS: SIMILAR TO CP/M'S



     Builtin:  copy <from_pattern> <to_path>                copy <from_pattern> <to_path>      ________
               co <from_pattern> <to_path>                co <from_pattern> <to_path>
      
     Copies the file(s) specified by <from_pattern> to the file or directory
     specified by <to_path>. 
      
     This command invokes the PCDOS "COPY" command, so see the PCDOS manual
     for details as to what's legal. 
      
     It also causes PCDOS to reload COMMAND.COM, so see "The PCDOS Environ-
     ment" section for further detail on that subject. 
      
     This command is roughly equivalent to CP/M's "PIP <outfile>=<infile>".
     You have the additional power of PCDOS's directory and device name
     support, however. 
      
     Example:

          Z80 A>copy *.* B:                 copy *.* B:
          Z80 A>co b:*.asm                 co b:*.asm
          Z80 A>copy \bin\*.* c:\backup                 copy \bin\*.* c:\backup
          Z80 A>copy *.asm combined.bak                 copy *.asm combined.bak
          Z80 A>co *.asm *.bak                 co *.asm *.bak
          Z80 A>co foo.asm lpt1:                 co foo.asm lpt1:
          Z80 A>co con autoexec.bat                co con autoexec.bat























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 45
     BUILTIN COMMANDS: GENERAL



     Builtin:  help [command]                help [command]     ________
               ? [command]                ? [command]
      
     Displays a brief description of the requested Builtin Command. 
      
     If no command name follows the "help" command, then a rather lengthy                                     help
     explanation of all commands is displayed. If you press the SPACE bar,
     this long listing will be interrupted at the next logical break.

     The listing can be paused with ^S/^Q, or CTRL-NumLock. You can turn
     printer copying on before the listing starts (which is recommended) with
     ^P or CTRL-PrtSc.
      
     Example:
      
          Z80 A>help xreg                 help xreg
          Z80 A>? list                 ? list
          Z80 A>?                 ?
          Z80 A>help ?                help ?
          Z80 A>help b:                help b:
          Z80 A>help !                help !



























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 46
     BUILTIN COMMANDS: GENERAL


      
     Builtin:  illop [fault | nop]                illop [fault | nop]      ________
               i [fault | nop]                i [fault | nop]
      
     Specifies how the Emulator is to handle illegal Z80 opcodes. 
      
     If "illop fault" is entered, then an illegal Z80 opcode will cause a Z80         illop fault
     fault, meaning that the Emulator will stop executing the Z80 program and
     will display an error message to the effect that an illegal opcode was
     encountered at such-and-such and address. 

     If "illop nop" is entered, then an illegal Z80 opcode will simply be         illop nop
     ignored. This is closer to true Z80 operation. Execution will continue
     with the next Z80 instruction after the illegal opcode. 
      
     If only "illop" is entered, then the Emulator simply reports how it is              illop
     currently handling illegal opcodes. 

     Example (from an actual session):
      
          Z80 A>i                 i
      
               Illegal opcodes will act as NOP's 

          Z80 A>illop fault                 illop fault
      
               Illegal opcodes will FAULT 

          Z80 A>illop nop                 illop nop
      
               Illegal opcodes will act as NOP's 


















     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 47
     BUILTIN COMMANDS: GENERAL



     Builtin:  exit                exit      ________
               e                e
      
     Exits the Emulator, and returns to PCDOS. 
      
     Due to certain limitations within PCDOS, you should not remove any
     floppy disks that are being used until you have exited the Emulator via
     this command, unless you know that the Z80 programs which you have run                              know
     have truly closed any files that have been written to. 

     We have used the Emulator extensively, and have frequently changed
     floppies while within the Emulator. We have never experienced corrupted
     floppy data. But then, we use only "safe" CP/M software like ASM.COM,
     M80.COM, L80.COM, and so on. Such programs are very good about closing
     files when they exit. 
      
     This warning is included not because it has ever happened to us, but
     because we wrote the code, and we know about certain "windows" within
     which a faulting CP/M program could conceivably confuse PCDOS into
     writing one floppy's data to another floppy, destroying the second
     floppy's file data and perhaps even its FAT (File Allocation Table). 
      
     Example: 
          Z80 A>exit                 exit
          A> 























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 48
     BUILTIN COMMANDS: GENERAL



     Builtin:  speed?                speed?      ________
               howfast?                howfast?
      
     Calculates the effective speed of the imaginary Z80 that exists within
     the Emulator. 

     In response to this command, a sample Z80 program is loaded into the
     CP/M segment. It is run, and its execution is timed. This program takes
     up to half a minute to run on a simple IBM PC with an 8088, and corres-
     pondingly less time on faster machines (i.e. - a PC with a NEC V20 chip,
     an IBM PC/AT, etc). 
      
     The effective clock speed is displayed at the end of the test. 
      
     The reported speed should be taken with a grain of salt. What it means
     is that if you had a real Z80 running the exact instruction mix found in
     the test program, then that real Z80 would have to run at the reported
     clock speed in order to perform as fast (or slow) as the Emulator's
     imaginary Z80. 

     For example, assume that the reported effective clock is 250,000 Hz.
     This means that the imaginary Z80 in the Emulator is running the test
     program at one fourth the speed of a 1 MegaHertz Z80 (as found on a
     Microsoft SoftCard in an Apple, for example), one eighth the speed of a
     2 MegaHertz Z80, etc. 
      
     Does this mean that your CP/M programs run under the Emulator will run
     at one fourth the speed of an Apple with a SoftCard? Not necessarily.
     The reported speed is for CPU-bound (no I/O) operation, of the exact mix
     of instructions found in the test program. Real CP/M programs tend to
     have a mix of CPU and I/O operations. I/O operations to disk are handled
     as fast as the IBM PC can do them. They aren't emulated, they are done.                                                                       done
     And CP/M programs whose CPU-bound operations involve a lot of register-
     to-register operations will be emulated faster than those requiring a
     lot of memory accesses. 
      
     It's a complicated relationship. Our experience has been that ASM.COM,
     for example, runs about 1/5th the speed under the Emulator on a stock,
     floppy-based IBM PC than it does on an Apple with a SoftCard and 1
     MegaHertz Z80. Target PlannerCalc (a spreadsheet program) runs about
     1/2 speed. The addition of a NEC V20 processor to the IBM PC improves
     the speed of the Emulator. So does using a hard disk instead of flop-
     pies. And moving the Emulator to a Compaq DeskPro 286 brings emulated
     performance close to that of a 1 MegaHertz Z80. 




     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 49
     BUILTIN COMMANDS: GENERAL


          NOTE: This command causes a Cold Boot of the CP/M segment.
          This destroys any CP/M program that you may have had in
          memory. 
      
     Example (from an actual session):
      
          Z80 A>speed?                 speed?
      
               *** CP/M Segment COLDBOOTED *** 
      
               Beginning Z80 timing test. Please wait... 
      
               Effective Z80 clock speed is 248101 Hz 
      
               *** CP/M Segment COLDBOOTED *** 


































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 50
     BUILTIN COMMANDS: DEBUG SUPPORT


      
     Builtin:  btrace [ SOME | ALL ]                btrace [ SOME | ALL ]      ________
               bt [ SOME | ALL ]                bt [ SOME | ALL ]
      
     Displays the current BDOS Trace Table (if no arguments are present), or
     controls the BDOS functions that will be traced. 

     As a CP/M program is run, the various BDOS calls that it makes are
     traced. This command displays the trace table as it has been left by the
     last CP/M program run. 
      
     Items reported include: 
      
          1) The logical sequence number. 
          2) The Program Counter of the CALL to the BDOS. 
          3) The contents of the Z80 DE register at the entry to the BDOS
               handler. 
          4) The DMA address in effect at the instant of this BDOS call. 
          5) The BDOS function # (as passed in the Z80 C-reg) and a text
               description of the function being performed.
      
     The BDOS Trace Table is cleared by a COLD BOOT, by the load of a new
     CP/M program, and at various other times when it seems logical to clear
     it out. 

     If an argument (either "SOME" or "ALL") is present, then the trace                             SOME      ALL
     table is not displayed. Instead, the Emulator adjusts (according to the
     argument) the way that future traces will be made:

          If "SOME" is specified, then the Console Status, Console              SOME
          Output, Direct Console I/O, and List Output BDOS functions
          will not be traced. This can help to keep the BDOS Trace Table
          from filling up with unimportant entries.

          If "ALL" is specified, then even these console character BDOS              ALL
          functions will be traced.













     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 51
     BUILTIN COMMANDS: DEBUG SUPPORT


     Example (from an actual run of DUMP.COM): 

          Z80 A>btrace all                 btrace all
      
          Future BDOS traces will include console character functions

          Z80 A>a:dump dump.com                a:dump dump.com

          0000 21 00 00 39 22 15 02 31 57 02 CD C1 01 FE FF C2 
          0010 1B 01 11 F3 01 CD 9C 01 C3 51 01 3E 80 32 13 02 
          0020 21 00 00 E5 CD A2 01 E1 DA 51 01 47 7D E6 0F C2 
          ...
          ...  (Much of DUMP.COM output deleted for brevity)
          ...
          0150 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 
          0160 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 
          0170 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 
      
          Z80 A>bt                 bt
      
          BDOS TRACE TABLE: 
          SEQ#  Z80PC  Z80DE Z80DMA FUNCTION 
          ----- -----  ----- ------ ---------------- 
            006 016BH  0030H  0080H 02H Console Output from E-reg = 0 
            007 016BH  0030H  0080H 02H Console Output from E-reg = 0 
            008 016BH  0020H  0080H 02H Console Output from E-reg = 

          ...
          ...  (Many entries deleted for brevity)
          ...

           049 016BH  0030H  0080H 02H Console Output from E-reg = 0 
           050 01D6H  005CH  0080H 14H Read File (Sequential), FCB at (DE)
           051 016BH  000DH  0080H 02H Console Output from E-reg = ^M
           052 016BH  000AH  0080H 02H Console Output from E-reg = ^J
           244 016BH  0020H  0080H 02H Console Output from E-reg = 
           245 016BH  0030H  0080H 02H Console Output from E-reg = 0 
           246 016BH  0030H  0080H 02H Console Output from E-reg = 0 
           247 016BH  0020H  0080H 02H Console Output from E-reg = 
           248 016BH  0030H  0080H 02H Console Output from E-reg = 0 
           249 016BH  0030H  0080H 02H Console Output from E-reg = 0 
           250 016BH  000DH  0080H 02H Console Output from E-reg = ^M
           251 016BH  000AH  0080H 02H Console Output from E-reg = ^J
           252 015EH  0070H  0080H 0BH Get Console Status to A-reg 
           253 016BH  0030H  0080H 02H Console Output from E-reg = 0 
           254 016BH  0031H  0080H 02H Console Output from E-reg = 1 
           255 016BH  0037H  0080H 02H Console Output from E-reg = 7 
           001 016BH  0030H  0080H 02H Console Output from E-reg = 0 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 52
     BUILTIN COMMANDS: DEBUG SUPPORT


           002 016BH  0020H  0080H 02H Console Output from E-reg = 
           003 016BH  0030H  0080H 02H Console Output from E-reg = 0 
           004 016BH  0030H  0080H 02H Console Output from E-reg = 0 
           005 016BH  0020H  0080H 02H Console Output from E-reg = 
          -- END OF BDOS TRACE TABLE -- 












































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 53
     BUILTIN COMMANDS: DEBUG SUPPORT



     Builtin:  break                break      ________
               break clear [n [n...]]                break clear [n [n...]] 
               break set n [n...]                break set n [n...] 
               b                b 
               b clear [n [n...]]                b clear [n [n...]] 
               b set n [n...]                b set n [n...]
      
     Manipulates the Breakpoint Table, which contains up to 50 Z80 addresses
     at which execution of the Z80 is to be halted, and control returned to
     the Emulator's command prompt. 
      
     Breakpoints are typically used in conjunction with the "read" and "go"                                                             read       go
     commands, and various other debug commands. 
      
     The Breakpoint Table is cleared when a new CP/M program is loaded, when
     the CP/M Segment is Cold Booted, and at various other times when it
     seems logical to clear it. 
      
     If only "break" is entered, then the current Breakpoint Table addresses              break
     are displayed. 
      
     If "break set" is entered followed by one or more Z80 addresses, then         break set
     the addresses following the command are added to the Table. 
      
     If only "break clear" is entered, then all active breakpoint addresses              break clear
     are removed. No execution breakpoints will occur. 
      
     If "break clear" is entered followed by one or more Z80 addresses, then         break clear
     only the specified addresses are removed from the Breakpoint Table. 
      
          NOTE: When a breakpoint is encountered during execution of the
          Z80 code, that breakpoint's address is automatically cleared
          from the table.















     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 54
     BUILTIN COMMANDS: DEBUG SUPPORT


     Example:

          Z80 A>break clear                 break clear
      
               0 Breakpoints cleared 

          Z80 A>b set startup startup+3 14f 210 221                 b set startup startup+3 14f 210 221
      
               5 Breakpoints set - 5 now in table 

          Z80 A>b clear 221                 b clear 221
      
               1 Breakpoints cleared, 4 left 

          Z80 A>b                 b
      
               Current Breakpoints: 
               0100H  0103H  014FH  0210H 
               4 Breakpoints currently set 

          Z80 A>b clear 210 startup                 b clear 210 startup
      
               2 Breakpoints cleared, 2 left 

          Z80 A>b                 b
      
               Current Breakpoints: 
               0103H  014FH 
               2 Breakpoints currently set 

          Z80 A>b clear                 b clear
      
               2 Breakpoints cleared 

          Z80 A>b                 b
      
               Current Breakpoints: 
               0 Breakpoints currently set 
      










COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 55
     BUILTIN COMMANDS: DEBUG SUPPORT


      
     Builtin:  dump [n1 [n2]]                dump [n1 [n2]]      ________
               d [n1 [n2]]                d [n1 [n2]]
      
     Dumps Z80 (CP/M) memory in HEX and ASCII.
      
     If n1 is given, then the first address dumped is n1. If no arguments are
     present, then the first address is the one following the last one
     done by a previous dump command.                         dump

     If n2 is given, then the dump continues through Z80 (CP/M) address n2.
     If n2 is not given, then n2 is assumed to be 255 bytes beyond the
     starting address. 
      
     A lengthy dump may be interrupted by pressing the SPACE bar. 
      
     Example (from an actual session):
      
          Z80 A>dump 100                 dump 100
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0100: 21 00 00 39 22 15 02 31  57 02 CD C1 01 FE FF C2 !..9"..1 W.MA.~.B
     0110: 1B 01 11 F3 01 CD 9C 01  C3 51 01 3E 80 32 13 02 ...s.M.. CQ.>.2..
     0120: 21 00 00 E5 CD A2 01 E1  DA 51 01 47 7D E6 0F C2 !..eM".a ZQ.G}f.B
     0130: 44 01 CD 72 01 CD 59 01  0F DA 51 01 7C CD 8F 01 D.Mr.MY. .ZQ.|M..
     0140: 7D CD 8F 01 23 3E 20 CD  65 01 78 CD 8F 01 C3 23 }M..#> M e.xM..C#
     0150: 01 CD 72 01 2A 15 02 F9  C9 E5 D5 C5 0E 0B CD 05 .Mr.*..y IeUE..M.
     0160: 00 C1 D1 E1 C9 E5 D5 C5  0E 02 5F CD 05 00 C1 D1 .AQaIeUE .._M..AQ
     0170: E1 C9 3E 0D CD 65 01 3E  0A CD 65 01 C9 E6 0F FE aI>.Me.> .Me.If.~
     0180: 0A D2 89 01 C6 30 C3 8B  01 C6 37 CD 65 01 C9 F5 .R..F0C. .F7Me.Iu
     0190: 0F 0F 0F 0F CD 7D 01 F1  CD 7D 01 C9 0E 09 CD 05 ....M}.q M}.I..M.
     01A0: 00 C9 3A 13 02 FE 80 C2  B3 01 CD CE 01 B7 CA B3 .I:..~.B 3.MN.7J3
     01B0: 01 37 C9 5F 16 00 3C 32  13 02 21 80 00 19 7E B7 .7I_..<2 ..!...~7
     01C0: C9 AF 32 7C 00 11 5C 00  0E 0F CD 05 00 C9 E5 D5 I/2|..\. ..M..IeU
     01D0: C5 11 5C 00 0E 14 CD 05  00 C1 D1 E1 C9 46 49 4C E.\...M. .AQaIFIL
     01E0: 45 20 44 55 4D 50 20 56  45 52 53 49 4F 4E 20 31 E DUMP V ERSION 1
     01F0: 2E 34 24 0D 0A 4E 4F 20  49 4E 50 55 54 20 46 49 .4$..NO  INPUT FI

          Z80 A>d primary_fcb secondary_fcb+.15                 d primary_fcb secondary_fcb+.15
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0050:                                      01 44 55 4D              .DUM
     0060: 50 20 20 20 20 43 4F 4D  00 00 80 00 80 01 00 00 P    COM ........
     0070: 6D 0B 1B BF 40 F3 00 00  00 F3 00 00             m..?@s.. .s.. 



     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 56
     BUILTIN COMMANDS: DEBUG SUPPORT



     Builtin:  go [n]                go [n]      ________
               g [n]                g [n]
      
      
     Begins execution of Z80 code at address n. If n is not specified, then
     the starting address defaults to the current Z80 Program Counter (PC).
      
     This is the usual way to run a program that has been read from disk. It                                                          read
     is also used to continue execution when the Z80 has been stopped via a
     breakpoint, or by the user pressing the BREAK key. 
      
          NOTE: A Z80 command (.COM) file that is invoked by typing
          its name is automatically run. It does not require this
          command in order to be executed. 
      
     Example: 
          Z80 A>go                 go
          Z80 A>g 100                 g 100
          Z80 A>g -.768                 g -.768
          Z80 A>go fixit5-3                 go fixit5-3




























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 57
     BUILTIN COMMANDS: DEBUG SUPPORT



     Builtin:  find n "text"               find n "text"     ________
               f n "text"                f n "text"
      
      
     Searches the CP/M Segment for the binary pattern represented by string
     "text". The search begins at Z80 address n, which is a numeric value as      text
     described at the start of this section. 

     The "text" string may (and usually does) include imbedded escape          text
     sequences, as follows:


               \\             (single "\" char) 
               \0             (NUL byte) 
               \b or \B       (Backspace char) 
               \t or \T       (TAB char) 
               \n or \N       (LINEFEED char) 
               \r or \R       (CARRIAGE RETURN char) 
               \'             (single apostrophe ("'") char) 
               \"             (single double-quote char ) 
               \xFF or \XFF   (byte with HEX value of FF) 
      

     The CP/M Segment address of each match is displayed as a four-digit HEX
     value. The search ends with CP/M Segment address 0FFFFh.

     Example (from an actual session): 

          Z80 A>patch 8000 "Joan Riff"                 patch 8000 "Joan Riff"
      
          Z80 A>find 100 "Joan"                 find 100 "Joan"
               8000H 

          Z80 A>f .256 "\xcd\x05\x00"                 f .256 "\xcd\x05\x00"
               015EH 016BH 019EH 01CAH 01D6H 













     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 58
     BUILTIN COMMANDS: DEBUG SUPPORT


      
     Builtin:  patch [n]               patch [n]     ________
               patch n "xxxx"                patch n "xxxx" 
               p [n]               p [n]
               p n "xxxx"                p n "xxxx"
      
     Either enters an interactive patch dialog which allows you to change
     CP/M memory a byte at a time, or else applies string patch "xxxx" to the                                                                 xxxx
     CP/M Segment and does not enter interactive patch mode. 
      
     If n (which is a numeric value as defined at the start of this section)
     is specified, then patching starts at address n. If n is not specified,
     then patching begins with next patch location (the one above the last
     location patched). Note that in the patch n "xxxx" format, numeric                                         patch n "xxxx"
     value n is required. 
      
     The interactive patch dialog consists of: 
      
          1) a prompt which shows the next address to be patched and its
          current contents.

          2) user responses. 
      
     User responses to the interactive patch prompt are as follows: 
      
          ?<return>  A question mark (followed by RETURN) to request a short          ?<return>
               help message showing available responses. 
      
          n<return> A standard numeric argument as described at the start          n<return>
               of this section. This is the byte value to be patched into the
               specified CP/M address. 
      
               NOTE: This may also be a 16-bit value. If the high-order
               byte of the resultant n is non-zero, then this is taken
               to be a 16-bit value, and fills 2 bytes.

          "xxx" A string of ASCII text, delimited by double-quote characters.          "xxx"
               The bytes of the string are patched into successive CP/M
               memory locations. The string may include ASCII escape se-
               quences as follows: 
      
               \\             (single "\" char) 
               \0             (NUL byte) 
               \b or \B       (Backspace char) 
               \t or \T       (TAB char) 
               \n or \N       (LINEFEED char) 
               \r or \R       (CARRIAGE RETURN char) 
               \'             (single apostrophe ("'") char) 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 59
     BUILTIN COMMANDS: DEBUG SUPPORT


               \"             (single double-quote char ) 
               \xFF or \XFF   (byte with HEX value of FF) 
      
      
          <space><return> to leave the addressed byte unchanged, and move to          <space><return>
               next one. 
      
          <return> to exit the interactive patch mode.           <return>
      
          ;xxx A comment (everything following the semicolon is ignored).          ;xxx

      
      
     Example (from an actual session):

          Z80 A>patch 400                 patch 400
      
      
          Enter '?' for help with PATCH entries 
      
      
          0400H (00H) = 'R                         'R
          0401H (00H) = 'I+20                         'I+20
          0402H (00H) = "ff\0"                         "ff\0"
          0405H (00H) = 
      
          Z80 A>d 400 40f                 d 400 40f
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0400: 52 69 66 66 00 00 00 00  00 00 00 00 00 00 00 00 Riff.... ........

          Z80 A>p primary_fcb "JoanRiff   "                 p primary_fcb "JoanRiff   "
      
          Z80 A>d primary_fcb secondary_fcb+.15                 d primary_fcb secondary_fcb+.15
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0050:                                      4A 6F 61 6E              Joan
     0060: 52 69 66 66 20 20 20 4D  00 00 80 00 80 01 00 00 Riff   M ........
     0070: 6D 0B 1B BF 40 F3 00 00  00 F3 00 00             m..?@s.. .s..  








     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 60
     BUILTIN COMMANDS: DEBUG SUPPORT



     Builtin:  xreg [rr n]                xreg [rr n]      ________
               x [rr n]                x [rr n]
      
     Sets Z80 register or flag rr to value n. 
      
     If no args are present, then the current Z80 register values and flags
     are displayed. 
      
     If args are present, then the register or flag represented by rr is set
     to the numeric value n (whose format is described at the beginning of
     this section). 
      
          NOTE: The Z80 has a primary and an alternate set of registers
          and flags. The alternate set is indicated by appending an
          apostrophe ("'") to the register or flag name. 
      
     The register or flag to be set (the rr argument) must be one of the
     following (in either upper or lowercase): 
      
          regs:     A    F    B    C    D    E    H    L 
                    A'   F'   B'   C'   D'   E'   H'   L' 
                    AF   BC   DE   HL 
                    AF'  BC'  DE'  HL' 
                    IX   IY   SP   PC 
                    IFF1 IFF2 IMF  I    R 
      
          flags:    SF   ZF   HF   P/V  NF   CF 
                    SF'  ZF'  HF'  P/V' NF'  CF' 
      
     Example (from an actual session):

          Z80 A>xreg pc 0                 xreg pc 0
      
          Z80 A>x                 x
      
          A F  B C  D E  H L  IX   IY   I  R  SP   PC   IFF1 IFF2 IMF
          0A01 000F 007F FEFC 0000 0000 00 00 FEFE 0000   0    0   0
          0000'0000'0000'0000'SF=0 ZF=0 HF=0 P/V=0 NF=0 CF=1 
          L0000:    C3 03 FF       JP   LFF03 
      
          Z80 A>xreg bc ffff                 xreg bc ffff
      






COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 61
     BUILTIN COMMANDS: DEBUG SUPPORT


          Z80 A>x                 x
      
          A F  B C  D E  H L  IX   IY   I  R  SP   PC   IFF1 IFF2 IMF
          0A01 FFFF 007F FEFC 0000 0000 00 00 FEFE 0000   0    0   0
          0000'0000'0000'0000'SF=0 ZF=0 HF=0 P/V=0 NF=0 CF=1 
          L0000:    C3 03 FF       JP   LFF03
      
          Z80 A>x c' 'A                 x c' 'A
      
          Z80 A>xreg de .256                 xreg de .256
      
          Z80 A>xreg AF' 55                 xreg AF' 55
      
          Z80 A>xreg                 xreg
      
          A F  B C  D E  H L  IX   IY   I  R  SP   PC   IFF1 IFF2 IMF
          0A01 FFFF 0100 FEFC 0000 0000 00 00 FEFE 0000   0    0   0 
          0055'0041'0000'0000'SF=0 ZF=0 HF=0 P/V=0 NF=0 CF=1 
          L0000:    C3 03 FF       JP   LFF03 
      





























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 62
     BUILTIN COMMANDS: DEBUG SUPPORT



     Builtin:  trace [n]                trace [n]      ________
               t [n]                t [n]
      
     Traces a certain number (specified by the n argument) of Z80 instruction
     executions, displaying Z80 regs and flags after each instruction's
     execution. 
      
     Execution begins at the current Z80 Program Counter (PC). 
      
     If no argument is given, then n defaults to 1. 
      
     The n argument is a numeric value as described at the beginning of this
     section. 

          NOTE: The PC of each executed instruction is saved in a
          circular buffer for later interpretation by the "pc?" builtin                                                           pc?
          command(q.v.).

     Example (from an actual trace of DDT.COM's opening lines): 

          Z80 A>read ddt.com                 read ddt.com
      
          *** Low = 0100H  Next = 1400H 
          *** Z80 DMA, PC and Stack automatically set for .COM file 

          Z80 A>t 4                 t 4
      
          A F  B C  D E  H L  IX   IY   I  R  SP   PC   IFF1 IFF2 IMF
          0A01 0FBC 0100 FEFC 0000 0000 00 00 FEFC 0103   0    0   0 
          0055'0041'0000'0000'SF=0 ZF=0 HF=0 P/V=0 NF=0 CF=1 
          L0103:    C3 3D 01       JP   L013D 
      
          A F  B C  D E  H L  IX   IY   I  R  SP   PC   IFF1 IFF2 IMF
          0A01 0FBC 0100 FEFC 0000 0000 00 00 FEFC 013D   0    0   0 
          0055'0041'0000'0000'SF=0 ZF=0 HF=0 P/V=0 NF=0 CF=1 
          L013D:    31 00 02       LD   SP,L0200 
      
          A F  B C  D E  H L  IX   IY   I  R  SP   PC   IFF1 IFF2 IMF
          0A01 0FBC 0100 FEFC 0000 0000 00 00 0200 0140   0    0   0 
          0055'0041'0000'0000'SF=0 ZF=0 HF=0 P/V=0 NF=0 CF=1 
          L0140:    C5             PUSH BC 
      
          A F  B C  D E  H L  IX   IY   I  R  SP   PC   IFF1 IFF2 IMF
          0A01 0FBC 0100 FEFC 0000 0000 00 00 01FE 0141   0    0   0 
          0055'0041'0000'0000'SF=0 ZF=0 HF=0 P/V=0 NF=0 CF=1 
          L0141:    C5             PUSH BC 


     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 63
     BUILTIN COMMANDS: DEBUG SUPPORT


      
     Builtin:  notrace [n]                notrace [n]      ________
               n [n]                n [n]
      
     Executes a certain number (specified by the n argument) of Z80 instruc-
     tions, beginning at the current Z80 Program Counter (PC). The Z80
     registers are not displayed after every instruction, but are displayed                   not                                        are
     after the last instruction. 

     If no argument is given, then n defaults to 1. 
      
     The n argument is a numeric value as described at the beginning of this
     section. 

          NOTE: The PC of each executed instruction is saved in a
          circular buffer for later interpretation by the "pc?" builtin                                                           pc?
          command(q.v.).
      
     Example: 

          Z80 A>n 3                 n 3
      
          A F  B C  D E  H L  IX   IY   I  R  SP   PC   IFF1 IFF2 IMF
          0A01 0F09 0130 FEFC 0000 0000 00 00 01FA FEFE   0    0   0 
          0055'0041'0000'0000'SF=0 ZF=0 HF=0 P/V=0 NF=0 CF=1 
          LFEFE:    76             HALT 
      






















     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 64
     BUILTIN COMMANDS: DEBUG SUPPORT


      
     Builtin:  pctrace? [FIRST/LAST n [FULL/BRIEF] ]                pctrace? [FIRST/LAST n [FULL/BRIEF] ]      ________
               pc? [FIRST/LAST n [FULL/BRIEF] ]                pc? [FIRST/LAST n [FULL/BRIEF] ]
      

     Displays the Z80 PC's which were saved during the last "trace" or                                                             trace
     "notrace" execution. This is very useful for finding out how the Z80      notrace
     wound up at a particular address, or where it went from there.

     The display may proceed from the oldest PC toward the newest (FIRST n),                                                                   FIRST n
     or in the reverse direction (LAST n).                                  LAST n

     The display may include only the PC itself (BRIEF) or the complete                                                 BRIEF
     disassembled instruction at each PC (FULL).                                          FULL

     Note that a FULL display assumes that instructions haven't been modified                 FULL
     since they executed. All that is saved in the circular PC queue is the
     PC itself. For a FULL display, the current contents of whatever is at                      FULL                                        _______
     that address is disassembled.
      
     The n argument is a numeric value as described at the beginning of this
     section. 

     The default is LAST .512 FULL.                    LAST .512 FULL

     Example: 

          Z80 A>pc?                 pc?
          Z80 A>pctrace? first .20 full                pctrace? first .20 full
          Z80 A>pc? last .20 brief                pc? last .20 brief                                  



















     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 65
     BUILTIN COMMANDS: DEBUG SUPPORT


      
     Builtin:  move nlow nhigh ndest                move nlow nhigh ndest      ________
               m nlow nhigh ndest                m nlow nhigh ndest
      
     Moves CP/M memory from one location within the CP/M Segment to another
     location within the CP/M Segment. 
      
     The block of memory to be moved is defined by nlow through nhigh.

     The new location for the block is defined by ndest. 
      
     All three arguments are numeric values as described at the start of this
     section. 
      
          NOTE: The move is done either left-to-right or right-to-left,
          as needed. So no smearing is possible. 
      
     Example (from an actual session): 

          Z80 A>p primary_fcb "JoanRiff   "                 p primary_fcb "JoanRiff   "
      
          Z80 A>d primary_fcb secondary_fcb+.15                 d primary_fcb secondary_fcb+.15
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0050:                                      4A 6F 61 6E              Joan
     0060: 52 69 66 66 20 20 20 4D  00 00 80 00 80 01 00 00 Riff   M ........
     0070: 6D 0B 1B BF 40 F3 00 00  00 F3 00 00             m..?@s.. .s.. 

          Z80 A>move primary_fcb secondary_fcb secondary_fcb                 move primary_fcb secondary_fcb secondary_fcb
      
          Z80 A>d primary_fcb secondary_fcb+.15                 d primary_fcb secondary_fcb+.15
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0050:                                      4A 6F 61 6E              Joan
     0060: 52 69 66 66 20 20 20 4D  00 00 80 00 4A 6F 61 6E Riff   M ....Joan
     0070: 52 69 66 66 20 20 20 4D  00 00 80 00             Riff   M .... 











     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 66
     BUILTIN COMMANDS: DEBUG SUPPORT


      
     Builtin:  math <expression>               math <expression>     ________
               ma <expression>               ma <expression>
      
     Prints 16-bit evaluated result of expression, which is composed of
     numeric values (as described at the start of this section) connected
     with '+' or '-' operators. 
      
     The evaluated result is printed in HEX and decimal, as both positive
     and negative numbers.

     Example (from an actual session): 

          Z80 A>math 0-7ff                 math 0-7ff
      
               HEX: F801H  -07FFH     Dec: 63489  -02047 

          Z80 A>ma secondary_fcb-primary_fcb                 ma secondary_fcb-primary_fcb
      
               HEX: 0010H  -FFF0H     Dec: 00016  -65520 

          Z80 A>ma 'A-40+'a                 ma 'A-40+'a
      
               HEX: 0062H  -FF9EH     Dec: 00098  -65438 

























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 67
     BUILTIN COMMANDS: CP/M ENVIRONMENT CONTROL



     Builtin:  args <tail>                args <tail>      ________
               ar <tail>                ar <tail>
      
     Formats default FCB's at 5Ch and 6Ch as well as default DMA at 80h per
     command tail, exactly as if <tail> had followed a Z80 command (.COM)
     filename. 
      
     This command is most useful for "filling in" a command tail for Z80 code
     that has been "read" into CP/M memory and which will look for command-                    read
     line arguments. 
      
     For instance, you may want to debug Digital Research's DDT.COM program,
     while telling DDT to load file FOO.COM. You would first load DDT via
      
          read 100 ddt.com           read 100 ddt.com
      
     You would then fill in DDT's command-line arguments with 
      
          args foo.com           args foo.com
      
     When executed, DDT would then see "FOO.COM" in both the first FCB at 5Ch
     and as a raw command tail at 80h. 
      
     Example (from an actual session): 

          Z80 A>args testfile001 file0002                 args testfile001 file0002
      
          Z80 A>d primary_fcb secondary_fcb+.15                 d primary_fcb secondary_fcb+.15
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0050:                                      00 54 45 53              .TES
     0060: 54 46 49 4C 45 30 30 31  00 00 00 00 00 46 49 4C TFILE001 .....FIL
     0070: 45 30 30 30 32 20 20 20  00 00 00 00             E0002    ....

          Z80 A>d 80 9f                 d 80 9f
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0080: 15 20 54 45 53 54 46 49  4C 45 30 30 31 20 46 49 . TESTFI LE001 FI
     0090: 4C 45 30 30 30 32 0D 00  00 00 00 00 00 00 00 00 LE0002.. ........

          Z80 A>args foo.c -n -b -v                 args foo.c -n -b -v
      




COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 68
     BUILTIN COMMANDS: CP/M ENVIRONMENT CONTROL


          Z80 A>d primary_fcb secondary_fcb+.15                 d primary_fcb secondary_fcb+.15
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0050:                                      00 46 4F 4F              .FOO
     0060: 20 20 20 20 20 43 20 20  00 00 00 00 00 2D 4E 20      C   .....-N 
     0070: 20 20 20 20 20 20 20 20  00 00 00 00                      .... 

          Z80 A>d 80 9f                 d 80 9f
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0080: 0F 20 46 4F 4F 2E 43 20  2D 4E 20 2D 42 20 2D 56 . FOO.C  -N -B -V
     0090: 0D 45 30 30 30 32 0D 00  00 00 00 00 00 00 00 00 .E0002.. ........



































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 69
     BUILTIN COMMANDS: CP/M ENVIRONMENT CONTROL



     Builtin:  coldboot!                coldboot!      ________
               cold!                cold!
      
     Cold Boots CP/M memory by zeroing the 64K CP/M Segment, installing the
     BIOS and BDOS hooks, formatting the first page of memory just as CP/M
     would, etc. 
      
     When you first start up the Emulator, the CP/M Segment has already been
     Cold Booted. 
      
     You may use this command to clean things up when you suspect that Z80
     software may have corrupted the BIOS or BDOS hooks, garbaged page zero,
     or whatever. 
      
     If a Z80 program exits with an Emulator message to the effect that the
     program requests termination via Cold Boot, then you should use this
     command to do it. The Z80 program probably had a good reason for asking
     for a Cold Boot.
      
     Example: 

          Z80 A>coldboot!                 coldboot!
      
               *** CP/M Segment COLDBOOTED *** 
























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 70
     BUILTIN COMMANDS: CP/M ENVIRONMENT CONTROL



     Builtin:  terminal [ BIOS | NONE | BOTH | BDOS ]                terminal [ BIOS | NONE | BOTH | BDOS ]      ________
               term [ BIOS | NONE | BOTH | BDOS ]                term [ BIOS | NONE | BOTH | BDOS ]

     Controls the builtin VT52 "emulated terminal" (described previously),
     whose I/O goes straight to the IBM PC screen via the IBM PC ROM BIOS
     routines and is therefore never seen by PCDOS.

     If BIOS is specified, then CP/M BIOS calls that deal with console input        BIOS
     or output will be routed to the builtin VT52 terminal emulator. Cor-
     responding CP/M BDOS functions will go to PCDOS for handling.

     If NONE is specified, then neither CP/M BIOS calls nor CP/M BDOS        NONE
     functions will be routed to the builtin VT52 terminal emulator. All
     will go to PCDOS for handling.

     If BOTH is specified, then console character CP/M BIOS calls and        BOTH                                                      and
     corresponding CP/M BDOS functions will be routed to the builtin VT52
     terminal emulator. None will go to PCDOS for handling.

     If BDOS is specified, then CP/M BDOS calls that deal with console input        BDOS
     or output will be routed to the builtin VT52 terminal emulator. Cor-
     responding CP/M BIOS functions will go to PCDOS for handling.

          NOTE: This command allows additional flexibility in configu-
          ring your CP/M programs to run under the Emulator. Some
          packages do console I/O via BIOS, others via BDOS. Now you
          can route either one to the builtin VT52 terminal emulator.


     Example: 

          Z80 A>term BOTH                 term BOTH
          Z80 A>terminal none                 terminal none















     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 71
     BUILTIN COMMANDS: CP/M ENVIRONMENT CONTROL


      
     Builtin:  read [n] <filename.typ>                read [n] <filename.typ>      ________
               r [n] <filename.typ>                r [n] <filename.typ>
      
     Reads data from specified file into the CP/M Segment, at address n.
      
     If n is absent, then it defaults to 0100. 
      
     This is the primary method used to load Z80 software for debugging. It
     is normally used to read Z80 command (.COM) files into memory, but this
     command will also read raw data files with no problem. 
      
     If <filename.typ> has a filetype of .HEX, then the file is assumed to be
     in standard Intel HEX format, and is loaded into memory at addresses
     specified by the HEX records. In such a case, the n argument may have no
     meaning.
      
     The n argument is a numeric value of the sort described at the beginning
     of this section. 

          NOTE: If a read of a file causes data to be read below 0100h                     read
          or above FD00h, then the CP/M environment will be clobbered.
          If you're developing non-CP/M Z80 code, then who cares? If
          you're reading in a file that expects to call CP/M, however,
          then running the thing with a clobbered CP/M environment just
          might scramble the brains of the imaginary Z80.
      
     This command is used by us at CCS to load test versions of our Z80
     software, which we leave in .HEX format when we run L80. 
      
     Example: 

          Z80 A>read 100 820init.com                 read 100 820init.com
      
               *** Low = 0100H  Next = 0380H 
               *** Z80 DMA, PC and Stack automatically set for .COM file 

          Z80 A>write 100 360 820init.hex                 write 100 360 820init.hex
      
               Writing HEX records for 0100H thru 0360H (609 bytes) to file
               '820INIT.HEX' 

          Z80 A>read 820init.hex                 read 820init.hex
      
               *** .HEX file Starting Address = 0100H 
               *** Low = 0100H  Next = 0360H 



     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 72
     BUILTIN COMMANDS: CP/M ENVIRONMENT CONTROL


      
     Builtin:  write nlow nhigh <filename.typ>                write nlow nhigh <filename.typ>      ________
               w nlow nhigh <filename.typ>                w nlow nhigh <filename.typ>
      
     Write a block of CP/M memory to a disk file. 
      
     The bounds of the block to be written are specified by nlow and nhigh,
     which are numeric values as described at the start of this section.
      
     The specified block of memory is written from the CP/M Segment to the
     specified file. It is written as a pure memory image, unless a .HEX
     extension is supplied.
      
     Specifying a filename of type .HEX will cause an Intel HEX file to be                                        will
     written. The final record of the generated HEX file is the special
     HEX record which specifies the starting execution address of the
     program. This address is assumed to be nlow.

     Example: 

          Z80 A>read 100 820init.com                 read 100 820init.com
      
               *** Low = 0100H  Next = 0380H 
               *** Z80 DMA, PC and Stack automatically set for .COM file 

          Z80 A>write 100 360 820init.hex                 write 100 360 820init.hex
      
               Writing HEX records for 0100H thru 0360H (609 bytes) to file
               '820INIT.HEX' 

          Z80 A>read 820init.hex                 read 820init.hex
      
               *** .HEX file Starting Address = 0100H 
               *** Low = 0100H  Next = 0360H 















     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 73
     BUILTIN COMMANDS: CP/M ENVIRONMENT CONTROL


      
     Builtin:  submit <filename.typ>                submit <filename.typ>      ________
               sub <filename.typ>                sub <filename.typ>
      
     Switches input (for Emulator commands only) to the specified file.

     This is roughly equivalent to the CP/M SUBMIT.COM program, except that
     it is built into the Emulator. 
      
     Z80 application input via BDOS and BIOS does not get switched. Only
     Emulator input is switched. Submit files cannot be nested.                                 Submit
      
     Input reverts to the standard input (as defined by PCDOS) when EOF is
     detected on the specified file. 

          NOTE: If a keypress is detected during submit file processing                                                 submit
          but outside of Z80 operation (i.e. - when the Emulator is
          expecting a command), then the submit file is aborted. This                                         submit
          is how you cancel a submit file - just press SPACE while it
          is running.
      
     Example: 
          Z80 A>submit script                 submit script
          Z80 A>sub c:\cpm\autoexec.z80                sub c:\cpm\autoexec.z80

























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 74
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS


      
     Builtin:  list [n1 [n2]] [>outfile | >>outfile]                list [n1 [n2]] [>outfile | >>outfile]      ________
               list prologue n1 n2 [>outfile | >>outfile]                list prologue n1 n2 [>outfile | >>outfile] 
               list include [A][O][F]                list include [A][O][F] 
               l [n1 [n2]] [>outfile | >>outfile]                l [n1 [n2]] [>outfile | >>outfile] 
               l prologue n1 n2 [>outfile | >>outfile]                l prologue n1 n2 [>outfile | >>outfile] 
               l include [A][O][F]                l include [A][O][F] 
      
     This is a multi-purpose disassembly command, which does one of three
     things (depending upon the arguments that are present):
      
          Lists disassembled Z80 object code (first form). 
      
          Generates an assembler prologue for the given range of Z80
          object code (second form). 
      
          Specifies fields to be included in disassembly lines (third
          form). 
      


     Format:  list [n1 [n2]] [>outfile | >>outfile]               list [n1 [n2]] [>outfile | >>outfile] 
              l [n1 [n2]] [>outfile | >>outfile]               l [n1 [n2]] [>outfile | >>outfile] 
      
     This form causes the disassembly of Z80 object code from CP/M address n1
     through CP/M address n2 (both of which are numeric values as defined at
     the start of this section). If n2 is absent, then n2 is assumed to be
     n1+22. If n1 is absent, then it defaults to the next address to be
     disassembled (as left by last list command).                                    list
      
     The generated disassembly is sent to (">outfile") or appended to                                            >outfile
     (">>outfile") the specified output file. If an output file is not       >>outfile
     specified (no ">" character present), then the generated disassembly
     goes to the standard output as defined by PCDOS (normally the screen). 

          NOTE: Disassembly speed decreases as the size of the control
          table increases. It may also be slowed by PCDOS being so
          lethargic with screen output. When disassembling the Radio
          Shack Model 100's memory (which required a control table of
          about 42K), for instance, we were only getting about 2 lines
          of disassembled code per second. 

     Generated source code is suitable for input to M80.COM in .Z80 mode.
     Note, however, that any RST instructions use as their argument the
     final address being jumped to, not the RST number (as is customary).
     Also, there is no END statement supplied.



     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 75
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS


      
     Format:  list prologue n1 n2 [>outfile | >>outfile]               list prologue n1 n2 [>outfile | >>outfile] 
              l prologue n1 n2 [>outfile | >>outfile]               l prologue n1 n2 [>outfile | >>outfile] 
      
     This form generates assembler source code suitable for inclusion at the
     front of a Z80 source file. The generated source code is the prologue
     for a given block of Z80 object code, defined by CP/M addresses n1 and
     n2. Both n1 and n2 are numeric values as defined at the start of this
     section. 
      
     The generated prologue contains equates for the various ASCII control
     characters. Additionally, it contains equated labels for any CP/M
     addresses that are referenced by the specified block of Z80 code (from
     n1 to n2), but not contained within it. 
      
     Such a prologue is generally needed at the front of any sizeable Z80
     disassembly. 
      
     The generated prologue is sent to (">outfile") or appended to (">>out-                                         >outfile                    >>out-
     file") the specified output file. If an output file is not specified,     file
     (no ">" character present), then the generated prologue goes to the
     standard output as defined by PCDOS (normally the screen). 


      
     Format:  list include [A][O][F]               list include [A][O][F] 
              l include [A][O][F]               l include [A][O][F] 
      
     Specifies the fields to be included in disassembled Z80 instructions.
      
     If the "A" arg is present, then CP/M addresses will be included at the             A                            addresses
     left of disassembled instructions. 
      
     If the "O" argument is present, then raw opcodes will be included after             O                                opcodes
     the address (if present) but before the Z80 mnemonic. 
      
     If the "F" argument is present, then the disassembled Z80 instruction             F
     will include a comment explaining the instruction's possible effect(s)
     on the Z80 flags.                 flags
      
     Arguments after "include" may be whole words. Only the first character                      include
     is checked. 
      
     If no arguments appear after "include", then the disassembled Z80                                   include
     instruction will consist only of the mnemonic field. 




     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 76
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS


      
     Example: 
          Z80 A>list include addresses                 list include addresses
          Z80 A>list include                 list include
          Z80 A>l prologue 100 7ff                 l prologue 100 7ff
          Z80 A>list prologue 0 ffff >model100.rom                 list prologue 0 ffff >model100.rom
          Z80 A>list 0 ffff >>model100.rom                list 0 ffff >>model100.rom
          Z80 A>list                list


          NOTE: The next section contains a sample Emulator session
          which generates source code from object code. Refer to it for
          more detail about this and related Resource commands.




































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 77
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS



     Builtin:  control list [n]                control list [n]      ________
               control clear                control clear 
               control read <filepath>                control read <filepath> 
               control write <filepath>                control write <filepath> 
               control n     i | b | w | t | s | c                control n     i | b | w | t | s | c 
               c list [n]                c list [n] 
               c clear                c clear 
               c read <filepath>                c read <filepath> 
               c write <filepath>                c write <filepath> 
               c n     i | b | w | t | s | c                c n     i | b | w | t | s | c 
      
     This is a multi-purpose command which manipulates the disassembly
     control table. 
      
     The disassembly control table holds CP/M addresses and any or all of the
     following which are associated with each address: 
      
          The data type of the Z80 object code at this address. This is
               called a "control break". 
      
          A symbolic label to be associated with the address. 
      
          A comment to be associated with the address. 
      
      
     This control table is used by the disassembler (the list command), and                                                         list
     tells it how to format the source code while disassembling. 
      
     The various data type control breaks that may be associated with a CP/M
     address are as follows: 
      
          Instructions (executable Z80 code, disassembled as mnemonics)
      
          Bytes (disassembled as DB pseudo-ops) 
      
          Words (disassembled as DW pseudo-ops, multiple entries per
               line) 
      
          Table of Words (disassembled as DW pseudo-ops, one per line)
      
          Storage (disassembled as DS with argument large enough to
               bring it up to next control entry) 
      
      
     This is how the disassembler knows which parts of your Z80 object code
     are instructions, which are data, and which are irrelevant buffers etc. 


     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 78
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS


     The specific formats are described below.


     Format:  control list [n]               control list [n]
              c list [n]               c list [n]
      
     This format of the command causes the Emulator to display all control
     table information that is currently known to it. If numeric value n (see
     definition of legal numeric values at start of this section) is present,
     then only control information associated with CP/M addresses greater
     than or equal to n are listed. 
      
     The list includes any control breaks, labels, and comments associated
     with the various CP/M addresses. 
      


     Format:  control clear               control clear
              c clear               c clear
      
     This format of the command clears out the control table, so that nothing
     is known about the Z80 object code. No CP/M addresses, control breaks,
     labels or comments are defined after this command is given. 
      
      

     Format:  control read <filepath>               control read <filepath>
              c read <filepath>               c read <filepath>
      
     This format of the command causes the Emulator to read a control table
     from the specified filename. The file must have been created by a                                           must
     "control write <filepath>" command.       control write <filepath>
      
     A currently-defined control table is cleared before the new one is read
     from disk. It is not possible to merge control tables using this
     command. 
      
      











     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 79
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS


     Format:  control write <filepath>               control write <filepath>
              c write <filepath>               c write <filepath>
      
     This command writes the current control table to the specified file, for
     later input via the "control read <filepath>" command. All known data is                          control read <filepath>
     written - CP/M addresses, control breaks, labels and comments. 
      
      

     Format:  control n     i | b | w | t | s | c               control n     i | b | w | t | s | c
              c n     i | b | w | t | s | c               c n     i | b | w | t | s | c
      
     This format of the command is the real workhorse of control table
     maintenance. It associates a Z80 data type with CP/M address n, which is
     a numeric value as defined at the start of this section. 
      
     The argument following CP/M address n is a directive to the disassembler
     (the list command), and may be any one of the following (note that only          list                          one
     the first character is required): 
      
          Instructions: switch to Z80 mnemonics when you get to this          I
               address. 
      
          Bytes: switch to DB pseudo-ops when you get to this address.          B
      
          Words: switch to DW pseudo-ops (multiple per line) when you          W
               get to this address. 
      
          Table of words: switch to DW pseudo-ops (one per line) when          T
               you get to this address. This is useful for jump tables,
               etc, where you want the source code to be neatly ar-
               ranged. 
      
          Storage: do a single DS (define storage) pseudo-op when you          S
               get to this address, and make the size field big enough
               to take you up to the next control break address (or the
               end of the disassembly, whichever is lower). 

      
     You may also specify a special argument, which is handled immediately
     and never gets to the disassembler: 
      
          Clear: Clear this address's control break data type. This does          C
               not remove an associated label or comment. It just undoes               not
               any control break (of one of the above types) associated
               with this CP/M address. 
      
      

COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 80
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS



     Example: 
          Z80 A>control list                 control list
          Z80 A>c clear                 c clear
          Z80 A>c read b:\model100\model100.ctl                 c read b:\model100\model100.ctl
          Z80 A>control write foo.ctl                 control write foo.ctl
          Z80 A>c read xyz                 c read xyz
          Z80 A>control 100 Instructions                 control 100 Instructions
          Z80 A>c 103 b                 c 103 b
          Z80 A>c table_start+1 S                 c table_start+1 S
          Z80 A>CONTROL bios_address W                 CONTROL bios_address W
          Z80 A>c FF00 Table                 c FF00 Table
          Z80 A>c 103 clear                c 103 clear




          NOTE: The next section contains a sample Emulator session
          which generates source code from object code. Refer to it for
          more detail about this and related Resource commands.
      




























COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 81
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS


      
     Builtin:  label n [label_name]                label n [label_name]      ________
               label autogen n1 n2                label autogen n1 n2 
               = n [label_name]                = n [label_name] 
               = autogen n1 n2                = autogen n1 n2 
      
     This command controls the assignment of symbolic label names to various
     CP/M addresses. Symbolic labels may be used as numeric values in many
     Emulator commands. They are also used by the disassembler when creating
     source code from Z80 object code. 


      
      
     Format:  label n [label_name]               label n [label_name]
              = n [label_name]               = n [label_name]
      
     This format associates label_name with CP/M address n, which is a
     numeric value as described at the start of this section. 
      
     Label names may be up to 32 characters in length. They must contain only
     alphanumeric characters and the underscore character "_". 
      
     If label_name is absent in this command, then any existing label name
     associated with the specified CP/M address is simply deleted. 
      
      
      
      
     Format:  label autogen n1 n2               label autogen n1 n2
              = autogen n1 n2               = autogen n1 n2
      
     This format causes the Emulator to automatically generate labels (of
     format AUTOxxxx) for all unlabeled CP/M addresses that are referenced by
     the block of Z80 code that starts at n1 and ends at n2 (both of which
     are numeric values as defined at the start of this section). 
      
     Labels that are generated are automatically entered into the current
     control table. Existing labels will not be altered. 
      
     This is a quick way to create labels. It can be useful for rapid
     generation of readable source code from Z80 object code. You should,
     however, define any recognizable labels before using this command. You
     should also make sure that you have pretty accurately defined all
     control breaks that apply to the specified block of Z80 code. There's
     nothing worse than getting a block of data confused with instructions,
     and having this command generate a few hundred bogus labels by misinter-
     preting the Z80 code. 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 82
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS


      
     So this is generally the last thing that you do before deciding that
     you have finished disassembling a complete Z80 program. 
      


          NOTE: 16-bit literals will be ignored. There's no way - short
          of human inspection - to tell if the 16-bit value is meant to
          be a Z80 address or just a binary value (like a loop counter).
          In previous versions of the Emulator, there were too many
          bogus labels being autogen'd from 16-bit literals. Now it is                             autogen
          up to you to decide whether a particular 16-bit literal
          should have a label associated with it. Specifically, the
          following instructions' 16-bit literals are ignored:

                    LD   IX,nn
                    LD   IY,nn
                    LD   BC,nn
                    LD   DE,nn
                    LD   HL,nn
                    LD   SP,nn


     Example: 
          Z80 A>= 100 program_entry                 = 100 program_entry
          Z80 A>label 7ff program_end                 label 7ff program_end
          Z80 A>= 0 warm_boot_jump                 = 0 warm_boot_jump
          Z80 A>= 5C FCB1                 = 5C FCB1
          Z80 A>= 5 BDOS                 = 5 BDOS
          Z80 A>label autogen 100 7ff                label autogen 100 7ff




          NOTE: The next section contains a sample Emulator session
          which generates source code from object code. Refer to it for
          more detail about this and related Resource commands.












     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 83
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS



     Builtin:  comment n ["text"]                comment n ["text"]      ________
               ; n ["text"]                ; n ["text"] 
      
     Associates source-code comment "text" with CP/M address n, which is a                                     text
     numeric value as defined at the start of this section. "text" may be up                                                             text
     to 254 characters long. 
      
     If "text" is absent, then any existing comment associated with address n         text
     is simply deleted. 
      
     Note that "text" must be enclosed in double quotes. It may include                text
     escape sequences as follows: 
      
          \\             Single "\" char 
          \0             NUL byte 
          \b or \B       Backspace char 
          \t or \T       Tab char 
          \n or \N       Linefeed char 
          \r or \R       Return char 
          \'             Single quote char 
          \"             Double quote char 
          \xFF or \XFF   Byte with HEX value FF 
      
     These escape codes made be used to make the comment more readable.

      
     When a comment is detected by the disassembler, it will be printed in
     one of two places: 
      
          As a single-line comment, after the mnemonic. Such a comment
               replaces the flags comment field (if present). If "text"                                                                  text
               starts with other than a "\n" escape, then the comment is
               printed in this manner. 
      
          As a multi-line comment, on lines before the instruction. If
               "text" starts with a "\n" escape, then the comment will                text
               be printed in this manner. Blank comment lines (starting
               with ";") are automatically provided before and after the
               comment, and ";" characters are inserted after every "\n"
               or "\r" found in the "text" string.                                      text
      
      
     If you want to create a nice-looking multi-line comment, then imbed "\n"
     escapes as line delimiters, and "\t" escapes to line things up on
     succeeding lines. 
      


COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 84
     BUILTIN COMMANDS: RESOURCE FACILITY COMMANDS


     If your comment is intended to be a single-line comment appended to the
     disassembled instruction's mnemonic, then avoid imbedded "\n" and "\r"
     escapes. 

      
     Example: 
          Z80 A>comment 100 "\nStart of main program"                 comment 100 "\nStart of main program"
          Z80 A>; 0 "Jump to BIOS Warm, Start"                 ; 0 "Jump to BIOS Warm, Start"
          Z80 A>; 100                 ; 100
          Z80 A>comment ff00 "\nBIOS Jump Table\n\n\t3 bytes per JMP"                comment ff00 "\nBIOS Jump Table\n\n\t3 bytes per JMP"





          NOTE: The next section contains a sample Emulator session
          which generates source code from object code. Refer to it for
          more detail about this and related Resource commands.































     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 85
     USING THE RESOURCE BUILTIN COMMANDS


      









                      USING THE RESOURCE BUILTIN COMMANDS                       USING THE RESOURCE BUILTIN COMMANDS


     This section presents an example of re-sourcing a piece of Z80 object
     code. It demonstrates the use of the various Emulator builtin commands
     that deal with regenerating source code from object code.

     We were recently presented with a piece of software which (wouldn't you
     know it?) existed only in object form on a Xerox 820 CP/M system. The
     owner of this little utility really wanted to move it to a 16-bit
     Hyperion system, cause the utility sets up a Z80 SIO and that's what the
     Hyperion has - an SIO.

     So he was wondering - could we regenerate the source code for this
     little beauty? What follows is an annotated record of the ensuing
     session:



          NOTE: The first step is to read the thing into Z80 memory
          with the Emulator, and clear any previous resource control
          breaks.
      
     Z80 C>read 100 820init.com            read 100 820init.com
      
     *** Low = 0100H  Next = 0380H 
     *** Z80 DMA, PC and Stack automatically set for .COM file 
     Z80 C>control clear            control clear
      
     Z80 C>list include addresses opcodes            list include addresses opcodes









     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 86
     USING THE RESOURCE BUILTIN COMMANDS


          NOTE: The next thing to do is take a quick look at the
          program, and get a general feel for what it does.
      
     Z80 C>list            list
      
     L0100:     11 45 02              LD     DE,L0245 
     L0103:     CD 40 02              CALL   L0240 
     L0106:     11 C8 02              LD     DE,L02C8 
     L0109:     CD 40 02              CALL   L0240 
     L010C:     CD 35 02              CALL   L0235 
     L010F:     FE 0D                 CP     CR 
     L0111:     C2 16 01              JP     NZ,L0116 
     L0114:     3E 36                 LD     A,'6' 
     L0116:     D6 30                 SUB    '0' 



          NOTE: This isn't real promising. Let's dump the thing and
          look for obvious ASCII strings.

     Z80 C>d 100 37f            d 100 37f
      
     ADDR  00 01 02 03 04 05 06 07  08 09 0A 0B 0C 0D 0E 0F 01234567 89ABCDEF
     ----  -- -- -- -- -- -- -- --  -- -- -- -- -- -- -- -- -------- --------
     0100: 11 45 02 CD 40 02 11 C8  02 CD 40 02 CD 35 02 FE .E.M@..H .M@.M5.~
     0110: 0D C2 16 01 3E 36 D6 30  FE 00 DA 06 01 FE 0A D2 .B..>6V0 ~.Z..~.R
     0120: 06 01 32 58 03 11 EF 02  CD 40 02 CD 35 02 FE 0D ..2X..o. M@.M5.~.
     0130: C2 35 01 3E 4E FE 45 CA  47 01 FE 4F CA 47 01 FE B5.>N~EJ G.~OJG.~
     0140: 4E CA 47 01 C3 25 01 32  5A 03 11 16 03 CD 40 02 NJG.C%.2 Z....M@.
     0150: CD 35 02 FE 0D C2 5A 01  3E 38 D6 30 FE 07 CA 69 M5.~.BZ. >8V0~.Ji
     0160: 01 FE 08 CA 69 01 C3 4A  01 32 59 03 3A 58 03 FE .~.Ji.CJ .2Y.:X.~
     0170: 00 C2 79 01 3E 0F C3 B7  01 FE 01 C2 83 01 3E 0E .By.>.C7 .~.B..>.
     0180: C3 B7 01 FE 02 C2 8D 01  3E 0C C3 B7 01 FE 03 C2 C7.~.B.. >.C7.~.B
     0190: 97 01 3E 0A C3 B7 01 FE  04 C2 A1 01 3E 07 C3 B7 ..>.C7.~ .B!.>.C7
     01A0: 01 FE 05 C2 AB 01 3E 06  C3 B7 01 FE 06 C2 B5 01 .~.B+.>. C7.~.B5.
     01B0: 3E 05 C3 B7 01 3E 02 32  58 03 3A 5A 03 FE 45 C2 >.C7.>.2 X.:Z.~EB
     01C0: C7 01 3E 03 C3 D3 01 FE  4F C2 D1 01 3E 01 C3 D3 G.>.CS.~ OBQ.>.CS
     01D0: 01 3E 00 32 5A 03 3A 59  03 FE 07 CA EB 01 3E 60 .>.2Z.:Y .~.Jk.>`
     01E0: 32 5B 03 3E C0 32 5C 03  C3 F5 01 3E 20 32 5B 03 2[.>@2\.  Cu.>2[.
     01F0: 3E 40 32 5C 03 F3 3E 18  D3 06 D3 06 3E 01 D3 06 >@2\.s>. S.S.>.S.
     0200: AF D3 06 3E 04 D3 06 3A  5A 03 C6 44 D3 06 3E 03 /S.>.S.: Z.FDS.>.
     0210: D3 06 3A 5C 03 C6 01 D3  06 3E 05 D3 06 3A 5B 03 S.:\.F.S .>.S.:[.
     0220: C6 8A D3 06 3E 47 D3 00  3A 58 03 D3 00 FB 11 3D F.S.>GS. :X.S.{.=
     0230: 03 CD 40 02 C9 0E 01 CD  05 00 FE 60 D8 D6 20 C9 .M@.I..M  ..~`XVI
     0240: 0E 09 C3 05 00 1A 49 4E  49 54 20 31 2E 30 20 66 ..C...IN  IT 1.0f
     0250: 6F 72 20 58 65 72 6F 78  20 38 32 30 0D 0A 0A 0A or Xerox  820....
     0260: 0D 0A 42 61 75 64 20 52  61 74 65 73 3A 0D 0A 31 ..Baud R ates:..1
     0270: 39 32 30 30 20 3D 20 30  0D 0A 39 36 30 30 20 20 9200 = 0 ..9600 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 87
     USING THE RESOURCE BUILTIN COMMANDS


     0280: 3D 20 31 0D 0A 34 38 30  30 20 20 3D 20 32 0D 0A = 1..480 0  = 2..
     0290: 32 34 30 30 20 20 3D 20  33 0D 0A 31 32 30 30 20 2400  =  3..1200
     02A0: 20 3D 20 34 0D 0A 20 36  30 30 20 20 3D 20 35 0D  = 4.. 6 00  = 5.
     02B0: 0A 20 33 30 30 20 20 3D  20 36 0D 0A 20 31 31 30 . 300  =  6.. 110
     02C0: 20 20 3D 20 37 0D 0A 24  0D 0A 53 65 6C 65 63 74   = 7..$ ..Select
     02D0: 20 62 61 75 64 20 72 61  74 65 20 20 20 20 20 20  baud ra te     
     02E0: 20 20 20 20 20 28 31 2D  39 29 3A 20 36 08 24 0D      (1- 9): 6.$.
     02F0: 0A 53 65 6C 65 63 74 20  70 61 72 69 74 79 20 20 .Select  parity 
     0300: 28 4F 64 64 2C 20 45 76  65 6E 2C 20 4E 6F 6E 65 (Odd, Ev en, None
     0310: 29 3A 20 4E 08 24 0D 0A  53 65 6C 65 63 74 20 77 ): N.$.. Select w
     0320: 6F 72 64 20 6C 65 6E 67  74 68 20 20 20 20 20 20 ord leng th     
     0330: 28 37 20 6F 72 20 38 29  3A 20 38 08 24 0D 0A 43 (7 or 8) : 8.$..C
     0340: 6F 6D 6D 75 6E 69 63 61  74 69 6F 6E 73 20 70 6F ommunica tions po
     0350: 72 74 20 73 65 74 2E 24  00 00 00 00 00 00 00 00 rt set.$ ........
     0360: 00 00 00 00 00 00 00 00  00 00 00 00 00 00 00 00 ........ ........
     0370: 00 00 00 00 00 00 00 00  00 00 00 00 00 00 00 00 ........ ........





          NOTE: Well, there are some strings that are terminated with
          dollar signs. This is a heavy hint that these strings are to
          be displayed by BDOS function 9. Let's start our control
          table by filling in what we know so far...


     Z80 C>c 100 instructions           c 100 instructions      (0100h, of course, starts code)
      
     Z80 C>= 100 startup           = 100 startup           (Give it a sensible name) 
      
     Z80 C>c 245 b            c 245 b                 (Start bytes at first ASCII string)
      
     Z80 C>= 245 init_msg           = 245 init_msg          (Give them sensible names) 
      
     Z80 C>= 2c8 baud_prompt            = 2c8 baud_prompt
      
     Z80 C>= 2ef parity_prompt            = 2ef parity_prompt
      
     Z80 C>= 316 databits_prompt            = 316 databits_prompt
      
     Z80 C>= 33d wrapup_msg            = 33d wrapup_msg
      






     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 88
     USING THE RESOURCE BUILTIN COMMANDS



          NOTE: Now let's look at the first code bytes again, and see
          if they make any more sense.

     Z80 C>l 100            l 100
      
      
                    STARTUP: 
     L0100:     11 45 02              LD     DE,INIT_MSG 
     L0103:     CD 40 02              CALL   L0240 
     L0106:     11 C8 02              LD     DE,BAUD_PROMPT 
     L0109:     CD 40 02              CALL   L0240 
     L010C:     CD 35 02              CALL   L0235 
     L010F:     FE 0D                 CP     CR 
     L0111:     C2 16 01              JP     NZ,L0116 
     L0114:     3E 36                 LD     A,'6' 
     L0116:     D6 30                 SUB    '0' 




          NOTE: So the routine at 0240h does something with a "$"-
          terminated string. Need we guess?

     Z80 C>l 240            l 240
      
     L0240:     0E 09                 LD     C,TAB 
     L0242:     C3 05 00              JP     L0005 
      
                    INIT_MSG: 
                         DB     SUB,"INIT 1.0 for Xero" 
     L0245:     1A 49 4E 49  
     L0249:     54 20 31 2E  
     L024D:     30 20 66 6F  
     L0251:     72 20 58 65  
     L0255:     72 6F             


          NOTE: First of all, note how the above disassembly changed
          from instructions to data, just as we told it to. Note also
          that this routine at 0240h is simple enough to document...

     Z80 C>= 5 bdos            = 5 bdos
      
     Z80 C>; 240 "\nPrint $-terminated string at (DE)"            ; 240 "\nPrint $-terminated string at (DE)"
      
     Z80 C>c 240 i            c 240 i
      

COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 89
     USING THE RESOURCE BUILTIN COMMANDS


     Z80 C>= 240 print_string            = 240 print_string
      
     Z80 C>l 240            l 240
      
      
                    PRINT_STRING: 
      
                    ;  
                    ; Print $-terminated string at (DE) 
                    ;  
     L0240:     0E 09                 LD     C,TAB 
     L0242:     C3 05 00              JP     BDOS 
      
                    INIT_MSG: 
                         DB     SUB,"INIT 1.0 for Xero" 
     L0245:     1A 49 4E 49  
     L0249:     54 20 31 2E  
     L024D:     30 20 66 6F  
     L0251:     72 20 58 65  
     L0255:     72 6F             




          NOTE: OK, one routine down. Referring back to our disassembly
          of the startup code, let's see what else we can figure out.

     Z80 C>= 106 get_baud_rate            = 106 get_baud_rate
      
     Z80 C>l startup            l startup
      
      
                    STARTUP: 
     L0100:     11 45 02              LD     DE,INIT_MSG 
     L0103:     CD 40 02              CALL   PRINT_STRING 
      
                    GET_BAUD_RATE: 
     L0106:     11 C8 02              LD     DE,BAUD_PROMPT 
     L0109:     CD 40 02              CALL   PRINT_STRING 
     L010C:     CD 35 02              CALL   L0235 
     L010F:     FE 0D                 CP     CR 
     L0111:     C2 16 01              JP     NZ,L0116 
     L0114:     3E 36                 LD     A,'6' 
     L0116:     D6 30                 SUB    '0' 





     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 90
     USING THE RESOURCE BUILTIN COMMANDS


          NOTE: We have another routine to decipher - at 0235h.

     Z80 C>l 235            l 235
      
     L0235:     0E 01                 LD     C,SOH 
     L0237:     CD 05 00              CALL   BDOS 
     L023A:     FE 60                 CP     '`' 
     L023C:     D8                    RET    C 
     L023D:     D6 20                 SUB    ' ' 
     L023F:     C9                    RET 
      
                    PRINT_STRING: 
      
                    ;  
                    ; Print $-terminated string at (DE) 
                    ;  
     L0240:     0E 09                 LD     C,TAB 
     L0242:     C3 05 00              JP     BDOS 
      
                    INIT_MSG: 
                         DB     SUB,"INIT 1" 
     L0245:     1A 49 4E 49  
     L0249:     54 20 31          




          NOTE: Notice how the disassembly continued way past the end
          of our routine. That's because we didn't give an ending
          address. At any rate, the routine at 0235h appears to call
          BDOS to get a keypress, then force it to uppercase. It
          contains a slight bug, but our job right now is to re-source
          it, not fix it.

     Z80 C>= 235 get_bdos_keypress            = 235 get_bdos_keypress
      
     Z80 C>c 235 i            c 235 i
      
     Z80 C>; 235 "\nReturn next keypress as Uppercase char in A-reg"            ; 235 "\nReturn next keypress as Uppercase char in A-reg"
      
     Z80 C>; 237 "Use BDOS to get next keypress"            ; 237 "Use BDOS to get next keypress"
      
     Z80 C>; 23a "Is it lowercase char?"            ; 23a "Is it lowercase char?"
      
     Z80 C>; 23c "No, return it as-is"            ; 23c "No, return it as-is"
      
     Z80 C>; 23d "Yes, convert to uppercase"            ; 23d "Yes, convert to uppercase"
      

COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 91
     USING THE RESOURCE BUILTIN COMMANDS


     Z80 C>l 235            l 235
      
      
                    GET_BDOS_KEYPRESS: 
      
                    ;  
                    ; Return next keypress as Uppercase char in A-reg
                    ;  
     L0235:    0E 01                LD    C,SOH 
     L0237:    CD 05 00             CALL  BDOS    ;Use BDOS to get next
                                                            keypress
     L023A:    FE 60                CP    '`'     ;Is it lowercase char?
     L023C:    D8                   RET   C       ;No, return it as-is
     L023D:    D6 20                SUB   ' '     ;Yes, convert to uppercase
     L023F:    C9                   RET 
      
                    PRINT_STRING: 
      
                    ;  
                    ; Print $-terminated string at (DE) 
                    ;  
     L0240:     0E 09                 LD     C,TAB 
     L0242:     C3 05 00              JP     BDOS 
      
                    INIT_MSG: 
                         DB     SUB,"INIT 1" 
     L0245:     1A 49 4E 49  
     L0249:     54 20 31          





          NOTE: OK, our little routines are understood and documented.
          Back to the main code, and add comments that clarify things.

     Z80 C>; 100 "Give intro screen"            ; 100 "Give intro screen"
      
     Z80 C>; 106 "Ask for baudrate value"            ; 106 "Ask for baudrate value"
      
     Z80 C>; 10f "RETURN only?"            ; 10f "RETURN only?"
      
     Z80 C>; 111 "No, look at keypress"            ; 111 "No, look at keypress"
      
     Z80 C>; 114 "Yes, use default value"            ; 114 "Yes, use default value"
      
     Z80 C>= 116 edit_baud_rate            = 116 edit_baud_rate
      

COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 92
     USING THE RESOURCE BUILTIN COMMANDS


     Z80 C>l get_baud_rate 12b            l get_baud_rate 12b
      
      
                    GET_BAUD_RATE: 
     L0106:   11 C8 02           LD     DE,BAUD_PROMPT ;Ask for baudrate
                                                                 value 
     L0109:   CD 40 02           CALL   PRINT_STRING 
     L010C:   CD 35 02           CALL   GET_BDOS_KEYPRESS 
     L010F:   FE 0D              CP     CR          ;RETURN only? 
     L0111:   C2 16 01           JP     NZ,EDIT_BAUD_RATE ;No, look at
                                                                 keypress 
     L0114:   3E 36              LD     A,'6'       ;Yes, use default
                                                                 value 
      
                    EDIT_BAUD_RATE: 
     L0116:   D6 30              SUB    '0' 
     L0118:   FE 00              CP     NUL 
     L011A:   DA 06 01           JP     C,GET_BAUD_RATE 
     L011D:   FE 0A              CP     LF 
     L011F:   D2 06 01           JP     NC,GET_BAUD_RATE 
     L0122:   32 58 03           LD     (L0358),A 
     L0125:   11 EF 02           LD     DE,PARITY_PROMPT 
     L0128:   CD 40 02           CALL   PRINT_STRING 
     L012B:   CD 35 02           CALL   GET_BDOS_KEYPRESS 




          NOTE: And so on, and so on, and so on....



     We'll not present all of the output here. Although the session actually
     lasted less than half an hour, the output is huge. Instead, let us skip
     ahead to the point where we've finished defining our control table.




          NOTE: At this point - having done all of this work to con-
          struct documentation of the object code - we should save the                                                              ________
          control table to disk!          ______________________

     Z80 C>control write 820init.ctl           control write 820init.ctl





     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 93
     USING THE RESOURCE BUILTIN COMMANDS


          NOTE: Having done that, we must prepare things for the actual
          generation of the .ASM file. Specifically, we should exclude
          addresses, opcodes, and flags from disassembly source lines.
      
     Z80 C>list include            list include



          NOTE: Now we can disassemble the object code to disk as source
          code. First we write the prologue, and then the program
          itself:
      
     Z80 C>list prologue 100 360 >820init.asm            list prologue 100 360 >820init.asm
      
     Z80 C>list 100 360 >>820init.asm            list 100 360 >>820init.asm


          NOTE: Having done that, let's test things by running the .ASM
          file through M80.COM...
      
     Z80 C>m80 820init.rel,820init.prn=820init.asm            m80 820init.rel,820init.prn=820init.asm
     %No END statement 
     %No END statement 
      
     No Fatal error(s) 
      




     That's it. We're done. The assembler version of 820INIT.COM has been
     written and verified.

     For your enjoyment, we have included with Z80MU the various 820INIT
     files that were used or created by the above session. Feel free to
     examine all of these files, especially 820INIT.ASM and 820INIT.PRN. They
     give you a good idea of the quality of source code that can be recreated
     from a given object program.











     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 94
     Appendix A: Layout of CP/M Segment


      
     Appendix A: Layout of Simulated CP/M Segment (as set by Cold Boot)      __________________________________________________________________
      
     0000:     JMP  0FF03H         ;to our fake BIOS 
     0003:     DB   ?              ;IOBYTE 
     0004:     DB   ?              ;Login Byte (drive, User Number) 
     0005:     JMP  0FEFEH         ;to our fake BDOS 
     005C:     DB   ?              ;Default FCB 
     0080:     DB   ?              ;Default DMA and Command Tail 
     0100:     DB   ?              ;start of TPA 
     FEFD:     DB   ?              ;last byte of TPA 
     FEFE:     HALT                ;our BDOS hook 
     FEFF:     RET                 ;return from BDOS 
     FF00:     JMP  0FF80H         ;BIOS COLD BOOT vector 
     FF03:     JMP  0FF82H         ;BIOS WARM BOOT vector 
     FF06:     JMP  0FF84H         ;BIOS console status 
     FF09:     JMP  0FF86H         ;BIOS console input 
     FF0C:     JMP  0FF88H         ;BIOS console output 
     FF0F:     JMP  0FF8AH         ;BIOS list output 
     FF12:     JMP  0FF8CH         ;BIOS punch output 
     FF15:     JMP  0FF8EH         ;BIOS reader input 
     FF18:     JMP  0FF90H         ;BIOS home disk 
     FF1B:     JMP  0FF92H         ;BIOS select disk 
     FF1E:     JMP  0FF94H         ;BIOS set track 
     FF21:     JMP  0FF96H         ;BIOS set sector 
     FF24:     JMP  0FF98H         ;BIOS set DMA address 
     FF27:     JMP  0FF9AH         ;BIOS read sector 
     FF2A:     JMP  0FF9CH         ;BIOS write sector 
     FF2D:     JMP  0FF9EH         ;BIOS list status 
     FF30:     JMP  0FFA0H         ;BIOS (unimplemented) 
     FF33:     JMP  0FFA2H         ;BIOS (unimplemented) 
     FF36:     JMP  0FFA4H         ;BIOS (unimplemented) 
     FF39:     JMP  0FFA6H         ;BIOS (unimplemented) 
     FF3C:     JMP  0FFA8H         ;BIOS (unimplemented) 
     FF3F:     JMP  0FFAAH         ;BIOS (unimplemented) 
     FF42:     JMP  0FFACH         ;BIOS (unimplemented) 
     FF45:     JMP  0FFAEH         ;BIOS (unimplemented) 
     FF48:     JMP  0FFB0H         ;BIOS (unimplemented) 
     FF4B:     JMP  0FFB2H         ;BIOS (unimplemented) 
     FF4E:     JMP  0FFB4H         ;BIOS (unimplemented) 
     FF51:     JMP  0FFB6H         ;BIOS (unimplemented) 
     FF54:     JMP  0FFB8H         ;BIOS (unimplemented) 
     FF57:     JMP  0FFBAH         ;BIOS (unimplemented) 
     FF5A:     JMP  0FFBCH         ;BIOS (unimplemented) 
     FF5D:     JMP  0FFBEH         ;BIOS (unimplemented) 
     FF60:     JMP  0FFC0H         ;BIOS (unimplemented) 
     FF63:     JMP  0FFC2H         ;BIOS (unimplemented) 
     FF66:     JMP  0FFC4H         ;BIOS (unimplemented) 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 95
     Appendix A: Layout of CP/M Segment


     FF69:     JMP  0FFC6H         ;BIOS (unimplemented) 
     FF6C:     JMP  0FFC8H         ;BIOS (unimplemented) 
     FF6F:     JMP  0FFCAH         ;BIOS (unimplemented) 
     FF72:     JMP  0FFCCH         ;BIOS (unimplemented) 
     FF75:     JMP  0FFCEH         ;BIOS (unimplemented) 
     FF78:     JMP  0FFD0H         ;BIOS (unimplemented) 
     FF7B:     JMP  0FFD2H         ;BIOS (unimplemented) 
      
     FF80:     HALT                ;BIOS COLD BOOT hook 
     FF81:     RET 
     FF82:     HALT                ;BIOS WARM BOOT hook 
     FF83:     RET 
     FF84:     HALT                ;BIOS console status 
     FF85:     RET 
     FF86:     HALT                ;BIOS console input 
     FF87:     RET 
     FF88:     HALT                ;BIOS console output 
     FF89:     RET 
     FF8A:     HALT                ;BIOS list output 
     FF8B:     RET 
     FF8C:     HALT                ;BIOS punch output 
     FF8D:     RET 
     FF8E:     HALT                ;BIOS reader input 
     FF8F:     RET 
     FF90:     HALT                ;BIOS home disk 
     FF91:     RET 
     FF92:     HALT                ;BIOS select disk 
     FF93:     RET 
     FF94:     HALT                ;BIOS set track 
     FF95:     RET 
     FF96:     HALT                ;BIOS set sector 
     FF97:     RET 
     FF98:     HALT                ;BIOS set DMA address 
     FF99:     RET 
     FF9A:     HALT                ;BIOS read sector 
     FF9B:     RET 
     FF9C:     HALT                ;BIOS write sector 
     FF9D:     RET 
     FF9E:     HALT                ;BIOS list status 
     FF9F:     RET 
     FFA0:     HALT                ;BIOS (unimplemented) 
     FFA1:     RET 
     FFA2:     HALT                ;BIOS (unimplemented) 
     FFA3:     RET 
     FFA4:     HALT                ;BIOS (unimplemented) 
     FFA5:     RET 
     FFA6:     HALT                ;BIOS (unimplemented) 
     FFA7:     RET 

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 96
     Appendix A: Layout of CP/M Segment


     FFA8:     HALT                ;BIOS (unimplemented) 
     FFA9:     RET 
     FFAA:     HALT                ;BIOS (unimplemented) 
     FFAB:     RET 
     FFAC:     HALT                ;BIOS (unimplemented) 
     FFAD:     RET 
     FFAE:     HALT                ;BIOS (unimplemented) 
     FFAF:     RET 
     FFB0:     HALT                ;BIOS (unimplemented) 
     FFB1:     RET 
     FFB2:     HALT                ;BIOS (unimplemented) 
     FFB3:     RET 
     FFB4:     HALT                ;BIOS (unimplemented) 
     FFB5:     RET 
     FFB6:     HALT                ;BIOS (unimplemented) 
     FFB7:     RET 
     FFB8:     HALT                ;BIOS (unimplemented) 
     FFB9:     RET 
     FFBA:     HALT                ;BIOS (unimplemented) 
     FFBB:     RET 
     FFBC:     HALT                ;BIOS (unimplemented) 
     FFBD:     RET 
     FFBE:     HALT                ;BIOS (unimplemented) 
     FFBF:     RET 
     FFC0:     HALT                ;BIOS (unimplemented) 
     FFC1:     RET 
     FFC2:     HALT                ;BIOS (unimplemented) 
     FFC3:     RET 
     FFC4:     HALT                ;BIOS (unimplemented) 
     FFC5:     RET 
     FFC6:     HALT                ;BIOS (unimplemented) 
     FFC7:     RET 
     FFC8:     HALT                ;BIOS (unimplemented) 
     FFC9:     RET 
     FFCA:     HALT                ;BIOS (unimplemented) 
     FFCB:     RET 
     FFCC:     HALT                ;BIOS (unimplemented) 
     FFCD:     RET 
     FFCE:     HALT                ;BIOS (unimplemented) 
     FFCF:     RET 
     FFD0:     HALT                ;BIOS (unimplemented) 
     FFD1:     RET 
     FFD2:     HALT                ;BIOS (unimplemented) 
     FFD3:     RET 
     FFD4:                         ;rest reserved for scratch use




     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 97
     Appendix B: Bugs and Future Plans



      
                        Appendix B: Bugs and Future Plans                        _________________________________

      
     This section describes known bugs and otherwise strange Emulator
     activity. Please help us to improve the product by sending us your own
     bug reports, with as much detail as possible (including programs
     which demonstrate the bug). 
      
     These bugs will be fixed as time allows and user interest demands.

      
          Issue: The disassembly (list) command can become quite pokey.                                  list          ______
               As the control table grows, disassembly speed decreases.
               When disassembling the Model 100's ROM, for instance, the
               poor disassembler is faced with a control table that is
               something bigger than 42K in size. It may have to
               search most of the table for each memory reference. This
               yields a disassembly speed of a line or two a second.
               Boo! The control table search routines should be changed
               from a sequential to an indexed method.

          Author's Response: Agreed. Will rewrite these for a future          __________________
               release. 
      

          Issue: Some commands (notably those that accept a range of          ______
               CP/M addresses) get confused if they are asked to wrap
               around the high end of the 64K CP/M segment.

          Author's Response: Have applied fixes for most glaring          __________________
               problems. Would appreciate specifics (i.e. - which
               commands fail, and how) to help track down the rest. 
      

          Issue: Internal I/O redirection (effected by the Emulator, not          ______
               PCDOS) should be available for any Emulator command, not
               just the list command.                         list
      
          Author's Response: Agreed. Will look into it.          __________________








     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 98
     Appendix B: Bugs and Future Plans



          Issue: The patch command ought to allow multiple entries per                     patch          ______
               line, and ought to accept arguments on the patch command                                                          patch
               line without dropping into interactive patch mode. 
      
          Author's Response: Have provided left-handed solution by          __________________
               allowing a patch string on same line as patch command.                                                       patch
               True fix (with multiple byte values as independent args
               on command line) will take a while to implement.


          Issue: The Emulator lacks a mini assembler. It needs one.           ______
      
          Author's Response: Agreed. We just don't have the memory left          __________________
               in the 64K Lattice code segment to do it right. Maybe
               after some major rework...


          Issue: The Emulator's main program ought to be rewritten in          ______
               Microsoft C version 3.0. This will speed it up consider-
               ably, and will make it a lot smaller. 
      
          Author's Response: Agreed. The major effort is in reworking          __________________
               the assembler subroutines. There are a lot of places                                                      lot
               where Lattice's calling conventions, register usage, and
               segments are assumed.


          Issue: It would be nice to somehow state to the Emulator that          ______
               what is in CP/M memory is actually an 8080 or 8085
               program. This would allow the 8085's RIM and SIM instruc-
               tions, for example, to be properly disassembled (instead
               of being misinterpreted as Z80 relative jumps). 
      
          Author's Response: Agreed. The biggest obstacle to doing this          __________________
               is the same old bugaboo - no memory left in 64K code
               segment. Will put this off until we free up a couple of
               K in the code segment.











     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 99
     Appendix B: Bugs and Future Plans




          Issue: The loading of Z80 .COM files to be executed - in fact,          ______
               any file load that is done directly or indirectly by the
               "read" command - is just too slow.                read

          Author's Response: Agreed! This should be redone to bypass          __________________
               Lattice C's slow I/O routines. This problem may go away
               if and when the Emulator is rewritten in Microsoft 'C'
               version 3.0.
      

          Issue: The disassembler can get confused when a multi-byte          ______
               opcode crosses a control break. In general, it reverts
               to DB pseudo ops up to the control break when this
               happens. Also, it's not too smart when disassembling
               code with addresses up around the 64K segment boundary.
      
          Author's Response: I have tried to locate and eliminate          __________________
               peephole problems. The nature of the problem, however,
               goes to the very core of the disassembler as designed.
               This is not quickly (or cheaply) fixable.


          Issue: There are too many CP/M applications which abort          ______
               because they use BDOS functions 27/1Bh and 31/1Fh. These
               BDOS functions should be supported, even if they mean
               little on a PCDOS system.

          Author's Response: Agreed. The only reason that they haven't          __________________
               been emulated is that I have yet to find a sensible
               writeup of just exactly what the various data formats
               are. DRI's writeup stinks. If someone can provide a
               clear explanation of just what they truly mean, then
               I'll emulate them.


          Issue: There are more than 600 distinct instructions in the          ______
               Z80. Have they all been validated as to the accuracy of
               the emulation?

          Author's Response: So far, all we've done is run Z80 stuff and          __________________
               try to guess that it has run fine. All opcodes have been
               desk-checked. Not all opcodes have been tested. Most, in
               fact, have not even been executed. Would somebody please                                                                 please
               create a definitive test program? The diagnostics that
               we've tried (like Supersoft's) have proven to be inac-
               curate.

     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 100
     Appendix B: Bugs and Future Plans




          Issue: There should be an option to allow pagination of          ______
               disassembled object code.

          Author's Response: Agreed. Will look into another list include                                                            list include          __________________
               option to specify pagination.


          Issue: Expressions are currently limited to "+" and "-"          ______
               operators. They should allow "*" and "/" also, and maybe
               even AND, OR, XOR, shifts, etc.

          Author's Response: I disagree. The amount of work involved          __________________
               isn't justified by the benefit.


          Issue: The Z80 IN and OUT instructions should have access to          ______
               real 8088 I/O ports on the IBM PC.

          Author's Response: Over my dead body.          __________________


          Issue: FCB+14 and FCB+15 aren't emulated properly. This keeps          ______
               certain Microsoft-written subroutines from running.

          Author's Response: This has been fixed in release 2.1b, by          __________________
               censoring PCDOS's use of these bytes.


          Issue: LU version 3.00 fails.          ______

          Author's Response: LU expects BDOS results to come back in          __________________
               HL, not A. This is an undocumented facet of CP/M, but
               every version of CP/M that I tested does indeed return                                                   does
               results in HL as well as A. Fixed in Emulator release
               3.00 to return results in HL and A. Tested with LU, and
               it works fine.


          Issue: Some packages do full-screen I/O via BDOS, thus          ______
               missing the built-in VT52 emulator (which only responds
               to BIOS calls).

          Author's Response: Fixed. See the new "terminal" command,                                                 terminal          __________________
               which allows you to control who (BIOS or BDOS) goes
               through the VT52 emulator.


     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 101
     Appendix B: Bugs and Future Plans



          Issue: Clearing a single breakpoint causes the wrong one to          ______
               be removed.

          Author's Response: In improving the "break" command, I broke                                               break          __________________
               this part of it. It is now fixed.


          Issue: Disassembler unreliable in version 3.00.          ______

          Author's Response: Due to a mistake made when compiling          __________________
               version 3.00, we broke parts of the disassembler. It is
               fixed in version 3.10.


          Issue: Serial I/O via PCDOS is too slow! How about a full-          ______
               screen version of the Emulator?

          Author's Response: This is being developed, along with the          __________________
               port to Microsoft C version 3.0.


          Issue: The Label AUTOGEN commands hangs if the ending address          ______
               is 0FFFFh.

          Author's Response: Will be corrected in first Microsoft C          __________________
               version 3.0 copy of the Emulator, as this is due to a bug
               in Lattice C and I've fixed enough Lattice bugs for one
               lifetime. 


          Issue: BDOS Function 10/0Ah (read buffered console input)          ______
               doesn't work like it does in CP/M. You must press RETURN
               before input is terminated.

          Author's Response: This has been fixed in release 3.10. This          __________________
               BDOS function is now entirely emulated by the Z80 engine.
               Formerly, we just called PCDOS to do it.


          Issue: The stack does not contain a word of zeroes when a          ______
               .COM program is entered.







     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101



     "Z80MU" Z80 and CP/M 2.2 Emulator User's Guide            Page 102
     Appendix B: Bugs and Future Plans


          Author's Response: The stack pointer is set to FEFC. A word          __________________
               of zeroes is then stored there via:

                    cpm[0xfefc] = 0;    /* Put word of zeroes */
                    cpm[0xfefd] = 0;

               Lattice C, however, takes the hex literals as signed
               ints, and stores our zeroes into who knows where. This
               is all the more reason to dump this bad C compiler and
               move to Microsoft v3.0 C. Anyway, the zero word is now
               on the stack in version 3.10.


          Issue: The Emulator's VT52 terminal uses ESC F to clear the                                                   ESC F          ______
               screen. This isn't what a real VT52 uses.

          Author's Response: Fixed in release 3.10 to use ESC E. The Ze-                                                          ESC E          __________________
               nith Z-89 manual used as the VT52 reference contained a
               typo, and I coded from it.






























     COMPUTERWISE CONSULTING SERVICES, P.O. BOX 813, MCLEAN, VA 22101